## Slide 1: PPPL – TE Collaboration
Confidential

## Slide 2: Contents
Tokamak Energy – Who are we?
ST40 – High field ST
ST40 first operations and results
  Merging-compression start-up
  Magnetic reconstruction and camera images
Future of ST40

## Slide 3: Tokamak Energy Ltd.
Privately funded company, established in 2009 as a spin-off from Culham Centre for Fusion Energy
Team of ~80 staff
Located at Milton Park, Oxfordshire, UK
Spherical tokamaks (STs):
High beta + high bootstrap fraction = high efficiency
High Temperature Superconductors (HTS):
Superconducting in high magnetic field
Compact reactors
Notes: Combining STs and HTS to examine the possibility of building small fusion reactors.
HTS allows high current density and remains superconducting at high fields  possibility to have 20T on centre column surface.

## Slide 4: ST40 – High field ST
Design:
Bt =3T, Ip =2MA, R0 =0.4-0.6m, R/a=1.6-1.8 κ=2.5
Solenoid-free start-up using merging-compression
2MW of auxiliary heating (NBI / ECRH)
Pulse flat-top length 1s at nominal Bt

## Slide 5: Highlights (thus far)
Assembly in 2017, first plasma 17 January 2018
First experimental campaign completed in June 2018
~700 plasma pulses
Ip up to 350kA, BT,0=1T, Ti ~1keV, ne above 1020m-3
Ip flattop up to ~13ms
More to come: solenoid, NBI, more PSUs, plasma control, improved diagnostics, longer pulses, …
Notes: Start with highlights to whet you appetite

## Slide 6: First operations
Coils installed
  TF (24 turns): Irod,max =1725 kA*t  1T @0.34m
  MC (11 turns)
  BvL (16 turns) and Div (28 turns) in series
  BvU (8 turns): added during campaign
Notes: Two more pairs of PF coils will be added

## Slide 7: Magnetic reconstruction
Photron camera:
dt=100 μs
tinteg=2.5μs
Notes: During the first operations, this is what we had. Reconstruction of the plasma matches the camera images.
First light is pre-ionization using a flashlamp.
At the moment, fire and forget, next operations: plasma control. Still, without control, we managed to get fairly long flat-tops.
Plasma gets smaller due to high external Bv and decaying image currents. q* ≈ 2  kink instability limit

## Slide 8: Research goals
Extend high field ST physics basis  reduce uncertainty in predicting performance of future STs
  Expand ST τE database, particularly towards low ν, and confirm favourable scaling with Bt
  Evaluate solenoid-free start-up methods, including merging compression (MC) and EBW assisted start-up
  Develop RF heated scenarios with limited or no NB heating
  Test reactor relevant divertor solutions

## Slide 9: Upcoming Programmes
Programme | Goals | Comment
Programme 1 Q1 2019: Test readiness for 100M degree plasma temperatures | Demonstrate TEs ability to design, construct and operate a high field spherical tokamak Establish operational procedures Demonstrate diagnostics capabilities and data analysis tools Develop plasma control system | Repeat earlier performance with rebuilt device; fully commissioned PSUs & diagnostics; solenoid.
Programme 2 Q1 2020: 100M degree plasma temperatures | Demonstrate plasma current and position control Optimise beam + solenoid heated regimes Confirm favourable confinement at high field Explore diverted configurations | Bt,0=3T; 25ms, 1MW NBI; more PF PSUs to improve plasma control.
Programme 3 Q4 2020: Establish fusion conditions* | Develop operation with highly elongated plasmas Develop and optimise divertor scenario with NB + solenoid heating in DD Validate predictions of improved energy confinement in high field STs and document transport properties Validate SOL width scalings | New IVC with divertor; 2s, 1MW NBI; more PF coils/PSUs to improve plasma control.
*Fusion conditions is defined as central ion temperatures >10keV and densities >1020m-3

## Slide 10: Programme 1 configuration
Coil name | R centre (m) | Z centre (m) | Turns | LN cooled (Y/N)
MC | 0.750 | 0.355 | 11 | N
Div | 0.193 | 0.808 | 28 | N
BvL | 1.386 | 0.268 | 16 | N
BvU | 1.047 | 1.039 | 24 | N
Psh | 0.861 | 0.649 | 8 | N
Sol | 0.130 | 0.000 | 190 | N
TF | N/A | N/A | N/A | N
PSU name | Maximum voltage (V) | Maximum current (kA) | Controllable Duration (ms)
MC | 11000 | 51 | N/A
BvL | 500 | 25 | 0.74
BvU | 500 | 12.5 | 0.33
Psh | 2000 | 20 | N/A
Sol | 1150 | 17.1/11 | 1.1/2.0
TF | 385 | 125 | 0.12 (flat top)

## Slide 11: Programme 1 diagnostics
Category | Diagnostic name | Application | Plasma Parameters | Est. time resolution | Sector (Port)
Vis/UV Spectroscopy | Princeton Spectrometer (x1) 50 Chord Spectrometer | Doppler Zeeman splitting Beam Emission Spectroscopy CXRS | <Ti>, Ti(R), <vphi>, vphi(R) ne(R), ¦B(R)¦ ni(R) | 1-5ms | 8 (mid)
 | Avantes Spectrometer (x1) Single Chord Spectrometer | Doppler (of multiple lines 200-750nm) Zeeman splitting Beam Emission Spectroscopy Visible Bremsstrahlung Impurity Identification/monitoring | <Ti>, Ti(R), <vphi>, vi(R) ne(R), ¦B¦(R) ni(R) <Zeff> Impurity content | 1-5ms | 8 (mid)
 | Ocean Spectrometer (x1) Survey Spectrometer | Impurity Identification/monitoring | Impurity content | 1-20ms | 3 (upper)
 | Line Emission Monitor (8+4) Spectral Line Diodes | Impurity monitoring | Impurity content | 0.02ms | 8 (mid) / 3 (lower)
X-Ray Spectroscopy | Canberra Spectrometer (x1) X-ray spectrometer | High energy tail bremsstrahlung Impurity Identification/monitoring | <Te> | 10ms | 1 (mid)
 | Crystal X-ray Spectrometer (x1) | Doppler (Fe-XXV) | Ti(R) | 1-10ms | 2 (mid)
 | SXR Tomography (x3) Soft X-ray spectrometer | No filter – Bolometry With filter – Tomography | Radiated power Te(R) | 1-10ms | 2 (lower / mid / upper)
Interferometry | Near-InfraRed interferometer (x1) |  | <ne> | 0.05ms | 3 (mid)
 | Submillimetre interferometer (x2) |  | <ne> | 0.05ms | 3 (mid)
Cameras | Fast Camera (x1) | Visible – monochrome | Boundary shape PFC temperatures | 0.067ms | 5 (mid)
 | H-alfa Camera (x1) | H-alpha – monochrome |  | 1-2ms | 3 (mid)
 | Marketing Camera (x1) | Visible – colour |  | N/A (acquires 1 frame) | 5 (mid)
 | IR Camera (x1) | IR - monochrome |  | 33.3ms | 3 (mid)
Magnetics | Rogowski Coils (x23) | EFIT/PFIT Specplot | Internal plasma parameters MHD modes | 0.01ms | N/A
 | Saddle Loops (13+3+3+3+13+3+3+3) |  |  | 0.01ms | 1/2/3/4/5/6/7/8
 | Flux Loops (x48) |  |  | 0.01ms | N/A
 | BP-Probes (34+1+34+1) |  |  | 0.01ms | 1/3/5/7
 | BT-Probes (2+2+2+2) |  |  | 0.01ms | 1/3/5/7
 | Diamagnetic Loops (2+2) |  |  | 0.01ms | 1/5
DNBI | Diagnostic Neutral Beam (x1) Budker DNBI (100kW/50keV) | Beam Emission Spectroscopy CXRS | (See Avantes and Princeton) | 5ms (beam modulation) | 7 (mid)
ECE Radiometer | ECE Radiometer (x8) |  | <Te> | 0.05ms | 3 (mid)
NPA | Neutral Particle Analyser (x1) |  | Ti (peak – no profile) | 0.01-1ms | 4 (mid)

## Slide 12: Programme 2 configuration
PSU name | Maximum voltage (V) | Maximum current (kA) | Controllable Duration (s)
MC | 11000 | 73 | N/A
Div | 500 | 23 | 2.0
BvL | 500 | 44 | 1.78
BvU (x2) | 500 | 12.5 | 2.0
Psh | 2000 | 20 | N/A
Sol | 1150 | 17.1/11 | 1.1/2.0
TF | 385 | 250 | 1.0 (flat top) TBD (pulse duration)
Coil name | R centre (m) | Z centre (m) | Turns | LN cooled (Y/N)
MC | 0.750 | 0.355 | 11 | N
Div | 0.193 | 0.808 | 28 | Y
BvU | 1.047 | 1.039 | 24 | N
BvL | 1.386 | 0.268 | 16 | Y
Psh | 0.861 | 0.649 | 8 | N
Sol | 0.130 | 0.000 | 190 | Y
TF | N/A | N/A | N/A | Y
Auxiliary system | Description
RFX NBI | 1MW / 25keV / 30ms

## Slide 13: Programme 3
Major upgrade after Programme 2:
  New inner vacuum chamber (IVC2) – divertor, passive plates, space allocated for EBW and pellet injector,…
  1MW, 55keV, 2.0s HNBI
  Two new pairs of PF coils – capability for 2MA operation, improved shaping, and strike-point control
Final design reviews in early 2019

## Slide 14: Programme 3 configuration
PSU name | Maximum voltage (V) | Maximum current (kA) | Controllable Duration (s)
MC | 11000 | 51 | N/A
Div | 500 | 23 | 2.0
BvL | 500 | 44 | 1.78
BvU (x2) | 500 | 12.5 | 2.0
BvM |  |  | 
SX |  |  | 
Psh | 2000 | 20 | N/A
Sol | 1150 | 17.1/11 | 1.1/2.0
TF | 385 | 250 | 1.0 (flat top) TBD (pulse duration)
Auxiliary system | Description
RFX NBI | 1MW / 25keV / 30ms
HNBI (Budker) | 1MW / 55keV / 2.0s
Coil name | R centre (m) | Z centre (m) | Turns | LN cooled (Y/N)
MC | 0.750 | 0.355 | 11 | N
Div | 0.193 | 0.808 | 28 | Y
BvL | 1.386 | 0.268 | 16 | Y
BvU | 1.047 | 1.039 | 24 | N
BvM |  |  |  | 
SX |  |  |  | 
Psh | 0.861 | 0.649 | 8 | N
Sol | 0.130 | 0.000 | 190 | Y
TF | N/A | N/A | N/A | Y

## Slide 15: Collaborations
For impact on Programme 3: now is the time!
IVC2 design on-going – diagnostic requests and recommendations still possible
Physics Programme flexible

## Slide 16: Thank you!

## Slide 17: Backup slides

## Slide 18: TE Milestones to date
ST25: working prototype with copper magnets achieved several second RF plasmas and
Demonstrated that Tokamak Energy can rapidly build and test working prototypes
ST25 (HTS): first tokamak featuring all high temperature superconducting magnets
Achieved continuous plasma for 29 hours – a new world record
ST40: worlds first high field spherical tokamak
First operations started in January 2018

## Slide 19: Merging-compression start-up
[1] F. Alladio et al., Status and perspectives of MAST start-up in the absence of solenoid flux, 33rd EPS Conference on Plasma Phys. Rome, 19 - 23 June 2006, P-1.095
MAST pulse #14412 [1]
Notes: Limited space in ST centre column  Solenoid-free start-up important
Method pioneered in START [1] and MAST [2] at Culham Centre for Fusion Energy by our founders
Converts magnetic energy of two plasma rings into plasma kinetic energy through magnetic reconnection
Current ramped down rapidly in high voltage MC coils to create a plasma around the coils
Compress plasma along major radius R to further increase Ip (W=LI2/2=const.)

## Slide 20: Diagnostics available already
Two fast monochrome cameras
Spectrometer (200-700nm), line diodes
Magnetics: Bp-probes, flux loops, Rogowski coils, diamagnetic loops
NIR interferometer, ECE radiometer

## Slide 21: Typical ST40 pulse
ST40 pulse #5118
  PF and TF coils ramped up
  MC PSU fired
  Induced currents in coils partly compensated by the PSUs
  Induced currents in passive structures decay naturally
Full pulse
Notes: Fast MC swing induces ~1MA into vessel.

## Slide 22: Typical ST40 pulse
ST40 pulse #5118
  PF and TF coils ramped up
  MC PSU fired
  Induced currents in coils partly compensated by the PSUs
  Induced currents in passive structures decay naturally
Full pulse

## Slide 23: Typical ST40 pulse
ST40 pulse #5118
  PF and TF coils ramped up
  MC PSU fired
  Induced currents in coils partly compensated by the PSUs
  Induced currents in passive structures decay naturally
disruption
Zoom in
MC coil
2nd trigger
merging-compression
flat-top
Notes: Merging starts before the bottom of the dip
Actually, induced currents are really important during compression…

## Slide 24: Magnetic reconstruction
Good match with camera images
Plasma gets smaller due to high external Bv and decaying image currents
Kink safety factor q* ≈ 2  instability
Longest flat-top durations achieved at highest TF
Highest Ip achieved with highest MC coil currents

## Slide 25: Temperature measurements
vessel
Spectrometer LoS
MC coil
LCFS
Ion Doppler broadening using spectrometer (200-700nm)
50 chords: vertical/horizontal and radial/tangential alignments to rule out effect of rotation
Experiments w/ various lines: CIII (464.74nm), CV (227.09nm), BIV (282.16nm)
Notes: Precise numbers still a work in progress. Unsuccessfully tried: , CVI (529.05nm), CV (494.4nm), FeXIV (530.29nm)

## Slide 26: Temperature measurements
Ion temperature in the range [800,1500] eV
  High, considering no auxiliary heating
  Maximum temperatures up to and even above 2keV measured in presence of transient events (small IREs etc.)
  More data analysis needed
Notes: Maximum temperatures, up to and even above 2keV, were measured in a presence of transient events (small IREs etc)

## Slide 27: Temperature measurements
Pulses #5079, #5080, #5081 and #5090 combined to improve statistics
Measuring CV line
Spectrometer aligned horizontally

## Slide 28: Temperature measurements
Pulses #5079, #5080, #5081 and #5090 combined to improve statistics
15M degrees!
Overall, Ti in the range [800,1500] eV
  Timax ~2keV in presence of transient events (IREs etc.)
15M deg

## Slide 29: High plasma densities
NIR interferometer: line averaged densities 1020 m-3
  Accurate measurements not yet possible due to vibrations
ECE radiometer: ne regularly above 1020 m-3 because 3rd harmonic signal (100GHz) is cut off
Midplane cross-section of plasma cut-offs and resonances for majority of ST40 first operations: ne = 1020 m-3, ITF = 50 kA (Bt,0=0.6 T)
Radiometer range
Frequency, GHz
fce
2fce
3fce
fpe
fX-cutoff
Major Radius, cm
17 22 27 32 37 42 47 52 57 62 67
110
100
90
80
70
60
50
40
30
20
10
0

## Slide 30: Well-defined plasma edge
ST40 – Pulse #5027 – 756.10 ms
ST40 – Pulse #5027 – 756.20 ms
ST40 – Pulse #5027 – 756.40 ms
ST40 – Pulse #5027 – 756.50 ms
ST40 – Pulse #5027 – 756.60 ms
ST40 – Pulse #5027 – 756.00 ms
ST40 – Pulse #5027 – 756.30 ms
Notes: Colour adjusted image

## Slide 31: Confinement scalings
Inverse scaling of normalized confinement with ν*
Aim to get to low collisionality
ST40
HNSTX=1
ST40
HITER=1
MAST
MAST
Electron neoclassical limit for ST40