Action: 	Decide on cryo-baffle entrance radius range (DONE):

“Decision”:  Should assume Rent = 0.7-0.75 (possibly a bit smaller) for now, i.e. will very likely need to modify/take over entire OBD plate/region.

Action: 	Still need to link cryo design analysis to projected line-avg densities and greenwald fractions

MJ and SG:  Identify two shots with good Langmuir probe data for SOL density profiles (need data from separatrix to far SOL, for linking separatrix ne to cryo-baffle entrance ne)

Find lowest Ip, lowest greenwald fraction ( 0.5 (look early in shot)

Find highest Ip, highest greenwald fraction ( 1 (look late in shot)

Mike J – maybe focus on comparing ne at psin = 1.05 vs. psin of 1?

Mike J - Te at far SOL, how does this scale with pedestal density and PSOL?  (JC wants this for his analysis/modeling)

Stefan:  density at separatrix vs. line average density – use TRANSP, or small set of relevant LRDFIT04s  or use Vlad’s paper Figure  3.

Cryo question:  NSTX-U 5 year plan is likely to be:  dedicate upper outer divertor to cryo-pumping, lower outer divertor to (liquid) lithium testing.  But is one cryo enough to pump relevant scenarios?  JC analysis will hopefully answer this.

Lithium persistence actions/questions:

JC has data for analysis of time-dependence of recycling vs time from:  129038 (low delta shot) from D. Boyle = reasonable profile fits – 3 times in shot:  320, 520, 620 ( no significant change in Rp = 0.9 approx. constant throughout the shot…

- Action: MJ and VS to send SG calibrations for gas input… ( HFS and LFS  (DONE)

- Action:  SG to give JC longer pulse shots (DONE)

  - Want to look at longer-pulse shots – longer pulse length…

  - Focus on 129125 range of shots with small ELMs after LiTER ran out – do these have saturated pumping?  Apparently not…

- Action:  JC to perform time-dependent recycling coefficient determination of above shots (if possible) or find similar shots.  Want a shot (few shots?) with 0.9-1.5s flat-top.