## Slide 1: NSTX-U extended RWM sensor calculations are underway
Extended RWM magnetics calculations initiated based on group meeting
  Add divertor plate detail to VALEN model
  Determine the change in measured mode amplitude in the sensors placed at various poloidal positions moving toward the divertor
    Examine potential Btan and Bnorm sensors at increased |poloidal angle| off midplane, plot field amplitude vs. R, or poloidal angle; consider sensor positions mirrored above the midplane
  Redo above calculation with the plasma shifted down in Z (-5 cm, -10 cm)
    Determine field amplitude vs. R, or poloidal angle, at different plasma Z position.
New sensor locations discussed (schematic) (includes possible locations in THIS range (+ one position above midplane)
n = 1 ideal eigenfunction for fiducial plasma
Present sensor locations
Z(m)
R(m)
BR sensors (nominally normal, Bnorm)
Bp sensors (nominally tangential, Btan)

## Slide 2: NSTX-U partial NCC coil – initial considerations taken in total point to a preferred placement of coils
Partial NCC coil considerations
  Partial NCC is VERY IMPORTANT, as it appears in the BASE budget
  Many key physics studies can be performed with the partial NCC (vs. full NCC)
Considerations / configurations for suggested partial NCC set (12 or 6)
  RWM: want n = 1,2 field toroidal propagation, compliment n = 3 phases from RWM coil
  EFC: (same considerations as RWM),
  ELM: symmetric placement gives greatest flexibility, but might desire higher-n
  NTV: symmetric placement / higher-n both allow important physics studies
  ITER / JT-60SA: symmetric coil set is most ITER-like (although lower-n), best to support ITER physics; partial set can support JT-60SA
  NSTX-U cryopump: any issues of NCC placement on 2ndary passive plates?
  Short-term conclusion: Symmetric placement to start (perform higher-n w/full NCC)
    Best: 12 new coils: 6 above / 6 below midplane, placed in front of every other passive plate
    2nd best: 6 new coils: 6 above or below midplane, placed in front of every other passive plate
    Possible: 12 new coils, either above / below midplane, placed in front of each passive plate
Ramifications for NCC section of 5Y Plan: section needed mods anyway
  Physics program needs to be strong w/o the NCC, but strongly compelling with the NCC
  With partial NCC in BASE budget, easier to integrate NCC in the physics deliverables
  Partial NCC provides a logical bridge to the full NCC / further physics deliverables

## Slide 3: NSTX-U partial NCC coil – initial discussion and planned calculations
Partial NCC coil RWM calculations planned (aimed in time for PAC)
  Re-run RWM active control calculations at the best gain from past analysis for a few partial coil options (coils in front of primary passive plates first)
    12 coils, positioned 6 above the midplane, 6 below the midplane
    6 coils, positioned above the midplane
  The second set of runs would be with coils in front of the secondary passive plates
    12 coils, positioned 6 above the midplane, 6 below the midplane
    6 coils, positioned above the midplane
Primary
PP option
Secondary PP option
Existing
coils
Full NCC calculations