## Slide 1: Goals of NSTX Advanced Scenario and Control TSG
Study, implement, optimize axisymmetric control techniques.
  Kinetic and magnetic profiles.
  Boundary and divertor magnetic geometry control.
  Vertical position control.
Combine various tools developed in other TSGs into integrated scenarios.
  For instance, ELM pacing XPs targeting density control were in ASC.
  Impurity control for scenario development in FY-10.
High non-inductive fraction under NB heating has been in ASC.
  Typically coupled with optimization to high-k.
  NBCD is ASC, but details of fast ion transport & redistribution are WEP
  However
    RF CD and low-current 100% NI scenarios with HHFW H&CD have historically been in WEP TSG.
    Maximization of bN part of ASC, but more in MS.
Discharge development for the NSTX team (sometimes).
NSTX ASC research was always cross-cutting, and will be even more so in NSTX-Upgrade

## Slide 2: Two Overarching Theory/Modeling Needs
1: Need advanced control algorithms for boundary shape, divertor geometry, kinetic and magnetic profiles, and divertor heat fluxes.
  Should include actuator dynamics & saturation.
2: In order to tune those control algorithms, need integrated codes with fast, benchmarked models for how sources of particles, momentum, heat and current modify the kinetic and magnetic profiles and free-boundary equilibrium.

## Slide 3: Need #1: Models for Scenario Development
NBCD with *AE modes
  In the absence of low-f MHD, the neutral beam drive current is apparently classical.
  At higher values of bfast, *AE modes can lead to redistribution/modification of the fast ion distribution.
  Theory is needed for when these modes will turn on, and what their effect on the pressure & current profile will be.
  Need measurements of fast ion distribution (FIDA, neutrons, ssNPA, fusion product detector) and NBCD profile for comparison.
Prediction of the thermal & momentum transport
  The bootstrap current depends sensitively on the gradients in the thermal profiles. NBCD depends on Te/ne. Global stability depends on rotation.
  Conversely, the transport, and hence thermal profiles, can be a strong function of the current and rotation profiles
  Need a model for the thermal and momentum transport and its response to actuators.
  Include both core & pedestal (and the joining region), including fast-ion MHD leading to transport.
Need accurate, benchmarked models for HHFW and EBW H&CD within integrated codes such as TRANSP.

## Slide 4: Need #2: Realtime Control
Need a reliable algorithm for the individual and combined control of the current and rotation profiles, along with bN.
  The theory of that algorithm should help us to understand to what extent these quantities can be independently controlled given the coupled actuators Vloop, Pinj, JNBCD, TNB and TNTV.
More generally, need the ability to test the actual control algorithms in simulations with high degrees of physics fidelity, i.e. flight simulator mode.
  Could in principle be accomplished by connecting PCS to PTRANSP, CORSICA, or TSC.
Need the ability to predict the future equilibrium and stability properties of the plasma.
  Faster than realtime look-ahead of the evolution of the equilibrium
    (Very) reduced transport models.
  Stability assessments of those future states (n=0, n=1, ELM?). Future coil currents and boundary shape.
  Control intervention based on the predictions.