## Slide 1: Flow and Shear behavior in the Edge and Scrape-off Layer in NSTX L-Mode Plasmas
Y. Sechrest and T. Munsat
University of Colorado at Boulder
S. J. Zweben and R. J. Maqueda
Princeton Plasma Physics Laboratory
D. D’Ippolito, J. Myra, and D. Russell
Lodestar Research Corporation
PPPL Monday Meeting – Sept. 20, 2010

## Slide 2: Overview
What we do: Extract/Analyze estimates of 2-D velocity field from image sequences obtained by Gas Puff Imaging
Purpose: Study behavior of plasma flow (2-D flow, shear, Reynolds stresses) in the NSTX edge region.
Why?
  Turbulent transport:
    significantly degrades confinement
    Turbulence interactions with large scale (Zonal) flows
      Self-generation of flow
      suppression of turbulence through shearing
  Explore flow organization and momentum transport in plasmas

## Slide 3: Outline
  Background
  Basic flow characteristics
  Quasi-periodic Turbulent bursts
  Characterization of 3 kHz fluctuations
  Shear, Reynolds stresses – Time permitting

## Slide 4: Gas Puff Imaging: Basics
GPI:
images edge turbulence
manifold discharges gas puff into edge region
images visible light emission
emission complicated function of ne and Te
GPI on NSTX:
view centered 20 cm above the outboard midplane
~ 25 cm x 25 cm view
~4 mm resolution
Dα line emission (656 nm)
285,000 fps (3.5 μs per frame)

## Slide 5: HOP-V Analysis: Basics
Hybrid Optical flow and Pattern-matching Velocimetry (HOP-V)
Optical Flow:
  Solves continuity equation for image brightness:
  assuming divergence free flow
Pattern Matching:
  Subdivide image into tiles
  Search for optimal displacement vector for each tile
  Minimize global error function
    Brightness difference
    Velocity field smoothness

## Slide 6: HOP-V Analysis: Basics

## Slide 7: Time-Averaged Velocities
10 ms time average
Cropped field to avoid edge effects
  vignetting of optics
  gas emission profile
Radial profiles of poloidal velocity
Fluctuation levels are comparable to size of mean flow
Vpol Shear
Ion diamagnetic

## Slide 8: Time Traces
GPI intensity (normalized), Poloidal Velocity, and Radial Velocity poloidally averaged at x = -1 cm
GPI signal:
  fluctuation amplitude as large as mean value
Poloidal flows:
  On the order of several km/s
  Large amplitude fluctuations
  Bursty flow oscillations
  Anti-correlated with GPI
Radial flow:
  significantly smaller: 100 m/s
  Large radial velocity usually associated with blobs
  Blobs are spatially localized and intermittent

## Slide 9: Quasi-Periodic Bursts
FSOL = Fraction of Dα light in the SOL
Flow Reversals
High correlations
Periodic bursts
R = -0.59
R = -0.61
R = -0.60

## Slide 10: Spectral Characteristics
Spectrogram of FSOL
  time window: 256 points (~0.9 ms)
  ~1 kHz frequency resolution
Strong feature near 3 kHz
Sporadically appears between 2-4 kHz
Intermittent with duration of 1-2 ms

## Slide 11: Spatial Structure of 3 kHz Oscillation

## Slide 12: Phase of the ~3 kHz Mode
Phase profiles for sections of 4 shots with rotating mode.
GPI Phase:
  Rapid phase change between x = -2 and x = 1
  Nearly linear poloidal phase dependence
  kpol ~ 10 m-1
Vpol Phase:
  Vs. X – Mostly in phase for several centimeters. Rigid Rotation?
  Vs. Y – Near linear phase dependence
  kpol ~ 5 m-1

## Slide 13: Coherence in Poloidal Direction
Coherence function and Phase vs. Frequency
  Vpol signals at x = -1 cm
  separated by ~12 cm in y
3 kHz mode:
  Strong coherence peak near 3 kHz
  Small phase difference
F > 10 kHz:
  Coherence drops off
  Phase differences become random
  Turbulent

## Slide 14: Coherence in Poloidal Direction
Coherence of Vpol as a function of poloidal separation for shot 135042
3 kHz:
  Maintains high coherence values over full ~12 cm
  Correlation length: 56 cm
20-30 kHz:
  Background Turbulence
  Correlation decays rapidly
  Correlation length: 4 cm

## Slide 15: Radial Dependence of Spectra
Vpol spectra for shot 135042 at 3 different radii
Frequency of peak approximately constant
Amplitude significantly smaller in SOL
Shot 135042, t: 240-243 ms

## Slide 16: Recap: 3 kHz mode
What we see:
  Strong mode seen intermittently in GPI, FSOL, and Vpol fluctuations
    Roughly 2 kHz spread in frequency space
    Duration of 1-2 ms
  Exhibits long poloidal wavelengths in both GPI, and Vpol
  Long poloidal correlation lengths
    - Large scale coherent flow oscillation
  Vpol phase difference remains near zero over ~4 cm radial separation inside sep.
  Frequency independent of radius
  Amplitude of flow oscillations decays in the SOL
    - Radial Size ≥ 4 cm

## Slide 17: Possible Explanations for 3 kHz Behavior
SOLT simulations illustrated the importance of zonal flows in controlling turbulence. (Russell PoP 2009)
  Shearing of flows suppress bursts
  Flow damping a critical control parameter
  Unclear what controls frequency of bursts
Geodesic Acoustic Mode (GAM):
  Finite frequency zonal flow
  n=0,m=0 velocity fluctuation – long poloidal wavelength/correlation
  finite kr , propagates radially
  ω = Cs/R
Refilling of plasma along field line
  Loss of plasma due to bursts
  Scales like V||/R
  f ~ 7 kHz for Te = Ti = 50 eV, R = 1.5 m

## Slide 18: Acknowledgements
We would like to thank K. Hallatschek, and R. Hager for their communications.
We would also like to acknowledge the NSTX Team for their contributions.
This work was supported by US DOE Contracts #DE-FG02-08ER54995, DE- SC0001966, and DE-AC02-09CH11466.
My thanks to the co-authors for their work and support.
Thank you for your attention.

## Slide 19: Shearing Rate and Reynolds Stresses
Shearing of poloidal flows predicted to modulate turbulent bursts
  recent SOLT simultations illustrated this (Russell PoP 2009)
Find that shear is correlated with bursts
  correlation = 0.52
However, relationship is not simple.
  Other sections don’t show high correlation
  shear threshold?
  low shear doesn’t always lead to burst

## Slide 20: Shearing Rate and Reynolds Stresses

## Slide 21: Shearing Rate and Reynolds Stresses
Radial profiles of Reynolds shear stresses
  averaged poloidally and over 10 ms time period preceding H-mode
Similar features seen in each shot
  local maximum near x = -1 cm
  negative slow between x = -1 and x = 2

## Slide 22: Phase of the ~3 kHz Mode
GPI
Vpol
GPI-Vpol
Rapid phase change between x= -2 and x= 1 cm
Phase changes slowly in poloidal direction
Slow phase change in both directions
Mostly in phase over entire view
Cross-Phase dominated by GPI signal

## Slide 23: Phase of the ~3 kHz Mode
GPI
Vpol
GPI-Vpol
Rapid phase change between x= -2 and x= 1 cm
Phase changes slowly in poloidal direction
Slow phase change in both directions
Mostly in phase over entire view
Cross-Phase dominated by GPI signal