## Slide 1: Impurity transport analysis & preparation of W injection experiments on KSTAR
February 18, 2014
Joohwan Hong*, Seung Hun Lee, H. Y. Lee, Juhyeok Jang,
Juhyung Kim, Siwon Jang, Taemin Jeon ,Jae Sun Park
and Wonho Choe**
Korea Advanced Institute of Science and Technology (KAIST), Daejeon, Korea
C. R. Seon, Suk-ho Hong, and KSTAR team
National Fusion Research Institute (NFRI), Daejeon, Korea
S. Henderson, M. O’Mullane
University of Strathclyde, UK
*joohwanhong@kaist.ac.kr
**wchoe@kaist.ac.kr

## Slide 2
Outline
1. Introduction
- Current issues on W in tokamak plasmas
2. Current analysis tools for impurity transport study on KSTAR
- ADAS-SANCO impurity code analysis
- Diagnostics: SXR and VUV
- Example : ECH effects on Ar transport experiments
3. Preparation of W experiments
- Upgrading diagnostics : SXR and VUV
- Estimation of Ar & W emission power on KSTAR for designing SXR
filters
4. Summary & Discussions

## Slide 3
  W injection experiments on KSTAR (superconducting machine)
  Influence of W divertor on the access to the H-mode
  Effect of W divertor on pedestal parameters and plasma confinement
  Predicted impacts of wall and divertor material on pedestal structure
  High radiation loss from W core accumulation
R. Neu, ADAS Workshop, 2007, Ringberg
Current issues on W in tokamak plasmas
  ITPA: “Transport of high Z impurities (including W) in the core plasma and possibilities for its control”

## Slide 4: Current analysis tools for impurity transport study on KSTAR - Focused on Ar injection experiments
Transport codes (ADAS-SANCO)
Diagnostics (SXR & VUV)
Experiments & analysis results

## Slide 5
SANCO (collaboration with JET) 1D radial continuity equation
- Radial particle flux
Impurity transport analysis
: impurity ion density
: particle flux via magnetic surface
: source and sink (ionization & recombination from ADAS)
Diffusion coefficient
Convection coefficient
- Impurity transport code SANCO
- Fitting analysis code
UTC
KSTAR diagnostics
Soft X-ray array
VUV spectrometer
X-ray imaging crystal spectrometer, etc…
Impurity transport modelling
Experimental
data
D, V
determination
Fitting

## Slide 6
Soft X-ray arrays with Ar Ross filter
16 ch (32)
16 ch (32)
X-ray Ross Filter (XRF)
  NaCl and CaF2
  Band pass filter within the narrow region between
  their L III or K absorption edges
KSTAR D-port
2.8-4.0 keV
Ar13+, Ar14+, Ar15+, mainly Ar16+, Ar17+

## Slide 7
Model for Ar emission in soft X-ray range
Power coeffs of Line Transition
Power coeffs of RecomBination
(2) Response function of Ross filter
(1) Calculation of local Ar radiation power (r,t)
Obtaining
2.8~4 keV
(3) LoS calculation and line integration
- ne from input data, nz from SANCO, PLT & PRB from ADAS

## Slide 8: ITER VUV spectrometer prototype
Current (15-60 nm, ~13-40 ms)
Vacuum extension
VUV spectrometer on the optical table
Collaboration with ITER KO-DA (C.R. Seon)
1 ch, survey
He I 53.70 nm
He II 25.63 nm
O V : 15.61, 19.28, 21.50 nm
O VI : 17.30, 18.40 nm
C III : 38.62 nm
C IV : 24.49, 38.41, 41.96 nm
C V : 22.72, 24.87 nm
Fe XV : 28.42 nm
Fe XVI : 33.54, 36.08 nm
Ar XIV 18.79 nm
Ar XV 22.11 nm
Ar XVI 35.39 nm
- All atomic coefficients are from ADAS
(2) Modeling of Ar line transitions
(1) Measurable major line transitions

## Slide 9
L-mode plasmas, Ip = 400 kA, Bt : 2 T
Argon gas injection through a piezo valve (trace amount of Ar : nAr/ne < 0.1%)
Different transport w/o and w/ ECH positions  Feasibility of impurity control?
On-axis ECH
Ar
0.4
0.2
0 1 2 3 4
Time (sec)
Ip (MA)
Ar puffing
20 ms
0.4
0.2
0 1 2 3 4
Time (sec)
Ip (MA)
Ar puffing
20 ms
ECH
110 GHz
300 kW
Non ECH
On-axis ECH
Ar puffing after ECH start  To see ECH effect on Ar
Ar transport experiments with ECH

## Slide 10
SXR emissivity
(Non ECH)
SXR emissivity
(On-axis ECH)
VUV Ar15+
t
2.8 – 4 keV photons
Mainly Ar16+ & Ar17+ emissions
ECH
r
r
Less core Ar emissivity with ECH
Ar puff
Non-ECH
ECH

## Slide 11
Ch1
Ch16
Convection
Diffusion
ADAS-SANCO analysis results
L-mode
Non-ECH

## Slide 12
Ch1
Ch16
Convection
Diffusion
L-mode
On-axis ECH
Diffusion & convection with ECH

## Slide 13: Preparation of W experiments
Upgrading current diagnostics (VUV & SXR)
Estimation of W & Ar emission power on KSTAR for designing filters of new SXR system

## Slide 14: VUV imaging spectrometer
This summer(5-20 nm, 13-130 ms)
28 ch, imaging
Collaboration with ITER KO-DA (C.R. Seon)
25.4 nm He II from Hollow Cathode Lamp
~5.5 mm Slit Imaged to CCD
Slit Pattern Spacing ~ 2mm
5~7 nm quasi-continuum
peaks of W are expected
24.6 nm
23.4 nm
Preparation in laboratory
• Active pixels: 1024 x 256
• Pixel size (W x H): 26 x 26 μm
• Image area: 40 mm x 12mm
of MCP adopted to CCD of 27.6
Clementson et al. Rev. Sci. Instrum. 81, 10E326 2010

## Slide 15
4 arrays, 256 ch
4 arrays, 256 chs
 2D Tomography
 Poloidal asym.
study
< 2 cm, 2 μs
1 array, 48 ch
3 filters
 multi energy,
neural network
< 1.3 cm, 2 μs
HU
HD
VD2
VU2
Soft X-ray array system
This summer
Current
16 ch (32)
16 ch (32)
2 arrays, 64ch
Be filters (10, 50 um)
Ar Ross filters (2.8-4.0 keV Ar16+, Ar17+)
Bolometer (No filter)
 2D fast MHD & transport study
edge

## Slide 16
For designing new multi-array SXR filter to measure W & Ar emission,
ADAS-SANCO simulation has been done
Estimation of W & Ar emission power
EFIT
Background
(Te, ne)
D, V
(Trial value)
Impurity Influx
Input
SANCO
nz(r, t)
ADAS
Calculates line emission for every line transition
Te, ne
Line integration along LOS
 Final power spectrum of W & Ar
Calculates…
nz(r, t) for every charge states z of W & Ar

## Slide 17
Te & ne profiles of typical KSTAR L-mode and H-mode
- Evaluated by ECE, TS, interferometer.
(3) EFIT
#7566 @ 2 s
By S. Sabbagh
(2) Influx : flow meter signal for both W & Ar
Input profiles for ADAS-SANCO
Recycling rate
Ar = 0.6
W = 0.0

## Slide 18
- D & V for L mode (experimentally obtained from KSTAR #7574 Ar)
- D & V for H mode (from ASDEX-U results)
T. Putterich, 2005, ‘Investigations on Spectroscopic Diagnostic of High-Z Elements in Fusion Plasmas’ , PhD Thesis University Augsburg
Input profiles for ADAS-SANCO

## Slide 19
Time evolution of line-integrated spectra
(1) L-mode
(2) H-mode
Ar
W
Ar
W
Photon energy (keV)
Time (s)
Brightness (W cm-2)

## Slide 20
L-mode case
H-mode case
W & Ar emission spectrum under KSTAR condition
W peaks
Ar peaks
(Ross filter)
W peaks
W quasi-continuum
(VUV)
where
with C dominant situation
Continuum radiation was calculated by
S. von Goeler et al., Nucl. Fusion 15, 301 (1975)
Zeff ~ 2.5
Ar peaks
(Ross filter)
W cm-2 eV-1
W cm-2 eV-1

## Slide 21: Summary
Impurity transport analysis tools on KSTAR
- ADAS-SANCO impurity transport code
- Soft X-ray array system and VUV spectrometer system
- It has well worked for KSTAR Ar injection experiments since 2012.
W injection experiment is under preparation on KSTAR
- Imaging VUV spectrometer having W quasi-continuum peaks is installed on KSTAR F-port.
- Additional SXR arrays will be installed on KSTAR D-port with Be filters for W and Ar measurement.
- ADAS database set is also ready for simulating W emissions in fusion plasmas.

## Slide 22
Discussions
(1) SXRA filter design for discriminating W and Ar emission
Delgado-Aparicio et al., Nucl. Fusion 49, (2009) 085028
50 m
100 m
250 m
300 m
400 m
Be filters of
L-mode case
W cm-2 eV-1

## Slide 23
Discussions
(1) SXRA filter design for discriminating W and Ar emission
Be 50 & 250 m seem to be appropriate for L- & H- modes.
50 m
100 m
250 m
300 m
400 m
H-mode case
W cm-2 eV-1
50 m
100 m
250 m
300 m
400 m
Be filters of
L-mode case
W cm-2 eV-1

## Slide 24
Estimated value ~ 6 X 1016 atoms (~ 18 g)  Too small!
Particles should be injected more, in order to obtain the same Ar emission level, since all particles can not penetrate into LCFS.
Calculated Brightness filtered by 50 m (in W/cm2)
Brightness from Continuum = 1.10 X 10-1
Brightness from Ar emission = 1.12 X 10-1
Brightness from W emission = 5.52 X 10-1
W emission level is larger than Ar by 5
Injected W should be reduced by 5 ?
Estimation conditions
  - Injected # of atoms = 3.0 x 1017 for W & Ar
  Find out amount of W providing similar Ar radiation level ( W/cm2 , > noise level of AXUV = 0.001 W/cm2) which was tested in previous Ar injection experiments.
(2) Estimation of amount of W injection
Discussions
50 m
W cm-2 eV-1

## Slide 25
Discussions
(3) W injector for KSTAR
- Gun-type injection system is under development
- Please see the other presentation material for W gun…
(4) Expected studies
- Z-dependence study of impurity transport with double injection (Ar & W)
- ECH power scan as well as other auxiliary heating (ICRH, LH) to control W & Ar impurities.
- Magnetic perturbation effects on impurity transport
- Asymmetric formation of impurity concentration with full 2-D tomography by new SXR system

## Slide 26
Z-dependence study of impurity transport
- Simultaneous injection of Ar & W for the 2014 campaign
Various turbulent-based transport theories have been trying to estimate impurity transport with varying Z. Nevertheless, there is no theory explaining experimental results well.
It is required to have more experimental data to develop and revise impurity transport models.
H Nordman et al, 2011 Plasma Phys. Control. Fusion
Giroud C. et al 13th ITPA Confinement Database & Modelling Topical Group, Naka, Japan
Expected studies
JET
result

## Slide 27
Controllability of Ar impurity was confirmed by ECH on KSTAR.
Applying ICRH, ECCD as well.
Effects on not only Ar but also W.
2. Control impurity transport by applying auxiliary power
3. Effects of RMP on impurity transport
  Find out the relationship and mechanism between magnetic perturbation and impurity transport from edge (ELM) to core (impurity accumulation).
  - Applying MP after injection and before injection.
Expected studies

## Slide 28
Expected studies
M Reinke, et al., E1/E2 Task force meeting 2012
4. Impurity formation of poloidal asymmetry
ICRH L-mode
H-mode
C-Mod, Mo injection
Full 2-D tomography reconstruction will be available with vertical arrays
 Finding poloidal asymmetry of high-Z impurities such as W
 Comparing between Ar & W cases
For various plasma modes and conditions
C-Mod
Mo injection

## Slide 29
Appendix

## Slide 30: UTC-SANCO analysis
UTC (Universal Transport Code)
calculate 2
Nonlinear least square fit
(Levenberg-Marquardt Method)
Proper?
Get
D, V
No
Yes
: Error range factor
: Simulated data
: Measured data
Parameterize Coeffs
D, V or Influx
Set proper derivative
to parameters
Find new
solution which
minimize 2
Geometry
Background
(Te, Ti, Ne)
D, V
(Trial value)
Impurity Influx
Input
Ar emission
diagnostic data
SANCO
 Ar emission

## Slide 31: Ar transport control experiments using ECH on KSTAR

## Slide 32
L-mode plasmas, Ip = 400 kA, Bt : 2 T
Argon gas injection through a piezo valve (trace amount of Ar : nAr/ne < 0.1%)
Different transport with varying ECH positions  Feasibility of impurity control?
Heating position
(r/a = 0, 0.16, 0.30, 0.59)
On-axis
Ar
0.4
0.2
0 1 2 3 4
Time (sec)
Ip (MA)
Ar puffing
20 ms
#7566
0.4
0.2
0 1 2 3 4
Time (sec)
Ip (MA)
Ar puffing
20 ms
#7574
ECH
110 GHz
300 kW
No ECH
On-axis ECH
Ar puffing after ECH start
 To see ECH effect on Ar
Ar transport experiments with ECH

## Slide 33
Ar transport experiments with ECH
Argon gas injection through a piezo valve (trace amount of Ar : nAr/ne < 0.1%)
Different transport with varying ECH positions  Feasibility of impurity control?
Heating positions
(r/a = 0, 0.16, 0.30, 0.59)
40 cm
20
10
Ar
Using 110 GHz ECH system
ECH
Launcher
N port
Ip
Bt
x
y
R=1.8m
~ 50°
- Target: R0 = 1.8 m (B0=1.964T), Tor = -5. deg.
- ECH power was fixed : 350 kW
- Heating position changed by tilting the lanching mirror
On-axis
Mi Joung, EC17, May 7-10, Deurne, Netherlands, 2012

## Slide 34
SXR emissivity
(No ECH)
SXR emissivity
(On-axis ECH)
VUV Ar15+
t
2.8 – 4 keV photons
Mainly Ar16+ & Ar17+ emissions
ECH
r
r
Less core Ar emissivity with ECH
Ar puff
No-ECH
ECH

## Slide 35
Most effective (i.e., least core impurity concentration) with on-axis ECH
Less effective with ECH heating position at larger radius
No ECH
On-axis
r/a = 0.16
r/a = 0.30
r/a = 0.59
r
r
Less core Ar emissivity with ECH
On-axis
ECH
0.16
0.30, 0.59
No ECH
Core
ch #8

## Slide 36
2-D Reconstructed Ar emissivity
Core-focused reconstruction (Cormack algorithm)
Emissivity images of mainly Ar16+ & Ar17+ impurities
No ECH
On-axis ECH
Z
R
Z
R

## Slide 37
With on-axis ECH, central (r/a = 0 ~ 0.3) diffusion and convection are increased.
For convection, the sign is reversed from – to +: Inward  Outward pinch
#7566: No ECH
#7574: On-axis ECH
Outward
Modification of D & V by ECH
Inward
Inward

## Slide 38
Effect on central impurity accumulation
◈ Radial distribution of total Ar density versus time by SANCO
Total Ar
No ECH (#7566)
On-axis ECH (#7574)
Hollow profile
Peaked profile
Time
r/a
Time
r/a

## Slide 39
Neoclassical contribution of Ar transport
No ECH
(#7566)
On-axis
ECH
(#7574)
D, V by NLCASS is smaller by an order of magnitude than the experimental D, V.  The impurity transport is anomalous, rather than neoclassical.
Neoclassical calculation of D and V was done by NCLASS
NCLASS
10*NCLASS
Exp
10*NCLASS
Exp
NCLASS

## Slide 40
Possible mechanism of impurity pinch
From quasi-linear calculation of Weiland multi-fluid model
 3 impurity pinch terms[1, 2]
Pinch type | Description | Pinch direction by turbulence type
Curvature pinch | Compressibility of ExB drift velocity | Inward
Thermodiffusion pinch | Compression of the diamagnetic drift velocity | ITG  Outward TEM  Inward
Parallel impurity compression | Parallel compression of parallel v fluctuations produced along the field line by fluctuating electrostatic potential | ITG  Inward TEM  Outward
[1] H. Nordman et al., 2011 Plasma Phys. Control. Fusion 53 105005
Curvature pinch
Thermodiffusion pinch
Parallel
compression
pinch
Is the outward convection of Ar due to ITG or TEM?
[2] Giroud C. et al 13th ITPA Confinement Database & Modelling Topical Group, Naka, Japan