## Slide 1: Design and tomography test of edge multi-energy soft X-ray diagnostics on KSTAR
PPPL, Feb. 18, 2014
Juhyeok Jang*, Seung Hun Lee, H. Y. Lee, Joohwan Hong,
Juhyung Kim, Siwon Jang, Taemin Jeon, Jae Sun Park
and Wonho Choe**
Korea Advanced Institute of Science and Technology (KAIST), Daejeon, Korea
Fusion Plasma Transport Research Center (FPTRC), Daejeon, Korea
*jjh4368@kaist.ac.kr **wchoe@kaist.ac.kr

## Slide 2: Outline
Motivation
  Expected research topics
Engineering design
  Installation position
  Array design
  Detector specification
Expected signal level & Tomography test
  Calculation method
  Test for trial ne, Te profiles
  Test for KSTAR L, H-mode ne, Te profiles
  Time resolution test
Summary & Discussions

## Slide 3: Motivation
NSTX*
* Kevin Tritz, KAIST seminar (2013)
Multi-energy soft X-ray (ME-SXR)
Tangential measurement
Multiple filter mode : bolometer, Be filters, etc
High spatial / time resolution : spatial ~ 1 cm, time > 10 kHz
Possible studies
Edge plasma physics : ELM, MHD instabilities
Edge electron temperature calculation by Neural Network

## Slide 4: Edge plasma physics
High time resolution measurement of MHD activities
ELM cycle dynamics  Comparison with ECEI results
Impurity transport  SANCO calculation constrained by edge SXR signal
Resistive Wall Mode (NSTX) *
* L Delgado-Aparicio, Plasma Phys. Control. Fusion, 53 (2011)
** G. S. Yun, PRL 107, 045004 (2011)
ELM filament (KSTAR ECEI) **

## Slide 5: Electron temperature measurement
Three-layer Neural Network *
Te measurement (NSTX) **
* Kevin Tritz, KAIST seminar (2013)
** D. J. Clayton, Plasma Phys. Control. Fusion, 55 (2013)
Neural Network: Three layer technique
Fast, real-time data analysis
Te profile measurement without atomic modelling

## Slide 6
Engineering Design
            Installation position
            Viewing range
            Array design
            Detector specification

## Slide 7: Installation position (1)
Poloidal edge array  Tangential edge array
  KSTAR F-port : possible location of tangential array design
  Fixed boundary, higher signal level
F-port
poloidal
tangential

## Slide 8: Installation position (2)
Position : KSTAR F-port
NBI
armor
F-port
Possible position
F-port
KSTAR top view
F-port

## Slide 9: Viewing range
30 - 50 cm from core
(r/a = 0.6-1.0)
Line of sight
F-port
D-port
Range : r/a = 0.6~1.0
Resolution ~ 1.3 cm

## Slide 10: Array Design (1)
NBI
armor
KSTAR wall
3 AXUV photodiodes
  1 bolometer mode, 2 Be filters
Preamp (106V/A) close to the detectors
NBI
armor
KSTAR wall
Welding plate
case
Sight guide
AXUV
photodiode
pinhole
Sight
line
Preamp

## Slide 11: Array Design (2)
2
1
1
Array size : 400 mm 220 mm  120 mm
Pinhole–detector distance : 320 mm
2

## Slide 12: Pinhole & Crosstalk
13 mm
3 mm
19 mm
Pinhole : 5 mm 1 mm
Resolution ~ 13 mm
Cross talk ~ 3mm
pinhole
30 - 50 cm from core
(r/a = 0.6-1.0)

## Slide 13: Detector specification
AXUV-16ELG photodiode
53 mm
15 mm
Requirement
  Fast response ~ MHz
  High sensitivity to XUV and soft X-ray
Specification
  Active area: 5  2 mm2
  Shunt resistance: 100 m
  Capacitance: 2 nF
  Rise time (10-90%): 0.5 s
  Gain: 106 V/A
  Detection efficiency: 0.27 A/W
AXUV-16ELG array
AMP-16 remote panel
AMP-16 main circuit
Ribbon cable
55 mm
73 mm
t = 2 s
r = 2 cm

## Slide 14
Expected signal level
& Tomography test
          Filter selection
          Calculation method
          Expected signal & tomography test
            trial ne, Te profiles
            KSTAR L, H-mode ne, Te profiles
          Filament structure calculation

## Slide 15: Filter selection
Edge SXR : 3 mode
1 bolometer mode (no filter)
2 Be filter modes (Be 5 μm, 10 μm)
Cutoff energy of Be filters
  Be 5 μm : 0.5 keV
  Be 10 μm : 0.6 keV
Be filter transparency
bolometer
Be 5 μm
Be 10 μm
* Photo-current
: transparency of filter
: transparency of Si detector

## Slide 16: Calculation condition
Top view
Poloidal view
3 cm
KSTAR magnetic flux #7566, 2.0 s
Toroidal symmetry
Edge SXR chord
r/a = 0.6~1.0
resolution ~ 1.3 cm
Continuum radiation
Brems. + Recomb.
Photon 0.1-100 keV
Mode
Bolometer, Be 5 μm, Be 10 μm

## Slide 17: Solid angle calculation
Plasma volume, dVp
h
Aperture, Aap,i
Detector, Adet,i
di
Line of sight, Li
Thickness, dli
dPi : measured power emitted from the plasma volume dVp
ci : calibration factor
5 × 1 mm2
5 × 2 mm2
322 mm

## Slide 18: Tomography
J = Laplacian + mean squared error
  /M
  Solution minimizing J
: regularization parameter
 GCV method
Phillip-Tikhonov method
Weight matrix
channel i
flux j
 Intersection length between
  sight line and magnetic flux surfaces

## Slide 19: Tomography test sequence
Phillips Tikhonov method
1-D radial emissivity profile
Line integrated signal
Noise test
( : random detection noise)
ne, Te profile
 Continuum radiation :
Edge SXR chord, flux surfaces
 Weight matrix : W
Input
Signal level
Output
Shape
Smoothness
error(%)
Evaluation

## Slide 20: Poloidal vs Tangential
Condition
  Same solid angle
Current level
  tangential ~ 3poloidal
  long integration length
Poloidal
Tangential
Radiation

## Slide 21
Trial ne, Te profile

## Slide 22: Trial profiles
ne, Te ~
Core : ne = 41019 m-3, Te = 2 keV
profile 1 : a=2, b=0.4 profile 2 : a=2, b=1
Signal level and tomography test with parabolic ne, Te profile
Electron density (1019m-3)
Electron temperature (keV)

## Slide 23: Continuum radiation
Profile1 radiation (kW/m3)
Profile2 radiation (kW/m3)
Viewing range
Viewing range
Radiation @ r/a~0.6 (kW/m3) | Detection mode |  | 
 | Continuum | Be 5 μm | Be 5 μm
Profile 1 | 8.0 | 4.6 | 4.0
Profile 2 | 4.9 | 2.4 | 2.0
Notes: Profiles
1. a=2, b=0.4
2. a=2, b=1

## Slide 24: Expected photo-current
Profile1 photo-current (μA)
Profile2 photo-current (μA)
Profile1 current (μA) | ch # |  | 
 | 1 | 5 | 10
Continuum | 0.10 | 0.070 | 0.036
Be 5 μm | 0.059 | 0.040 | 0.018
Be 10 μm | 0.051 | 0.034 | 0.015
Profile2 current (μA) | ch # |  | 
 | 1 | 5 | 10
Continuum | 0.048 | 0.027 | 8.8e-3
Be 5 μm | 0.023 | 0.011 | 2.2e-3
Be 10 μm | 0.019 | 8.4e-3 | 1.5e-3
Notes: Profiles
1. a=2, b=0.4
2. a=2, b=1

## Slide 25: Tomography test (1)
Reconstruction Error (%) | Noise (%) |  | 
 | 0 | 5 | 10
Be 5 μm | 4.3 | 4.7 | 6.4
Be 10 μm | 3.7 | 4.1 | 6.0
Be 5 μm
Be 10 μm
Phatnom
Reconstruction
Phatnom
Reconstruction
Random noise test
: Chord signal + Random noise
 Stability of reconstruction solution
Notes: Random noise test ~ 30 times

## Slide 26: Tomography test (2)
Phatnom
Reconstruction
Be 5 μm
Be 10 μm
Phatnom
Reconstruction
Reconstruction Error (%) | Noise (%) |  | 
 | 0 | 5 | 10
Be 5 μm | 5.8 | 8.2 | 9.2
Be 10 μm | 5.8 | 8.5 | 9.4
Reconstruction results agree with parabolic profiles.
Notes: Profiles
1. a=2, b=0.4
2. a=2, b=1

## Slide 27
KSTAR L, H-mode

## Slide 28: KSTAR L, H-mode
Signal level and tomography test with KSTAR L, H mode ne, Te profile
Electron density (1019m-3)
Electron temperature (keV)

## Slide 29: Continuum radiation
Power density @ r/a~0.6 (kW/m3) | Detection mode |  | 
 | Continuum | Be 5 μm | Be 5 μm
L-mode | 1.1 | 0.42 | 0.32
H-mode | 6.5 | 3.3 | 2.7
L-mode radiation (kW/m3)
H-mode radiation (kW/m3)
Viewing range
Viewing range

## Slide 30: Expected photo-current
L-mode current (μA) | ch # |  | 
 | 1 | 5 | 10
Continuum | 0.011 | 7.0e-3 | 2.8e-3
Be 5 μm | 3.5e-3 | 1.6e-3 | 2.9e-4
Be 10 μm | 2.6e-3 | 1.0e-3 | 7.0e-5
H-mode current (μA) | ch # |  | 
 | 1 | 5 | 10
Continuum | 0.071 | 0.048 | 0.013
Be 5 μm | 0.036 | 0.022 | 4.4e-3
Be 10 μm | 0.030 | 0.018 | 3.9e-3
L-mode photo-current (μA)
H-mode photo-current (μA)

## Slide 31: L-mode tomography test
Be 5 μm
Be 10 μm
Reconstruction Error (%) | Noise (%) |  | 
 | 0 | 5 | 10
Be 5 μm | 3.8 | 7.8 | 14.0
Be 10 μm | 2.9 | 7.5 | 14.1
Phatnom
Reconstruction
Phatnom
Reconstruction
Reconstruction results match with L-mode phantoms.
Reconstruction error increases with random detection noise.
Notes: Random noise test ~ 30 times

## Slide 32: H-mode tomography test
Phatnom
Reconstruction
Be 5 μm
Be 10 μm
Phatnom
Reconstruction
Reconstruction Error (%) | Noise (%) |  | 
 | 0 | 5 | 10
Be 5 μm | 4.2 | 8.3 | 13.9
Be 10 μm | 3.7 | 8.1 | 14.0
Pedestal structure is well reconstructed.
Notes: Pedestal structure is well reconstructed!
Random noise test ~ 30 times

## Slide 33
Filament structure
calculation

## Slide 34: ELM filament calculation
Goal : possibility of investigation of
high frequency edge dynamics
  ELM cycle dynamics
  Edge MHD activity
Phantom
  = ELM filament structure (m/n=8/1)
  + toroidal rotation
Toroidal
rotation
D-shape
Filament
Phantom
Notes: D-shape : KSTAR L-mode, elongation 1.8, triangularity 0.2, Shafranov shift 0.1m
core 4000 W/m3
filament : 20% of core

## Slide 35: Expected signal
Line-integrated signal
: ~40 μs fluctuation observed
rotation velocity ~ 250 km/s
time resolution ~ 500 kHz (2 μs)
Signal change due to filament ~ 5 %
* Kevin Tritz, KAIST seminar (2013)
Possible studies
Possibility of high time resolution
(~500 kHz) measurement
Neural Network
 fast Te fluctuation measurement
Line-integrated signal
MHD activity in NSTX *

## Slide 36
Summary & Discussion

## Slide 37: Summary
Edge tangential soft X-ray design
  KSTAR F-port
  r/a = 0.6~1, spatial resolution ~ 1.3 cm
  Three modes will be available (bolometer, Be 5 μm, Be 10 μm)
Expected photo-current level (bolometer, Be 5, 10 μm)
  L-mode profile ~ 10 nA, 3.5 nA, 2.6 nA
  H-mode profile ~ 70 nA, 36 nA, 30 nA
Tomography tests
  Reconstruction results match with phantoms.
  Error increases with random detection noise.
Filament structure calculation
  ~ 40 μs fluctuation observation possible

## Slide 38: Discussion
Signal level
  Proper photo-current level for detection of edge soft X-ray
  NSTX ME-SXR signal level : S/N ratio of AXUV 20ELG…
  Optimized design for increasing signal level
Spatial resolution
  Proper spatial resolution for investigation of edge plasma physics
Te calculation by Neural Network
  Be filter selection for Neural Network method : energy range?
  Mode number : 3 modes are enough?
  Emissivity profile without tomography