## Slide 1
Wonho CHOE
Fusion Plasma Transport Research Center (FPTRC)
Korea Advanced Institute of Science and Technology (KAIST)
February 18, 2014
Research Activities in
KAIST-FPTRC
PPPL Visit

## Slide 2: SXR & VUV imaging diagnostics on KSTAR (as of now)
Soft X-ray array (SXRA)
  2 arrays, 32 ch (64 ch)
  t = 2 μs, r = 5 cm
  Ar Ross filters (Cl & Ca K-edge): 2.8 – 4.0 keV
  Be filters (10, 50 μm: 0.5, 1.0 keV): 2 color
VUV spectroscopy
  28 ch for imaging (5 - 20 nm), t = 13 ms
  1 ch for survey (15 - 60 nm), t = 13 ms
2-D Tangential X-ray pinhole camera (TXPC)
  Duplex (2 color), 50x50 ch
  t = 0.1 ms, r = 2 cm
GEM detector for 2-D X-ray camera
  12x12 pixels, 128 ch
  t = 1 ms, r = 2 - 6 cm
  3 – 30 keV
Tomographic reconstruction codes developed
Max. Entropy Method
Phillips-Tikhonov
Min. Fisher Information
Cormack

## Slide 3: (1) SXR array diagnostic system
edge
16 ch (32)
16 ch (32)
HU
HD
VD2
VU2
4 arrays, 256 ch
2 cm, 2 μs
1 array, 60 ch
2 filters  multi energy, neural network
1.3 cm, 2 μs
4 array, 256 channels
2013
2014
2 array, 64 ch
Be filters (10, 50 mm)
Ar Ross filters (Ar transport)
Bolometer (No filter)
S.H. Lee
J. Jang

## Slide 4: (2) Imaging VUV spectroscopy
2013 (5-20 nm, ~3 ms)
2012 (15-60 nm, 13-40 ms)
ITER prototype on KSTAR (5 – 60 nm)
Vacuum extension
VUV spectrometer on the optical table
28 ch, imaging
In collaboration with ITER KO-DA (C.R. Seon)
1 ch, survey
He I : 53.70 nm
He II : 25.63, 30.37 nm
O V : 15.61, 19.28, 21.50 nm
O VI : 17.30, 18.40 nm
C III : 38.62 nm
C IV : 24.49, 38.41, 41.96 nm
C V : 22.72, 24.87 nm
Fe XV : 28.42 nm
Fe XVI : 33.54, 36.08 nm
W : 5-20 nm
Ar XIV 18.79 nm
Ar XV 22.11 nm
Ar XVI 35.39 nm

## Slide 5: (3) ‘Tangential’ X-ray pinhole camera
(a)
(b)
Sawtooth crash in #7640
In collaboration with KAERI (M. Moon)
‘Duplex (2-color) Multi-Wire Proportional Counter (MWPC) detector
(a)
(b)
Channel
Channel
Channel
Outboard
Outboard
(b) - (a)

## Slide 6: X-ray imaging of VDE
TXPC, RT-EFIT
Major radius, R
Visible camera
Major radius, R
Vloop
Ip
Stored energy
ECE
Da
Shot 7886
Consistent with RT-EFIT and visible camera
Tangential reconstruction on-going
S. Jang et al., CAP 13, 819 (2013)

## Slide 7: Te by TXPC (PHA mode)
Pulse Height Analyzer mode

## Slide 8: (4) GEM detector for TXPC
Front
Back
128 ch in 12x12 cm2
Spatial & time resolution: 2-6 cm, 1 ms
In collaboration with ENEA (D. Pacella)
55Fe Source
Gas in
Gas out
Lan cable
HV cable
FPGA
Zoom in & out
GEM
[4] W. Bonivento et al., Nucl. Instr. and Meth. A, 491, 233 (2002)
X-position movable
  GEM foils: 50 µm thick kapton foil, copper clad on each side
  Triple-GEM geometry: 3/1/2/1 mm
  Front-end electronics: CARIOCA micro chips by LNF and CERN [4]
  Active area: 10 x 10 cm2
  Channels: 12 x 12 pixels (each pixel has 0.8 x 0.8 cm2)
  Temporal: 10 µs (up to 255 frames), 1 ms (60k frames)
  Mixed gas (flow): 70% Ar, and 30% CO2 at 1 atm
  Movable system (zoom in & out and horizontally movable)

## Slide 9: Preliminary result of GEM detector
shot 9033
Zoom in
shot 9034
shot 9035
shot 9056
Zoom in & out

## Slide 10: Sawtooth crash in H-mode
m = 1 (f = 19 kHz) is shown by spectrogram.
Maximum displacement from the initial position: 0.13 m
Maximum rotation speed: 10.7 km/s
Spectrogram
m = 1
f = 19 kHz
Trajectory of the hot core
rtEFIT

## Slide 11: Comparison between L- & H-mode
Crash
< 5 km/s
0.1 m
Crash
< 10 km/s
< 0.1 m
L-mode, low vФ
H-mode, high vФ
Crash in multi steps
Crash in a single step
Displacement from central position
Displacement from central position
Poloidal velocity
Poloidal velocity
Notes: L-mode와 H-mode 비교를 하자면, crash가 일어나는 양상이 앞서와 같이 다릅니다. 확대한 신호를 보면 L-mode 에서는 crash가 한 번에 일어나 oscillation 피크값이 최대가 되었다가 바로 잠잠해지는 모양이고, H-mode에서는 최대 피크점이 있고 그 이후에도 oscillation이 세 번에 걸쳐 그 진폭이 잦아드는 모양입니다. (9, 11 페이지 그림과 일치)

## Slide 12: Correlation between SXR rotation speed & vФ (XICS)
The m=1 SXR rotation speed is compared with toroidal rotation speed (XICS).
Toroidal rotation frequency
Notes: 이러한 m=1 모드의 주파수와 토로이달 회전 속도와 비교해보면 이와 같습니다. 6개의 실험에서 일어난 모든 sawtooth crash를 fft하여 알아낸 주파수와 그 시간에 해당하는 토로이달 회전속도와 비교한 값입니다. 이에 따르면 m=1 모드의 주파수는 토로이달 회전 속도에 의해 결정된다고 할 수 있겠습니다.

## Slide 13: ECH effect on Ar transport
Argon gas injection through a piezo valve (nAr/ne < 0.1%)
Different transport with varying ECH positions  Feasibility of impurity control?
Analysis of Ar transport coefficients in L-mode (#7566, #7574) & H-mode (#7745, #7863) by using UTC-SANCO code with diagnostic results (SXR, VUV, XICS)
0.4
0.2
0 1 2 3 4
Time (sec)
Ip (MA)
Ar puffing
20 ms
#7566
0.4
0.2
0 1 2 3 4
Time (sec)
Ip (MA)
Ar puffing
20 ms
#7574
ECH
110 GHz
350 kW
#7863
L-mode
w/o ECH
Heating positions
(r/a = 0, 0.16, 0.30, 0.59)
w/ ECH
40 cm
20
10
0
Ar puffing after ECH start
Ar

## Slide 14: Depending on ECH position
No ECH
On-axis ECH
ECH @
r/a = 0.16
0.30
0.59
Less core accumulation of Ar impurity with ECH
Most effective (i.e., least core impurity concentration) with on-axis ECH
Less effective with resonance layer position at larger radius
No ECH
On-axis ECH
0.16
0.30
r/a = 0.59
L-mode

## Slide 15: 2-D Reconstructed Ar emissivity
Core-focused reconstruction (Cormack algorithm)
Emissivity images of mainly Ar16+ & Ar17+ impurities
No ECH
On-axis ECH

## Slide 16
With ECH, central diffusion and convection are increased.
The pinch direction reverses at r/a < 0.3.
Modification of D & V by ECH
Non ECH (#7566)
On-axis ECH (#7574)
Outward
Inward
Inward

## Slide 17
◈ Radial profile of total Ar density at peak time (2.3 s)
◈ Total Ar density
No ECH (#7566)
On-axis ECH (#7574)
Total Ar
Total Ar
Hollow Ar density profile by ECH

## Slide 18: Neoclassical contribution of Ar transport
No ECH
(#7566)
On-axis ECH
(#7574)
Neoclassical calculation of D and V by NCLASS
- The same input (Te, ne) of SANCO calculation
- Ar16+ (dominant charge state) distribution at the peak time is used.
D, V calculated by NLCASS is smaller by an order of magnitude than the experimental D, V.
 The impurity transport is anomalous, rather than neoclassical.
NCLASS
Exp

## Slide 19
Impurity pinch
3 impurity pinch terms[1] in Weiland multi-fluid model
Pinch type | Description | Pinch direction by turbulence type
Curvature pinch | Compressibility of ExB drift v | Inward
Thermodiffusion pinch | Compression of the diamagnetic drift v | ITG  Outward TEM  Inward
Parallel impurity compression | Parallel compression of parallel v fluctuations produced along the field line by fluctuating electrostatic potential | ITG  Inward TEM  Outward
GYRO and XGC simulations are on-going to find the dominant turbulence mode of No ECH and on-axis ECH cases.
 It is expected that TEM is the dominant mode because of ECH effect on Te profile.
It may be due to parallel impurity compression driven by increased R/LTe[2]
[1] H. Nordman et al., 2011 Plasma Phys. Control. Fusion 53 105005 [2] C. Angioni et al.,2006 Phys. Rev. Lett. 96 095003
Curvature pinch
Thermodiffusion pinch
Parallel
compression
pinch

## Slide 20: Diagnostics & analysis tools ready for W injection experiment
5 - 20 nm wavelength range is mainly used for measurement of W emission spectra.
ASDEX-U: VUV (~5 nm)
JET: VUV (~5 nm) & SXR
JT-60U: VUV (6.23 nm)
LHD: EUV (6.09, 6.23 & 12.7 nm)
KSTAR
  - VUV (5 – 60 nm): ITER prototype
  - SXR
Simulation & Atomic data: SANCO-ADAS
W test particle injector under preparation/consideration
  Particle gun (under preparation on KSTAR)
  Laser blow-off system (C-Mod)
  Particle dropper (NSTX)
  Pellet injection (LHD)

## Slide 21: Presentations and discussions
Design and tomography test of Soft X-ray Array diagnostics on KSTAR (Seung Hun LEE)
Design and tomography test of Edge Multi energy Soft X-ray Array diagnostics on KSTAR (Juhyeok JANG)
Impurity transport analysis and preparation of W injection experiments (Joohwan HONG)
Development of a tungsten injection injector for high Z impurity study (Joohwan HONG)