## Slide 1
Three-Dimensional Edge Transport and Impact on Plasma Surface Interactions with Resonant Magnetic Perturbation Fields in Tokamaks
Oliver Schmitz
University of Wisconsin – Madison,
Department of Engineering Physics, Madison, WI, USA
PPPL General Seminar, May 13, 2014
Acknowledgements to
M. Becoulet, P.Cahyna, T.E. Evans, Y.Feng, N.Ferraro, M.E. Fenstermacher, H. Frerichs, G. Huijsmans, M. Jakubowski, A.Kirschner, L. Lao, C.L. Lasnier, M. Lehnen, A.Loarte, R.Nazikian, D. Orlov, H. Reimerdes, D.Reiter, G.Saibene, U. Samm, P.Snyder, H. Stoschus, M. Wade and the DIII-D and TEXTOR Teams

## Slide 2
Executive summary as structure of talk
1
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust

## Slide 3
Executive summary as structure of talk
1
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust
The perturbed separatrix defines 3D edge topology and transport

## Slide 4
Position of open field line domain and fueling front determine location and width of plasma boundary and wall interaction domain
2
Radial Transport into SOL
D^, c^
Parallel Heat q|| and Particle G|| Fluxes to Target
Mass conservation in open field line region:
[B. Unterberg and U. Samm, Transact. Fusion Science and Technology 45 (2004) 229-236]
Radial constant diffusion, parallel flow with
Exponential decay in SOL
Thin deposition width
Simplified Example for Calculation of Deposition Width
Strong symmetry assumptions are used!

## Slide 5
A 3D plasma edge magnetic topology is detected at DIII-D
3

## Slide 6
A 3D plasma edge magnetic topology is detected at DIII-D
3
The separatrix is very sensitive to external and internal perturbation fields

## Slide 7
A 3D plasma edge magnetic topology is detected at DIII-D
4
The separatrix is very sensitive to external and internal perturbation fields
Separatrix lobes show interaction of RMP with separatrix
T.E.Evans et al. J. Phys.: Conf. Series 7 (2005) 174
O. Schmitz et al. PPCF 50 (2008) 124029

## Slide 8
“Stochastic edge layer” is a heterogeneous helical scrape off layer
5
Perturbed separatrix represents envelope for stochastic interior

## Slide 9
EMC3-Eirene modeling reflects 3D edge structures
6
Fluid plasma and kinetic neutral transport modeling predicts 3D boundary in electron and ion temperature and density fields
H. Frerichs et al. Nuclear Fusion 50 (2010) 034004

## Slide 10
Qualitative appearance of strike line striation is proxy for effective level of perpendicular transport
7
Low level of diffusive perpendicular transport is required to see striated magnetic footprints
Parallel transport along open field lines prevails similar to SOL

## Slide 11
Striation of target particle fluxes is a reliable signature during RMP ELM suppression at DIII-D
8
[T.E. Evans et al., Journ. Phys. 7, 174 (2005)]
[O. Schmitz et al., PPCF 50 (2008) 124029]
[M. Jakubowski et al., Nucl. Fusion 49 (2009) 095013]
Shows existence of the separatrix lobes as new definition for 3D plasma boundary
This is a reliable finding during RMP application on other devices, e.g. NSTX, MAST, Asdex-Upgrade
Center post
45° tile
floor
Outer shelf

## Slide 12
Heat and particle fluxes into 3D boundary appear to be very different
9
L-mode plasma
H-mode plasma
CII emission
heat flux
CII emission
heat flux
Field line penetration
Field line penetration
Plasma response: Exact shape is determined by sum of all radial perturbations at the separatrix
Good match between modeling and experiment found in L-mode, in H-mode measured striation is consistently 10-13% wider then modeled
Striation is always clearly seen in particle flux
Weak heat flux filling of lobes
Recycling features in lobes have been suggested recently as possible explanation
[O. Schmitz et al., JNM 415 (2011) 886-893]

## Slide 13
High density divertor solution reproduces small outward heat influx due to localized high recycling
1
e=10%
e=2%
[H. Frerichs et al., PoP 21 (2014) 020702]
10

## Slide 14
Executive summary as structure of talk
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust

## Slide 15
Dynamic Ergodic Divertor at TEXTOR as flexible tool to generate different mode number & rotating RMP fields
3 pitch resonant base mode spectra: m/n=12/4, 6/2, 3/1
AC operation: 1,2,5,10 kHz
11

## Slide 16
The perturbed edge layer consists out of SOL like field lines and stochastic domains
T. Eich et al. Nucl. Fusion 40 (2000) 1757
Stochastic layer
Laminar flux tubes as helical SOL
O. Schmitz et al. Nucl. Fusion 48 (2008) 025009
12

## Slide 17
The helical SOL acts as a chanel of strong parallel transport to the wall
Short connection length, laminar flux tubes represent helical SOL
O. Schmitz et al. Nucl. Fusion 48 (2008) 025009
13

## Slide 18
The helical SOL acts as a chanel of strong parallel transport to the wall
Short connection length, laminar flux tubes represent helical SOL
O. Schmitz et al. Nucl. Fusion 48 (2008) 025009
The “stochastic edge” is not a region of dominant magnetic braiding but governed by SOL like transport
13

## Slide 19
Executive summary as structure of talk
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust

## Slide 20
Edge magnetic islands were identified in C-III light and in transport features
Edge island can be invoked on demand in a very controlled and reliable manner
14

## Slide 21
Magnetic island can act as convective cell and enhance outward transport
X-point
O-point
O-point
X-point
Electric fields towards
island center ~ 2-20 V/cm
tp drops by 30% with island -refuel of plasma hardly possible
2cm
15

## Slide 22
Hamiltonian guiding center code ORBIT shows poloidal structure in connection length …
Parallel Connection Length
G. Ciaccio et al. Nucl. Fusion submitted (2014)
16

## Slide 23
… and correlated structure in radial electric field (based on plasma potential from electron and ion separation)
G. Ciaccio et al. Nucl. Fusion submitted (2014)
17

## Slide 24
Island location can be fine tuned relative to exhaust system by DED current phase sweeps
This method was shown to move island poloidally by about 15 degree at the outer mid plane
Toroidal movement will determine position relative to ALT-II ducts and pumps
18

## Slide 25
Helium confinement in plasma is largely reduced with island present
Line averaged density
Density decay rate
Density decay rate is reduced by 50% with island present
Shallow increase for island cases shown reduced effective fueling efficiency
Fueling less efficient
Island acts as effective outward transport interface yields reduced fueling efficiency
19

## Slide 26
Helium is flushed out into plasma edge with overall reduced helium confinement times
He-II (468nm) intensity in edge
tp* for He in edge is reduced with some dependence on DED phase
Accumulation of He in edge due to reduced core fueling efficiency
Increase of He level in SOL
tp* for He in edge
Helium exhaust is enhanced with 3D boundary
20

## Slide 27
Executive summary as structure of talk
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust

## Slide 28
Impact of 3D boundary on erosion properties was teased with DiMES facility at DIII-D
A. McLean et al. Rev. Scientific Inst. 80 (2009) 043501 c
Graphite cap with 4.8 cm diameter
Measure directly the chemical erosion properties within the 3D boundary
Measure chemical erosion within lobes by slow sweeping of the outer strike point
PPI
A. McLean et al. Journal Nucl. Mater. 390-391 (2009) 160-163
GCH4 PPI = 4.7x1017 s-1
UNIVERSITY OF TORONTO
Institute for Aerospace Studies
21

## Slide 29
A significant reduction of the chemical erosion was measured
Evidence for decrease of chemical and increase of physical sputtering with separatrix lobes as end point of open field lines from stochastic boundary
Ychem
CII emission
Coupling of EMC3-Eirene with ERO ongoing to assess relevance for ITER divertor
[O. Schmitz et al., JNM 415 (2011) 886-893]
22

## Slide 30
Executive summary as structure of talk
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust

## Slide 31
Decay of plasma response yields stochastic edge signatures
23
LSN L-mode discharge with decay of n=3 response
Toridal rotation profiles
[O. Schmitz et al., Nucl. Fusion, 54 (2014) 012001]
Braking
Spin-Up

## Slide 32
MARS-F modeling predicts resonant screening response
Local resonant sheet currents reduce n=3 resonant mode amplitude
[O. Schmitz et al., Nucl. Fusion, 54 (2014) 012001]
Plasma response commences with intuitive understanding and in agreement with modeling
Ideal MHD type response with RFA not detected
[M. Lanctot et al., PoP 18 (2011) 056121]
24

## Slide 33
Strike line splitting is strongly enhanced after response decayed
Note residual splitting with low influx during screening phase!
[O. Schmitz et al., Nucl. Fusion, 54 (2014) 012001]
25

## Slide 34
Strike line splitting is strongly enhanced after response decayed
Lobe location agree (for this case) with vacuum prediction
This is a result particular to this case!
We also saw cases with much wider striation widths!
[O. Schmitz et al., Nucl. Fusion, 54 (2014) 012001]
26

## Slide 35
Executive summary as structure of talk
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust

## Slide 36
ELM coil set at ITER gives large flexibility
In vessel coil set for ITER
In vessel coils mounted behind blanket
9x3 coils with single power supplies
Coil set with wide spectral flexibility
Toroidal mode number n=3 and n=4 fields seem to be advantageous at the moment
27

## Slide 37
RMP amplitude is a fine tuned actuator for plasma edge transport
Implementation of screening and linear reduction of RMP amplitude have similar impact on plasma edge
High q95=4.2 case shows compression of invariant manifolds
O. Schmitz et al., IAEA FEC 2012, San Diego, USA
28

## Slide 38
Overall shape of divertor fluxes and magnitudes is controlled by RMP field
Implementation of screening and linear reduction of RMP amplitude have similar impact on plasma edge
High q95=4.2 case shows compression of invariant manifolds
O. Schmitz et al., IAEA FEC 2012, San Diego, USA
29

## Slide 39
Toroidal average of profiles is comparable for all cases but the high current vacuum case
[O. Schmitz et al., JNM 415 (2011)]
30

## Slide 40
Toroidal average of profiles is comparable for all cases but the high current vacuum case
30

## Slide 41
Toroidal average of profiles is comparable for all cases but the high current vacuum case
30

## Slide 42
Helical SOL flux bundles establish helical sonic flows with direct impact on particle balance
90kAt vacuum case
screened case
Screened case: can be compensated with ITER pellet fueling capability
[O. Schmitz et al., JNM 415 (2011)]
31

## Slide 43
[O. Schmitz et al., JNM 415 (2011)]
Radial outflow with flattening of density profile
3D flow channels as candidate for enhanced outward particle flux and reduced fueling
Increase pressure in 3D SOL equivalent
Downstream n up
Downstream T down
3D flow channels
Helical SOL flux bundles establish helical sonic flows with direct impact on particle balance
32

## Slide 44
Magnetic fields from M3D-C1 solutions was included and solutions were compared to previous results
33
Non-linear, one fluid M3D-C1 solution
Vacuum field as used in M3D-C1
Linear, two fluid M3D-C1 solution
Vacuum field as used in M3D-C1
equdsk: 4.4keVm, time step 5 was used, ~ 500 tA
equdsk: 3.8keVm, time step 1 was used, linear response
M3D-C1 solutions used
EMC3-Eirene boundary conditions

## Slide 45
Magnetic topology is vacuum-like for both M3D-C1 cases
34
Wider extension of helical lobes with stronger deformation
Additional high order mode number resonant components
Stochasticity prevails at 5/3 surface
Outermost island chain present inside helical boundary
Clean 6/3 resonant island
Good flux surfaces in between 5/3 and next inner resonant island chain
Only saddle differences between
non-linear response and vacuum field

## Slide 46
Marginal modification of field line connection length pattern with non-linear response from M3D-C1
35
Vacuum field as used in M3D-C1
Non-linear response from M3D-C1

## Slide 47
Non-linear response causes only a small shift of heat flux towards outer lobes
36
Non-linear M3D-C1 response
Vacuum in M3D-C1
Non-linear response yield higher heat outflow into outer tips and 3D SOL domain of perturbed edge layer
Almost no difference in extension and width of heat flux pattern!!

## Slide 48
Radial profiles show small outward shift of divertor fluxes
37

## Slide 49
38
Enhanced lobe excursion with with linear response from M3D-C1
ISP
ISP
Vacuum field as used in M3D-C1
Linear response from M3D-C1

## Slide 50
Linear response causes only a shift of heat flux towards outer lobes with some form of flux brodening
39
Linear M3D-C1 response
Vacuum in M3D-C1
Linear response yield higher heat outflow into outer tips and 3D SOL domain of perturbed edge layer
Small difference only in extension and width of heat flux pattern!!

## Slide 51
Linear response causes more significant shift of divertor fluxes towards outer lobes
40
Strong reduction of splitting width is not seen!

## Slide 52
There is controversy in plasma response modeling results, e.g. plasma response predicted with JOREK is very different
22
F. Orain et al., SFP 2013, JOREK modeling

## Slide 53
Executive summary as structure of talk
Three-Dimensional effects are significant in tokamaks during application of resonant magnetic perturbation fields for ELM control
The perturbed separatrix defines 3D edge topology and transport
Connection length in helical scrape off layer governs transport features
Plasma surface interaction is directly affected by 3D boundary
Plasma response defines extension and actual shape of the 3D boundary
Extrapolation capability of these effects towards ITER is progressing but still controversial
Magnetic islands act as radial transport actuator on transport and exhaust