## Slide 1: Update on NSTX-U Plasma Operations
Devon Battaglia
On Behalf of the NSTX-U team
NSTX-U Monday Physics Meeting
March 7, 2016

## Slide 2: Summary of NSTX-U Plasma Operations
3 weeks of operations December - January
  Neutral beam heating: typically 3MW total from four sources
  Diverted L-mode and H-mode operations at Ip = 600 kA
  Gap and Ip control, simple vertical position control
  Followed by 2 weeks of maintenance
3 weeks of operations in February – early March
  Neutral beam heating: up to 4MW total from three sources
    Beamline 1B routinely runs at 90kV
  Diverted L-mode (0.8 – 1.0MW) and H-mode (Ip = 0.8 MA)
  ISOFLUX, vertical position improvements, error field correction commissioned
  Now starting another 2 weeks of maintenance

## Slide 3: Achieved H-mode scenarios at larger Ip, kappa and stored energy
Steady progress toward 1.4MA ELMy H-mode goal
202946: Best H-mode in January period
203655 and 203679: Best H-mode in Feb-March period
efit02

## Slide 4: Making Progress in Shaping And High Stored Energy
Nearly Matching the NSTX Stored Energy for the Same Plasma Current
(at higher BT, but lower volume)
Are approaching vertical stability boundaries similar to NSTX
(but at higher A)
NSTX-U Team!

## Slide 5: ELMy H-mode shot with quiescent period achieved with highly-shaped LSN discharge
Ip | 0.78 MA
BT0 | 0.61 T
PNBI | 4 MW
POH | 0.2 MW
A | 1.58
κ | 2.18
li | 0.83
δlower | 0.64
W | 206 kJ
βT | 7.84%
βP | 1.14%
βN | 3.58
τe | 50 ms
EFIT02 now available between shots

## Slide 6: But, putting power on new divertor surfaces requires some “clean up” time
Average AXUV diode signal (A.U.)
20 – 70ms
70 – 120ms
Two H-mode shots following first shot with strike in CHI gap
Second H-mode shot after half-day of ohmic shots
Shots following first shot on inner div
Shots since last boronization

## Slide 7: Stationary diverted L-mode operations have been extended to flattops > 1s
DN plasma boundary is steady for > 1 second as OH swings:
0.66 seconds 1.73 seconds
0.9 MW NBI
203577
OH swings ± 19 kA
(80% of maximum flux)
Sawteeth oscillations

## Slide 8: L-Mode discharges have run with Ip = 1MA for a 700ms flattop
Plasma Current [MA]
elongation
Internal inductance
Stored Energy [kJ]
Injected Power [MW]
203577
203582
Both discharges have sawteeth and use the full OH flux swing

## Slide 9: New Capabilities Already Evident When Flat-Top Averages Are Plotted
New solenoid has much greater capability
(and we are only allowing use of 80% of the available flux)
Can sustain L-mode plasma for physics studies much longer
NSTX-U Team!

## Slide 10: Scenario development enabled by commissioned control tools
rtEFIT / ISOFLUX shape control
  See Dan Boyer’s Science talk from 2/22
  PF5 and PF3s control outboard boundary (outer gap, kappa)
  X-points, inner gap controlled via PF1As and PF2s versus Ip and IOH
Improved vertical control tools
  Multi-sensor Z*dZ/dt measurement
  Filtering to remove power supply noise
  Signal conditioning to improve signal-to-noise
  Tools have not been fully exploited
EFIT02
rtEFIT

## Slide 11: On Friday, dr-sep control was demonstrated
dr-sep controls bias of plasma toward X-points
  Critical parameter for boundary and pedestal physics studies
Biased Up
Biased Down

## Slide 12: n=1 Error Field Correction Has Shown Success
EFC proportional to PF5
  See Clayton Myers Science meeting talk from 2/29
  Correct for PF5 out-of-roundness
n=1 fields applied with various phases
  Reference shot 203565 disrupts at t=0.6
  203562 uses correcting phase, extended duration.
  203556 uses anti-correcting phase, shorter discharge.

## Slide 13: Key Accomplishments of Second Operations Period
Made rtEFIT a reliable tool every shot
Commissioned ISOFLUX plasma control
  Outer-gap control through the PF-5 coil.
  Elongation control via PF-3 coils.
  Vertical position and dr-sep control via PF-3 coils
Improved fast vertical position control
Developed error field correction strategy
Developed long pulse and high current L-mode scenarios with ISOFLUX control
Developed H-mode scenarios with ISOFLUX control, at higher elongation and reduced internal inductance