## Slide 1
Automated Identification of MHD Mode Bifurcation and Locking in Tokamaks
S.A. Sabbagh1, J.D. Riquezes1, R.E. Bell2, Y.-S. Park1, C. Myers2, L.A. Morton3
1Department of Applied Physics, Columbia University, New York, NY, USA
2Princeton Plasma Physics Laboratory, Princeton, NJ, USA
3Oak Ridge Associated Universities, Oak Ridge, TN, USA
NSTX-U Physics Meeting
PPPL
November 30th, 2017
Princeton, NJ
V1.0
V1.0
Supported by US DOE grant DE-SC0016614
Columbia U. student

## Slide 2: An algorithm has been created to automatically identify aspects of MHD activity supporting disruption prediction
Motivation
  Identify time-evolving rotating MHD instabilities in a tokamak plasma
  Automate detection of key mode characteristics with the purpose of connecting them to plasma disruptions
  Create portable code for general use on tokamaks as a module for the disruption event characterization and forecasting code (DECAF)
Outline
  Standard analysis of rotating MHD modes by FFT
  Automation of MHD characteristics analysis for DECAF
  Testing on various plasma scenarios
  Simple torque balance model of bifurcations to test in DECAF

## Slide 3: DECAF uses threshold tests and more sophisticated models to declare events and create event chains
Events
  RWM: resistive wall mode
  VDE: vertical instability
  WPC: wall proximity control
  LON: low density warning
  IPR: not meeting Ip request
  LOQ: low q warning
  DIS: disruption
Disruption event chain
0.60
0.65
0.70
0.75
t (s)
RWM
DIS
VDE
WPC
LON
IPR
LOQ
(0.717s)
(0.724s)
(0.729s)
(0.731s)
(0.736s)
(0.747s)
Critical need for new code objects that identify rotating/locking MHD events

## Slide 4: Automated mode identification starts with FFT analysis of magnetic probe data
Consecutive FFTs give the phase and amplitude of a signal in frequency and time
shot 138854
Channel at φ = 302.8°
Mirnov signal & FFT amplitude

## Slide 5: Toroidal mode numbers are determined by toroidal phase matching of peaks in FFT
Input data from a toroidal array of magnetic probes
Toroidal mode number determined by best match to measured phase
Created a portable Python code for general use in tokamaks (e.g. NSTX/-U, KSTAR, etc.)
  Diagnostic configuration files allow easy setup for any tokamak
shot 138854
time = 0.72 s
(rad)
Single channel FFT
Match to n = 2

## Slide 6: Principal components can be optionally selected by SVD
SVD allows for decomposition of signals into principal components
  Can be used to pre-condition data for analysis (e.g. noise reduction, or to analyze dominant activity
  Capability to be tested in DECAF to determine advantages
shot 109810
shot 109810
Choosing only first two principal components
Magnetic spectrograms
Toroidal mode number
Toroidal mode number

## Slide 7: Discrete modes are processed as objects, key mode characteristics are determined and tracked
Frequency vs. time determined for continuous mode activity defines an object, fit for analytic determination of f’(t)
Quasi-steady state, rotation (bifurcation), and mode locking are automatically flagged for use by the DECAF code
shot 138854
n = 1 mode
“Quasi-steady-state” frequency
bifurcation
mode lock
Measured frequency
Fit frequency

## Slide 8: Algorithm tracks each mode as desired, searching for bifurcations, locking
NSTX 138854
bifurcation
lock
Zoomed-in View
Each “separate” mode considered a separate object in DECAF
Ongoing work to determine best ways to fully distinguish activity

## Slide 9: Examine mode locking in NSTX-U H-mode plasma
Experiment switching NBI and using beam blips leads to mode lock at insufficient plasma rotation

## Slide 10: Mode bifurcation and locking identified well in NSTX-U H-mode plasma
Code shows two n = 1 modes match frequency near time of bifurcation, apparently separate at mode lock
mode spin up
mode spin down
Lock (separation)
Magnetic spectrogram
Mode object and event analysis
NSTX-U 204091

## Slide 11: Richer mode activity somewhat more difficult to handle – concentrate on most dangerous modes
Code to ignore n = 3, 4 modes here due to high frequency, discontinuity
What will happen to frequency-separated n = 1 activity?
NSTX-U 204715
NSTX-U 204715

## Slide 12: n = 1, 2 modes are tracked, bifurcations and locking identified
Frequency separated n = 1 modes ~ 0.8s – 1.0s sometimes joined
Good identification of bifurcation and lock (most important)
NSTX-U 204715
bifurcations
lock
Steady-state frequency
Zoomed-in View

## Slide 13: Sawteeth reveal that bifurcation algorithm needs somewhat greater intelligence
Algorithm does identify sawtooth activity as continuous
Inflections in frequency presently interpreted as bifurcations (to be fixed)
NSTX-U 204077
errant bifurcations
steady-state f
Automated processing
Spectrogram

## Slide 14: Simple physics model for mode rotation evolution / mode lock forecasting derived, can be tested in DECAF as next step
Model derived to allow island drag for both “slip” and a “no slip” condition
Simple “W0” defines steady state
  Robust way to define this using the automated code?
Simple “W0/2” defines bifurcation point
Model based on
R. Fitzpatrick et al., NF 33 (1993) 1049
Bifurcation frequency
“steady-state”
~ W0/2
W0
mode frequency

## Slide 15: Automated characterization of rotating MHD modes is a key capability for disruption analysis, forecasting goal
Automated algorithm developed to characterize rotating MHD modes, spot their bifurcation and locking
  A critical capability to process general tokamak databases (ubiquitous rotating MHD activity)
General algorithm in portable Python code discriminates toroidal mode number, tracks modes as objects for DECAF
The algorithm was tested on a set of expected plasma scenarios in NSTX/-U
Code reads and can process KSTAR data. Needed next step to improve reading speed for long pulse data with high sampling rate