## Slide 1
S.A. Sabbagh1, J.W. Berkery1, Y.S. Park1, J.H. Ahn1, Y. Jiang1, J.D. Riquezes1, R.E. Bell2, M.D. Boyer2, A.H. Glasser3, J. Hollocombe4, J. Kim5, A. Kirk4, J. Ko5, W. Ko5, L. Kogan4, B. LeBlanc2, J.H. Lee5, Y.K. Oh5, F. Poli2, S.D. Scott2, A. Thornton4, L. Terzolo5, S.W. Yoon5, S.J. Wang5, Z.R. Wang2
V2.1
1Department of Applied Physics, Columbia University, New York, NY
2Princeton Plasma Physics Laboratory, Princeton, NJ
3Fusion Theory and Computation, Inc., Kingston, WA
4Culham Centre for Fusion Energy, UKAEA, Abingdon, UK
5National Fusion Research Institute, Daejeon, Republic of Korea
Progress on Disruption Event Characterization and Forecasting (DECAF) in Tokamaks
NSTX-U / Magnetic Fusion Science meeting
24 Sep 2018
PPPL
Princeton, NJ USA

## Slide 2: A broadened disruption prediction and avoidance analysis is progressing for ITER and future tokamaks
Motivation: Disruption prediction/avoidance is a critical need
  A highest priority DOE FES (Tier 1) initiative - present “grand challenge” in tokamak stability research:
    Can be done! (JET: < 4% disruptions w/C wall, < 10% w/ITER-like wall)
    ITER disruption allowance: < 1 - 2% (energy + E&M loads); << 1% (runaways)
Talk Outline
  Disruption Event Characterization and Forecasting (DECAF) review
  Present DECAF development and initial multi-device examination (now including MAST)
  Key related analysis (e.g. long pulse, high beta KSTAR kinetic equilibrium reconstruction, stability analysis, high non-inductive plasmas)
  “Predict-first” TRANSP analysis: 2018/2019 KSTAR operation with 2nd NBI system
  Summary / next steps

## Slide 3: International collaborative research on disruption prediction/avoidance expands effort to MAST-U, KSTAR
US DOE supports our efforts
  Multi-institutional collaborative grant on KSTAR, new grant on MAST-U
  Multi-faceted physics research includes equilibrium, stability, transport, control, diagnostic hardware elements
    Research originated on the NSTX spherical torus
Personnel
  Columbia U.:
    S.A. Sabbagh* (Lead PI), Y.S. Park, J.H. Ahn*, Y. Jiang* (post-doctoral)
    J.W. Berkery*, J. Bialek (part time); J.D. Riquezes* (Columbia student)
  PPPL: S. Scott (~full time, inst. PI), M. Boyer, B. LeBlanc (part time)
  MIT/ORISE: E.S. Marmar (inst. PI), B. Mumgaard
*PPPL TSDW meeting speakers

## Slide 4: Brief review: the DECAF code automatically computes events + disruption event chains leading to disruption
Events (in this chain)
  RWM: resistive wall mode
  VDE: vertical instability
  WPC: wall proximity control
Disruption event chain
0.60
0.65
0.70
0.75
t (s)
RWM
DIS
VDE
WPC
LON
IPR
LOQ
(0.717s)
(0.724s)
(0.729s)
(0.731s)
(0.736s)
(0.747s)
  LON: low density warning
  IPR: not meeting Ip request
  LOQ: low q warning
  DIS: disruption
NSTX
n = 1 RWM amplitude
Plasma rotation
bN

## Slide 5: DECAF reduced kinetic MHD model computations forecast the instability boundary to unstable global MHD modes
Favorable characteristics
  Stability contours CHANGE for each time point
  Possible to compute growth rate prediction in real time
ideal
Ideal + kinetic
unstable
stable
Norm. growth rate vs. time
gtw
139514
disruption
predicted instability
J.W. Berkery, S.A. Sabbagh, R. Bell, et al., Phys. Plasmas 24 (2017) 056103
Disruption forecasting
Global kinetic MHD mode growth
gtw
Increasing time
Collisionality (kHz)
Rotation
Predicted instability statistics
84% of shots are predicted unstable (stringent evaluation)
44% predicted unstable < 320 ms (approx. 60tw) before current quench
33% predicted unstable within 100ms of a minor disruption
NSTX

## Slide 6: DECAF code and initial successful research/results is now advancing to a new level
DECAF brief highlights of prior results
  First automated event chain analysis (followed deVries’ manual work)
  Excellent performance on smaller, targeted databases (NSTX)
    DIS event always found (100%), VDE event appeared in 90% of cases
    Computed events accurately represented experiment (~ 10 events)
    Physics model forecasted global MHD disruptions with ~ 85% reliability
  Disruption chains often repeated, e.g.:
Recent progress
  New DECAF MHD events allow analysis of general databases
  Coupling of new physics analysis tools and DECAF events
  Multi-machine databases (analysis now starting)
  Large database processing with small number of verified events
Very rapid progress on DECAF in these directions occurring day-to-day at the moment
RWM
DIS
VDE
WPC
IPR

## Slide 7: Progress on DECAF now moving to processing of multi-machine databases
Analysis
  Kinetic equilibrium / stability analysis on KSTAR; planned for MAST
DECAF database started
  Requires storage of DECAF analysis
Device / Capability | KSTAR | MAST | NSTX | DIII-D | TCV
Full database access (type) | Yes (MDSplus) | Yes (UDA) | Yes (MDSplus) | Yes (MDSplus) | Yes (MDSplus)
Database analysis | started | started | started |  | started
Equilibrium analysis | Kinetic + MSE | scheduled | Kinetic + MSE | available | 
Stability | Ideal, Resistive Kinetic MHD | scheduled | Ideal, kinetic MHD (resistive) | Ideal, kinetic MHD | 
shot*seconds (for kinetic analysis) | 1,886 (2016+2017) | 2,667 (est) (M7,M8, M9 runs) | 2,000 / year (est) |  | 
Aim to bring in ASDEX-Upgrade, JET, and C-Mod databases

## Slide 8: Initial analysis of large databases further supports published result that disruptivity doesn’t increase with plasma β
DECAF analysis of event
  Similar to a “standard” disruptivity analysis
  Shots analyzed at 10 ms intervals
Analysis during Ip flat-top
  MAST: 8902 plasmas analyzed
  NSTX: 4706 plasmas analyzed
  KSTAR: 750 plasmas analyzed (so far)
MAST
NSTX
KSTAR
DIS

## Slide 9: Experiments directly measuring global MHD stability verify that highest bN/li is not the least stable scenario (NSTX)
Resonant Field Amplification (RFA) measurement of stability
RFA Amp. (G/G)
Less stable
Non-intuitive stability increase at high bN/li
  decreases up to bN/li = 10, increases at higher bN/li
Understanding: Results consistent with kinetic stabilization theory invoking physical resonances
S. Sabbagh,et al., 2016 EPS Landau-Spitzer Award lecture
J. Berkery, et al., PoP 21 (2014) 156112
Less stable
More stable

## Slide 10: Initial analysis of large databases further supports published result that disruptivity doesn’t increase with βN
DECAF analysis of event
  Shots analyzed at 10 ms intervals
  NEXT STEP: DECAF event chain analysis
Analysis during Ip flat-top
  MAST: 8902 plasmas analyzed
  NSTX: 4706 plasmas analyzed
  KSTAR: 750 plasmas analyzed (so far)
DIS
MAST
NSTX
KSTAR

## Slide 11: DECAF density limit analysis started: global, local density limits examined, correlation of MHD onset near limits
Disruptivity vs. density
DIS
Magnetic spectrogram
(toroidal array)
Greenwald limit
  Approaches 1 near mode lock
Rad. island power balance
  Examining utility of this physics model for disruption warning
GWL
IPB
See talk by J. Berkery, Wednesday
GWL

## Slide 12: More powerful automated MHD event objects have been developed for DECAF
More capable MHD event objects required for analysis of wider tokamak databases
DECAF MHD events now include
  Mode number (n) discrimination
  Full history of mode evolution, including bifurcation and locking
  Many disruption warning criteria
DECAF automated MHD events
MHD-n1
MHD-n3
MHD-n2
Magnetic spectrogram
(toroidal array)
GWL
IPB

## Slide 13: New DECAF MHD events utilize history of 15 criteria to define time evolving disruption warning level
MHD-n1
MHD-n3
MHD-n2
DECAF automated MHD events
LTM-n1
LTM-n2
BIF-n1
BIF-n2
DECAF “heat map” (for MHD)
“quasi-steady
state (O)”
Initial findings
  Clear “safe” and “unsafe” periods of MHD appear in warning level
  Criterion history of wider range of plasma parameters improved the disruption warning reliability  illustrated by “Heat Map”
DECAF MHD warning level

## Slide 14: MHD heat map illustration summarizes understanding of disruption warning level
MHD-n1
MHD-n3
MHD-n2
DECAF MHD warning level
DECAF automated MHD objects
LTM-n1
LTM-n2
BIF-n1
BIF-n2
DECAF “heat map” (for MHD)
“quasi-steady
state (O)”
Very low f mode 
f below bifurcation 
 High amplitude 
Decreasing plasma rotation 
 Core plasma rotation < 6 kHz 
Locked mode > 25G 
Some notables for this heat map
  Mode frequency below bifurcation, decreasing plasma rotation key
  Early, slow warning level evolution
  Locked mode amplitude important, but warning comes in late
See TSDW talk by J. Riquezes

## Slide 15: While disruptivity plots provide important information, they can be misleading when used incorrectly
NSTX
Example: What are the most important regions to study on this plot?

## Slide 16: While disruptivity plots provide important information, they can be misleading when used incorrectly
NSTX
Example: What are the most important regions to study on this plot?
  A human might focus on the high disruption probability regions
  What causes the disruptions? (low bN, mid-li ???)

## Slide 17: While disruptivity plots provide important information, they can be misleading when used incorrectly
NSTX
Example: What are the most important regions to study on this plot?
  A human might focus on the high disruption probability regions
  Black-box machine learning might segregate disruptive from non-disruptive regions of the plot and learn from that division

## Slide 18: While disruptivity plots provide important information, they can be misleading when used incorrectly
NSTX
Example: What are the most important regions to study on this plot?
  A human might focus on the high event probability regions
  A machine learning algorithm might segregate disruptive from non-disruptive regions of the plot and learn from that division
  Problem plasma conditions can change significantly between first problem detected and when disruption happens
DIS
DIS

## Slide 19: While disruptivity plots provide important information, they can be misleading when used incorrectly
NSTX
Example: What are the most important regions to study on this plot?
  A human might focus on the high event probability regions
  A machine learning algorithm might segregate disruptive from non-disruptive regions of the plot and learn from that division
  Problem plasma conditions can change significantly by the time the disruption happens
Answer: the circles mark the key region to study!
  The shots suffer different “events” that are started in this region, and end up far from that region when they disrupt (at the crosses )

## Slide 20: While disruptivity plots can provide information, they can be highly misleading when used incorrectly
NSTX
Example: What are the most important regions to study on this plot?
  A human might focus on the high event probability regions
  A machine learning algorithm might segregate disruptive from non-disruptive regions of the plot and learn from that division
  Problem plasma conditions can change significantly by the time the disruption happens
Key Lessons:
  Using a “disruption database” that only contains data near the disruption time is misleading for disruption forecasting
  Only analyzing plasma conditions near the disruption time is not useful in many cases, even if one can figure out a way to forecast 100% accurately

## Slide 21: Standard disruptivity plots give no insight into physics; DECAF reveals the physics to provide improved forecasting
NSTX
MHD-n1
PRP
DIS
IPR
WPC
VDE
(0.490s)
BIF-n1
LTM-n1
(+.068s)
(+.073s)
(+.073s)
(+.077s)
(+.080s)
(+.005s)
(+.045s)
Long interval leading up to disruption
  Rotating MHD slows, bifurcates, and locks
126962
DECAF MHD warning level
DECAF automated MHD events
DECAF event chain
n =
1
2
3
  Then, plasma has an H-L back-transition (pressure peaking warning PRP) before DIS

## Slide 22: Standard disruptivity plots give no insight into physics; DECAF reveals the physics to provide improved forecasting
NSTX
123856
IPR
DIS
PRP
VDE
RWM
LOQ
(0.629s)
(+.010s)
(+.012s)
(+.058s)
(+.101s)
(+.101s)
(+.107s)
MHD-n1
LTM-n1
WPC
(+.106s)
(+.101s)
DECAF MHD warning level
DECAF automated MHD events
DECAF event chain
n =
1
2
3
Global MHD (RWM) can also be “slow”
  Rotating MHD warning level decreases after 0.46s  DANGEROUS for RWM onset
  H – L back transition (PRP) drags out time to disruption (> 100 ms)

## Slide 23: DECAF is fueled by coordinated research that continues to validate/develop physics models
Global MHD
  Detection: available magnetic diagnostics, plasma rotation, equilibrium
  Forecasting: Kinetic MHD model has high success in NSTX, DIII-D
Resistive MHD
  Detection / forecasting: available magnetic diagnostics, plasma rotation
  Forecasting: starting examination of MRE  start with D’ evaluation
Density limits
  Detection: rad. power, global empirical limit
  Forecasting: starting examination of rad. island power balance model
Physics analysis / experiments to build DECAF models
  Interpretive and “predict-first” analysis of KSTAR long-pulse, high beta plasmas with high non-inductive fraction
See talk by J. Berkery in 2 weeks
See TSDW 2018 talk by J. Riquezes
See TSDW 2018 poster by Y. Jiang
See TSDW 2018 poster by J.H. Ahn

## Slide 24: KSTAR kinetic equilibria w/ MSE are examined in the context of past published database
Y.S. Park, S.A. Sabbagh, et al., Nucl. Fusion 53 (2013) 083029 (magnetics-only)
16295
  High βN plasma
16325
  Higher BT (q95)
  Higher edge bootstrap current
18476 & 16498
  Internal Transport Barrier (ITB)
Examples in talk
16325
16295
(high bN)
18476 & 16498 (ITB)
Many thousands of kinetic equilibria run during testing

## Slide 25: Kinetic equilibria with MSE produces greater detail in P and q profiles than magnetics-only
Chart: Pressure Profile
Chart: Safety factor at Midplane
16325 @5.975s
16325 @5.975s
Global parameter | c2 | Error | Raxis (cm) | Zaxis (cm) | k | δTOP | δBOT | βT | βp | βn | li | q95
Magnetic only | 202 | 1.60E-07 | 186.1 | -0.7 | 1.68 | 0.54 | 0.80 | 0.95 | 1.86 | 1.89 | 1.05 | 6.39
Kinetic | 231 | 9.70E-05 | 185.6 | -2.4 | 1.68 | 0.50 | 0.80 | 1.09 | 1.95 | 2.10 | 0.97 | 5.91
See TSDW 2018 poster by Y. Jiang

## Slide 26: A broad non-inductive current fraction profile leads to low shear at low q in high plasma
t=1.482s
t=3.484s
t=4.084s
106
Current profile components
TRANSP
(67% non-inductive)
16295 t=1.75s
Magnetic spectrogram
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
8
6
4
2
0
q
q
q
Kinetic + MSE reconstructed q profile evolution
Evolves to low shear at low q
Weak n = 2 mode
βN>3
10
6
4
2
0
8
12
10
8
6
4
2
0

## Slide 27: Kinetic EFIT reconstructed again shows evolution to low-sheared q-profiles but now at high q
16325 t=2.05s
t=4.979s
t=10.491s
t=1.906s
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
0.0 0.2 0.4 0.6 0.8 1.0
yN
15
10
5
0
20
5
0
10
15
Kinetic + MSE reconstructed q profile evolution
106
Current profile components
TRANSP
(71% non-inductive)
Magnetic spectrogram
Low shear forms again, but at high q
q
q
q
15
10
5
0
20
Tearing modes absent

## Slide 28: Higher q95 plasma has greater ideal n = 1 no-wall stability in DCON, closer to marginal stability
Unlike higher bN plasma, equilibria is mostly stable to n = 1 ideal modes in DCON
  Note generally smooth evolution of stability criterion – reached with improved kinetic equilibria
The q-profile at higher BT evolves higher qmin above 1
  Sawteeth disappear
Reconstructed lower q shear at higher values of q does not lead to n = 1 instability in DCON
High q95 equilibria
DCON
KSTAR 16325
High q95 equilibria
qmin (w/ MSE)
}

## Slide 29: Classical tearing stability examined using resistive DCON code for high bN and higher q95 plasmas
Higher q95 equilibria
Resistive DCON
High bN equilibria
Resistive DCON
16325
16295
Classical tearing stability index, D′, computed at the q = 2 surface using outer layer solutions
At higher q95, D′ is mostly positive predicting unstable classical tearing mode
  Indicates that neoclassical effects or wall effects need to be invoked to produce stability
A.H. Glasser, et al., Phys. Plasmas 23 (2016) 112506
Experimentally
Unstable 2/1
Experimentally
2/1 stable

## Slide 30: Kinetic reconstructions focused first on KSTAR plasmas with high-non-inductive fraction
18492
16498
18476
16325
16295
See TSDW 2018 poster by J.H. Ahn (Columbia U.)
TRANSP analysis
Non-inductive fraction
  Beam-driven
  Bootstrap
Non-inductive fraction is key for stable high beta steady state operation
Volume average electron density (m-3)

## Slide 31: Predictive transport capability (TRANSP) allows “predict-first” projections for upcoming runs
6.5 MW NBI (2018)
96%
TRANSP 16325 | 2016 actual | 2018 NBI | 2019 NBI
NIC fract. (%) | 71% | 96% | 130%
bN | 2.7 | 3.4 | 4.4
li | 0.9 | 0.91 | 0.95
Ti(0) (keV) | 4.5 | 5.5 | 7.2
Te(0) (keV) | 4.6 | 3.3 | 3.3
ne(0) (1020m-3) | 5.2 | 5.6 | 5.5
fGreenwald | 0.5 | 0.5 | 0.5
H98y2 | 1.25 | 1.25 | 1.25
16325 projection
Project from existing KSTAR plasmas
  Set fraction of Greenwald density and confinement factor ITER H98y2
    Neoclassical ion transport, electron transport set to match H98y2
  KSTAR 1st and 2nd NBI systems are modeled (incl. aiming angles); power levels set realistically based on MSE needs, etc.
See TSDW 2018 poster by J.H. Ahn (Columbia U.)

## Slide 32: Transport analysis projections allow for variations of plasma parameters to meet targets
TRANSP 16295 (BT; Ip) | 2016 actual (1.2T) | 2018 NBI (1.2T) | 2018 NBI | 2019 NBI
NIC fract. (%) | 67% | 105% | 95% | 126%
bN | 3.5 | 5.4 | 3.5 | 4.4
li | 0.9 | 0.83 | 0.95 | 0.84
Ti(0) (keV) | 3.6 | 4.8 | 5.4 | 7.3
Te(0) (keV) | 2.3 | 2.8 | 3.2 | 3.3
ne(0) (1019m-3) | 6.0 | 4.8 | 5.6 | 5.6
fGreenwald | 0.6 | 0.5 | 0.5 | 0.5
H98y2 | 1.25 | 1.25 | 1.25 | 1.25
105%
6.5 MW NBI (2018)
16295
95%
BT = 2T, Ip = 0.5 MA
6.5 MW NBI (2018)
(2T, 0.5 MA)
BT=1.2T, Ip=0.44 MA

## Slide 33: Predictive TRANSP analysis shows KSTAR design target ~5 can be approached with ~100%
n=1 no-wall limit
n=1 with-wall limit
/=6
/=5
=1.5T
Predicted
NBI increased
  existing shot: 4.5 MW
  2018 NBI taken as 6.5 MW
By altering and values, , up to KSTAR design target 5 can be achieved with 100% non-inductive current fraction
=2.0T
=1.7T
Interpretive

## Slide 34: Rapidly-expanding DECAF approach provides a new paradigm for disruption prediction research
Multi-faceted, integrated approach to disruption prediction and avoidance with several key characteristics
  Physics-based approach yields understanding that is needed for confident extrapolation of disruption forecasting
  Physics-based DECAF events can guide how to avoid disruption
  Full multi-machine databases used (full databases needed!)
  Open to all methods of data analysis (physics, machine learning, etc.)
Automated determination of disruption event chains teach us the important regions of operating space to study
  Disruption DB “boundaries” are often NOT the important regions
Next steps
  Couple new MHD events to other events to reduce false positives
  Expand number of DECAF events evaluated in large database analysis
  Begin evaluation of simple quantitative figures of merit on large databases  aim for APS DPP 2018 meeting for these results

## Slide 35: Announcement: Research Activity RA(19-1): “Expand disruption prediction and avoidance capability for tokamaks”
NSTX-U Research Activity milestone for FY19
  Research activity will allow for communication of continuing DECAF analysis on multiple devices, interaction with interested researchers
    follows from prior NSTX disruption prediction/avoidance Working Group effort)
  Expand disruption event characterization, prediction, avoidance to more tokamaks (KSTAR, MAST expansion, continue NSTX, DIII-D, etc.)
Some subjects
  Continued improvement of the accuracy of disruption event warnings, disruption event chains vs. experiment, while reducing false positives
  Discussion/development of new physics, empirical, AI/ML models to improve disruption prediction performance
  Assessment of technical causes for disruptions, relation to physics
Format
  Monthly meetings planned discussing DECAF research progress
  Open to NSTX-U Team + all interested (contact: sabbagh@pppl.gov)

## Slide 36: Supporting slides follow

## Slide 37: Disruption event characterization is a critical and logical step in a disruption avoidance plan
Approach to disruption prevention
  Identify disruption event chains
  Predict events in disruption chains
  Cue disruption avoidance systems to break event chains
    Attack events at several places with active control
Expand analysis to more tokamak data
  Requires expansion of code analysis tools
t
Disruption prediction/avoidance framework (from DOE “Transient Events” report (2015))

## Slide 38: A reduced kinetic RWM model was created for DECAF code analysis
Ideal component dW
  Equilibrium quantities including li, p0/<p>, A, used in beta limit models for dWb, dWinf
Kinetic component dWk
  Functional forms (mainly Gaussian) used to reproduce precession and bounce/transit resonances
  Height, width, position of peak depend on collisionality
J.W. Berkery, S.A. Sabbagh, R.E. Bell, et al., NF 55 (2015) 123007
Bounce/transit resonances
Precession resonances
<n> = 1 kHz
DCON calculation of n=1 no-wall limit
Elements: mode growth rate calculation

## Slide 39: KSTAR magnetic diagnostics provide the basis for “magnetics-only” equilibrium reconstruction
KSTAR equilibrium magnetics
  Flux loops (45)
  Magnetic probes (105)
  Plasma currents (1)
  Coil currents (18)
  Loop voltage monitors (5)
  Vessel wall current groups (12)
Stabilizing plates / divertor plates included in model
PF, IVC, IVCC currents in model
S.A. Sabbagh, et al., Nucl. Fus. 41 (2001) 1601
Y.S. Park, et al., Nucl. Fus. 51 (2011) 053001
- Magnetic probes on the passive
plates and outboard limiter
(Photo courtesy of J.G. Bak and S.H. Hahn)

## Slide 40: Kinetic data supplements magnetics input for KSTAR kinetic equilibrium reconstructions
Motional Stark Effect (MSE)
  MSE (up to 25 channels) measuring plasma magnetic field pitch angle
Thomson scattering (TS)
  TS 27 channels
  Electron density & temperature (Ne, Te)
Charge exchange spectroscopy (CES)
  CES 32 channels
  Ion Temperature (Ti)
TS
CES
MSE
0 1 2 3 4
R (m)
2
1
0
-1
-2
Z (m)
Measured along Z=0

## Slide 41: Motional stark effect data provides magnetic pitch angle, q-profile constraint
1.7 1.8 1.9 2.0 2.1 2.2
R (m)
0.10
0.05
0.00
-0.05
-0.10
-0.15
Pitch angle at z=0
Angle (rad)
0.0 0.2 0.4 0.6 0.8 1.0
yN
20
15
10
5
0
q
Safety factor
△ data
— fitted
16325
4.555s
16325
4.555s
Systematic and statistical error estimates included in error bars
  E.g. background light subtraction (w/ Jinseok Ko, S. Scott)

## Slide 42: “Partial kinetic” approach for total pressure allows greater flexibility in profile shape
Electron Pressure Pe ← 27 Thomson scattering (Te & Ne), systematic error
Ion Pressure Pi ← 32 CES (Ti & Ni estimated from Ne)
Fast particle pressure Pfast “based” on Pe with 100% error bar
Total pressure Ptot = Pe + “Pi” + “Pfast” with large total error
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
3.0
2.5
2.0
1.5
1.0
0.5
0.0
Pe (104Pa)
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
5
4
3
2
1
0
Ti (103eV)
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
Total Pressure (104Pa)
△ data
△ data
Electron pressure profile
Ion temperature profile
Total Pressure profile
10
8
6
4
2
0
Total Pressure (104Pa)
16325
4.555s
16325
4.555s
16325
4.555s
△ data
— fitted
boundary
boundary
boundary

## Slide 43: Kinetic equilibrium with MSE has similar global parameters to magnetic-only equilibrium, some differences do occur
Magnetic only | Global parameter | Kinetic
202.4 | c2 | 222.6
1.86 | Raxis(m) | 1.86
-0.01 | Zaxis(m) | -0.02
1.68 | k | 1.68
0.54 | δTOP | 0.51
0.80 | δBOT | 0.81
0.95 | βT | 1.04
1.86 | βp | 1.86
1.89 | βn | 1.99
1.05 | li | 0.96
6.39 | q95 | 5.96
g016325.05986 (1013B2v15a2)
g016325.05975 (TST53b1)
Poloidal flux contours
LCFS
LCFS
Poloidal flux contours
16325 5.975s
16325 5.986s

## Slide 44: Clear pressure profile distinction between Internal Transport Barrier and H-mode phases
Broad pedestal pressure reconstructed in H-mode is not observed in earlier ITB phase
ITB
H-mode
L-mode
2.5
4.8
Xp by Jinil Chung
Safty factor q
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
Total Pressure (105Pa)
0.0 0.2 0.4 0.6 0.8 1.0
yN
15
10
5
0
1.8 1.9 2.0 2.1 2.2 2.3
R (m)
1.2
1.0
0.8
0.6
0.4
2
0.0
-0.2
16498
0.0 0.2 0.4 0.6 0.8 1.0
yN
15
10
5
0
Safety factor
t = 2.5s
Safety factor
t = 4.8s
Total Pressure
t = 2.5s
Total Pressure
t = 4.8s
1.2
1.0
0.8
0.6
0.4
2
0.0
-0.2
△ data
— fitted
△ data
— fitted
t = 2.5s
t = 4.8s
ITB phase
H-mode phase
 see poster by Y. Jiang (CU) Tuesday

## Slide 45: In contrast, kinetic equilibrium reconstruction with MSE produces substantial detail in P and q profiles
8
6
4
2
0
q
8
6
4
2
0
P (104Pa)
1.2 1.6 2.0 2.4
R (m)
Pressure profile
Safety factor
P (104Pa)
1.2 1.4 1.6 1.8 2.0 2.2 2.4
R (m)
q
8
6
4
2
0
Pressure profile
Safety factor
8
6
4
2
0
Pressure profile
Kinetic + MSE
Magnetics only
16325 5.975s
16325 5.986s

## Slide 46: DCON ideal stability of kinetic equilibria with good convergence yield steady analysis evolution
DCON stability calculations of δW indicate if plasma exceeds the ideal no-wall beta limit
Analysis of new KSTAR kinetic equilibria indicates ideal stability (below no-wall limit) during period shown (as expected)
4
3
2
1
0
-1
ITB
Limited plasma
0 2 4 6 8 10
Time (s)
Plasma total stored energy vs. time
Stored energy (105J)
KSTAR
18476
DCON: (A. H. Glasser, Physics of Plasmas 23 (2016) 072505

## Slide 47: Strong 2/1 tearing mode onset terminated high bN
Weak n = 2 activity during high bN phase
  |dBp| ~ 2 G
High bN operation was limited by strong 2/1 tearing mode onset
  Measured mode amplitude > 20 G
  Both Wtot and bN were reduced by ~35% but maintained H-mode
Plasma rotation profile significantly reduced by > 20% due to the 2/1 mode onset
Mode amplitude and toroidal magnetic probe spectrum in high bN discharge
Weak n = 2 mode
16295

## Slide 48: Resistive tearing mode stability of higher q95 plasma examined using M3D-C1
Perturbed toroidal current
M3D-C1
1.0
0.5
0
-0.5
-1.0
1.2
1.4
1.6
1.8
2.0
2.2
2.4
R (m)
Z (m)
Kinetic equilibrium 16325 at t = 5.668s
  bN = 2.0, bp = 1.9, qmin = 1.4
  DCON  ideal stable)
Resistive MHD computed to be stable by M3D-C1
  Consistent with experiment
  Initial analysis showing capability – will be continued
16325
Perturbed poloidal flux
q = 2
q = 2
g016325.05668
g016325.05668
1.2
1.4
1.6
1.8
2.0
2.2
2.4
R (m)
1.0
0.5
0
-0.5
-1.0
(M3D-C1: S.C. Jardin, et al., J. Comput. Phys. 226 (2007) 2146)

## Slide 49: High bN > 3 equilibria limited by rotating MHD
High bN plasmas were significantly extended to longer pulse by utilizing improved plasma control
Sustained high bNavg = 3.3 achieved for 3 s
  Ip ~ 450 kA, BT = 1.2 T, q95 = 4.0-4.5, Wtot = 270 kJ
2/1 tearing mode onset at high bN phase
  Consequently reduces bN and Wtot by ~35%
  Measured mode amplitude >20 G (2G at weak activity)
Stored energy (magnetics only)
bN > 3
q95 ~ 4

## Slide 50: Comparative equilibria having higher q95 shows significantly different MHD stability (shot 16325)
Plasma operation at elevated BT produced equilibria having higher q95 and bp
Unlike shot 16295, discharge doesn’t experience major beta-limiting MHD activity
Stored energy
bN ~ bp > 2
q95 > 6
Tearing modes absent
KSTAR 16325
Magnetic probe spectrogram

## Slide 51: Several stability codes are being used to analyze KSTAR kinetic equilibrium reconstructions
Ideal MHD analysis (kink/ballooning, resistive wall modes)
  Ideal DCON
  PEST
Kinetic MHD analysis (kinetic kink, resistive wall modes)
  MISK
Tearing modes
  Resistive DCON
  M3D-C1
(A. H. Glasser, Phys. Plasmas 23 (2016) 072505)
(A.H. Glasser, et al., Phys. Plasmas 23 (2016) 112506)
(S.C. Jardin, et al., J. Comput. Phys. 226 (2007) 2146)
(B. Hu, R. Betti, and J. Manickam, Phys. Plasmas 12 (2005) 057301)
(J.W. Berkery, S.A. Sabbagh, et al., Phys. Rev. Lett. 104 (2010) 035003)
(R.C. Grimm, J.M. Greene, and J.L. Johnson, Methods in Comp. Phys. 16 (1976) 253
INITIAL EMPHASIS on determining the quality of equilibrium convergence needed for reliable stability analysis
 see poster by Y. Jiang (CU) Tuesday

## Slide 52: DCON stability calculation shows high bN equilibria are subject to n = 1 ideal instability
At observed high bN phase, DCON calculates unstable n = 1 mode with no-wall (bN > bN no-wall)
Hypothesis: global kink / resistive wall modes stabilized by kinetic effects
High bN equilibria
DCON dW
KSTAR 16295
bN > 3 phase
DCON: A.H. Glasser, Phys. Plasmas 23 (2016) 072505
DCON computed dBn of unstable n = 1 mode at t = 2.356 s
Unperturbed
boundary
n = 1
bN = 3.2
DCON analysis, ideal n = 1 mode, no-wall boundary condition

## Slide 53
Kinetic modification to ideal MHD
Stability depends on
  Trapped / circulating ions, trapped electrons
  Particle collisionality
  Energetic particle (EP) population
  Integrated wf profile matters: broad rotation resonances in dWK
plasma integral over particle energy
collisionality
wf profile (enters in wE)
precession drift
bounce
Calculations of kinetic modifications to ideal stability examined with the MISK code
ion gyro-orbit
and trajectory
(Fig. adapted from R. Pitts et al., Physics World (Mar 2006))
Trapped particle orbit precession drift
Trapped particle
orbit
Trapped orbit 2D
projections
NSTX CALCULATIONS: Some references:
J. Berkery et al., PRL 104 (2010) 035003
S. Sabbagh, et al., NF 50 (2010) 025020
J. Berkery et al., PRL 106 (2011) 075004
S. Sabbagh et al., NF 53 (2013) 104007
J. Berkery et al., PoP 21 (2014) 056112
J. Berkery et al., NF 55 (2015) 123007
J. Berkery, et al., NF 24 (2017) 056103

## Slide 54: MISK kinetic RWM stability analysis shows stability, significant stabilizing effect of energetic particles
Resistive wall modes (RWM) computed to be stable (consistent with experiment)
  Close to marginal stability when examining variation of experimental rotation profile and without considering energetic particles
  Additionally, energetic particles contribute large stabilizing effect
Chart: Re(δWK)
 | -0.0141 | -0.013434 | -0.013074 | -0.012659 | -0.012268 | -0.012544 | -0.013329 | -0.01405 | -0.015871 | -0.015236 | -0.016387 | -0.015918 | -0.01532 | -0.019047 | -0.022566 | -0.026623 | -0.027417 | -0.027686 | -0.027285 | -0.028443
 | 11.975
 | 0 | 16325
 | -0.0029827 | -0.0033845 | -0.0036843 | -0.0038398 | -0.0040455 | -0.0043458 | -0.0047816 | -0.0048825 | -0.0058051 | -0.0041741 | -0.0044284 | -0.0027139 | -0.00081225 | -0.0020292 | -0.0027491 | -0.0035003 | -0.0040161 | -0.0041345 | -0.0042823 | -0.0046271
Chart: Scaled Rotation Profile (ωφ/ωφexp)
| 9.9999999999999006E-2 | 0.19999999999999901 | 0.29999999999999899 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2
 | -0.85352 | -0.84134 | -0.83529 | -0.82949 | -0.82549 | -0.83307 | -0.84757 | -0.86263 | -0.883 | -0.86522 | -0.8838 | -0.87386 | -0.85846 | -0.8884 | -0.90939 | -0.92763 | -0.93467 | -0.93789 | -0.93623 | -0.93906
 | -0.30806 | -0.46425 | -0.5813 | -0.66605 | -0.74316 | -0.82319 | -0.81414 | -0.90549 | -0.93726 | -0.61356 | -0.97573 | -0.59576 | -0.083202 | -0.20678 | -0.28979 | -0.38473 | -0.47232 | -0.50185 | -0.51646 | -0.58855
stable
unstable
Unstable region
Without EPs
With EPs
Without
EPs
With EPs
16325
t = 11.975s
experimental Vf profile

## Slide 55: TRANSP analysis shows new off-axis NBI sources can broaden current profile somewhat
110%
TRANSP 16325 | 2016 actual | 4 NBI (mid- plane) | 4 NBI (2 off axis)
NIC fract. (%) | 71% | 103% | 110%
bN | 2.7 | 3.65 | 3.65
li | 0.9 | 0.96 | 0.92
Ti(0) (keV) | 4.5 | 6.3 | 5.6
Te(0) (keV) | 3.6 | 3.3 | 3.3
ne(0) (1019m-3) | 3.2 | 5.5 | 5.5
fGreenwald | 0.5 | 0.5 | 0.5
H98y2 | 1.25 | 1.25 | 1.25
7 MW NBI (2 off-axis)
16325
projection
 see poster by J.H. Ahn (Columbia U.) on Tuesday for further KSTAR TRANSP analysis

## Slide 56
Transferred 10 channel MSE background light polychrometer from C-Mod to KSTAR (4/2017)
  Investigating improvement of MSE measurement by background light subtraction
  DOE has funded 15 additional BL polychrometer channels (for 2018)
Collaborative interaction to further improve Thomson scattering data
Continued improvement of kinetic equilibrium reconstruction / stability analysis
  E.g. Improved modeling / planned neural net delivery of fast particle pressure Pfast
(S.D. Scott (PPPL), et al.,)
Pitch angle can be troublesome on some channels due to neglect of background light subtraction
R (m)
1.7
1.9
2.1
2.3
pitch angle error (deg)
-1.5
0.0
-0.5
-1.0
0.5
1.5
1.0
      Kinetic equilibrium / stability analysis will continue to improve thru Columbia / PPPL / MIT Collaboration
 All supporting the main disruption prediction and avoidance research goals
Notes: Poly krou meter; In-vessel control coils(IVCC)

## Slide 57: Broadened disruption prediction and avoidance research centered around DECAF is progressing for future tokamaks
DECAF code is rapidly developing
  Initial published results showed strong promise of new, automated “event chain-based” research paradigm
  DECAF event objects expanded in capability now include event criteria histories; innovation continues (e.g. direct coupling of events)
  Models defining events are highly flexible (e.g. can include diagnostic comparisons, physics models, machine learning tools/techniques)
Physics-based approach on multiple devices key to success
  Understanding is key to disruption forecasting extrapolability, reliability
  New DOE funding for disruption prediction/avoidance on MAST; KSTAR research including kinetic equilibria, stability, TRANSP analysis
  Research includes active mode detection/control, directed experiments
“DECAF database” has begun
  Storage of intermediate results, est. growth to 100’s of TB (“big data”!)