## Slide 1: ITPA Global H-mode database update
S.M. Kaye, G. Verdoolaege, C. Angioni, F. Ryter, O. Kardaun, K. Thomsen, M. Maslov, M. Romanelli
20 Nov. 2018

## Slide 2: Genesis of upgrade effort
IO has encouraged community to update database and scaling
  Some parametric trends in scaling not reproduced machine-to-machine
  Scaling is old (1998); more data is available
  98y,2 scaling may not adequately reflect trends in ITER H-mode-baseline collection of discharges (Luce, IOS)
AUG

## Slide 3: Genesis - Very few of the entries in the present database approach ITER baseline conditions
McDonald et al. (2007) defined “ITER-like” subset
  Standard selection +
  1.4 < κ < 1.85
  1.6 < qcyl < 2.5
  1.83 < M < 2.17
In (private) database DB4V5, Standard Selection+ITER-Like (as above) yields very small, not entirely descriptive dataset
TOKAMAK Count
JET 53
MAST 3
NSTX 1
PBXM 72
TCV 17
Total 146

## Slide 4: Scope of task
Improve quality of predictions and inform and address physics investigations
In the latter case, a separation between core and pedestal needs to be made
Both objectives important, but requires careful consideration of what to include in update
  More of the same will not be sufficient
  Need to expand in types of entries, info in each entry
Expect scaling to change as data closer to the ITER baseline included

## Slide 5: Issues to consider in update of DB
Triangularity not included in old scaling, but is known to have an effect on confinement
  Incorporate into scalings
Rotation/torque/rotation shear have clear impact on local transport, confinement in various devices
  Include data
Include data from devices with high-Z divertor/walls
  JET, AUG (+ already existing C-Mod)
Confinement is known to depend on plasma characteristics close to or beyond pedestal
  Include SOL/separatrix density (JET, AUG)
  2-term scalings (need more info re pedestal top positions)

## Slide 6: Database update: DB5
Addition of data from fully metallic wall/divertor devices
  627 time slices from JET-ILW H-modes
  825 from AUG full W wall
Improved fast particle estimates (AUG)
DB5v7: 13913 points from 19 devices
  STD5: standard H-mode selection criteria 7294 points
  STD5-SEL1: q95>2.8, 1.3<κ<2.2, ε<0.5, Zeff<5 5956 points
  STD5-SEL2: 2.8<q95<3.5, 1.6<κ<2.0, 0.28<ε<0.385, Zeff<3 1674 points
ne,sep, ne,SOL, torque added (JET, AUG)

## Slide 7: Ranges of main scaling parameters in STD5

## Slide 8: Individual device scalings
Scaling with Ip similar for ITER-like devices (C-Mod, DIII-D JET) except AUG, but weaker for other devices
BT dependence weak in ITER-like devices, slightly negative in AUG
Scaling with ne weak in ITER-like devices, slightly stronger in JET-C. Stronger dependence in smaller or more circular devices
Power degradation weakest in ITER-like devices
Device | αI | αB | αn | αP | αδ | ακ | αM | RMSE | R2
ASDEX | 0.69 | 0.13 | 0.68 | -0.65 | - | - | 0.78 | 0.17 | 0.71
 | ±0.11 | 0.16 | 0.08 | 0.05 |  |  | 0.12 |  | 
AUG-C | 1.5 | -0.26 | 0.03 | -0.66 | - | - | - | 0.17 | 0.73
 | 0.07 | 0.08 | 0.04 | 0.03 |  |  |  |  | 
AUG-W | 1.60 | -0.30 | 0.06 | -0.53 | - | - | - | 0.11 | 0.89
 | 0.07 | 0.09 | 0.06 | 0.03 |  |  |  |  | 
C-Mod | 1.10 | - | 0.10 | -0.60 | - | - | - | 0.10 | 0.79
 | 0.20 |  | 0.18 | 0.15 |  |  |  |  | 
DIII-D | 1.10 | 0.08 | 0.10 | -0.67 | 0.70 | - | 0.45 | 0.20 | 0.80
 | 0.09 | 0.11 | 0.06 | 0.04 | 0.16 |  | 0.11 |  | 
JET-C | 1.10 | 0.16 | 031 | -0.76 | - | 1.20 | 0.05 | 0.16 | 0.89
 | 0.04 | 0.04 | 0.02 | 0.02 |  | 0.02 | 0.04 |  | 
JET-ILW | 1.10 | -0.16 | 0.07 | -0.57 | - | - | 0.40 | 0.11 | 0.86
 | 0.10 | 0.08 | 0.06 | 0.03 |  |  | 0.05 |  | 
JFT2M | 0.99 | - | 0.38 | -0.86 | - | - | 0.11 | 0.10 | 0.93
 | 0.08 |  | 0.08 | 0.04 |  |  | 0.06 |  | 

## Slide 9: H98y2 overpredicts confinement
STD5-SEL1
Overpredicts near Greenwald limit
Overpredicts for high-Z wall devices

## Slide 10: Scaling results

## Slide 11: Scaling results - continued
We are NOT suggesting ‘H18’ is a formal replacement for H98y2

## Slide 12: Scaling results - continued

## Slide 13: Summary and future steps
DB updated with high-Z wall data, additional variables
Single devices scalings reveal trends represented in 98y2
  ITER-like devices show more favorable trends
Scaling with updated DB
  Weaker dependence on toroidal field and density
  Noticeable influence of triangularity on confinement
  Further subsets (ELMy, no ELM, GELM, SELM, no PBXM) reflect “variations on the theme”
Include additional data (some in ITER-relevant regimes)
  DIII-D, C-Mod, EAST, Globus-M
Further analysis to focus on data and variable selection, model comparison, treatment of data subsets (weighting)
Dimensionless scalings