## Slide 1: The Role of Edge Locked Modes in ELMs Suppression and Density Pump-out in the DIII-D Tokamak

## Slide 2: N=2 RMP Used to Achieve ELM Suppression in Low Collisionality ITER Shape Plasmas in DIII-D
RMP causes ELM suppression and density pump-out
Hard to separate the two phenomena with fast RMP turn on

## Slide 3: Slow Phasing Scan Allows Exploration of Density Pump-out and ELM Suppression Dependence on RMP Spectrum
static
rotating
ΔΦUL
Vacuum
Plasma
Response
The varying coil phase changes the resonant coupling and amplitude of edge 3D magnetic field
MARS-F (S. Haskey)

## Slide 4: Slow Spectral Scan Separates Time Scales of ELM Suppression and Density Pump-out
ELM suppression requires low density, higher RMP amplitude
Density pump-out appears continuous with RMP amplitude
C. Paz-Soldan, et al., PRL 114, 105001 (2015)
R. Nazikian, et al., PRL 114, 105002 (2015)

## Slide 5: Locked-mode-like events are observed to coincide with onset of ELM suppression
Flattened Te at pedestal top
Locked mode like magnetic response
R. Nazikian, et al., PRL 114, 105002 (2015)

## Slide 6: Locked modes like events are also observed to correlate with ELM suppression and density pump-out in EAST
Phase jump in magnetic response suggests locked mode formation at the onset of ELM suppression in EAST
Y. Sun, et al., PRL 117, 115001 (2016)

## Slide 7: Main results
Simple nonlinear two-fluid MHD model used to identify the role of edge locked modes in density pump-out and ELM suppression
  Locked modes at the bottom of pedestal cause main density pump-out
  Locked modes at the top of the pedestal consistent with onset of ELM suppression
  Edge penetration threshold decreases for ITER due to lower perpendicular plasma flow
Screening
Field penetration

## Slide 8: Outline
Introduction of non-linear MHD code-TM1
Edge locked modes versus ELM suppression
Density pump-out due to edge locked modes
Scaling of the field penetration threshold
Summary

## Slide 9: TM1 - nonlinear MHD model
Cylindrical geometry, circular cross-section
Nonlinear, resistive, two-fluid equations
Q. Yu, et al., POP 10, 797 (2004); NF 48, 024007 (2008); NF 50, 025014, (2010); NF 51, 073030 (2011)

## Slide 10: Source terms are derived by initial profiles
The sources of momentum (Sm), particle (Sn) and energy (Se) are determined by the initial ωE, ne and Te profiles and fixed in the time evolution to maintain the initial profiles
The parallel current density gradient term comes from the two-fluid Braginskii equation
S.I. Braginskii, in Review of Plasma Physics, edited by M.A. Leontovich (Consultants Bureau, New York, 1965), Vol. 1, p. 205

## Slide 11: Source terms are derived by initial profiles
The sources of momentum (Sm), particle (Sn) and energy (Se) are determined by the initial ωE, ne and Te profiles and fixed in the time evolution to maintain the initial profiles
The parallel current density gradient term comes from the two-fluid Braginskii equation
S.I. Braginskii, in Review of Plasma Physics, edited by M.A. Leontovich (Consultants Bureau, New York, 1965), Vol. 1, p. 205

## Slide 12: Capability of TM1
Effects do not include compared to real tokamak
  Toroidal geometry:
    Toroidal mode coupling effect strong flow shear in pedestal region will suppress this effect
    Toroidal curvature effect will be canceled due to thermal transport
  Shape effect
  Finite ion temperature effect (Δr ~ W)
  Wall condition (free boundary or ideal wall in TM1)
TM1 is capable
  Nonlinear and two-fluid effects
  Able to run for high S (up to 1010) and (up to 1012) with good numerical convergence
  Runs faster even with tens of harmonics

## Slide 13: Thermal transport cancels the stabilizing effect of toroidal curvature
No thermal transport
Toroidal curvature causes screening at low rotation
RMP caused thermal transport will cancel it
Y.Q. Liu, J.W. Connor, S.C. Cowley, et al., POP 19, 072509 (2012)
X. Bai, Y.Q. Liu., Z. Gao, POP 24, 102505 (2017)
With thermal transport

## Slide 14: Some key results from TM1
Plasmoid
TM1 simulation found that both two-fluids effect & plasmoid formation speed up magnetic reconnection, being consistent with AUG experiment
Cooperation: Max-Planck/Princeton Center for Plasma Physics Q. Yu, S. Gunter, K. Lackner, NF 072005 (2014), 113008 (2015)
S. Gunter, Q. Yu, et al., PPCF 014017 (2015)
TM1 prediction
TM1 predicted density pump-out/pump-in by RMP, confirmed by J-TEXT experiment
Q. Hu, et al., NF 54, 122006 (2014)

## Slide 15: Input & output of TM1 for DIII-D analysis
=1 m2/s are used in TM1 simulation based on TRANSP analysis
Porter method* is used to derive (τp~300 ms~2τE)
Definition of island width:
Input parameters | Profiles: q, ωE, ne, Te  kineticEFIT Transport coefficients:  TRANSP * RMP amplitude at plasma edge  GPEC (Bv+Bres) Other parameters derived from the profiles
Output parameters m/n=0 & ≠0 | Profiles: j, ωE, ne, Te, ψ Other derived quantities: island width W, growth rate γ, phase, plasma response, etc
Porter, G. D. POP 5, 4311 (1998)

## Slide 16: Outline
Introduction of non-linear MHD code-TM1
Edge locked modes versus ELM suppression
  Locked modes at both the top and bottom of pedestal cause similar phenomena with ELM suppression
Density pump-out due to edge locked modes
Scaling of the field penetration threshold
Summary

## Slide 17: Shot 158115: input profiles for TM1 taken at a time when the RMP amplitude is at a minimum
Profiles at minimum RMP strength are used as initial profiles
m/n=7/2, 8/2, 9/2, 10/2 and 11/2 helicities are included
Initial profiles

## Slide 18: Shot 158115: Multiple helicity fields taken from GPEC for each DF as initial condition for TM1
GPEC calculation based on equilibrium at 3.3s
Br from GPEC
static
rotating
ΔΦUL

## Slide 19: TM-1 shows formation of top and bottom of pedestal locked modes
Locked modes (LMs) occur gradually when increasing Br
  7/2 LM appears
   11/2 LM appears, 7/2 decays
   8/2 LM appears, coexists with 11/2 LM
@ 1.1ψN

## Slide 20: TM-1 shows formation of top and bottom of pedestal locked modes
Locked modes (LMs) occur gradually when increasing Br
  7/2 LM appears
   11/2 LM appears, 7/2 decays
   8/2 LM appears, coexists with 11/2 LM
R. Nazikian, et al., PRL 114, 105002 (2015)
@ 1.1ψN

## Slide 21: Locked modes cause change in density, temperature and rotation
11/2 LM has low threshold
  causes continuous decrease in ne, Te and ωE
8/2 LM has high threshold
  causes sharp decrease in ne, Te and ωE

## Slide 22: Modeled parameters are consistent with experiment
The 8/2 LM window is wider than ELM suppression window
  Br is lower when βN is lower
   1/Ln=-ne’/ne
Experimental density changes more than simulation
   Other transport effect beyond TM1 model ?
Separatrix density does not change significantly
   1/Ln=-ne’/ne

## Slide 23: Change in density and temperature profiles consistent with experiment at the top of pedestal
initial
ELM supp.

## Slide 24: Change in density and temperature profiles consistent with experiment at the top of pedestal
Modeled ne and Te profiles are quantitatively consistent with experiment
Modeled ωE profile is different to experiment
   The change in ωE due to the change in Pi gradient is not included in TM1 model
  ωE ≈ 0 at q=4 surface
Enhanced fluctuations at top of pedestal may play a role in Er profile
Sim
Exp
R. Nazikian, et al., PRL 114, 105002 (2015)
G. Mckee, et al., NF 53, 113011 (2013)
initial
ELM supp.

## Slide 25: Predicted island width is larger than ion orbit width, so some density flattening is expected
 | Vacuum island width | TM1 Island width |  | LFS midplane |  | Averaged minor radius |  | Ion orbit width | 
 | W (ψN%) | W (ψN%) |  | r | W | r | W | Δr | ρi
8/2 | 3.4 | 2.2 |  | 47 | 0.9 | 79 | 3.8 | 1.2 | 0.3
11/2 | 1.4 | 1.34 |  | 49 | 0.5 | 90 | 3.2 | 0.55 | 0.1
Unit: cm
Passing ion orbit width Δr=qρi
  Ti ≈ Te is assumed based on main ion CER results *
  Main ion CER is resolving the anomaly in the negative power balance
* S.R. Haskey, et al., PPCF 60, 105001 (2018)

## Slide 26: Predicted island width is challenging to detect with Geometry of Thomson scattering system
Spatial resolution is not high enough to detect the predicted island width
8/2 island
11/2 island

## Slide 27: Outline
Introduction of non-linear MHD code-TM1
Edge locked modes versus ELM suppression
Density pump-out due to edge locked modes
  Locked modes at the bottom of pedestal cause main density pump-out
Scaling of the field penetration threshold
Summary

## Slide 28: TM-1 shows that at higher density there is no ELM suppression, consistent with experiment
Higher ne, lower Te, other parameters are the same
Higher moment of inertia requires higher torque for penetration
158115
159326

## Slide 29: Simulation shows single 11/2 locked mode at pedestal bottom causes density pump-out
Single 11/2 LM occurs in most of the period with maximum island width of 1.5%ψN
Causes modulation in ne, Te and ωE

## Slide 30: Simulation shows single 11/2 locked mode at pedestal bottom causes density pump-out
Single 11/2 LM occurs in most of the period with maximum island width of 1.5%ψN
Causes modulation in ne, Te and ωE
The modeled evolution of ne, Te and ωE are consistent with experiment
  Δt=t-3.4s
• Higher collisionality reduces parallel transport, pumpout

## Slide 31: Simulation shows single 11/2 locked mode at pedestal bottom causes density pump-out
Single 11/2 LM occurs in most of the period with maximum island width of 1.5%ψN
Causes modulation in ne, Te and ωE
The modeled evolution of ne, Te and ωE are consistent with experiment
    Δt=t-3.4s
Modeled ne and Te profiles are consistent with experiment
11/2 LM flattened ne and Te profiles at q=11/2 surface

## Slide 32: Reminder: Predicted 11/2 island width is too small to detect using Thomson scattering system
Spatial resolution is not high enough to detect the predicted island width
11/2 island

## Slide 33: RMP causes even weaker density pump-out at higher collisionality (density) due to smaller χ||
Simulation for shot 161202 is also consistent with experiment
ne,ped = 7.5, more than two times of shot 158115 and 159326
11/2 LM causes much weaker density pump-out (4%)
Higher collisionality reduces parallel transport, pump-out

## Slide 34: What parameters govern the locked modes causing density pump-out ?
The electron continuity equation
governs the particle transport due to LM, and hence*
Locked mode causes less density pump-out for higher collisionality, higher particle diffusivity and smaller island width
Higher collisionality leads to lower and weaker flattening on density
 | 158115 | 159326 | 161202
ne,ped | 2.8 | 3.5 | 7.5
Exp: Δne/ne | -20% | -15% | -4%
TM1: Δne/ne | -18% | -14% | -4%
* Q. Yu, et al., NF 51, 073030 (2011); F.L. Waelbroeck, et al., NF 52, 074004 (2012)

## Slide 35: Outline
Introduction of non-linear MHD code-TM1
ELM suppression versus edge locked modes
Density pump-out due to edge locked modes
Scaling of the field penetration threshold
Summary

## Slide 36: Scaling of 8/2 Penetration threshold for ELM suppression studied using 21x15 TM1 simulations
Scaling* power law obtained by fitting
Penetration is easier to happen for a lower density or less negative ωE
* Profiles of ne and ωE are shifted up and down (21×15)
ne in unit of 1019m-3, rotation in krad/s, Bt in T

## Slide 37: Predicted scaling consistent with experiment on DIII-D for rotation and density threshold
Scaling* power law obtained by fitting
Penetration is easier to happen for a lower density or less negative ωE
ne in unit of 1019m-3, rotation in krad/s, Bt in T
C. Paz-Soldan, R. Nazikian, et al., NF (just accepted)

## Slide 38: Simulation reproduced the density threshold (≈2.6e19) for ELM suppression seen in DIII-D
Scaling agrees with TM1 for different plasmas
   TM1 simulations are based on equilibrium & profiles prior to ELM suppression or at minimum density
There is an upper ne limit for threshold due to the limit of RMP strength

## Slide 39: TM1 simulated threshold for ITER n=3 penetration at pedestal top is an order of magnitude lower
Equilibrium profiles are generated based on EPED and TGLF prediction *
  q95=3.1
  Zero toroidal rotation
The onset threshold for 9/3 locked mode is Br/Bt=2.1×10-5
   An order lower than DIII-D
• Reason due to much lower expected ωE and ω*e in ITER
* O. Meneghini, et al., POP 23, 042507 (2016)

## Slide 40: The edge locked mode onset threshold for ITER is consistent with DIII-D scaling
The penetration threshold for ITER n=3 RMP will be an order lower than DIII-D due to lower flow frequencies
 | ITER | DIII-D 158115
Bt (T) | 5.15 | 1.98
ne (1019 m-3) | 9 | 3
Te (keV) | 4 | 1.5
ωE (krad/s) | -3 | -25
ω*e (krad/s) | -3 | -40

## Slide 41: The much lower rotation and diamagnetic drift frequency in ITER leads to the lower field penetration threshold
Our conclusions for edge resonant field penetration consistent with core locked mode studies for ITER [R.J. La Haye, et al., Phys. Fluids B 4, 2098 (1992)]

## Slide 42: Smaller island width at penetration threshold will cause less main ion density pump-out in ITER
 | TM1 Island width |  | LFS midplane |  | Averaged minor radius |  | Ion orbit width | 
 | W (ψN%) |  | r | W | r | W | Δr | ρi
9/3 | 0.8 |  | 172 | 1.0 | 316 | 4.0 | 0.72 | 0.24
11/3 | 0.5 |  | 178 | 0.6 | 348 | 3 | 0.2 | 0.05
Unit: cm
Lower penetration threshold leads to smaller island width and less density pump-out
Ion orbit width is even smaller than island width
  TM1 model should work better in ITER parameters than DIII-D
TM1 simulation does not address impurity transport

## Slide 43: Outline
Introduction of non-linear MHD code-TM1
ELM suppression versus edge locked modes
Density pump-out due to edge locked modes
Scaling of the field penetration threshold
Summary

## Slide 44
Summary
Locked mode at pedestal bottom causes the main density pump-out
The formation of locked modes at both the top and bottom of pedestal causes similar phenomenon of ELM suppression
The scaling power law implies that the penetration threshold for ITER will be an order lower than present devices

## Slide 45: Model limitations and next steps
Model limitation
   Cylindrical geometry, circular cross-section
    Toroidal coupling effect (almost updated)
    Shape effect
  Does not include NTV or finite orbit width effects
  Utilizing constant transport coefficients
    Update to radial transport profiles
Next step work
  Compare with more complete models (M3D-C1, XGC)
  Extend to n=1 on KSTAR & EAST and n=3 on DIII-D
  Explore q95 windows of ELM suppression

## Slide 46: Thanks for your attention

## Slide 47: Shot 158115: transport coefficients input from TRANSP
=1m2/s are used in TM1 simulation based on TRANSP analysis
Porter method is used to derive particle diffusivity

## Slide 48: 11/2 locked mode enhances parallel transport to produce density pump-out
The density gradient is mainly changed around 11/2 island region
 LM enhances parallel transport to produce density pump-out
   8/2 screening current also causes slight decrease in ne
The change in density linearly depends on the 11/2 island width
8/2 screening
current induced
11/2 island

## Slide 49: Hysteresis effect is observed in ELM suppression experiment and simulation
The required RMP amplitude to cause ELM suppression (and jump in ωE) is stronger than that for exiting ELM suppression
Similar hysteresis loop appears in the simulation

## Slide 50: Sensitivity study on transport coefficients
Smaller (larger) transport coefficients lower (increase) the penetration threshold
Penetration is hard to happened when turning off the parallel transport due to RMP

## Slide 51: Density and ωE of shot 158115 are shifted up and down to scan penetration threshold
8/2 penetration threshold is scanned at each density and ωE profiles (21×15 points)

## Slide 52: 8/2 Penetration threshold depends on density and ωE
TM1 simulation
Reproduced by scaling
Scaling power law obtained by fitting
ne in unit of 1019m-3, rotation in krad/s, Bt in T