## Slide 1
Princeton Plasma Physics Laboratory FES seminar
December 10, 2019
Oliver Schmitz1, Y. Feng2, M. Jakubowski2, R. Koenig2, M. Krychowiak2, M. Otte2, F. Reimold2, G. Anda3, T. Barbui1, C. Biedermann2, S. Bozhenkov2, S. Brezinsek4, B. Buttenschoen2, K.J. Brunner2, P. Drewelow2, F. Effenberg1,
D. A. Ennis5, T. Estrada4, E. Flom1, H. Frerichs1, O. Ford2, G. Fuchert2, Y. Gao4, D. Gradic2, O. Grulke2,
K. C. Hammond2, U. Hergenhahn2, U. Höfel2, J. Knauer2, P. Kornejew2, G. Kocsis3, T. Kremeyer1, S. Kwak2,
H. Niemann2, E. Pasch2, A. Pavone2, V. Perseo2, L. Rudischhauser2, G. Schlisio2, T. Sunn Pedersen2, J. Svensson2,
T. Szepesi3, U. Wenzel2, V. Winters1, G.A. Wurden6, D. Zhang2, S. Zoletnik3 and the W7-X experiment team
1Univ. of Wisconsin - Madison, Dept. of Engineering Physics, WI, USA
2Max Planck Institute for Plasma Physics, Greifswald, Germany
3Wigner, RCP RMI, Budapest, Hungary
4Inst. of Energy- and Climate Research, FZ Jülich, Jülich, Germany
5Auburn University, Auburn, USA
6Los Alamos National Laboratory, Los Alamos, USA
First time realization of a detached, stable, efficient particle and heat exhaust regime in the island divertor of Wendelstein 7-X
Acknowledgement: This work was funded in part by the U.S. Department of Energy under grant DE-SC00014210 and DE-SC00013911 and has been carried out within the framework of the EUROfusion Consortium with funding from the Euratom research and training program 2014-2018 and 2019-2020 under grant agreement No 633053. The views and opinions expressed herein do not necessarily reflect those of the European Commission.

## Slide 2
Heat flux detachment and a low level of eroding particle fluxes need to be combined with sufficient particle exhaust in a successful divertor concept
Radial Transport into SOL
D^, c^
What’s a divertor supposed to do?
Pumping system: stable particle exhaust needs sufficient pn
Plasma core performance is to be maximized
Stable density control
Low impurity influx (Zeff)
Helium exhaust (tp,He*/tE)
1
Divertor plasma defines
plasma wall interface
Heat and particle flux handling within technical limits
Power dissipation
Neutral compression
Impurity retention

## Slide 3
Heat flux detachment and a low level of eroding particle fluxes need to be combined with sufficient particle exhaust in a successful divertor concept
Upstream
where particle and heat flux come from (separatrix region)
Radial Transport into SOL
D^, c^
What’s a divertor supposed to do?
Downstream
where particle and heat flux go to (divertor targets)
Pumping system: stable particle exhaust needs sufficient pn
Plasma core performance is to be maximized
Stable density control
Low impurity influx (Zeff)
Helium exhaust (tp,He*/tE)
1
Divertor plasma defines
plasma wall interface
Heat and particle flux handling within technical limits
Power dissipation
Neutral compression
Impurity retention

## Slide 4
Heat flux detachment and a low level of eroding particle fluxes need to be combined with sufficient particle exhaust in a successful divertor concept
Radial Transport into SOL
D^, c^
Downstream
2
Upstream
Importance of high ned == high Gd ?
[Y. Feng et al., Contri. Plasma Phys. 54 (2014) 426-431]

## Slide 5
Heat flux detachment and a low level of eroding particle fluxes need to be combined with sufficient particle exhaust in a successful divertor concept
Radial Transport into SOL
D^, c^
Downstream
2
Upstream
Importance of high ned == high Gd ?
Ionization energy loss
Energy loss by impurity radiation
Rapid ionization
[Y. Feng et al., Contri. Plasma Phys. 54 (2014) 426-431]

## Slide 6
The island divertor at Wendelstein 7-X is a promising helical resonant divertor1 concept for stellarators
A low order resonance placed in the plasma edge defines the divertor structure
[X. Bonin et al., Nuclear Fusion 45 (2005) 22-29]
Magnetic islands
Plasma core
Plasma edge
3
1[F. Karger und K. Lackner, Phys. Lett. A, 66 (1977) 385 ], [R. Koenig et al., PPCF 44 (2002) 2365 ]

## Slide 7
A low order resonance placed in the plasma edge defines the divertor structure
[X. Bonin et al., Nuclear Fusion 45 (2005) 22-29]
Magnetic islands
Plasma core
Plasma edge
The island divertor at Wendelstein 7-X is a promising helical resonant divertor1 concept for stellarators
1[F. Karger und K. Lackner, Phys. Lett. A, 66 (1977) 385 ], [R. Koenig et al., PPCF 44 (2002) 2365 ]
The Island Divertor is a modular divertor
The divertor target plates intersect the islands
Plasma contour
4

## Slide 8
A low order resonance placed in the plasma edge defines the divertor structure
[X. Bonin et al., Nuclear Fusion 45 (2005) 22-29]
Magnetic islands
Plasma core
Plasma edge
The island divertor at Wendelstein 7-X is a promising helical resonant divertor1 concept for stellarators
Structure of 1 out of 10 divertor modules
1[F. Karger und K. Lackner, Phys. Lett. A, 66 (1977) 385 ], [R. Koenig et al., PPCF 44 (2002) 2365 ]
5

## Slide 9
Structure of 1 out of 10 divertor modules
A low order resonance placed in the plasma edge defines the divertor structure
[X. Bonin et al., Nuclear Fusion 45 (2005) 22-29]
Magnetic islands
Plasma core
Plasma edge
Horizontal Target
Vertical Target
The island divertor at Wendelstein 7-X is a promising helical resonant divertor1 concept for stellarators
1[F. Karger und K. Lackner, Phys. Lett. A, 66 (1977) 385 ], [R. Koenig et al., PPCF 44 (2002) 2365 ]
5

## Slide 10
A low order resonance placed in the plasma edge defines the divertor structure
The island divertor at Wendelstein 7-X is a promising helical resonant divertor1 concept for stellarators
1[F. Karger und K. Lackner, Phys. Lett. A, 66 (1977) 385 ], [R. Koenig et al., PPCF 44 (2002) 2365 ]
Standard divertor configuration (SDC): pairs of modules 180 degree apart toroidally are connected by magnetic flux tubes
6
[Y. Gao et al., Nuclear Fusion (2019)]

## Slide 11
A low order resonance placed in the plasma edge defines the divertor structure
This divertor concept was tested at W7-AS and now needs to be qualified as a viable stellarator system component for steady state plasma operation.
The island divertor at Wendelstein 7-X is a promising helical resonant divertor1 concept for stellarators
6
[Y. Gao et al., Nuclear Fusion (2019)]

## Slide 12
Outline of this talk in form of an executive summary
A stable, thermally fully detached island divertor regime with small divertor particle fluxes but still sufficient divertor neutral pressures was shown for the first time.
This island divertor regime is compatible with steady state particle exhaust for the upcoming high-performance campaign of W7-X.
The geometry of the magnetic islands forming the divertor allow to fine tune the divertor neutral distribution for maximized neutral pressure in the detached state.
This detached island divertor regime is reached with minimal feedback control in a reliable fashion and the divertor operational point is defined through sufficient radiative losses at a given input power.
7

## Slide 13
Outline of this talk in form of an executive summary
A stable, thermally fully detached island divertor regime with small divertor particle fluxes but still sufficient divertor neutral pressures was shown for the first time.
The geometry of the magnetic islands forming the divertor allow to fine tune the divertor neutral distribution for maximized neutral pressure in the detached state.
This detached island divertor regime is reached with minimal feedback control in a reliable fashion and the divertor operational point is defined through sufficient radiative losses at a given input power.
8
This island divertor regime is compatible with steady state particle exhaust for the upcoming high-performance campaign of W7-X.

## Slide 14
qmax = 1.5MW m-2
t=5s, ne,l.i.=9.5 1019 m-2, frad=0.35
qmax = 3MW m-2
Full and homogeneous thermal detachment was obtained during a gradual density increase by just 20% - a reliable access scenario due to frad dependence
20180814.024
Target heat flux density q [MW m-2]
qmax
0
t=6s, ne,l.i.=10.2 1019 m-2, frad=0.7
t=7s, ne,l.i.=11.3 1019 m-2, frad=0.8
qmax = 0.5MW m-2
9
Line integrated density ne,l.i. [1019 m-2]

## Slide 15
The homogeneous dissipation of the divertor power load during the density increase is reproduced in EMC3-EIRENE modeling
11

## Slide 16
The heat flux reduction is driven by a density scaling of frad and a complete thermal detachment is combined with significant neutral pressures
20180814.024
Integral heat flux to targets vanishes with increasing density
12
Line integrated density ne,l.i. [1019 m-2]

## Slide 17
20180814.024
20180814.024
Integral heat flux to targets vanishes with increasing density
Radiative fraction drives heat flux dissipation into detached regime
The heat flux reduction is driven by a density scaling of frad and a complete thermal detachment is combined with significant neutral pressures
12
Line integrated density ne,l.i. [1019 m-2]

## Slide 18
20180814.024
Small heat flux can be combined with significant neutral pressures
20180814.024
20180814.024
Integral heat flux to targets vanishes with increasing density
Radiative fraction drives heat flux dissipation into detached regime
A regime of small integral heat flux (<0.5MW) and small peak (<0.2 MW m-2) has been accomplished at up to 0.05-0.1 Pa (10-3 mbar) neutral pressure levels
The heat flux reduction is driven by a density scaling of frad and a complete thermal detachment is combined with significant neutral pressures
12
Line integrated density ne,l.i. [1019 m-2]

## Slide 19
This stable detachment was obtained with high divertor neutral pressures for up to 30s only limited by input energy limits in the uncooled divertor phase
13

## Slide 20
Outline of this talk in form of an executive summary
A stable, thermally fully detached island divertor regime with small divertor particle fluxes but still sufficient divertor neutral pressures was shown for the first time.
The geometry of the magnetic islands forming the divertor allow to fine tune the divertor neutral distribution for maximized neutral pressure in the detached state.
This detached island divertor regime is reached with minimal feedback control in a reliable fashion and the divertor operational point is defined through sufficient radiative losses at a given input power.
This island divertor regime is compatible with steady state particle exhaust for the upcoming high-performance campaign of W7-X.

## Slide 21
Moderate divertor neutral pressures within a quite limited density range was seen at W7-X without a boronization
2MW, pre-boronization
3MW, pre-boronization
Averaged neutral particle pressure at pumping gap
Neutral particle compression in divertor
Before boronization: oxygen and carbon were the dominant impurities
14
Line integrated density ne,l.i. [1019 m-2]
Line integrated density ne,l.i. [1019 m-2]

## Slide 22
Boronization of W7-X yielded build up of substantial divertor neutral pressure at largely increased density limits
3MW, post-boronization
2MW, post-boronization
6MW, post-boronization
Averaged neutral particle pressure at pumping gap
Neutral particle compression in divertor
32 - 45
10 - 15
After boronization: oxygen content was reduced by up to a factor of 20
15
Line integrated density ne,l.i. [1019 m-2]
Line integrated density ne,l.i. [1019 m-2]

## Slide 23
Structure of the magnetic island
This attractive scenario could be fine tuned by adjustment of the structure of the magnetic island that form the divertor
3MW, post-boronization
2MW, post-boronization
6MW, post-boronization
Plasma core domain
Pumping gap
Wall to wall connection length Lc [m]
Averaged neutral particle pressure at pumping gap
16
Line integrated density ne,l.i. [1019 m-2]
>1000
Icc=0.0kA

## Slide 24
3MW, 2kA ICC
6MW, 2kA ICC
Applying a stationary divertor control current allows to increase the divertor neutral pressure by up to 50%
3MW, post-boronization
2MW, post-boronization
6MW, post-boronization
Plasma core domain
Pumping gap
Island widening, closure of outer gap
Strike point moves towards gap
Connection length Lc reduced
Icc=2.0kA
Change of island structure with divertor control coil current Icc
Wall to wall connection length Lc [m]
Averaged neutral particle pressure at pumping gap
17
Line integrated density ne,l.i. [1019 m-2]
>1000

## Slide 25
3MW, 2kA ICC
6MW, 2kA ICC
Increasing the divertor island size allows to increase the divertor neutral pressure by up to 50% compared to small island configuration
3MW, post-boronization
2MW, post-boronization
6MW, post-boronization
Plasma core domain
Pumping gap
Island widening, closure of outer gap
Strike point moves towards gap
Connection length Lc reduced
Analysis target
Icc=2.5kA
Wall to wall connection length Lc [m]
Change of island structure with divertor control coil current Icc
17
Line integrated density ne,l.i. [1019 m-2]
>1000

## Slide 26
Particle flux detachment develops together with power detachment and pressure build up due to increasing radiation
18

## Slide 27
Both, heat and also particle fluxes are detached but still a high neutral pressure of up to 6.5 10-4 mbar are reached! What is behind this interesting feature?
Particle flux detachment develops together with power detachment and pressure build up due to increasing radiation
18

## Slide 28
Particle flux detachment can be combined with sustainment of neutral particle exhaust under power detachment in the island divertor
Distribution of neutrals in island divertor module defines neutral influx Gin, H0 into pumping domain.
19

## Slide 29
Intuitive model:
Neutral distribution is defined by local plasma parameters in island
Mean free ionization lio lengths vs. mean distance to pump entrance lp defines pn
Increasing frad reduces Te and hence increases ionization length scale lio, also ne,target is reduced
More neutrals can enter the pumping domain
[Y. Feng et al., W7-X workshop, 2017]
Distribution of neutrals in island divertor module defines neutral influx Gin, H0 into pumping domain.
[Y. Feng et al., Nuclear Fusion 56 (2016) 126011]
Particle flux detachment can be combined with sustainment of neutral particle exhaust under power detachment in the island divertor
19

## Slide 30
[Y. Feng et al., W7-X workshop, 2016]
Distribution of neutrals in island divertor module defines neutral influx Gin, H0 into pumping domain.
Intuitive model:
attenuation factor
recycling flux
mean distance to pumping gap
mean ionization length scale
[Y. Feng et al., Nuclear Fusion 56 (2016) 126011]
Key plasma parameter
Regulated through
3D modeling predicts that frad moderates the neutral ionization distribution such that an increase of lio yields increasing pn with reduced Ftarget
20

## Slide 31
Experimental data support this intuitive model
Averaged neutral pressure [10-4 mbar]
Isat [1022 m-2 s-1]
Frec, integral [1021 s-1]
Particle flux detachment can be combined with sustainment of neutral particle exhaust under power detachment in the island divertor
21

## Slide 32
Experimental data support this intuitive model
Averaged neutral pressure [10-4 mbar]
No pn roll-over is observed in the experiment due to frad limit from ECH heating scenario
Isat [1022 m-2 s-1]
Frec, integral [1021 s-1]
Particle flux detachment can be combined with sustainment of neutral particle exhaust under power detachment in the island divertor
21

## Slide 33
The radiation fraction is dependent of the heating power for a given density range – this is the basis for the regulation of divertor temperature in the island
The radiated fraction depends on density which in turn is defined by the available heating power through ECRH – this sets the stage for the detached regime.
3MW, Icc=0kA
Pre-boronization
5.8MW, Icc=0kA
6.2MW, Icc=2kA
Heat and particle flux detachment domain with stable neutral pressure
3.0MW, Icc=0kA
22
5.8MW, Icc=0kA
6.2MW, Icc=2kA
5.8MW, Icc=2.5kA
3MW, Icc=0kA
Line integrated density ne,l.i. [1019 m-2]

## Slide 34
Radiation in detached state is localized predominantly around separatrix – exact resolution so far very challenging due to limited resolution of bolometer
Exact power balance in the plasma edge layer is a high priority topic to disentangle radiation contributions
23

## Slide 35
Radiation in detached state is localized predominantly around separatrix – exact resolution so far very challenging due to limited resolution of bolometer
Exact power balance in the plasma edge layer is a high priority topic to disentangle radiation contributions – modeling suggests radiation inside SOL up to frad ~0.8
24
Island size dependence of C radiation around islands at frad=0.8
Small island
Medium island
Large island
Radiation localized at strike point
Radiation fills island domain
Radiation reaches separatrix

## Slide 36
Carbon impurity source and C-II line emission define the local radiation equilibrium which detaches from surface
Detachment transition
LCFS
25
0.1
0.2
0.2
0.3
0.1
Divertor target

## Slide 37
Carbon impurity source and C-II line emission define the local radiation equilibrium which detaches from surface
Detachment transition
Detachment transition
LCFS
25
0.1
0.2
0.2
0.3
0.1
Divertor target
The integrated C-II emission is reduced but the C-source estimated (1022 part. s-1) shows almost no significant reduction.
Effect of local plasma parameters!

## Slide 38
Carbon radiation distribution is followed by position of 15 eV isothermal surface in island divertor domain
Iso-thermal surface (Te ~15 eV) moves inward with radiation front.
Detachment transition
LCFS
Divertor target
10
15
15
20
25
He-I emission too low
Density at the position of this surface is almost constant (ne ~ 5.0 1019 m-3)
26

## Slide 39
Outline of this talk in form of an executive summary
A stable, thermally fully detached island divertor regime with small divertor particle fluxes but still sufficient divertor neutral pressures was shown for the first time.
The geometry of the magnetic islands forming the divertor allow to fine tune the divertor neutral distribution for maximized neutral pressure in the detached state.
This detached island divertor regime is reached with minimal feedback control in a reliable fashion and the divertor operational point is defined through sufficient radiative losses at a given input power.
This island divertor regime is compatible with steady state particle exhaust for the upcoming high-performance campaign of W7-X.

## Slide 40
Linear scaling of plasma density with input power enables build up of sufficient divertor neutral pressures and maximize by island size increase
Data were averaged over stable detached windows for various experimental programs with [0.75<frad<0.9]
27
Line integrated density ne, l.i. [1019 m-2]
Line integrated density ne, l.i. [1019 m-2]

## Slide 41
The divertor neutral pressures obtained scale favorably towards steady state
Data were averaged over stable detached windows for various experimental programs with [0.75<frad<0.9]
Linear scaling of plasma density with input power enables build up of sufficient divertor neutral pressures and maximize by island size increase
27
Line integrated density ne, l.i. [1019 m-2]
Line integrated density ne, l.i. [1019 m-2]

## Slide 42
Pumping particle flux level reached under reliably detached conditions is compatible with exhaust requirements for steady state
Existing pumping capacity from Turbo-Pumps: 10 x 3 x 1250 l/s=37500 ltr. Hydrogen /s
Expected pumping capacity with Cryo-pump: 70.000 ltr. Hydrogen /s
Basic observation: increase of neutral back pressures of <8.0 10-4 mbar averaged across all available pump ducts for after Boronization from <5.0 10-5 mbar before Boronization
Value | TMP scenario | Cryo scenario
Pumped flux Gpump | 5.2 1020 H2/s | 9.25 1020 H2/s
Fueled flux Gin | 5.0 1020 - 1.0 1021 H2/s | 5.0 1020 - 1.0 1021 H2/s
Based on example 20180814.024 with 8.0 10-4 mbar averaged divertor pressure |  | 
Pumped flux Gpump | 9.0 1019 H2/s | 1.6 1020 H2/s
Fueled flux Gin | 2.2 1020 - 2.0 1021 H2/s | Does not scale, low ne
Executed based on example 20180801.039 and 20171207.024 with 5.0 10-5 mbar averaged divertor pressure |  | 
OP1.2.b
OP1.2.a
28

## Slide 43
Summary and conclusions
The attractive detached island divertor regime was reached through intrinsic radiation scaling with density, which is defined by the input power.
29
Input power level defines density, Frec and frad level
Frec builds pn with ln tuned by local Te
A possible hierarchy of the process
frad >0.75 yields detachment
Heat and particle flux detachment with large enough neutral source access to pump domain for steady state exhaust
Magnetic island size, magnetic connection length and strike line position as actuators
This regime was only limited by input energy limits, which will be overcome with the actively cooled High-Heat Flux (HHF) divertor.
The results so far have laid ground for a promising outlook on the overall steady state compatibility of the island divertor concept.

## Slide 44
Appendix

## Slide 45
Carbon charge states emit across the island divertor volume featuring a quadratic dependence on density which defines divertor Te
Quadratic rise of carbon line radiation close to the target (C-III), in the island domain (C-IV) and around separatrix (C-VI) supports facilitation of detachment by intrinsic impurity radiation
Carbon as intrinsic impurity supports the necessary radiative losses localized inside and in the close vicinity of the island domain.
A2
6.0MW, Icc=2.0kA
3MW, Icc=0kA
3MW, 2kA ICC
3MW, post-boronization

## Slide 46
Heat and particle flux detachment domain with stable neutral pressure
The divertor neutral pressure level depends on density scaling with increasing heating power – access to detachment for frad>0.75
5.8MW, Icc=0kA
6.2MW, Icc=2kA
5.8MW, Icc=2.5kA
3MW, Icc=0kA
Common compression ratio of >30 is seen at detachment level radiative fractions
At a radiated fraction of 0.75 < frad < 0.9 a saturated neutral pressure pn regime is seen with pn being set by the plasma density
A3

## Slide 47
The volume of the magnetic island is predicted to serve as a reliable interface layer with a beneficial radiation and ionization equilibrium
Island size dependence of C radiation around islands at frad=0.8
Small island
Medium island
[Y. Feng et al., Nuclear Fusion 56 (2016) 126011]
Large island
Radiation localized at strike point
Radiation fills island domain
Radiation reaches separatrix
Interplay of radiation distribution with power dissipation and divertor neutral capture is key to understand the island divertor!
A4

## Slide 48
The EMC3-EIRENE model in a nutshell
A6
[Y. Feng et al., JNM 266-269 (1999) 812]
[Y. Feng et al., PPCF 59 (2017) 034006]
[Y. Feng et al., Contri. Plasma Phys. 54 (2014) 426-431]
Figure courtesy of H. Frerichs

## Slide 49
The radiation fraction is dependent of the heating power for a given density range – this is the basis for the regulation of divertor temperature in the island
The radiated fraction depends on density which in turn is defined by the available heating power through ECRH – this sets the stage for the detached regime.
3MW, Icc=0kA
Pre-boronization
5.8MW, Icc=0kA
6.2MW, Icc=2kA
Heat and particle flux detachment domain with stable neutral pressure
EMC3-EIRENE predicts comparable scaling of radiation in island with density
3MW, ICC=0kA, 10% O
5.8MW, Icc=2kA, 4% C
5.0MW, Icc=0kA, 4% C
3.0MW, Icc=0kA
A7

## Slide 50
3MW, Icc=0kA
Pre-boronization
5.8MW, Icc=0kA
6.2MW, Icc=2kA
3.0MW, Icc=0kA
EMC3-EIRENE modelling
Dependence of target parameters on frad is consistent between experiment and EMC3 model, but a significantly weaker dependence is found in measurement
A8

## Slide 51
3MW, Icc=0kA
Pre-boronization
5.8MW, Icc=0kA
6.2MW, Icc=2kA
3.0MW, Icc=0kA
EMC3-EIRENE modelling
Dependence of target parameters on frad is consistent between experiment and EMC3 model, but a significantly weaker dependence is found in measurement
Power level defines density and hence Frec
Frec provides source for pn
Optimal neutral particle distribution for good pump access is defined by frad
A possible hierarchy of the process
A9

## Slide 52
Dependence of target parameters on frad is consistent between experiment and EMC3 model, but a significantly weaker dependence is found in measurement
EMC3-EIRENE modelling
5.8MW, Icc=0kA
6.2MW, Icc=2kA
3MW, Icc=0kA
Pre-boronization
Power dissipation due to radiation from intrinsic impurity yields thermal detachment
A10

## Slide 53
Particle flows are reduced at transition into detachment
Detachment
achieved
Acknowledgement: V. Perseo
A11