## Slide 1
NSTX Upgrade for Establishing Physics and Technology Basis for FNSF
Masayuki Ono
for the NSTX-U Team
2014 TOFE Meeting
November 10 – 13, 2014
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Tsukuba U
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
NFRI
KAIST
POSTECH
SNU
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
NSTX-U
Supported by

## Slide 2
Introduction and Motivation for NSTX-U
NSTX Upgrade Project
NSTX-U ST-FNSF Targeted Experiments
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 3
NSTX-U is nearing its first plasma
New center-stack and 2nd NBI are major upgrade scopes
NSTX (1999-2011)
New CS and Highly tangential 2nd NBI for non-inductive operations
R0 ~ 0.85 m
NSTX-U (2015 - )
R0 ~ 0.90 m

## Slide 4
ST-FNSF
ST Pilot Plant
ITER
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop solutions for the plasma-material interface challenge
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop ST as fusion energy system
Liquid Lithium
“Snowflake”
NSTX Upgrade Mission Elements

## Slide 5
Substantial Increase in NSTX-U Device / Plasma Performance ~ X 2 BT, Ip and PNBI and ~ x 5 pulse length from NSTX
NSTX
Previous
center-stack
New
center-stack
 | R0 (m) | Amin | Ip(MA) | BT (T) | TTF(s) | RCS (m) | ROB (m) | OH flux (Wb)
NSTX | 0.854 | 1.28 | 1 | 0.55 | 1 | 0.185 | 1.574 | 0.75
NSTX-U | 0.934 | 1.5 | 2 | 1 | 6.5 | 0.315 | 1.574 | 2.1
New CS together with highly tangential NBI injection provides ~ 2x higher CD efficiency for sustained 100% non-inductive operations needed for FNSF
TF OD = 40cm
TF OD = 20cm
New 2nd NBI
Present NBI

## Slide 6
An ST is a low-aspect-ratio, high bT tokamak
Higher bT enables higher fusion power and compact FNSF
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Data base from START, MAST, PEGASUS and NSTX
Pfusion ∝ p 2 x Vol
Pfusion ∝ bT2 BT04 x Vol
Physics Knob
Product
Investment
Wn ∝ Pfusion / Area
High neutron wall loading Wn possible in a compact FNSF
Wn ∝ bT2 BT04 a (not strongly size dependent)
Wn ~ 1-2 MW/m2 with R ~ 1 m ST-FNSF feasible!
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a

## Slide 7: There have been several studies of ST-FNSF showing the potential attractiveness of this approach
Projected to access high neutron wall loading at modest R0, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R0 ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R0, careful design
NSTX-U to address ST-FNSF R&D needs
  Non-inductive start-up, ramp-up, sustainment
  Confinement scaling (especially electrons)
  Stability and steady-state control
  Divertor solutions for (ss) high heat flux
  Radiation-tolerant magnets, design
Culham (UK)
UT Austin
ORNL
PPPL
Example ST-FNSF concepts
ST-FNSF by T.G. Brown and J. Menard at this conference

## Slide 8
Introduction and Motivation for NSTX-U
NSTX Upgrade Project
NSTX-U ST-FNSF Targeted Experiments
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 9
NSTX Upgrade Project Progress Overview
R. Strykowsky, E. Perry, T. Stevenson, L. Dudek, S. Langish, T. Egebo, M. Williams and the NSTXU Project Team
9
Inner TF bundle
TF Flex bus
OH coil
Inner PF coils
Enhance outer TF supports
Enhance PF supports
Reinforce umbrella structure
New umbrella lids
Power systems
I&C, Services, Coil protection
Center stack
Structure
Ancillary Sys
Decontaminate TFTR beamline
Refurbish for reuse
Relocate pump duct, 22 racks and numerous diagnostics to make room in the NSTX Test Cell
Install new port on vacuum vessel to accommodate NB2
Move NB2 to the NSTX Test Cell
Install power, water, cryo and controls
2nd NBI Project Scope
New Center Stack Project Scope
NSTX-U Analyses – P. H.Titus at this conference

## Slide 10: Innovations and Challenges in Manufacturing New Center-Stack
TF Flex-bus - EDM cuts from solid copper chromium zirconium block
Friction stir welding enabled joining of two different copper alloys without annealing in TF lead area.
Copper cooling tubes were soldered into the TF conductor assemblies using solder paste with non-ionic “R” flux (instead of Zn-Cl-based flux) .
Vacuum Pressure Impregnation performed with CTD-425 (Cyanate Ester / Epoxy Blend Resin. (highly exothermic).
Water soluble “Aquapour” was applied to provide 0.1” gap between TF and OH coils.
Radially very thin Rogowski and magnetic sensors.
CS Casing
TF cooling lines
TF Coil
OH Coil
PF Coil 1a
PF Coil 1b
PF Coil 1c
CHI bus

## Slide 11
Assembly of Inner TF Quadrants
(9) individual conductors into each Quadrant mold
Quadrant manufacturing technique was used to maintain precision for the long length and relative ease of assembly

## Slide 12
Assembled TF mold ready for Vacuum Pressure Impregnation with CTD-425 resin
This is first of six VPI operation conducted on NSTX-U. Care must be taken due to the highly exothermic nature of the Cyanate Ester / Epoxy Blend Resin. Raised temperature very slowly ~ 2 days.

## Slide 13
Completion of First TF Quadrant
NSTX-U PPPL Magnet Fabrication Team

## Slide 14
Much thanks to Jim Chrzanowski for 40 years of pioneering fusion magnet manufacturing

## Slide 15
The quadrants assembled with S-2 glass tape between layers & pre-insulated G-10 core

## Slide 16
Full TF Bundle in oven after successful VPI

## Slide 17: A movie of OH coil winding at PPPL

## Slide 18
Center-stack Components Fabricated
Center-stack assembly complete
Vacuum Pressure Impregnation
of OH Complete
Inner TF/OH coil bundle complete
CS casing installed over the TF/OH coil bundle

## Slide 19
New Center-Stack Installed In NSTX-U (October 24, 2014)
First plasma scheduled in Mar. 2015 and research operation in May 2015.

## Slide 20
Relocation of the 2nd NBI beam line box from the TFTR test cell into the NSTX-U Test Cell Complete.
Beam Box being lifted over NSTX
Beam Box placed in its final location and aligned
Beam Box being populated with components
TFTR NBI beam box / components successfully tritium decontaminated.

## Slide 21
Highly Tangential 2nd NBI Enabled by JK-Cap
Outer Wall Radius Moved Outward to Avoid Beam Clipping
JK cap
Interior View of Bay J-K
Exterior View of Bay J-K

## Slide 22
NSTX Upgrade Project Is Nearly Complete
Recent aerial view of NSTX-U Test Cell (Oct. 27, 2014)
CS Casing
HHFW System
1st NBI
2nd NBI
NSTX-U

## Slide 23
Introduction and Motivation for NSTX-U
NSTX Upgrade Project
NSTX-U ST-FNSF Targeted Experiments
Summary
Talk Outline
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 24
Compact ST-FNSF has no/small central solenoid
NSTX-U Addressing Critical Issues for FNSF
Solenoid-free high beta operation
ST-FNSF Scenarios to be tested in NSTX-U
IP [MA]
NBI
Time
HHFW
,
CHI, EHC/EBW
Solenoid-free
Start-up
high bT, bN, k, disruption avoidance, high H, heat flux mitigation
Current ramp-up and profile control
• Tools are in place in NSTX-U to test:
  Coaxial Helicity Injection for start-up
  HHFW for current ramp-up
  NBI for 100 % non-inductive operation
  Advanced divertor for heat flux mitigation
~ 1-2 MA of solenoid-free start-up current needed for FNSF
Notes: ST has been addressing critical issues for FNSF: A compact FNSF facility does not have solenoid. So, the solenoid-free start-up is a critical issue for ST-FNSF. But solenoid-free start-up is attractive for tokamak reactor design as well. Other issues are ramp-up….

## Slide 25
Helicity Injection Is an Efficient Method for Current Initiation
FNSF needs ~ 1-2 MA of start-up current
CHI achieved solenoid-free 160 kA ST plasma in NSTX
R. Raman et al., PRL (2006)
CHI projects to achieve ~0.4 MA of start-up current in NSTX-U
Injector flux in NSTX-U is ~ 2.5 times higher than in NSTX  supports ~ 0.4 MA current
R. Raman at this conference

## Slide 26
Current Ramp-Up with HHFW for FNSF
Up to Ip level sufficient for NBI heating and CD
G. Taylor et al., PoP (2010), (2012)
Efficient HHFW electron heating due to high be achieved in NSTX.
HHFW current ramp-up will be tested in NSTX-U at higher power ~ 4 MW.
NSTX
Near sustained discharges obtained with modest HHFW power.
Antennas were re-installed with the new compliant feeds and back-plate grounding
Prototype compliant feeds tested to 46 kV in the RF test-stand. Benefit of back-plate grounding for arc prevention found.

## Slide 27
NSTX has accessed A, bN, k needed for ST-based FNSF
Requires fBS ≥ 50% for plasma sustainment
fBS º IBS / Ip = CBS bp / A0.5 = (CBS/20) A0.5 q* bN µ A5 (1+k2) bN2/ bT
SC-ST
NSTX achieved fBS ~ 50% and fNI ~ 65-70% with beams.
NSTX-U expects to achieve fNI ~100% with the more tangential (~ x1.5- 2 more current drive efficient) NBI.
S.P. Gerhardt et al., NF (2011)

## Slide 28
Divertor flux expansion of ~ 50 achieved with
Snow Flake Divertor with large heat flux reduction in NSTX
NSTX-U will investigate novel divertor heat flux mitigation concepts needed for FNSF and Demo.
• Up-and-down symmetric Snow Flake / x-Divertors
• Lithium + high-z metal PFCs
Divertor heat flux (MW/m2)
Snowflake divertor in NSTX
OSP
V. A. Soukhanovskii et al., PoP (2012)
D. Ryutov, et al., PoP (2007)
P.M. Valanju, et al., PoP (2009).
X-Divertor: CREST
Snow-flake

## Slide 29
Summary of NSTX-U
• NSTX-U’s main mission is to establish basis for FNSF while providing data for ITER operation and PMI solutions.
• Unique ST features include high beta and compact geometry which would be suitable for compact FNSFs.
• ST-FNSF can be compact, low tritium consumption, and lower cost, satisfying the FSNF criteria of Abdou report.
• With new center-stack and 2nd tangential NBI, NSTX-U plans to demonstrate 100% non-inductive operation at high beta needed for FSNF.
• The new center-stack was completed and installed in NSTX-U. The pump down is planned this month.
• 2nd NBI is nearly complete and the commissioning is planned in Jan. 2015.
• NSTX-U plan to have the first plasma in Mar. 2015 and commence research operation in May 2015.

## Slide 30: Back-up Slides

## Slide 31
ST is a low aspect ratio tokamak with A < 2
Natural elongation makes its spherical appearance
Y-K.M. Peng, D.J. Strickler, NF (1986)
A. Sykes, et al., Nucl. Fusion (1999).
Camera image from START
Aspect Ratio A = R /a
Elongation k = b/a
“natural” = “without active shaping”
ITF
ITF
BTF ∝ ITF/R
Ip
Ip
Ip
x
Ip
x
x
Ip
Ip
Note: ST differs from FRC, spheromak due to BTF

## Slide 32
ST can be compact, high beta, and high confinement
Higher elongation k and low A lead to higher Ip, bT and tE
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Ip ~ ITF (1 + k2 / (2 A2 q*)
bTº bN Ip / (aBT0)
S. Jardin et al., FS&T (2003)
D.A. Gates et al., NF (2007).
High κ ∼ 3.0 equilibrium in NSTX.
tE ∝ Ip
Ip ~ ITF for ST due to low A and high k
• ST has high Ip due to high κ and low A
• Ip increases tokamak performance
• ST can achieve high performance cost effectively
$
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 33
If the cost of volume neutron source (FNSF) facility is “modest” << ITER, DEMO, it becomes highly attractive development step in fusion energy research. M.A. Abdou, et al., FTS (1996)
Fusion needs FNSF(s) (modest cost, low T, and reliable) to Test and Qualify Fusion Components
FNSFs
Without R&D, fusion components could fail prematurely which often requires long repair/down time. This would cripple the DEMO operation.
FNSF can help develop reliable fusion components.
Such FNSF facilities must be modest cost, low T, and reliable.
Fusion needs to develop reliable/qualified components which are unique to fusion:
Divertor/PFC
Blanket and Integral First Wall
Tritium Fuel Cycle
Remote Maintenance Components
Advanced Power Generation
FNSF-ST
FNSF-AT

## Slide 34: Inner TF Bundle Comparisons- Physical
Description | Present Design | Upgrade Design
Operating Current | 1013 volts | 1013 volts
Number of Turns | 36 | 36
Number of Layers | Double | Single
Cooling | water | water
Maximum T/T Voltage stress | 970 volts | 28 volts
Maximum T/T voltage/mil | 14.9 volts/ mil | 0.432 volts /mil
Maximum volt/mil across leads | 14.9 volts/mil | 9.65 volts/mil
Turn to Turn Insulation thickness | 0.0648 inch | 0.0648 inch
Groundwrap insulation thickness | 0.054 inch | 0.222 inch
Insulation Scheme | B-stage (Pre-preg) | Vacuum Pressure Impregnation
Outside Diameter | 7.866 inch | 15.572 inch
Cooling Hole Inside Diameter | 0.186 inch | 0.305 inch
TF Conductor material | C10700 | C10700
Current TF Bundle 7.9 inch diameter
Upgraded TF Bundle 15.7 inch diameter

## Slide 35: TF Bundle Comparisons- Materials
Material | Existing TF Bundle | Upgraded TF Bundle
Copper Conductor | C10700 (OFHC w/ Silver) | C10700 (OFHC w/Silver)
Primer | DZ-80 (Ciba-Geigy) | CTD-450 (Cyanate-Ester primer)
Insulation Scheme | CTD-112P B-stage tape B-stage did not have ample resin to fill all voids between conductor corners | VPI w/CTD-425 Cyanate Ester Hybrid Provides good resin fill minimizing/eliminating void areas between conductor corners
Solder | 95%-5% Tin-Antimony | 95%-5% Tin-Antimony
Cooling tube | ACR (0.032 inch wall) | Type K (0.035 inch wall)
Flux | “NOKORODE” Paste flux (Contains Chlorides that may of contributed to insulation failure) | Rosin Flux (Does not contain Chlorides- organic material)

## Slide 36
TF flex-bus
CS Casing
TF cooling lines
TF Coil
OH Coil
PF Coil 1a
PF Coil 1b
PF Coil 1c
CHI bus
Improved Center-Stack Design to Handle Increased Forces
Identical 36 TF Bars and Innovative Flex-Bus Design
Tested for
300 k cycles
EDM cuts from solid
copper chromium zirconium block

## Slide 37: Upgrade Design- Insulation Scheme
TF leads will be located across the quadrant region where additional insulation is present < 10 volts per mil
Maximum turn to turn insulation voltage <30 volts turn to turn
(< 0.5 volts per mil)
S-2 glass tape insulation will be used for the turn and groundwall insulation.

## Slide 38
Friction stir weld joint
36 TF Bars manufactured by Major Tools
With innovative friction stir weld joints

## Slide 39
Friction stir weld joint
Friction stir welding enabled joining of two different copper alloys without annealing!

## Slide 40
Copper cooling tubes were soldered into the TF conductor assemblies using solder paste with non-ionic “R” flux
Contaminant from the flux containing Zn and Cl caused gradual insulation deterioration which led to the TF coil failure in NSTX

## Slide 41
Applying S-2 Glass TF Turn Insulation

## Slide 42
Maximize “gain” – wire turns x area – by flattening cross sections
Rogowski coil for measuring plasma currents wound around thin teflon mandrel
  - 30 turns of AWG 30 wire per cm
  - Thickness kept at ~2.5 mm over ~11 m length
Magnetic pickup coils fit in pockets in graphite plasma-facing components
  - AWG 26 copper wire around MACOR mandrel and coated with high temperature adhesive
  - Capable for use up to 800°C
Fewer turns on edge with more area to measure normal to plane
More turns around body with less area to measure parallel to plane
Coil dimensions: 3.8 x 2.3 x 0.5 cm
Limited Center Stack Space Requires Compact Designs for Magnetic Sensors

## Slide 43
New Digital Coil Protection System (DCPS)
Provides Comprehensive Coil Protection
Protects the NSTX-U coils and mechanical structure against electromagnetic loads
Computes forces and stresses in realtime based on reduced models of the full mechanical structure
Redundant systems
Full commissioning system will be a key part of early operations
Integrated DCPS software/hardware testing is being performed now in anticipation of FCPC dummy load testing in December.
Coil and Plasma Current Measurements
Realtime Acquisition #1
Realtime Acquisition #2
Stand Alone Digital Coil Protection Computer
Digital Coil Protection & Plasma Control Computer
Level-1 Fault Interface
Power Supply Suppress and Bypass
Rectifier Hardware Controls
Notes: A bunch of sensors give conditioned current inputs
Output is Go/NoGo… Fault/No Fault

## Slide 44
1st year goal: operating points with forces up to ½ the way between NSTX and NSTX-U, ½ the design-point heating of any coil
  Will permit up to ~5 second operation at BT~0.65
2nd year goal: Full field and current, but still limiting the coil heating
  Will revisit year 2 parameters once year 1 data has been accumulated
3rd year goal: Full capability
 | NSTX (Max.) | Year 1 NSTX-U Operations (2015) | Year 2 NSTX-U Operations (2016) | Year 3 NSTX-U Operations (2017) | Ultimate Goal
IP [MA] | 1.2 | ~1.6 | 2.0 | 2.0 | 2.0
BT [T] | 0.55 | ~0.8 | 1.0 | 1.0 | 1.0
Allowed TF I2t [MA2s] | 7.3 | 80 | 120 | 160 | 160
IP Flat-Top at max. allowed I2t, IP, and BT [s] | ~0.4 | ~3.5 | ~3 | 5 | 5
Formulating Strategy Toward Full NSTX-U Parameters
After CD-4, the plasma operation could enter quickly into new regimes

## Slide 45
Aqua Cement- Teflon Layer With Friction Elements, Mu=.1 and Mu=.3
Preload Mechanism Springs
TF Copper
11.5 mill
12 <–> 100°C
OH Copper
11.9 mill
12 <–> 100°C
187.5 mill
Glass Epoxy Insulation
108 mill
Glass Epoxy
Ground Insulation
8 mill Teflon Slip Plane
36 mill
TF-turn Insulation
48 mill OH turn Insulation with kapton
Aquapour
487.5 mill
100 mill
Schematics of OH-TF bundle configuration
100 mill gap between OH and TF to provide free OH-TF operation
TF-OH Gap Details
Both TF and OH expand about 12 mills during the full parameter operation reaching ~ 100 °C from 12 °C.
If TF expands more than OH, the gap region could be compressed leading to insulation stress as the TF and OH grow radially and axially.
• The full 1 T, 2 MA, 5 sec (third year) scenario maybe affected since TF temperature could exceed OH by as much 19°C which could cause insulation stress.
• Bringing the temperature gap down to 10°C range reduces the stress to acceptable range.
• This can be accomplished by pre-heating the OH with respect to TF by ~ 10°C.
45

## Slide 46
Upper Al Block External Reinforcements
Upper Al Block Internal Reinforcements
Upper Umbrella Arch Reinforcements
TF-VV Clevis &TF Outer Leg Support
Bay-L Cap
Support Structural and VV Enhancements Complete
Must handle 4 x higher electromagnetic loads
See back-up slides 44 for more detail

## Slide 47
Neutral Beam & TIV valve
Vacuum Vessel Bay J/K port
Neutral Beam Armor Installed
Final 2nd NBI Component being Installed
2nd NBI duct with pumping section and NBI armor installed
2nd NBI Commissioning planned in Jan. 2015

## Slide 48
HHFW System for Electron Heating and Current Ramp-up
Improved Antennas were installed on NSTX-U
4 MW is available for HHFW heating and current ramp-up
Antennas were re-installed with the new compliant feeds and back-plate grounding
Additional ground installed
Prototype compliant feeds tested to 46 kV in the RF test-stand. Benefit of back-plate grounding for arc prevention found.
New Compliant Antenna Feeds
Will allow HHFW antenna feedthroughs to tolerate 2 MA disruptions

## Slide 49
OH Winding Station
Taping Machine

## Slide 50
Each braze joint was mechanically loaded (stretched) and helium leak tested to ensure a quality braze joint.
On-line Brazing: 32 in line induction brazes were performed during the OH winding operations

## Slide 51
Inconel Center-Stack Casing Fabrication
51

## Slide 52
From GTS (ITG) and GTC-Neo (neoclassical):
  ci,ITG/ci,Neo ~ 10-2
  Assumption of neoclassical ion thermal transport should be valid
BT [T] | Pinj [MW] | IP [MA]
0.75 | 6.8 | 0.6-0.8
0.75 | 8.4 | 0.7-0.85
1.0 | 10.2 | 0.8-1.2
1.0 | 12.6 | 0.9-1.3
1.0 | 15.6 | 1.0-1.5
Projected Non-Inductive Current Levels for k~2.85, A~1.75, fGW=0.7
BT = 1.0 T, IP = 1MA, Pinj = 12.6MW
Contours of Non-Inductive Fraction
Contours of qmin
S. Gerhardt, et al., Nucl. Fusion 52 (2012) 083020
100% non-inductive operating points projected for a range of toroidal fields, densities, and confinement levels