## Slide 1
Is there any confinement degradation going to NSTX-Upgrade Elongation and Aspect Ratio
Stefan Gerhardt
NSTX 2011 & 12 Research Forum
ASC Breakout Session
Wed. March 16th, B318 PPPL
NSTX
Supported by
College W&M
Colorado Sch Mines
Columbia U
CompX
General Atomics
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec

## Slide 2: Big Picture Description
Aspect (A) ratio and elongation (k) are the lowest order shape parameters in a tokamak…and their impact on the ST is the focus of R11-2.
NSTX has a large database of confinement with A<1.55 and k<2.4.
  NSTX upgrade will run at larger values of both these parameters.
It is hard to scan these parameters independently in NSTX.
  Will be even harder in NSTX-U…this may be the last chance.
Propose to do three scans:
  A scan at fixed k
    at constant IP, and/or
    at constant q (this very interesting for possible/inevitable decreased tearing stability at higher A)
  k scan at fixed A
    at constant IP, and/or
    at constant q
  Push to very high A and k
Goals:
  1: Confirm (or not) confinement and current drive assumptions used in Upgrade modeling.
  2: Study toroidal physics of confinement.
  3: Develop the shapes to be used in further XPs targeting R11-2, JRT, Upgrade support.

## Slide 3: Limited Data Set Last Year Showed a Reduction in Normalized Confinement When A & k Were Increased
IP=900 kA, BT=0.45 T
Some drop in bN at higher A (for fixed Pinj).
Big hit in q95. (10->7.5)
Confinement is degraded by ~10%.
  H from 1.02 to 0.85.
Te is a bit lower, which hurts the NBCD.
Data collected at the end of the run, when machine performance was sub-optimal.

## Slide 4: NSTX-U Scenarios Need H>1.0 to Meet Non-Inductive Targets At High Current
Free-boundary TRANSP calculations
  Zeff=2, DFI=0.
Scale the Te profile and use neoclassical ion transport.
Current profile is fully relaxed.
All six sources at 90 kV.
A=1.81, k=2.9, gap_out=20 cm
  Large gap helps with off-axis NBCD.
Can be fully non-inductive at 1000 kA with H~1.0.
H=0.85 drops fNI to ~70%.
Want to get new/better confinement data in these configurations.

## Slide 5: In General, It is Hard to Scan A and k Independently
Fundamental Issue: the inner gap is not an independently controlled quantity.

## Slide 6: Scan of Kappa At Fixed A. With Constant IP or Constant q95
Low elongation limit is set by current limit on the PF-1A coil.
  Otherwise the inner gap shrinks
  700 kA plasma need 19.6 kA of PF-1A
Chart: 
| 2.69 | 2.55 | 2.3
"PF-1A Current (kA) vs. Elongation" | 6.3 | 11.55 | 19.6
A | k | IP | q95 | IPF-1A
1.56 | 2.66 | 825 | 12.1 | 10.7
1.55 | 2.69 | 700 | 17.9 | 6.3
1.55 | 2.55 | 700 | 13.9 | 11.6
1.52 | 2.3 | 700 | 12.03 | 19.6
Scan of k at fixed A and IP

## Slide 7: Scan of A at Fixed Kappa With Constant IP or Constant q95
High aspect ratio limit set by the PF-1A coil current limit.
Chart: 
| 1.54 | 1.65 | 1.74
PF-1A Current (kA) vs. Aspect Ratio | 7 | 13.3 | 19.6
A | k | IP | q95 | IPF-1A
1.53 | 2.64 | 1000 | 9 | 18.9
1.54 | 2.7 | 700 | 18 | 7
1.65 | 2.69 | 700 | 12 | 13.3
1.74 | 2.67 | 700 | 9.5 | 19.6
Scan of A at fixed k and IP
700 & 1000 kA

## Slide 8: XP Summary
Part 1: Aspect Ratio Scan at Fixed Kappa
  Base configuration: 700 kA, k=2.7
  Scan of A at fixed Ip (6 shots)
  Scan of A at fixed q (6 shots)
Part 2: Kappa Scan at Fixed Aspect Ratio
  Scan of k at fixed Ip (6 shots)
  Scan of k at fixed q (6 shots)
Part 3: Go as close as possible to the A=1.8, k=3 shape indicated earlier. (6 shots)
Questions:
  Fix 4 MW input power, or try to fix b? May not be important if b scaling is weak.
  Which of the turbulence diagnostics can handle the wide range of shapes?
  How much lithium? Pick the amount thought representative of Upgrade operations?
Analysis:
  TRANSP for global confinement and current drive trends.
  Turbulence measurements?
Run time request: 1 day, possibly broken into two sub-sections.