## Slide 1
M&P TSG Prioritization for FY2015 and campaign startup
M.A. Jaworski, C.H. Skinner, R. Kaita
NSTX-U Science and Topical Science Group organizational meeting #1
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: FY 2016 research milestone will drive XP/XMP development (ITPA-DSOL experiments relevant to high-Z upgrade)
R(16-2): Assess high-Z divertor PFC performance and impact on operating scenarios (joint with divertor-SOL TSG)
  Carbon-only baseline needed in FY2015 for comparison
  Validate high-Z PFC design in actual operation
  Establish additional heat-flux mitigation schemes needed for whole-machine high-Z conversion
  Determine high-Z impurity production/influx and impact on operations and mitigate if necessary
DSOL-31: Leading edge power loading and monoblock shaping
  High-spatial resolution IR measurements of existing carbon tile gaps to determine whether heat flux is “missing” in NSTX-U as in JET-ILW
DSOL-34: Far-SOL fluxes and link to detachment
  Diagnose whether conditions at strike-point enhance cross-field transport into far-SOL to better predict first-wall power loading (e.g. LPs + GPI)
DSOL-35: In/out divertor ELM-energy density asymmetries
  Determine power splitting during ELMs and impact on design margins for PFCs during ELMy discharges

## Slide 3: Develop high-Z relevant baseline discharge in FY2015
Incremental upgrade to high-Z proposed for outboard row 2 tiles
Proposed figure-of-merit (FOM) for divertor PFC is unmitigated heat-flux to divertor surfaces
  High-delta NSTX-U reference discharge: Pinj~12MW FOM up to 60MW/m2
  Medium-delta, high-Z discharge: Pinj~9MW FOM up to 40MW/m2
FY2015 development of medium-delta shape and create “standardized” parameter scans
  Pinj, q95, divertor gas puffing, B-field and angle-of-incidence, other mitigation
  Duplicate scans in FY2016 (single variable experiment!)
Medium-delta high-Z fiducial discharge FOM ~ 40 MW/m2
High-delta “fiducial”
discharge FOM ~ 60 MW/m2
Row 2 Tile location

## Slide 4: Critical diagnostics for milestone and DSOL activities
ASC-support with wall conditioning experiments
  MAPP characterization of boronization and lithiumization
Critical diagnostics/capabilities for milestone R16-2:
  IR thermography for heat flux, including high-spatial resolution view (DSOL-31)
  Langmuir probe for particle fluxes to divertor under different operating conditions (low-high density, detached, etc.) (also DSOL-34)
  Visible and X-ray emission spectroscopy to characterize impurity production, SOL and core conditions
  Managing plasma-surface interactions of boronized and lithiumized high-Z PFCs with MAPP and standard plasma diagnostics
Additional diagnostics/capabilities would be beneficial:
  IR view on vertical target for DSOL-35 (or new plasma shape)
  GPI to support far-SOL effects (DSOL-34)
  Divertor bolometry for power-balance evaluation
  MAPP measurements and post-run coupon analysis for material transport studies (support new model capabilities with WallDYN)
  Surface science studies, e.g. mixed-material sputtering and detailed plasma-exposed sample characterization