## Slide 1
The PF-1aU coil will remain unpowered and out of service for the remainder of this run. It will stay connected to the open SDS switch to allow monitoring of induced Voltages and continued ground fault monitoring.
Analysis of loading on the PF4 coil leads is nearing completion, and only modest updates are needed. Use of that coil in NSTX-U experiments is expected.
Analysis of additional PF1c supports in progress. Fabrication and installation required before PF1c is available. Test Cell time would be needed.
PF1b operation is not planned for this run period.
.75 Tesla TF operation is planned:
  Outer TF strain gauges are installed and ready to take data
  Considering the need for accelerometers on passive plates.
Coil Systems

## Slide 2
A chronic electrical leakage path exists between the inner and outer vessel exists. Checked daily and varies between 6 and 200 K.
Specific troubleshooting activities continue, but a full analysis /repair may require a dismantling of the upper umbrella.
At this resistance this leakage path does not impact operations (Inner and Outer Vessel shorted for ohmic operations via the motorized ground switch).
Configurations are being prepared to allow operation if this leakage path increases to unacceptable levels
  Fixed resistive shorts are being added at the top of the vessels to limit circulating currents.
  Modifications to GFM to continue loop fault monitoring with the I/O VV combined
  MOV’s at top and bottom of the vessel to limit fast Voltage.
  High energy resistors on order to allow for CHI Operation
Inner/Outer Vacuum Vessel

## Slide 3
The Lithium Granule Injector (LGI) is ready for operations.
Bake-out of the F2 & K2 Lithium Evaporator (LITER) probes (mounted on the Fill Stand) has been completed to 700C. Pre-operational testing of the LIFTER system used for lithium fills has been completed.
The F1 & K1 LITER probes have also been baked, and are now on the vessel. Probe motion controls have been successfully synchronized to the shot clock and tested.
The NSTX-U Activity Certification Committee (ACC) has reviewed the preparations to resume lithium operations.
  All Pre-op procedures have completed and Operations Procedures are approved and ready.
  The NSTX-U Safety Certificate is being updated to include finalized procedures.
  Lithium fills and evaporation ready this month
Pre-operational testing of the new Massive Gas Injector has been completed. The lower and mid-plane MGI valves have been operated in nitrogen, helium and neon.
New Capabilities for this run

## Slide 4
Neutral Beam conditioning has continued during this maintenance period. All six ion sources are operational:
  Sources operating at an average of 90kV and a total combined power or ~ 12MW.
  Reliability continues to improve, including during beam modulation.
  NB1A is operating at 89kV.
All Corrective Actions associated with the failure of RF Source # 5 have been completed. New AC system protective relaying has been installed on RF source 1-6, and on upstream circuit breakers.
Dummy load testing of all six RF sources has been completed. Vacuum conditioning of the HHFW antennas was performed in parallel with plasma operations.
Ready for the first HHFW XMP.
Heating Systems

## Slide 5
MG#1 and controls have supported NSTX-U operations flawlessly since re-commissioning the Cycloconvertor this past winter.
The MG#2 Cycloconvertor is currently being re-commissioned per the same procedures as MG#1.
  Rotor welds on MG#2 need to be restored as was done on MG#1.
FCPC Maintenance has been completed, and all systems are ready to resume operations.
  New DCCT’s are being used to replace aging Halmar DC current feedback devices and shunts to reduce noise and improve reliability.
  FCPC Fault Detector (FD) functions not rectifier current related are being moved from the FD to the new HCS PLC
  Methods to take data from FCPC rectifiers to MDS signal plotting to monitor performance are being considered.
Energy Conversion Systems