## Slide 1: Gas Systems Requirements for NSTX-U Research Operations 28 August 2012 Peer Review
R. Raman, L. Roquemore,
W. Blanchard, D. Mueller,
V. Soukhanovskii, S.P. Gerhardt

## Slide 2
  1) Plasma Fueling
  Inductive Plasma start-up: Low field side gas injection (D2) [CD-4]
  Inductive H-mode initiations and Ip ramp-up: Center stack gas injection [Ops]
  Density control during Li operation: Additional gas injection from LFS & center stack or shoulder gas injection [Ops]
2) CHI Start-up [Research]
  Branch 5 gas injection from divertor gap
3) HeGDC
  Low field side (LFS) [CD-4]
4) Boronization
  Up/down organ pipe locations & LFS [CD-4]
5) Div. heat flux mitigation studies
  Localized divertor impurity gas injection at multiple locations [Research]
6) Disruption Mitigation studies
  MGI from multiple locations [Research]
NSTX-U Plasma Operations Requires Capability for Gas Injection form Multiple Locations

## Slide 3: Summary of NSTX / NSTX-U Gas Systems (YR 1)
Name | NSTX | NSTX-U
Plasma Fueling Inj 1-PZV [CD-4] Inj 2-PZV [CD-4] Inj-3PZV [CD-4] | Bay K Top (89 cc) Bay J Mid-Lo (72cc) Bay J Mid-Up (70cc) | Same (Bay K Top) Bay I/J Mid-Lo (Install port) Bay F/G Mid-Lo-Left (Install port)
SGI [Research] | Bay I Midplane | Bay I Midplane
Inj 4a [Ops] Inj 4b [Ops] Inj 5a[Ops] Inj 5b[Ops] | CS – Mid (42.5cc) Shoulder (43.9cc) | Same Same CS-2 Shoulder-2
Branch 5 – Single Pulse [Research] | Bay K bot (1.3cc) | CHI-1 Bay K bot CH-2 Bay G bot (add Tee to CHI Penning gauge port)
Diagnostics [Research] Argon –PZV – single pulse GPI – PZV – single pulse | Bay-B Lo Flow Bay-B Hi Flow | Bay-B Hi Flow Bay-B Hi Flow
Diruption Mitigation[Research] LDGIS-1 LDGIS-2 LDGIS-3 LDGIS-4/MGI-1 | Bay C – AV120 (organ pipe - OP) Bay I – AV121 (OP) Bay F – AV122 (OP) Bay K – AV123 (OP) | MGI-1 Bay A 15 deg bot. MGI-2 Bay G 180 deg bot. MGI-3 Bay L 345 deg top MGI-Midplane-4 Bay I/J Mid-Up (Install port)
Divertor Studies DivL-1- PZV (YR 1) DivL-2-PZV (~180 degree apart) DivU-1- PZV DivU-2-PZV | Bay E bottom | Bay-E bottom Bay-J bottom TBD Upper dome port to be identified By Lane Roquemore
RED: new port location, Green: port to be identified, Black: work in progress

## Slide 4: Divertor & MGI Gas Systems Upgrade (YR 2 or later)
Name | NSTX | NSTX-U
Divertor Studies YR-2 or later (based on YR-1 results) Lower Divertor (YR 2) DivL-3-PZV DivL-4-PZV Upper Divertor (YR 2) DivU-3-PZV DivU-4-PZV Massive Gas Injection Studies YR-2 or later (based on YR-1 results) MGI-2 | Bay K-Mid (Outer Vessel - OV) | Ports to ne identified Ports to be identified MGI-5 Bay F Up Horiz. dome (drill hole in div. plate)

## Slide 5: NSTX-U Gas Injection / Delivery System
Injectors in Black and Red are for YR-1 availability. Injectors in Green are for YR-2 or YR-3 availability

## Slide 6: NSTX Gas Delivery System
SGI & Bay-E (& Argon and GPI) systems use existing gas delivery system controls – So these are a Hybrid of the present 1-4 gas delivery system

## Slide 7
Examined installation of a single large 6-inch port to support three gas injectors and found the only location identified (Bay F/G Lo) to be unsuitable due to severe interference with the Thomson Scattering system

## Slide 8: Ion / Penning Gauge Locations
Existing digitizers and cabling can be used, but need to ensure digitizers support 10 sec operations

## Slide 9: Reference Plan: Install Four 2-3/4 inch ports (1.5 inch dia. pipe) on the vessel wall
Port-1 & 2: Bay I / J Mid-Lo (2 ports at this location for Inj. 2 and MGI-4)
Port 3: Bay F / G-Left Mid-Lo (1 ports at this location for Inj. 3)
Port 4: Bay B/C - MIG-3 (1 port)
MGI-5 mid upper [Bay F upper Horizontal Dome]
Port near Turbo pump for MIG-4 (1 port, but not on vacuum vessel)
OPTIONAL spares- Install one additional port in Bay F/G-Right-Right & Bay G/F-Up (GPI Upgrade)

## Slide 10: Number of Gas Delivery Systems Needs to be increased from 4 to 6
System 1 (D2) [Mid-plane GIS]
System 2 (He for GDC)
System 3 (D2) [Mid-plane GIS]
System 4 (D2) as on NSTX [CS & Branch-5 GIS]
System 1-H (D2 and impurity gas) SGI & Bay-E Lower
System 1-H (3 impurity gases) as on NSTX Argon and GPI
System 5 (5000 Torr) for MGI – NEW for YR1
  Will support Divertor Gas Injection system
  Improves flexibility by freeing up SGI delivery system
System 6 (for new Boronization system)
Bill Blanchard to investigate if System 5 and 6 could be combined into a single system

## Slide 11: New Boronization (TMB) Gas Delivery System would have additional safety measures
Doubly-contained piping
Diaphragm or bellows sealed pumps
Soft seal valves
Flow monitoring or limiting devices
Gas cabinets with appropriate purging
Automatic monitoring of the secondary eneclosure
Installed in test cell

## Slide 12: Some Scope is with NSTX Operations, and some with the Upgrade Project
Upgrade Project Scope: Restore previous operations capabilities
  Outer vessel penetrations for replacement valves and gauges [CD-4]
  Plumbing to all LFS and CS injectors [CD-4, Ops]
  Restoration of at least partial divertor gas injection (single divertor gas injection at bay E as before) [Research]
NSTX Operations Scope: Prepare for physics program (in rough priority order)
  Additional gas delivery system for boronization
  Full divertor gas injection (2 injectors top, two bottom)
  Additional gas delivery system for the high pressure impurities (System #5, for MGI and Divertor injection)
  Second MGI location in upper horizontal dome port (requires plate modification)
Should begin basic engineering assessments of these tasks in order to refine prioritization

## Slide 13: Appendix

## Slide 14: EPICS Gas Systems Control Page

## Slide 15: LDGIS / CS / Branch-5 Gas Systems Control Page

## Slide 16: Top-Down View of GIS & MIGs

## Slide 17: Photo of Bay I / J Mid-Lo (Ports 1 & 2)
Two gas injection ports removed to provide space for tangential NBI port

## Slide 18: Bay I / J Port (Port 2- Partial view as previous photo)

## Slide 19: Photo of Bay G Mid-Lo (Port 3)

## Slide 20: MIG-4 Port (Port 4)
Outside and inside views

## Slide 21: MGI-5 Requires Modification to Bay-F Horizontal Dome Port

## Slide 22: CHI Brach-5 Injectors

## Slide 23: Branch 5 Injectors
CHI-1
CHI-2 & Penning gauge

## Slide 24: CHI-1 Bay K bottom port

## Slide 25: CHI-2 & Penning gauge Bay G Bottom
Install Tee and install both the Penning gauge and a second line for CHI gas injection

## Slide 26: Configuration for Divertor Gas Injection

## Slide 27: Bay-E Lo Vacuum & Air side connection

## Slide 28: Bay-E DIV-1 gas injection pipe photo

## Slide 29: Organ Pipe Usage

## Slide 31: Upper / Lower Gas Injection and Spectroscopy Organ Pipes

## Slide 32: Center Stack & MGI-3

## Slide 33: MGI 1, 2 & Spectroscopy Ports

## Slide 34: Neutral Pressure Gauge Locations

## Slide 35: IG 1, 2 and MGI-4 Locations

## Slide 36: Penning Gauges
PEN-1 Bay G_LD (PG1P)
PEN-2 Bay K_UP (PG2P)

## Slide 37: Bay K Top (Penning gauge port)

## Slide 38: CHI-2 & Penning gauge Bay G Bottom
Install Tee and install both the Penning gauge and a second line for CHI gas injection

## Slide 39: Plenum Sensotec Requirements

## Slide 40: CHI/ MGI / Divertor Plenum Sensors (Sensotek)
Pressure Sensor | Availability | Max Press (Torr)
CHI1-Bay K bot CHI2-Bay G/L | YR-1 YR-1 | 2400 Gas Delivery System 4)
MGI-1 MGI-2 MGI-3 MGI-4 MGI-5 | YR-1 YR-1 YR-1 YR-1 YR-1 | 5000 (Gas Delivery System 6)
DIV1L DIV2L DIV3L DIV4L DIV1U DIV2U DIV3U DIB4U | YR-1 YR-1 YR-2 YR-2 YR-1 YR-1 YR-2 YR-2 | 5000 (Gas Delivery System 5,6 – YR1 And add 7,8 during YR2)

## Slide 41: High and Low Field Sensotek Sensors
Pressure sensor | Availability | Max press (Torr) / system #
Inj-1a-CS1 | YR-1 | 2400 / 4
Inj-1b-CS2 | YR-1 | 2400 / 4
Inj-2a-SH1 | YR-1 | 2400 / 4
Inj-2b-SH-2 | YR-1 | 2400 / 4
Inj-1 | YR-1 | 2400 / 1
Inj-2 | YR-1 | 2400 / 2
Inj-3 | YR-1 | 2400 / 3
GPI | YR-1 | 5000 / 5
Argon | YR-1 | 5000 / 5
SGI | YR-1 | 5000 / 4