## Slide 1: Navigating the PCS Interface
Devon Battaglia,
Keith Erickson, Dennis Mueller
NSTX-U Physics Operators Training
September 15, 2015

## Slide 2: Starting the PCS Interface
Become a member of PCS Unix group
  Submit a ticket to helpdesk
Log in to the real deal when sitting at the P.O. station
  ssh -Y user@pcs-rt-3
  ssh -Y user@pcs-srv-3 (preferred once it is ready)
  Navigate to folder /opt/pcs/INTEL_DIR/
    ./run_wave
Or run stand-alone PCS anywhere
  Set up PCS for future shots or run simulations
  Keith or Roman can help you get this code in your area
  ssh -Y user@pcspool
  Navigate to folder /trunk/INTEL_DIR/
    ./runsa

## Slide 3: You get the purple box
File
  Version
  Quit
Control
  Next shot
  Future shot
  Shared shot
Utilities
  View PCS log

## Slide 4: PCS log provides useful feedback on status and communication with realtime system
File
  Quit
Utilities
  Show pcs log messages
  Hide pcs log messages
    This is the default
  PCS process table
    Shows what computers are up
  Show realtime errors only
I like to keep this window open on the desktop

## Slide 5: Choose the type of control
Control
  Next shot
    Changes made in GUI are written to the realtime computer
      On pcspool … change parameters for next simulation
      On pcs-rt-3 … change parameters for next shot
  Future shot
    Set up a shot for restoring later
  Shared shot
    Change a future shot made by someone else

## Slide 6: Choosing “Next shot” opens the PCS GUI
Talk will now focus on navigating this window
  But first, let’s take a step back

## Slide 7: PCS baseline categories align with control actuators
PF Power supplies
TF Power supplies
OH Power supplies
Shape
TF Control
Ip/OH Control
Gas valves
Gas Injection
Neutral beam blocks
Neutral beam injection
RWM Control
SPA Power supplies
Power Supply RT Control (PSRTC)
PLC
138’ level
“Baseline Categories” provide control and/or control switches for a single actuator
Protection against out-of-bounds requests from PCS
Actuators
System

## Slide 8: Upper level categories send requests to baseline categories
Discharge Shape
Vertical Position Control
ISOFLUX
Mode ID
Equilibrium
Snowflake
Density control
Profile (DBC)
PF Power supplies
TF Power supplies
OH Power supplies
TF Control
Ip/OH Control
Gas valves
Gas Injection
Neutral beam blocks
Neutral beam injection
RWM Control
SPA Power supplies
Power Supply RT Control (PSRTC)
EPICS
138’ level
This is illustrative, not complete and still changing
System

## Slide 9: Every category has “Algorithms”
TF control has two Algorithms
  TF current control: request TF coil current versus time
  TF rampdown control: ramp TF current from initial value to zero over a specified time interval
Discharge Shape has three Algorithms
  Do Nothing: category is disabled
  Day0: Current control of PF coils
  PCC: Day0 capability plus IPF vs IOH, IPF vs IP, outer gap
    Categories accrue algorithms as new versions come along

## Slide 10: Every category has “Phases”
Each phase runs one algorithm with unique parameters
  P.O. can add/delete phases, cannot add/delete algorithms
You could have multiple phases calling the same algorithm but with different control parameters
  Divide pulse into separate experiments where a number of algorithm parameters change
  Or save different settings for an algorithm
    For example “rampdown” and “fast rampdown” in the IP/OH category
Most categories have just one phase for each algorithm
  For example, TF Control category has two Algorithms and Phases
    [Phase] ShotStart = TF current control [Algorithm]
    [Phase] Rampdown = TF rampdown control [Algorithm]

## Slide 11: Every category has a “Primary” phase sequence
“Primary” phase sequence sets timing of the phases
  For example, TF Control Primary Phase Sequence:
    T = -5s [Phase] ShotStart = TF current control [Algorithm]
    T = +3s [Phase] Rampdown = TF rampdown control [Algorithm]
Category may also have “Alternate” phase sequences
  P.O. cannot add/delete alternate phase sequences
    P.O. can change the phases in each alternative sequence
  Algorithms switch to these alternate phase sequences
    For example, IP/OH category has two alternate phases that are activated by the IP0 algorithm
      Insufficient Ip: Switch to this sequence if Ip is below a threshold
        [Phase] Rampdown = IP1 [Algorithm]
      Ip LOC: Switch to this sequence if OH coil current exceeds bounds
        [Phase] Fast rampdown = IP1 [Algorithm]

## Slide 12: Let’s review
PCS control is divided into categories
Every category has a library of algorithms
You create a library of phases
  Each phase uses a single algorithm
You define the timing of phases in the Primary phase sequence
  You also define the timing of phases in any Alternative (dynamic) phase sequences

## Slide 13: The main task of a P.O. is to change the input parameters for control algorithms
Inputs to algorithms are organized into subsets
  [Cat] TF Control, [Phase] ShotStart, [Alg] TF current control
    Coil Current
      TF Coil Current
    TF gains
      TF Gain, P
      TF Gain, I
    Rampdown Info
      Automatic Rampdown
      Ip Rampdown Threshold
Subset
Waveform, table or GUI
We aim to have specs for each algorithm

## Slide 14: Let’s begin the tour
Open a category:
Select from Category menu
--- or ---
Click Ctgy radio button and select from menu

## Slide 15: Selecting a category
I have selected “TF Control”
Category
Now we see the first waveform in the first subset of the algorithm in the first phase of the primary sequence

## Slide 16: Enter a waveform
You can…
Draw in points
Type in points
Restore points
… more on this later
Yellow: bounds
Blue: switch to new phase

## Slide 17: Navigate to a new waveform
Select Sub radio button
Subsets appear in menu window

## Slide 18: Enter values for a new waveform
I selected TF Gains subset
Now editing TF proportional gain

## Slide 19: Navigate to Phase sequence
Select the “Seq” radio button

## Slide 20: Primary sequence describes order and timing of phases within category
You can add/delete phases in the category using the phase menu
The waveform describes timing of phase switching
TF category has one alternative sequence called Shutdown.
It is called if
Ip < threshold

## Slide 21: Restoring data from older shots or prepared shots is a common activity
Restore menu
  Reference plot
    Plot data from a shot to compare
  MDS archive
    Restore data from an old shot
  Prepared setup
    Restore data from a future shot
  Flush cache

## Slide 22: Loading data from an old shot or prepared setup
Load data from shot
Load data from a prepared setup
Load all categories: Reload everything it can
Load sel category: Just reload selected category
Select data to load: Opens a new window

## Slide 23: “Select data to load” gives full control over what to load and where
Load selected data item
  Loads that data item from the source
Show selected data item
  Plots that data item for comparison

## Slide 24: Using “Show selected data item” before restore is good practice
Comparing the TF current request waveform (blue) to the TF request for shot 201085 (pink)

## Slide 25: Load a data item into a target with a different name
The radio button “show targets” is selected
Loading the PZV1 Flow Rate from shot 201085 into PZV2 Flow rate for the next shot

## Slide 26: Changing a waveform
A point is added by entering the new x and new y coordinates and pressing “add”
THE CHANGE IS NOT MADE UNTIL YOU PRESS APPLY

## Slide 27: Press apply and the change is made
You have until first lockout (t = -60s in countdown)
to APPLY changes

## Slide 28: Entering and manipulating waveforms is best learned on the job
Mouse control lets you select points, add points, delete points, pan and zoom
There is a clipboard for cutting, copying and pasting
Scale or shift selected points
Overplot references, proposed changes
Load points from a text file or use a function generator

## Slide 29: Some data items are GUIs instead of waveforms
GUIs are indicated with “…” in the list of data items within a algorithm subset
GUI could have a mix of menus, radio buttons, sliders and single number parameters
Don’t forget to hit APPLY!

## Slide 30: GUIs can also be tables
Multiple versions of the table can exist (a waveform is used to select which table to use)
You can edit the same cell in multiple tables
Don’t forget to hit APPLY!

## Slide 31: The ISOFLUX GUIs deserve a separate talk

## Slide 32: Indicators on the PCS GUI
Note the title of the window. You could have multiple “Next shot” and “Future shot” GUIs open
Data light:
Green means all GUI parameters are in a valid configuration
Status light:
Green means computer systems are running
Shot will not run if either light is red

## Slide 33: If you get a red or yellow Data light …
Go to “Information” > “Raw data problems”
  Window shows the issue(s)
  Most likely to occur when restoring a shot

## Slide 34: Start exploring the PCS GUI
Get in the PCS Unix group
Get the stand-alone PCS software
Refer to:
  PCS programmers manual:
  http://nstx.pppl.gov/nstx/controls/pcs/PCS_doc/master.pdf
  NSTX-U PCS specs in the NSTX PCS shared google folder
Read the specs and navigate through the categories
  Practice changing things
  Ask questions

## Slide 35: Summary
PCS software is divided into Categories
  Each category has a library of control algorithms
The PCS interface is used to set the sequence of phases where each phase runs a single algorithm
Each algorithm has waveforms and GUIs that can be edited using the PCS interface
Dennis: “With power and flexibility comes complexity”
  With time and practice, it all makes sense