## Slide 1
Progress and Plans for Macroscopic Stability
Jack Berkery (Columbia University)
Jong-Kyu Park, Allen Boozer
and the NSTX-U Research Team
NSTX-U PAC-35 Meeting
PPPL – B318
June 11-13, 2014
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2: Outline
Introduction
  Macroscopic stability (MS) group research in stability, 3D fields, and disruptions is key for NSTX-U, ITER, and FNSF
  MS research is prominent in NSTX-U milestones as well as JRTs
Progress in the last year – in preparation for upcoming run
  Collaborations at KSTAR and DIII-D
  Three main areas: Stability, 3D fields, and disruptions
  Non-axisymmetric control coil (NCC) design
MS research goals and plans for FY15
MS research goals and plans for FY16
Key results expected by the end of the FY16 run, and how they will impact further NSTX-U operation and future devices

## Slide 3: Macroscopic stability research is crucial for the successful sustainment of high performance in future devices
Macroscopic stability research is in three key areas:
  Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
  Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
  Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas
Demonstrate 100% non-inductive sustainment at performance that extrapolates to ≥ 1MW/m2 neutron wall loading in FNSF
Access reduced n* and high-b combined with ability to vary q and rotation to dramatically extend ST physics understanding

## Slide 4: Macroscopic stability research and capabilities play an instrumental role in the success of NSTX-U
MS group’s crucial role is reflected in milestones and JRTs in:
  Preparation for high performance in NSTX-U
  Development of NSTX-U capabilities
  U.S. program-wide high priority research
Quantify impact of broadened J(r) and p(r) on tokamak confinement, stability
Assess disruption mitigation, initial tests of real-time warning, prediction
Develop physics+operational tools for high-performance (k, d, b, EF/RWM)

## Slide 5: Collaborations at KSTAR and DIII-D support macroscopic stability research thrusts on NSTX-U
MGI1
MGI2
DIII-D
KSTAR collaboration
  Improved control and ran XPs accessing βNno-wall
  Pitch-crossing field drives n=1 NTV with bounce harmonic resonances
  Non-resonant NTV slows ωφ (no hysteresis)
DIII-D collaboration
  Participated in radiation asymmetry campaign: # of injectors had little effect on TQ/CQ Prad asymmetry
  Kinetic effects explain RFA experiments (MARS-K)
  XP and MISK calcs. to understand kinetic RWM stability and enable high β
DIII-D
Fluid
Kinetic

## Slide 6: Kinetic stability theory and comparison to NSTX is setting the stage for practical use in NSTX-U for disruption avoidance
  Moving kinetic RWM stability theory from successful theory/experiment comparison to actual implementation
    MISK (perturbative) benchmarked with other leading codes
    A simplified model based on these results will be implemented in the NSTX-U disruption avoidance algorithm
Growth rate vs. ωE for ITER case
Instability measure (RFA) vs. exp. ωE for NSTX
  Ideal Wall Mode destabilization by rotational shear vs. stabilization by kinetic effects explained with MARS-K
βN
exp
    Also may help explain low-density/ramp-up disruptions in NSTX in prep for low ν operation (fast ions important)

## Slide 7: Non-resonant Neoclassical Toroidal Viscosity (NTV) physics analysis progresses, will be used for rotation feedback control
NTV torque profile (n = 3)
Experimental
-dL/dt
NTVTOK
Leading theory/codes under active development
  IPEC-PENT, MARS-K, MARS-Q, and POCA (δf guiding-center particle code) have been benchmarked
NTVTOK code analysis
  NTVTOK modified, incl. Shaing’s connected NTV model, covers all n, superbanana plateau regimes (like MARS-Q)
  Full 3D geometry and coil, ion & ele. effects
  Plasma response from penetrated 3D field used in exp. analysis matches M3D-C1 single fluid model
  FY14: Analyzing NTV data from 6 experiments on n dependence and other NTV characteristics
(NTVTOK)
(n = 3 configuration)
Strong TNTV region
core
edge
<dB> (G)
(Columbia U., GA)
1.6
1.2
0.8
0.4
-0.4
Scaled x2
JRT-14

## Slide 8: Rotation feedback controller using NTV designed; supported by key results from international collaboration research
NSTX-U controller will use Neoclassical Toroidal Viscosity (NTV) physics for the first time in rotation feedback control
Dedicated long-pulse KSTAR experiments show no hysteresis in wf profile vs. applied 3D field strength (important for control)
NSTX-U state-space wf controller w/NTV as actuator
NTV torque density (N/m2)
Plasma rotation (rad/s)
Radial coordinate
NTV
region
0
2
4
6
104
desired wf
t1
t2
t3
KSTAR non-resonant (“n = 2”) NTV experiments
(Columbia U.)
Plasma rotation profiles
3D field current (kA/t)
3D current stepped up / down
0 kA/t
2.7 kA/t
3.3 kA/t
wf (krad/s)
3.3 kA/t
2.7 kA/t

## Slide 9: Non-axisymmetric control coils (NCC) (incremental) will enhance physics studies and control
NCC design (on passive plates)
NCC designed with multiple physics metrics for error field, RWM, rotation control by NTV, and RMP characteristics
  Analysis updated with IPEC-PENT and more NSTX-U targets (see back-up)
Torque
Existing coils
PPPL Theory Partnership,
JRT-14
Rho
Now utilizing stellarator optimization tools without coil constraints to determine theoretical max performance (PAC recommendation)
  The IPECOPT code developed (from STELLOPT) to optimize IPEC equilibrium for core and edge NTV Torque
  IPECOPT will be extended to analyze additional figures of merit: EF, RMP
  Deliverable: assess physics benefits of potentially improved coil sets within 9 months to drive subsequent engineering analysis
Optimized for core
Optimized for 0.5<Ψ<0.9
Rho
Examples of initial IPECOPT NTV torque profile localization optimization
n=3
n=1
Iteration count

## Slide 10
FY14:
  Offline RWMSC already expanded for 6 coil control and n > 1 physics
    Now comparing past 3 coil algorithm with open-loop 6 coil tests in generalized code
Stability plans, FY15:
  EFIT, available Day 0
    New parallel CPUs implemented, increased between-shots spatial / time resolution
  Examine RWMSC with:
    six control coils and multi-mode control with n up to 3
  Establish Br + Bp active control capability in new operational regime
Active control techniques (Br + Bp, RWM state-space (RWMSC)) will enable long pulse, high β operation
Brn = 1 (G)
Br phase = 0o
Br phase = 90o
Br phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback control
Br phase = 225o
Feedback on
RWMSC
137722
t (s)
40
0
80
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
40
0
80
No NBI Port:
With NBI Port:
Controller
(observer)
Measurement
JRT-16

## Slide 11: Correction of intrinsic error fields is critical for performance; NSTX-U will have new disruption research capabilities
Gain
3D fields research plans, FY15:
  Assess intrinsic EFs in NSTX-U
  Optimize dynamic EF correction, including n>1 and using 6 SPAs and RWMSC
  Resonant EF effects on tearing mode onset (+Resistive DCON)
Disruption research plans, FY15:
  FY14: substantial contributions to the ITPA disruption database
  Investigate halo current toroidal asymmetry and loading on the center column, using 18 newly installed shunt tiles
  Commission MGI system
    ITER-like valves tested to pressure above spec: fast rise time
Dynamic error field correction in NSTX
NSTX-U ITER-like MGI Valve
PPPL Theory: optimal sensor position/type
0
10
20
30
40
50
60
70
80
Time (ms)
Pressure
Planned normal current tiles

## Slide 12: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI
Disruption research plans, FY16:
  Compare the mismatch between the RWMSC observer model and sensor measurements, and disruption occurrence
  Study spatial extent and timing of the heat deposition during VDEs
    Eroding thermocouples and new IR cameras
  Characterize density assimilation vs. poloidal location of MGI system
    JRT-16 support, DEGAS-2 modelling
    Valves in poloidal location 2 & 3 identical to location 1 or 4 (locations 1, 2 & 4 for FY15)
    Injection into the private flux region is possible
Dual-band fast IR cameras
Divertor fast eroding thermocouples
Divertor fast pressure gauge
4

## Slide 13: NSTX-U will investigate NTV and stability theory in lower ν regime for implementation in active rotation control
3D fields plans, FY16:
  Assess NTV profile and strength at reduced ν, examine NTV offset rotation at long pulse, at zero torque
  Prepare an initial real-time model of NTV profile for use in initial tests of the plasma rotation control system
Stability plans, FY16:
  Examine RWMSC with rotational stabilization in the controller model
  Investigate the dependence of stability on reduced ν through MHD spectroscopy; compare to kinetic stabilization theory
n=3 experiment
n=3 POCA
n=2 POCA
NSTX -> NSTX-U
(Bounce freq.  ,
Collisionality )
Modified bounce orbits may be strongly resonant at low collisionality
JRT-16

## Slide 14: Summary: MS research during FY2015-16 will enable long-pulse high performance in NSTX-U and future devices
Advancing passive stability and active feedback control will be integrated into a disruption avoidance system, allowing us to sustain macroscopic stability in the new low collisionality regime
Understanding 3D field effects will provide a physics basis for optimizing stability through new capabilities of equilibrium profile control
Understanding disruption dynamics, and development of techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas will be greatly beneficial to future devices

## Slide 15: Backup

## Slide 16: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI
Plasma Operations
Avoidance Actuators
PF coils
2nd NBI: q, vf, p control
3D fields (upgraded + NCC):
EF, vf control
n=1-3 feedback
Divertor gas injection
Mitigation
Early shutdown
Massive Gas Injection
EPI (tbp)
Control Algorithms: Steer
Towards Stable Operation
Isoflux and vertical position ctl
LM, NTM avoidance
RWM and dynamic EF control
RWMSC (plasma response)
Divertor radiation control
Disruption Warning
System
Predictors (Measurements)
Shape/position
Eq. properties (b, li, Vloop,…)
Profiles (p(r), j(r), vf(r),…..)
Plasma response (n=0-3, RFA, …)
Divertor heat flux
Loss of Control
General framework & algorithms applicable to ITER

## Slide 17: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI (2)
RWMSC observer
MHD Spectroscopy
Kinetic Physics
Compare mismatch between the RWMSC observer and sensor measurements, and disruption occurrence
Evaluate simple physics criteria for global mode marginal stability in real-time
Use real-time MHD spectroscopy while varying rotation, qmin, and βN to predict disruptions
  ITER gas-loading :
  Injection into private flux region with higher assimilation efficiency?
γ contours
Avoidance Actuators
Control Algorithms
Disruption Warning System
Predictors
Mitigation
q, vf , βN control
3D fields, feedback
Resonant Field
Amplification (G/G)
1

## Slide 18: Participated in DIII-D National Campaign on Radiation Asymmetry XP
Thermal imaging indicates MGI location cooler than nearby wall
  ITER concerned about localized melting near gas injection port location
# of injectors had little effect on TQ/CQ Prad asymmetry
  No significant variation with valve delay
MGI1
MGI2
MGI2
MGI2
N.W. Eidietis, et al, G04-2, APS2013

## Slide 19: Valve has same time response for operation in <0.4T magnetic fields
Vacuum solenoid field is 0.67T
Skin depth in Al is 2.2cm, valve wall thickness is 1cm. Fields inside valve side wall ~0.4T
Future tests will use SS304L valve and further slow down solenoid current waveform
Shots 19,20, 21 are with solenoid energized
Shots 22 and 23 are comparison shots without solenoid

## Slide 20: ITER-like MGI Valve Designed, Built and Tested for Installation on NSTX-U
NSTX-U MGI Valve
FY15 MGI Research Plans
  Operate valves at ~5000 Torr (200 Torr.L Neon)
  Compare mid-plane and PFR locations for gas assimilations studies using identical gas injection set-up
  Possible Poloidal injection effect on VDE (multi-machine experiment with DIII-D & C-MOD)
  3 valves to be installed for FY15 Experiments

## Slide 21: Version 4 Valve evacuates into chamber in < 3ms, for gas injection amounts of 200 Torr.L N2
NSTX-U MGI Valve

## Slide 22: Physics analysis for Non-axisymmetric Control Coil (NCC) has been updated with IPEC-PENT and more NSTX-U targets
NTV calculations are updated using IPEC-PENT, without previous large-aspect-ratio approximation and pitch-angle simplification
  In NSTX and NSTX-U, PENT torque is typically larger than previous analysis by a factor of 2~3
1.5MA~2MA NSTX-U targets were studied
  2x6-odd is better than 12U or 2x6-even in general, but its advantages decrease when IP= 1.52MA
  FOM table updated accordingly (Purple : 2MA)
Figures of Merit | Favorable values | MID | 12U | 2x6-Odd | 2x12
EF (n=1) | High FN-R | 0.07 | 0.13 | 1.24 | 1.24
RWM (n=1) | High Fβ | 1.25 | 1.54 | 1.61 | 1.70
NTV (n≥3) | Wide ΔFN-N | 1.00 | 1.44~6.08 | 1.75~11.33 | 6.38~59.4
RMP (n≥3) | High FN-C | 0.25~0.30 | 0.31~1.04 | 0.43~0.77 | 1.18~3.53
 | Wide ΔFN-C | 1.00 | 2.20~12.3 | 10.4~17.4 | 888~14400

## Slide 23: Non-axisymmetric Control Coil (NCC) capability on NTV braking has been successfully studied with STELLOPT
The IPECOPT code has been developed from STELLOPT to optimize IPEC equilibrium for NTV Torque
  Initial attempts focus on variation of boundary harmonics for core and edge torque
  The applied n=1 spectrum shows the possibility to drive core (rho < 0.5) torque while minimizing edge torque
  The applied n=3 spectrum shows the ability to drive a broad edge torque
n=3
Levenberg-Marquardt (Modified) optimization
Torque
PPPL Theory Partnership, JRT-14
Unconstrained
Constrained to partial NCC + Midplane coil
Rho
n=3
Partial NCC (2x6-only) 4kAt,
Midplane coil 4kAt
Total torque ~2Nm
Total normal δB
on the plasma boundary
NCC design (on passive plates)
Existing coils

## Slide 24: RWM active control capability of the NCC continues to be assessed
NCC 2x12 with favorable sensors, optimal gain
NCC 2x6 odd parity, with favorable sensors
Full NCC coil set allows control close to ideal wall limit
  NCC 2x6 odd parity coils: active control to bN/bNno-wall = 1.61
  NCC 2x12 coils, optimal sensors: active control to bN/bNno-wall = 1.70
  (RWM coil bN/bNno-wall = 1.25)
Existing
RWM
coils
NCC full
2x12 coils
NCC partial
2x6 coils
  Design now needs sensor assessment

## Slide 25: Extensive benchmark among various NTV codes has been active and successful
There are three main branches in semi-analytic NTV codes as described in details below
All three have been successfully benchmarked
A particle code POCA also shows consistent trends with semi-analytic NTV codes, with some quantitative differences depending on regimes
Connected NTV formula | Combined NTV theory | Drift kinetic energy theory
Analytic NTV formulation is derived in the collisionality regimes, SBP, ν-√ν regime and 1/ν regime separately. Pade approximation to smoothly connect the formulations in different colisionality regimes. | NTV torque due to different particle motions are combined by a generalized equation. No need to separate the collisionality regimes | Drift kinetic energy is studied to determine ideal MHD instabilities e.g. Resistive Wall Modes. The torque is calculated based on the equivalence between NTV torque and drift kinetic energy. TΦ=2inδWK
Precession resonance | Precession resonance + Bounce-harmonic resonance | 
Pitch angle scattering collisional operator (accurate in the ν-√ν regime) | Krook collisional operator (allows to derive one generic equation of NTV torque and drift kinetic energy) | 
Geometric simplification | Full toroidal geometry | 
MARS-Q | IPEC-PENT | MARS-K
Liu and Sun, PoP 20 (2013) 022505 Sun et al, NF 51 (2011) 053015 Shaing et al, NF 50 (2010) 025022 | Park et al, PRL 102 (2009) 065002 Logan et al, PoP 20 (2013) 122507 | Park, PoP 18 (2011) 110702 Liu et al, PoP 15 (2008) 112503

## Slide 26: In lower ν regime, NSTX-U will investigate NTV for rotation control and stability theory implemented in active control
n=3 exp.
n=3 POCA
n=2 POCA
3D fields research plans, FY16:
  Assess NTV profile and strength at reduced ν and examine the NTV offset rotation at long pulse
  Prepare an initial real-time model of NTV profile for use in initial tests of the plasma rotation control system
Stability research plans, FY16:
  Examine RWMSC with:
    rotational stabilization in the controller model
  Investigate the dependence of stability on reduced ν through MHD spectroscopy; compare to kinetic stabilization theory
Resonance between ExB and Bounce motion
Collision (1/ν)
Dominant transport mechanism
NSTX
NSTX-U
(Bounce freq. 
Collision )
Bounce-harmonics become important and SBP too if ExB is low
SBP becomes important and offset too if ExB is low
Modified bounce motion

## Slide 27: Drift-kinetic effects on 3D plasma response and non-resonant error field effects are being actively investigated
Drift-kinetic 3D plasma response
  MARS-K self-consistent calculations successfully compared with n=1 DIII-D RFA
  Preliminary NSTX RFA calculations indicate kinetic stabilization effects important (especially near no-wall limit), and rotation can be destabilizing
Res. and non-res. error field effects
  Resonant-coupling schemes (IPEC-PENT) are being used to optimize n=2 error field correction in DIII-D and n=1-4 correction in TBM mock-up
  Extremely small resonant errors were found so far in KSTAR, and non-resonant error field will be investigated
  Non-resonant error field effects on locking/tearing are being investigated in NSTX, with newly developed resistive DCON
DIII-D
I+C-coil circuit optimization for TBM n=1-4 correction
NSTX
Ideal
Kinetic

## Slide 28: KSTAR 3 rows of internal coils were used to produce n=1 pitch-crossing field lines and to find rotational resonances
The unique 3 rows of internal coils in KSTAR were utilized to produce pitch-crossing field lines (orthogonal to pitch-aligned field lines)
This n=1 field is almost purely non-resonant :
  Successfully induced NTV without n=1 resonant perturbation
  Used to find the 1st bounce-harmonic rotational resonance, as the gap to 2nd resonance is the widest with n=1 (predicted by and agreed with theory and computation)
Mirror image to RMP
m~nq
J.-K. Park, PRL 111, 095002 (2013)

## Slide 29: Non-resonant Neoclassical Toroidal Viscosity (NTV) physics will be used for the first time in rotation feedback control
Momentum force balance – wf decomposed into Bessel function states
NTV torque:
133743
I. Goumiri (PU), S.A. Sabbagh (Columbia U.), D.A. Gates, S.P. Gerhardt (PPPL)
radius
t(s)
Plasma rotation (rad/s)
t(s)
State-space model
TRANSP run
(non-linear)
Feedback using NTV: “n=3” dB(r) spectrum
NTV
region
Desired
Computed
0
2
4
6
104
Radial coordinate
NTV torque density (N/m2)
Plasma rotation (rad/s)

## Slide 30: Plasma rotation control has been demonstrated for the first time with TRANSP using NBI and NTV actuators
3D coil current and NBI power (actuators)
t (s)
This case uses pre-programmed 3D coil current and NBI feedback
Rotation evolution vs. desired
rotation setpoints
desired wf (#1)
desired wf (#2)
feedback on
Plasma rotation (rad/s)
t (s)
t (s)
t (s)
3D Coil Current (A)
NBI power (MW)
feedback on
Plasma rotation (rad/s)
Normalized radius

## Slide 31: Plasma response from fully-penetrated 3D field used in NTV experimental analysis matches M3D-C1 single fluid model
Surface-averaged dB from fully penetrated model vs. M3D-C1 single fluid model
  M3D-C1 analysis (Evans/Ferraro (GA), Jardin (PPPL))
  NTVTOK analysis (S.A. Sabbagh)
(NTVTOK)
(n = 3 configuration)
Strong TNTV region
core
edge
Flux surface-avg <dB> (G)
NTV experimental data is a strong quantitative constraint on plasma response of dB
  Because the measured NTV scales as TNTV µ dB2,
Level of agreement varies with profile
  Good agreement between NTVTOK / M3D-C1 single fluid models in strong NTV region
  M3D-C1 core <dB> larger than NTVTOK
    Core mode in M3D-C1
  M3D-C1 edge <dB> smaller
    Experimental TNTV too small in this region to constraint dB
Analysis ongoing in 2014

## Slide 32: Model-based RWM state space controller including 3D plasma response and wall currents used at high bN in NSTX
Potential to allow more flexible control coil positioning
  May allow control coils to be moved further from plasma, and be shielded (e.g. for ITER)
Katsuro-Hopkins, et al., NF 47 (2007) 1157
RWM state space controller in NSTX at high bN
137722
t (s)
40
0
80
0.56
0.58
0.60
137722
t (s)
0.56
0.58
0.60
0.62
dBp90
dBp90
-40
0.62
40
0
80
Effect of 3D Model Used
No NBI Port
With NBI Port
3D detail of model is important to improve sensor agreement
S.A. Sabbagh, et al., Nucl. Fusion 53 (2013) 104007
Controller
(observer)
Measurement

## Slide 33: Dual-component PID (Br + Bp) and model-based RWM state-space (RWMSC) active control will enable long pulse, high β operation
2014:
  Expand/analyze RWMSC for 6 coil control and n > 1 physics
2017 and 2018:
  Upgrade for NCC, utilize model-based active control with the new NCC to demonstrate improved global MHD mode stability and very low plasma disruptivity, producing highest-performance, longest-pulse plasmas
Brn = 1 (G)
Br phase = 0o
Br phase = 90o
Br phase = 180o
t (s)
6
4
2
0
0.0
0.2
0.4
0.6
0.8
1.0
1.2
bN
140124
140125
140126
140127
6
4
2
0
Active n = 1 Bp + BR feedback control
Br phase = 225o
Feedback on
RWMSC
2015 and 2016:
  Establish Br + Bp active control capability in new machine, use with snowflake divertor
  Examine RWMSC with:
    independent actuation of six coils
    multi-mode control with n up to 3
    rotational stabilization in the model
  Advantages:
  potential for use of external coils with less power

## Slide 34: Research plans and needs for this year (FY2014) in preparation for NSTX-U operations in FY2015
RWM State-space Controller generalization – available “Day 0”
  Offline IDL version of code already generalized
  Changes to r/t version to be made. Small PCS programming support will be needed
NSTX EFIT (of course, “Day 0”)
  Plan to upgrade to faster processing to support increased between-shots spatial resolution / time resolution (eta 2014-2015); present code available as default
  New code components acquired Dec 2013; new dedicated prototype 32 core CPU computer online at PPPL (planned to be expanded); consistent with PPPL IT plan
NSTX rotation control
  Continuing work with PU student (I. Goumiri) on rotation control algorithm
  Present quantitative NTV analysis of Columbia U. NSTX experiments supports this

## Slide 35: MISK analysis of DIII-D discharges is helping to enable their path to high beta operation
Chart: Scaled experimental rotation
| 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
 | 0.57332 | 0.60824 | 0.63471 | 0.54948 | 0.40391 | 0.30109 | 0.78854 | 0.75814 | 0.65692 | 0.40077 | 0.46541 | 0.85358 | 0.82092 | 0.51843 | 0.33805 | 0.61846 | 0.11434 | -0.14901 | -0.21437 | -0.26361
 | 0.52757 | 0.54369 | 0.59784 | 0.58227 | 0.62177 | 0.82596 | 0.9007 | 0.92045 | 0.8241 | 0.7896 | 0.71248 | 0.60421 | 0.56117 | 0.48281 | 0.42449 | 0.45712 | 0.52932 | 0.51478 | 0.43847 | 0.34315
High βN, high qmin shots with similar, relatively high plasma rotation have varied stability due to q profile variation and related changes to bounce resonance stabilization
Educated follow-on experiment forthcoming
Chart: Scaled experimental rotation
| 0.05 | 0.1 | 0.15 | 0.2 | 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7 | 0.75 | 0.8 | 0.85 | 0.9 | 0.95 | 1
 | -0.81455 | -0.83655 | -0.2205 | -0.87264 | -0.87857 | -0.87536 | -0.91983 | -0.98801 | -0.99639 | -0.99375 | -0.99037 | -0.98407 | -0.97923 | -0.97703 | -0.97373 | -0.97307 | -0.97151 | -0.96915 | -0.96748 | -0.96576
 | 0.57332 | 0.60824 | 0.63471 | 0.54948 | 0.40391 | 0.30109 | 0.78854 | 0.75814 | 0.65692 | 0.40077 | 0.46541 | 0.85358 | 0.82092 | 0.51843 | 0.33805 | 0.61846 | 0.11434 | -0.14901 | -0.21437 | -0.26361
 | -0.37062 | -0.2003 | -0.24604 | -0.60645 | -0.68834 | -0.67887 | -0.67356 | -0.70843 | -0.78806 | -0.8555 | -0.90005 | -0.91669 | -0.92509 | -0.92731 | -0.92987 | -0.93024 | -0.93098 | -0.93065 | -0.92911 | -0.92841
Unstable
Stable
MISK stability vs. rotation
150312
147634
133103
Experimental rotation magnitude
t = 2.990s
t = 2.970s

## Slide 36: Measured toroidal plasma rotation profile shows non-resonant NTV rotation control using n = 2 field
8064
8062
With n = 2 field
(step current up)
With n = 2 field
(step current down)
1
1
2
3
3
2
1
2
3
1
3
2
IVCC n = 2 current
At same IVCC
current, rotation
profile shows no hysteresis – important for control
S.A. Sabbagh,
Y.S. Park (Columbia U.)

## Slide 37: Collaborations at KSTAR have aided high beta operation
KSTAR collaboration
  High βN, over no-wall limit has been achieved