## Slide 1
Limiter at end of antenna
Limiter tiles in NB armor
Wave Heating and Current Drive TSG
R. Perkins and J. Hosea
Polar region change impact:
  Research objectives will be compromised if changes are made to rows 2 – 4 of the outer divertor tiles that require removal of the divertor RF probes
    These probes are necessary for quantifying heat deposition due to far field RF rectification
Plasma Parameters needed for HHFW experiments
  HHFW experiments are compatible with all plasma parameters except for the outboard antenna/separatrix gap
    An outboard limiter is needed to shield the antenna from energetic ions in the SOL
    An outboard limiter located away from the antenna should also result in less gas entering the antenna and thus in more robust coupling into high power NB heating conditions.

## Slide 2
Limiter at end of antenna
Limiter tiles in NB armor
Impact of possible PFC changes for rows 2 – 4 of the outer divertor tiles
A. Brooks
Recovery project is still working to determine requirements for the tiles shown
Initial studies indicate that their may be sufficient thermal margin in an average sense.
Risk of strong leading edge heating on vertical target
Recently revised both physics and analysis assumptions regarding halo currents on the CS.
Halo current loads are large and likely problematic
    Refining both the requirements and the analysis to better assess this issue.
Outboard divertor tiles
Rows 2 - 4
RF probes in outboard divertor tiles need to be maintained to support RF deposition physics in the SOL

## Slide 3
Probes for measuring IV characteristics and RF fields: Coaxial Langmuir at Bay J top and bottom tiles in Rows 2 - 4
IR camera and probes are critical for documenting RF edge heating
Bay J probes (Langmuir and RF)
6 poloidal Langmuir probe array for radial coverage top and bottom
135325
Bay I
Wide angle IR view
Bay G
IR view
-90°
452 ms
135333
BT = 4.5 kG, IP = 0.8 MA
Antenna
IR view
& visible view
Antenna probes,
reflectometer

## Slide 4
Plasma parameter needed for HHFW experiments is a controlled outer gap to the antenna
NB energetic ions bombard the HHFW antenna when the gap is too small
Limiter on NB armor should prevent this and excessive gas flow into the antenna

## Slide 5
NB bombardment of antenna follows the center of the plasma (smallest gap)
A central mid-plane limiter on the NB armor should be sufficient to protect the antenna
Scan of Z position of plasma with PNB = 2 MW, PRF ~ 1 MW, IP ~ 0.65 MA
141858
141861
141863
0.545 s
0.583 s
0.583 s
Midplane gap ~ 6 cm ~ 6 cm ~ 5 cm
Gap at interaction zone
~ 6 cm ~ 4 cm ~ 4 cm
ZC position ~ -3.5 cm ~ - 20 cm ~ + 16 cm
Antenna
Antenna
Antenna