## Slide 1: Progress and Plans for NSTX Upgrade and Kinetic Resistive Wall Mode Stability
Jack Berkery, Columbia University
and the NSTX-U team
University of Washington,
Seattle, WA
October 26, 2015

## Slide 2: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 3
ST
“Spherical” tokamak (ST) has aspect ratio A < 2
A ~ 1.2-2,
k = 2-3,
q95 = 6-20,
bT = 10-40%
A ~ 3-4,
k = 1.5-2,
q95 = 3-4,
bT = 3-10%
Tokamak
Toroidal beta bT = p / (BT02/2m0)
Aspect Ratio A = R /a
Elongation k = b/a
IP ~ ITF (1 + k2) / (2 A2 q*)
Energy confinement time tE ∝ IP
Access high pressure, rapid rotation, low collisionality
• ST has high IP, economically, due to high κ and low A
• Favorable average curvature improves stability at high beta

## Slide 4
Design studies show ST potentially attractive as FNSF
Projected to access high neutron wall loading at moderate R, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R, careful design
PPPL ST-FNSF concept

## Slide 5: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 6
~2x higher BT, Ip, PNBI and ~5x pulse length vs. NSTX
NSTX-U
NSTX (1999-2011)
The National Spherical Torus Experiment Upgrade (NSTX-U) at the Princeton Plasma Physics Lab

## Slide 7
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New 2nd NBI
Present NBI
New
center-stack
New center column doubles toroidal magnetic field, plasma current
  Access conditions closer to FNSF
  Pulse lengths increase from 1 to 5 seconds
Second neutral beam injection system
  Doubles heating power, increases flexibility available for experiments
  More tangential injection improves current drive, especially at small plasma current
Increased flexibility in divertor configuration
The National Spherical Torus Experiment Upgrade (NSTX-U) at the Princeton Plasma Physics Lab

## Slide 8: NSTX Upgrade mission elements
ITER
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for the plasma-material interface (PMI) challenge
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop ST as fusion energy system
Lithium
“Snowflake”
ST-FNSF / Pilot-Plant

## Slide 9
New 2nd NBI
1st NBI
NSTX Upgrade project recently completed
On cost and schedule, first test plasma ~100kA (Aug. 10, 2015)

## Slide 10
Center stack installed
NSTX Upgrade project recently completed
On cost and schedule, first test plasma ~100kA (Aug. 10, 2015)

## Slide 11
NSTX Upgrade project recently completed
On cost and schedule, first test plasma ~100kA (Aug. 10, 2015)
First test plasma
(Ohmic heating only)

## Slide 12
NSTX Upgrade project recently completed
On cost and schedule, first test plasma ~100kA (Aug. 10, 2015)
EFIT Ip
NSTX-U EFIT Model created and used for first test shots
  Challenging at Ip/Iwall ~ ¼, but successful (good magnetics)
First test plasma
(Ohmic heating only)
Physics research operations to begin in December 2015

## Slide 13: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 14: Low collisionality operation achieved on NSTX using lithium wall coatings
Lithium coatings on carbon tiles reduced gas source from wall
  Lead to a larger H-mode pedestal, larger core temperature
  Confinement continued to improve with reduced collisionality
Longer discharges will address first wall solutions
  New diagnostics and campaigns with different wall materials will advance studies of plasma-wall interaction
R. Maingi, PRL 2011

## Slide 15: Major motivation for NSTX Upgrade: Determine if confinement trend continues, or is like conventional A
Normalized electron collisionality
ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors
NSTX-U
NSTX
W. Guttenfelder, PoP 2013, PoP 2012, PRL 2011
Micro-tearing-driven transport may explain ST tE collisionality scaling
Confinement
S. Kaye, NF 2013

## Slide 16: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 17: NSTX-U will test ability of radiation and advanced divertors to mitigate very high heat-fluxes
NSTX: reduced heat flux 2-4×via radiation (partial detachment)
Additional null-point in divertor expands field, reduces heat flux
Snowflake/X Divertor
Standard Divertor
NSTX-U has additional coils for up-down symmetric snowflake, improved control
NSTX-U peak heat fluxes will be up to 4-8× higher than in NSTX
V. Soukhanovskii, JNM, 2013

## Slide 18: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 19
Compact ST-FNSF has no/small central solenoid
IP Start-up/Ramp-up Critical Issue for ST-FNSF/Demo
ST-FNSF Scenarios
IP [MA]
NBI
Time
HHFW
EC/EBW, HI, PF
Solenoid-free
Start-up
high bT, bN, k, disruption avoidance, high H, heat flux mitigation
Current ramp-up and profile control
• Two novel techniques for solenoid-free start-up and ramp-up will be investigated
  RF: ECH/EBW and HHFW
  Helicity Injection
~ 1-2 MA of solenoid-free start-up current needed for FNSF

## Slide 20
Helicity Injection is efficient method for current initiation
Coaxial Helicity Injection (CHI) concepts being developed
CHI developed on HIT, HIT-II
Transferred to NSTX / NSTX-U
Discharge evolution of 160 kA closed flux current produced by CHI alone in NSTX
R. Raman et al., PRL 2006
Standard NSTX inductive start-up, requires 50% more inductive flux than CHI started discharge
R. Raman et al., POP 2011

## Slide 21: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 22: NSTX achieved 70% “transformer-less” current drive Will NSTX-U achieve 100% as predicted by simulations?
Steady-state operation required for ST, tokamak, or stellarator FNSF
TRANSP Contours of Non-Inductive Fraction
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
H98y2
ITER H-mode confinement scaling multiplier
S. Gerhardt, NF 2012

## Slide 23: NSTX-U developing a range of profile control actuators for physics studies, scenario optimization
NTV torque density (N/m2)
Plasma rotation (rad/s)
Radial coordinate
NTV
region
0
2
4
6
104
desired wf
t1
t2
t3
Variations in Outer Gap
Variations in Beam Sources
800 kA Partial Inductive, 87% < fNI < 100%
27 22 17 12 7 2
Outer Gap
800 kA and 1 T
[50,60,70,130] cm
[50,60,120,130] cm
[60,70,110,120] cm
[70,110,120,130] cm
q-Profile Actuators
Torque Profiles From 6 Different NB Sources
Neutral
Beams
(TRANSP)
Rotation Profile Actuators
Largest Rtan
Smallest Rtan
S. Gerhardt,
NF 2012
NSTX-U state-space ωφ controller w/NTV as actuator
S. Sabbagh, IAEA 2014

## Slide 24
  High βN for fusion performance, high non-inductive fraction for continuous operation
    High bootstrap current fraction -> Broad current profile -> Low li = <Bp2>/<Bp>ψ2
  Unfavorable for ideal stability since low li reduces the ideal n = 1 no-wall beta limit
The highest βN/li is not the least stable in NSTX
  Passive stability of the resistive wall mode (RWM) must be explained
Record bN and bN / li accessed in NSTX using passive + active resistive wall mode stabilization
Major NSTX-U mission is to achieve fully non-inductive operation at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM
S. Sabbagh, NF 2013; J. Berkery, POP 2014

## Slide 25: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Transport and Turbulence
  Power Exhaust
  Plasma Start-up
  Scenarios, Control, and Stability
Modifications to Ideal Stability by Kinetic Effects
Summary

## Slide 26: An unstable RWM is an exponential growth of magnetic field line kinking that can cause disruptions
The resistive wall mode (RWM) is a kinking of magnetic field lines slowed by penetration through vessel structures
where
Bp
RWMs in NSTX cause a collapse in β, disruption, and termination of the plasma
130235
[S. Sabbagh et al., Nucl. Fusion 46, 635 (2006)]

## Slide 27: RWM dispersion relation evaluated with ideal and kinetic components allows for passive stabilization of the RWM
Resistive Wall Mode (RWM) fluid dispersion relation:
τw-1 is slow enough for active stabilization (feedback)
[B. Hu et al., Phys. Rev. Lett. 93, 105002 (2004)]
However, experiments operate above the no-wall limit without active control!
Passive stabilization
  Collisional dissipation
  Rotational stabilization
    Models with scalar “critical rotation” for stability could not explain experiments
[S. Sabbagh et al., Nucl. Fusion 50, 025020 (2010)]
βNno-wall
βNwith-wall
unstable
stable
0
Ideal Kink Mode
Resistive Wall Mode
~τw-1

Ideal Stability
Kinetic Effects

## Slide 28: Kinetic effects arise from the perturbed pressure, are calculated in MISK from the perturbed distribution function
Force balance:
leads to an energy balance:
Kinetic Energy
Change in potential energy due to perturbed kinetic pressure is:
Fluid terms
is solved in MISK by using from the drift kinetic equation for
Precession Drift
~ Plasma Rotation
Collisionality

## Slide 29
NSTX 121083
unstable
(marginal stability)
unstable
Precession drift resonance stabilization
Bounce/transit resonance stabilization
Plasma evolution
Marginal stability
νeff/νexp (marginal stability)
Kinetic RWM theory consistent with RWM destabilization at intermediate plasma rotation; stability altered by collisionality
Destabilization appears between precession drift resonance at low ωφ, bounce/transit resonance at high ωφ
Stability gradient with ωφ stronger at low collisionality
γτw contours vs. ν and ωφ
instability
(experiment)
ωφ/ωφexp (marginal stability)
MISK code
[J. Berkery et al., Phys. Rev. Lett. 104, 035003 (2010)]

## Slide 30: MISK calculations are grounded in validation against unstable experimental plasmas
MISK calculations (at tMISK) include kinetic effects, have been tested against many marginally stable NSTX experimental cases
NSTX
[J. Berkery et al., accepted by Nuclear Fusion (2015)]

## Slide 31: MISK calculations generally reproduce the approach towards marginal stability seen in experiments
In each case, the calculations trend towards instability (γτw = 0) as the time approaches the time of experimental RWM instability growth
  Twelve equilibria from discharges with no RWM show no trend and are more stable in the calculations
Thermal particles
with energetic particles
unstable
stable
unstable
stable
NSTX
NSTX
[J. Berkery et al., accepted by Nuclear Fusion (2015)]

## Slide 32
More: Berkery APS poster Tues. morning, Sabbagh talk Weds. afternoon
NSTX-U project recently completed on cost and schedule with ~100kA test plasma in August
  Physics research to begin in December 2015
NSTX began, and NSTX-U will extend, opportunities to study toroidal confinement physics in novel regimes:
  Low aspect ratio, strong shaping, high b, low collisionality
  Advanced divertors, lithium walls, unique start-up solutions
  Will inform optimal configuration for next-step FNSF device
Modification of ideal stability by kinetic effects can explain resistive wall mode stability at high beta
Summary

## Slide 33: Backup

## Slide 34
ST Extends Predictive Capability for ITER and Toroidal Science
  High β physics, rotation, shaping extend stability, transport knowledge
  NBI fast-ions in present STs mimic DT fusion product parameters in ITER  study burning plasma science
  STs can more easily study electron scale turbulence at low collisionality  important for all magnetic fusion
Unique ST properties also support ITER
Burning Plasma Physics - ITER

## Slide 35: Brief Overview of FY2016-18 NSTX-U Goals
FY2016
  Obtain first data at 60% higher field/current, 2-3× longer pulse:
    Re-establish sustained low li / high-k operation above no-wall limit
    Study thermal confinement, pedestal structure, SOL widths
    Assess current-drive, fast-ion instabilities from new 2nd NBI
FY2017
  Extend NSTX-U performance to full field, current (1T, 2MA)
    Assess divertor heat flux mitigation, confinement at full parameters
  Access full non-inductive, test small current over-drive
  First data with 2D high-k scattering, prototype high-Z tiles
FY2018
  Assess causes of core electron thermal transport
  Test advanced q profile and rotation profile control
  Assess CHI plasma current start-up performance
  Study low-Z and high-Z impurity transport
    Possibly test/compare pre-filled liquid-Li tiles/PFCs vs. high-Z solid

## Slide 36
New
center-stack
2nd NBI
Li granule injector
High-Z PFC diagnostics
Off-midplane 3D coils (NCC)
up to 1 MA plasma gun
Lower divertor cryo-pump
Upgraded CHI for ~0.5MA
LLD using bakeable cryo-baffle
DBS, PCI, or other intermediate-k
Divertor Prad
Snowflake
Run Weeks:
Five Year Facility Enhancement Plan (green = ongoing)
2015: Engineering design for high-Z tiles, Cryo-Pump, NCC, ECH
MGI disruption mitigation
4 coil AE antenna
HHFW limiter upgrade
Establish control of:
Rotation
Upward
LiTER
High kq
Laser blow-off
Boronization
Enhanced MHD sensors
Neutron collimator
Charged fusion product
Upgraded halo sensors
Pulse-burst MPTS
14-16
10-12
16-18
ne
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
2015 | 2016 | 2017 | 2018 | 2019
Upgrade Outage
1.5  2 MA, 1s  5s
MAPP
42 ch MPTS
48 ch BES
MSE/LIF
FIReTIP
Major enhancements:
Base funding
+15% incremental
Fiscal Year:
12-16
High-Z tile row on lower OBD
dB diag. - incremental
0.5-1 MA CHI
qmin
1 MW ECH/EBW