## Slide 1: Progress and plans for NSTX Upgrade and prospects for next-step spherical tori
Jonathan Menard, PPPL
Plasma Physics Seminar (Physics/ECE/NE 922)
Physics Building, Room 2241
September 14, 2015

## Slide 2: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 3
ST
“Spherical” tokamak (ST) has aspect ratio A < 2
Toroidal Beta bT = p / (BT02/ 2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Natural elongation makes its spherical appearance
Favorable average curvature improves stability at high beta  access high normalized pressure, rapid rotation, low collisionality
A ~ 1.2-2,
k = 2-3,
q95 = 6-20,
bT = 10-40%
A ~ 3-4,
k = 1.5-2,
q95 = 3-4,
bT = 3-10%
Tokamak
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 4
ST can be compact, high b, and high confinement
Higher elongation k and low A lead to higher IP , bT and tE
IP ~ ITF (1 + k2) / (2 A2 q*)
Normalized pressure bT [%] º bN IP / (aBT0)
High κ ∼ 3.0 equilibrium in NSTX
Energy confinement time tE ∝ IP
IP ~ ITF for ST due to low A and high k
• ST has high IP due to high κ and low A
• IP increases tokamak performance
• ST achieves high performance cost effectively
$
Toroidal beta bT = p / (BT02/2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 5
Fusion technology development is major challenge
Fusion Nuclear Science Facility (FNSF) could aid development
Without R&D, fusion components could fail prematurely
FNSF can help develop reliable fusion components
FNSF facilities must be: modest cost, low T, and reliable
Need to develop reliable, qualified nuclear and other components unique to fusion:
Divertor, plasma facing components
Blanket and Integral First Wall
Vacuum Vessel and Shield
Tritium Fuel Cycle
Remote Maintenance Components
ST-FNSF

## Slide 6
Design studies show ST potentially attractive as FNSF
Projected to access high neutron wall loading at moderate R, Pfusion
  Wn ~ 1-2 MW/m2 , Pfus ~ 50-200MW, R ~ 0.8-1.8m
Modular, simplified maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R, careful design
PPPL ST-FNSF concept

## Slide 7: Tritium breeding at top/bottom of ST device important for achieving high Tritium Breeding Ratio (TBR) > 1
Inner Blanket Segment = 0.81
Outer Blanket Segment = 0.15
Total TBR ~ 1.03 with no penetrations or ports
(heterogenous outboard blanket)
0.0004
0.0004
0.034
0.034
Breeding at CS ends important:
DTBR = +0.07
R=1.7m configuration
Compatible with long-leg / Super-X divertor

## Slide 8: Recent studies show sufficiently large major radius ST-FNSF can be tritium self-sufficient
R=1.7m: TBR ≥ 1
R=1.0m: TBR < 1 (≈ 0.9)
TBM
NBI
MTM
TBM
MTM
NBI
1m device cannot achieve TBR > 1 even with design changes
Requirement: purchase ~0.4-0.55kg of T/FPY from outside sources
NBI = Neutral Beam Injector,
TBM = Test Blanket Module, MTM = Materials Test Module

## Slide 9: HTS potentially attractive for making electrically efficient ST* (~10× lower magnet cooling power vs. copper)
Possible missions:
  Steady-state toroidal PMI facility, FNSF
  ST Pilot Plant (Qeng~1 for weeks/months)
    Requires high H98y2 = 1.7-2
Initial configurations favorable:
  A=1.8-2, strong shaping: k~2.5-2.7, d~0.5
  All equilibrium PF coils outside TF
    No joints needed for HTS TF coils
  Long-legged divertor for qdiv-pk < 5MW/m2
  Vertical port-based maintenance
  WC inboard thermal shield for TF
Now actively investigating:
  HTS lifetime in radiation environment
  Blanket/shield thickness, location, TBR
*Work supported by Tokamak Energy (UK) - 2014
R0 = 1.4m, BT = 3.2T, IP = 7-8MA, Pfusion-DT = 100MW

## Slide 10
ST Extends Predictive Capability for ITER and Toroidal Science
  High b physics, rotation, shaping extend stability, transport knowledge
  NBI fast-ions in present STs mimic DT fusion product parameters in ITER  study burning plasma science
  STs can more easily study electron scale turbulence at low collisionality  important for all magnetic fusion
Unique ST properties also support ITER
Burning Plasma Physics - ITER

## Slide 11: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 12: NSTX Upgrade mission elements
ITER
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for the plasma-material interface (PMI) challenge
Advance ST as candidate for Fusion Nuclear Science Facility (FNSF)
Develop ST as fusion energy system
Lithium
“Snowflake”
ST-FNSF / Pilot-Plant

## Slide 13
NSTX and MAST are undergoing major upgrades
~2x higher BT, Ip, PNBI and ~5x pulse length vs. NSTX / MAST
Super-X divertor configuration for FNSF/DEMO divertor solution
Tangential 2nd NBI + high bN and fBS
for full non-inductive sustainment, ramp-up
NSTX-U
MAST-U
First test plasma 2017
First test plasma ~1 month ago
Conventional
Super-X

## Slide 14
New 2nd NBI
1st NBI
NSTX Upgrade project recently completed
On cost and schedule, first test plasma ~100kA (Aug. 10, 2015)

## Slide 15: New centerstack (CS) highlights: Jan – Aug 2015
CS crane lift
CS installed
First test plasma
(Ohmic heating only)
Magnetics functional  EFIT reconstructions

## Slide 16: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 17: Mega-ampere-class STs rely heavily on co-injected neutral beams for heating, current drive
New 2nd NBI
(RTAN=110, 120, 130cm)
5MW, 5s, 80keV
Original NBI
(RTAN = 50, 60, 70cm)
5MW, 5s, 80keV
NSTX-U

## Slide 18: NSTX-U developing a range of profile control actuators for physics studies, scenario optimization for FNSF/Pilot
Variations in Outer Gap
Variations in Beam Sources
800 kA Partial Inductive, 87% < fNI < 100%
27 22 17 12 7 2
Outer Gap
800 kA and 1 T
[50,60,70,130] cm
[50,60,120,130] cm
[60,70,110,120] cm
[70,110,120,130] cm
q-Profile Actuators
Torque Profiles From 6 Different NB Sources
Neutral
Beams
(TRANSP)
Rotation Profile Actuators
Largest Rtan
Smallest Rtan
(n=3)
Measured and Calculated Torque Profiles from 3D Fields

## Slide 19
Record bN and bN / li accessed in NSTX using passive + active resistive wall mode stabilization
High bN regime is important for bootstrap current generation.
High bN / li regime important since high fBS regime has low li.
Major NSTX-U mission is to achieve fully non-inductive operation at high b
ST-FNSF
Unstable RWM
Stable / controlled RWM
S. Sabbagh, PRL 2006
J. Berkery, PRL 2011
W. Zhu, PRL 2006

## Slide 20: Kelvin-Helmholtz (KH) instabilities predicted when central sound-speed Mach number Ms ≈ 0.7-0.8
Rotation profile
n=1 K-H
Eigenfunction
I. Chapman, NF 2012

## Slide 21: Hybrid MHD-drift-kinetic stability calculations find rotation + fast-ions reduce stability of p-driven Ideal Wall Mode
Low-rotation fluid with-wall limit is very high  marginal bN ~ 7-8
Increasing rotation lowers max bN to ~5.5 at mode onset time
Full kinetic treatment including fast-ions  marginal bN ~3.5  most consistent with experiment
MARS-K code needed to explain NSTX Ideal Wall Mode (IWM) onset at highest rotation, bfast
J. Menard, PRL 2014
Experimental bN
Rotation, rotation shear, fast-ion content must be optimized to maximize RWM and IWM limits

## Slide 22: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 23
High confinement multiplier H needed for compact ST
Fusion gain Q depends strongly on “H”, Q µ H 5-7
• Ion energy transport in H-mode ST plasmas near neoclassical level due to high shear flow and favorable curvature
• Electron energy transport anomalous (as for all tokamaks)
EPH
H-mode
NSTX
ST-FNSF
Y. Ren (PPPL)
NSTX
R. Maingi, PRL 2010
S. Gerhardt NF 2014
Enhanced pedestal H-mode (EPH) has H up to 1.5-2  attractive for ST-FNSF

## Slide 24: Electron and ion tE scale differently in ST, and different than at higher aspect ratio
Ions: tE  Ip
Neoclassical
(r/a=0.5-0.8)
Ion tE  IP, consistent with neoclassical ion transport
  Implies ion turb. suppressed by high E×B shear  possibility of isolating causes of e-transport
Electron tE  BT
  Could imply Electron Temperature Gradient (ETG) modes, and/or electromagnetic turbulence
Electrons: tE  BT
3.5 kG
5.5 kG
S.M. Kaye, PRL 2007

## Slide 25
Favorable confinement trend with collisionality, b found
Important implications for future ST FNSF, Demo with lower n*
Fig. 70. (a) Normalized confinement time as a function of collisionality at mid-radius in NSTX. Blue points are from discharges that used HeGDC+B wall conditioning, while red points are from discharges that used Li. Reprinted with permission from S.M. Kaye et al., Nucl. Fusion 53 063005 (2013). Copyright (2013). Institute of Physics.
(b) Collisionality scan of thermal energy confinement time in MAST. Reprinted with permission from M. Valovic et al., Nucl. Fusion 51 073045 (2011). Copyright (2011) Institute of Physics.
NSTX
Very promising ST scaling to reactor condition, if continues on NSTX-U/MAST-U
NSTX
tE, th µ n*e-0.1 b-0.9 tokamak empirical scaling (ITER 98y,2)
tE, th µ n*e-0.8 b-0.0 ST scaling
S.M. Kaye, NF 2007, 2013
MAST
B tE,th [ T s]
~ n*e -0.82
n*e
M. Valovic, NF 2011

## Slide 26
Micro-tearing-driven (MT) transport
may explain ST tE collisionality scaling
MT-driven ce vs. nei using the GYRO code
W. Guttenfelder, PoP 2013, PoP 2012, PRL 2011
MT growth rate decreases with reduced collisionality in qualitative agreement with the NSTX experiment.
Further electron confinement improvement expected due to reduced collisionality.
NSTX-U
NSTX
W. Wang: Recently found dissipative TEM has similar n* scaling (GTS)

## Slide 27: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 28: CAE mode-conversion to kinetic Alfvén waves (KAW) predicted to transfer core NBI power to mid-r electrons
GAE/CAEs cause large ce through stochastic orbits (N. Gorelenkov, NF 2010)
CAEs also couple to KAW - Poynting flux redistributes fast ion energy near mid-radius, E|| resistively dissipates energy to thermal electrons
  PCAEKAW ~ 0.4 MW from QL estimate + experimental mode amplitudes
  Pe,NBI ~ 1.7 MW for r <0.3, NBI power deposited on core electrons
wA(R,Z)=wCAE
CAE
(n=8)
KAW
HYM code
E. Belova, PRL 2015
Radial Poynting flux
EBR
~rbeam
Up to 25% of electron heating power transferred to KAW off-axis

## Slide 29
NBI-heated STs excellent testbed for a-particle physics
Alfvenic modes readily accessible due to high Vfast > VAlfvén
a-particles couple to Alfvénic modes strongly when Va > VA ~ b-0.5 Cs
Va > VA in ITER and reactors: condition easily satisfied in ST due to high b
Fast-particle-driven Alfvén Eigenmodes: Toroidal, Global, Compressional
NSTX-U will also explore Vfast < VA regime giving more flexibility
  M.P. Gryaznevich, PPCF 2004
Stabilization of TAEs at high b in MAST
TAEs significantly modified at high b as VA  Cs
  E. Fredrickson, NF 2013
EP parameter space
NSTX data:

## Slide 30
“TAE avalanche” shown to cause energetic particle loss
Uncontrolled a-particle loss could cause reactor first wall damage
Multi-mode TAE avalanche can cause significant EP losses as in “sea”of TAEs expected in ITER
  E. Fredrickson, NF 2013
Time (ms)
(a)
Time (ms)
Neutron rate (a.u.)
Fast ion loss rate (a.u.)
Frequency (kHz)
Progress in simulation of neutron rate drop
due to TAE avalanche
D.S. Darrow, NF (2013)

## Slide 31: Rapid TAE avalanches could impact NBI current-drive in advanced scenarios for NSTX-U, FNSF, ITER AT
Discrepancy between reconstruction and total assuming
classical JNBCD
Minor radius
700kA high-bP plasma with rapid
TAE avalanches has time-average DFI = 2-4m2/s
NSTX: rapid avalanches can lead to redistribution/loss of NBI current drive
NSTX-U TRANSP simulations
1 MA, 1T, H98=1, near non-inductive
1.6 MA, 1T, partial inductive
1.2 MA, 0.55T, high bT
All: fGW=0.7, H98=1
S. Gerhardt NF 2011, NF 2012

## Slide 32: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 33: All modern tokamaks / STs use a “divertor” to control where power and particles are exhausted
Power / particles contact target plates here
Power exhaust width outside main plasma can be very narrow (few mm)

## Slide 34
Tokamak + ST data: power exhaust width varies as 1 / Bpoloidal
Will previous ST trend continue at 2× IP , BP , BT, power?
ST data breaks aspect ratio degeneracy of data set
Wider heat-flux width may offset smaller R  maybe better than tokamak?
Issue: If peak heat flux in divertor region exceeds 10 MW/m2  material damage

## Slide 35: NSTX-U will test ability of radiation and advanced divertors to mitigate very high heat-fluxes
NSTX: reduced heat flux 2-4×via radiation (partial detachment)
Additional null-point in divertor expands field, reduces heat flux
Snowflake/X Divertor
Standard Divertor
NSTX-U has additional coils for up-down symmetric snowflake/X, improved control
NSTX-U peak heat fluxes will be up to 4-8× higher than in NSTX

## Slide 36: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 37
Compact ST-FNSF has no/small central solenoid
IP Start-up/Ramp-up Critical Issue for ST-FNSF/Demo
ST-FNSF Scenarios
IP [MA]
NBI
Time
HHFW
EC/EBW, HI, PF
Solenoid-free
Start-up
high bT, bN, k, disruption avoidance, high H, heat flux mitigation
Current ramp-up and profile control
• Two novel techniques for solenoid-free start-up and ramp-up will be investigated
  RF: ECH/EBW and HHFW
  Helicity Injection
~ 1-2 MA of solenoid-free start-up current needed for FNSF
Notes: ST has been addressing critical issues for FNSF: A compact FNSF facility does not have solenoid. So, the solenoid-free start-up is a critical issue for ST-FNSF. But solenoid-free start-up is attractive for tokamak reactor design as well. Other issues are ramp-up….

## Slide 38
Helicity Injection is efficient method for current initiation
Coaxial Helicity Injection (CHI) concepts being developed
CHI developed on HIT, HIT-II
Transferred to NSTX / NSTX-U
Discharge evolution of 160 kA closed flux current produced by CHI alone in NSTX
R. Raman et al., PRL 2006

## Slide 39: NIMROD simulations  CHI in NSTX has resemblance to 2D Sweet-Parker reconnection
Toroidal electric field generated in injector region by reduction of injector voltage and current
  Etoroidal × Bpoloidal drift brings oppositely directed field lines closer and causes reconnection, generating closed flux
F. Ebrahimi, PoP 2013, PoP 2014
Elongated Sweet-Parker-type current sheet
n > 0 modes / MHD not strongly impacting 2D reconnection
Direction of plasma flows
In Injector Region only
Current
sheet

## Slide 40: CHI current sheet unstable  plasmoids  merging Possible lab observation of plasmoids  contribute to lab-astro
Possible plasmoids during NSTX CHI
F. Ebrahimi , PRL 2015

## Slide 41: Outline
ST Overview and Motivation
NSTX-U Mission and Status
NSTX/NSTX-U Research Highlights
  Global MHD Stability
  Transport and Turbulence
  Energetic Particles
  Power Exhaust
  Plasma Start-up
Brief Overview of NSTX-U Research Plans
Summary

## Slide 42: Brief Overview of FY2016-18 NSTX-U Goals
FY2016
  Obtain first data at 60% higher field/current, 2-3× longer pulse:
    Re-establish sustained low li / high-k operation above no-wall limit
    Study thermal confinement, pedestal structure, SOL widths
    Assess current-drive, fast-ion instabilities from new 2nd NBI
FY2017
  Extend NSTX-U performance to full field, current (1T, 2MA)
    Assess divertor heat flux mitigation, confinement at full parameters
  Access full non-inductive, test small current over-drive
  First data with 2D high-k scattering, prototype high-Z tiles
FY2018
  Assess causes of core electron thermal transport
  Test advanced q profile and rotation profile control
  Assess CHI plasma current start-up performance
  Study low-Z and high-Z impurity transport
    Possibly test/compare pre-filled liquid-Li tiles/PFCs vs. high-Z solid

## Slide 43
New
center-stack
2nd NBI
Li granule injector
High-Z PFC diagnostics
Off-midplane 3D coils (NCC)
up to 1 MA plasma gun
Lower divertor cryo-pump
Upgraded CHI for ~0.5MA
LLD using bakeable cryo-baffle
DBS, PCI, or other intermediate-k
Divertor Prad
Snowflake
Run Weeks:
Five Year Facility Enhancement Plan (green = ongoing)
2015: Engineering design for high-Z tiles, Cryo-Pump, NCC, ECH
MGI disruption mitigation
4 coil AE antenna
HHFW limiter upgrade
Establish control of:
Rotation
Upward
LiTER
High kq
Laser blow-off
Boronization
Enhanced MHD sensors
Neutron collimator
Charged fusion product
Upgraded halo sensors
Pulse-burst MPTS
14-16
10-12
16-18
ne
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
2015 | 2016 | 2017 | 2018 | 2019
Upgrade Outage
1.5  2 MA, 1s  5s
MAPP
42 ch MPTS
48 ch BES
MSE/LIF
FIReTIP
Major enhancements:
Base funding
+15% incremental
Fiscal Year:
12-16
High-Z tile row on lower OBD
dB diag. - incremental
0.5-1 MA CHI
qmin
1 MW ECH/EBW

## Slide 44
NSTX-U will provide many opportunities to study toroidal confinement physics in novel regimes:
  Low aspect ratio, strong shaping, high b, low collisionality
  Access strong fast-ion instability drive, high rotation
  Advanced divertors, high-Z PFCs, lithium walls
NSTX-U/ST results will inform optimal configuration, aspect ratio for next-step PMI, FNSF, Pilot devices
Physics research to begin in Nov/Dec 2015
  Many UW researchers already collaborating on NSTX-U!
Thank you!
Summary
Notes: Here is the outline of this review to give you an overview of the world ST research.

## Slide 45: Backup

## Slide 46
NSTX-U Milestone Schedule for FY2016-18
FY2017
FY2016
18
16
Develop physics + operational tools for high-performance: k, d, b, EF/RWM
Assess H-mode confinement, pedestal, SOL characteristics at higher BT, IP, PNBI
Assess disruption mitigation, initial
tests of real-time warning, prediction
Develop high-non-inductive fraction NBI H-modes for sustainment and ramp-up
Assess fast-wave SOL losses, core thermal and fast ion interactions at increased field and current
Run Weeks:
FES 3 Facility Joint Research Target (JRT)
Integrated Scenarios
Core Science
Boundary Science
+ Particle Control
C-Mod leads JRT
Assess effects of NBI injection on fast-ion f(v) and NBI-CD profile
Assess scaling, mitigation of steady-state, transient heat-fluxes w/ advanced divertor operation at high power density
R17-1
Assess high-Z divertor PFC performance and impact on operating scenarios
R17-2
Assess impurity sources and edge and core impurity transport
R18-1
Assess role of fast-ion driven instabilities versus micro-turbulence in plasma thermal energy transport
IR18-2
Control of current and rotation profiles to improve global stability limits and extend high performance operation
R18-2
Assess transient CHI current start-up potential in NSTX-U
R18-3
Investigation of power and momentum balance for high density and impurity fraction divertor operation
IR18-1
FY2018
16
12
IR17-1
R17-4
R16-1
R16-2
R16-3
Incremental
TBD… possibly something
on energetic particles
DIII-D leads JRT
14
Assess E and local transport and turbulence at low * with full confinement and diagnostic capabilities
R17-3
TBD
NSTX-U leads JRT
Begin ~1 year outage for
major facility enhancement(s) sometime during FY2018
16

## Slide 47: Backup
NSTX Physics Results

## Slide 48
NSTX 121083
unstable
(marginal stability)
unstable
Precession drift resonance stabilization
Bounce/transit resonance stabilization
Plasma evolution
Marginal stability
neff/nexp (marginal stability)
Kinetic RWM theory consistent with RWM destabilization at intermediate plasma rotation; stability altered by collisionality
Destabilization appears between precession drift resonance at low wf, bounce/transit resonance at high wf
Destabilization moves to increased wf as n decreases
gtw contours vs. ν and wf
instability
(experiment)
wf/wfexp (marginal stability)
MISK code
S. Sabbagh, NF 2010
J. Berkery, PRL 2010

## Slide 49: NCC Physics Design completed: Optimization for NTV braking performed with IPEC coupling matrix
NCC and midplane coils can be combined to remove the dominant resonant modes up to the second, giving the optimized NTV for core
  NCC 2x12 provides n=1,2,3,4,6 optimized NTV, and 2x6 provides n=1,2,6
  Optimized NTV can be used to control local torque with minimized resonance
Higher n’s
*Ratio of coil currents (phasing)
*Tmax is based on max. 3kAt
n=1
n=6

## Slide 50: Study of RMP characteristics with NCC extended with TRIP3D (T. Evans, GA) – 2x12 NCC (and 2x7) favorable for RMP
Vacuum Island Overlap Width (VIOW) analysis shows full NCC 1kAt can produce sufficient VIOW in a wide range of q95, but partial NCC needs more currents with low q95 targets
  Also shows 2x7, with “one” more additional array upon partial NCC can provide the greater VIOW by toroidal coupling (n=2,4,9)

## Slide 51: Excellent Agreement between TRANSP and FIDAsim when Using the Same ADAS Ground State Cross Section Tables (2)
The peak of halo neutrals shifts in the same direction as toroidal rotation, as expected
Halo neutral
beam neutral
beam neutral
rotation
halo neutral

## Slide 52: Linear stability analysis of fishbones with M3D-K finds rotation / rotation shear destabilizing at elevated q
Guoyong Fu, Feng Wang
NSTX-U / theory partnership
Eigenfunction broadens with rotation
  Enhanced fast-ion transport or triggering / seeding of tearing modes?
  Next step: investigate with non-linear runs.

## Slide 53: New “kick” model for fast-ion transport predicts different JNB, ion/electron power split, inferred thermal transport

## Slide 54: Major motivation for NSTX/MAST Upgrades: Determine if confinement trend continues, or is like conventional A
Normalized electron collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors

## Slide 55: NSTX achieved 70% “transformer-less” current drive Will NSTX-U achieve 100% as predicted by simulations?
Steady-state operation required for ST, tokamak, or stellarator FNSF
TRANSP Contours of Non-Inductive Fraction
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
H98y2
ITER H-mode confinement scaling multiplier

## Slide 56: Progress in predicting Te using reduced ce models in regimes where single micro-instability is dominant
Reduced model for micro-tearing ce (Rebut-Lallia-Watkins (RLW) - 1988) shows reasonable agreement between predicted & measured Te for r/a > 0.3
  ce >> RLW must be used in core to match central Te - may be due to GAE/CAE
Reduced ETG models in low-b L-modes also show reasonable Te agreement for r/a > 0.3 (not shown)
Linear gyrokinetic simulations find microtearing unstable in mid-radius region of high-collisionality H-modes
  Other micro-instabilities subdominant at this location for this class of discharge
S. Kaye
Micro-tearing
ExB
r/a
r/a
H
i
g
h
n
*
H
-
M
o
d
e
1
2
0
9
6
7
0
.
5
1
s
M
e
a
s
u
r
e
d
P
r
e
d
i
c
t
e
d
0
.
0
0
.
2
0
.
4
0
.
6
0
.
8
1
.
0
0
.
4
0
.
0
T
e
(
k
e
V
)
A
d
-
h
o
c
c
e
2
0
-
3
0
m
2
/
s
(
G
A
E
p
r
o
x
y
)
c
e
(
R
L
W
)
0
.
8

## Slide 57: Strong flow shear can destabilize Kelvin-Helmholtz (K-H) instability in NSTX (Wang, TTF 2014)
K-H instability expected for |MLn/Lw|>1 from linear analytic theory (Catto, 1973; Garbet, 1999)
K-H identified in global electrostatic ITG simulations for NSTX low b L-mode (Ren, 2013)
  Mostly unstable K-H modes have finite k|| (shifted away from nq=m)
K-H/ITG + neoclassical close to experiment ci
  ce underpredicted
  ETG possibly important
GTS code
Nonlinear ETG simulations to be run in FY14-15 to investigate contribution in NSTX L-modes
nq=m

## Slide 58
Collaborating with QUEST to explore CHI + ECH solenoid-free start-up in support of ST-FNSF
Refurbishment of CHI Cap Bank completed.
Fabrication of the CHI gas injection system and operation procedure for the QUEST ST experiment in Japan completed.
Fabrication of the CHI capacitor bank for QUEST is nearing completion.
• Inj. Flux in NSTX-U is about 2.5 times higher than in NSTX
• NSTX-U coil insulation greatly enhanced for higher voltage ~ 3 kV operation
CHI Start-Up
CHI Implementation on QUEST
showing installed electrodes
U. Washington

## Slide 59: Magnum-PSI experiments on high-temperature Li show strongly reduced erosion and stable cloud production
Gross erosion measured spectro-scopically in divertor-like plasma
  Neon plasma reproduces Langmuir Law
  Deuterium suppresses erosion
Reduced gross erosion and strong re-deposition result in 10× longer lifetime of 1 micron coating
  Consistent with Li trapping in pre-sheath
  Pre-sheath scale length consistent with neutral Li emission region (~3mm)
Jaworski, PSI 2014
Neutral Li emission, t=2.5s
Incident Plasma
Target
Abrams, PSI 2014

## Slide 60: Backup
Copper TF ST-FNSF

## Slide 61
High bT enables compact Fusion Nuclear Science Facility (FNSF) with high neutron wall loading
Tokamak
bN = 6
5
4
3
2
Ip/aBT0 (MA/mT)
Toroidal b (%)
ITER
0
20
40
0
4
8
ST-FNSF
Database from START, MAST, PEGASUS, NSTX
Pfusion ∝ p 2 x Vol
Pfusion ∝ bT2 BT04 x Vol
$
Physics limited
Investment & engineering limited
Wn ∝ Pfusion / Area
Wn ∝ bT2 BT04 a (not strongly size dependent)
Wn ~ 1-2 MW/m2 with R ~ 1-2m FNSF feasible!

## Slide 62: ST-FNSF shielding and TBR analyzed with sophisticated 3-D neutronics codes
CAD coupled with MCNP using UW DAGMC code
Fully accurate representation of entire torus
No approximation/simplification involved at any step:
  Internals of two OB DCLL blanket segments modeled in great detail, including:
    FW, side, top/bottom, and back walls, cooling channels, SiC FCI
  2 cm wide assembly gaps between toroidal sectors
  2 cm thick W vertical stabilizing shell between OB blanket segments
  Ports and FS walls for test blanket / materials test modules (TBM/MTM) and NNBI
TBM
LiPb,
cooling channel,
FCI
Heterogeneous OB Blanket Model,
including FW, side/back/top/bottom walls, cooling channels, and SiC FCI
NBI

## Slide 63: Two sizes (R=1.7m, 1m) assessed for shielding, TBR
Parameter:
Major Radius 1.68m 1.0m
Minor Radius 0.95m 0.6m
Fusion Power 162MW 62MW
Wall loading (avg) 1MW/m2 1MW/m2
TF coils 12 10
TBM ports 4 4
MTM ports 1 1
NBI ports 4 3
Plant Lifetime ~20 years
Availability 10-50%
30% avg
6 Full Power Years
(FPY)
Neutron source distribution

## Slide 64: Peak Damage at OB FW and Insulator of Cu Magnets
Peak dpa at OB midplane = 15.5 dpa / FPY
3-D Neutronics Model of Entire Torus
Dose to MgO insulator = 6x109 Gy @ 6 FPY < 1011 Gy limit
Dose to MgO insulator = 2x108 Gy @ 6 FPY < 1011 Gy limit
Peak He production at OB midplane = 174 appm/FPY
He/dpa ratio = 11.2
Center Stack
OB Blanket
R=1.7m configuration

## Slide 65: Mapping of dpa and FW/blanket lifetime (R=1.7 m Device)
dpa / FPY
Peak =
15.5 dpa / FPY
FW/blanket could operate for 6 FPY
if allowable damage limit is 95 dpa
R=1.7m configuration
 Peak EOL Fluence = 11 MWy/m2

## Slide 66: Options to increase TBR > 1
Add to PF coil shield a thin breeding blanket (DTBR ~ +3%)
Smaller opening to divertor to reduce neutron leakage
Uniform OB blanket (1m thick everywhere; no thinning)
Reduce cooling channels and FCIs within blanket (need thermal analysis to confirm)
Thicker IB VV with breeding
Potential for TBR > 1 at R=1.7m
PF Coils

## Slide 67: UW has carried out most advanced and detailed analysis of Dual-Coolant Lead-Lithium (DCLL) blanket for ST-FNSF
No ports or penetrations,
homogeneous breeding zones:
TBR = 1.03
Add 4 Test Blanket
Modules (TBMs)
TBR = 1.02 (DTBR = -0.01)
TBM
LiPb,
cooling channel,
FCI
1 Materials Test Module (MTM)
TBR = 1.01 (DTBR = -0.02)
Ferritic Steel
MTM
4 TBM + 1 MTM + 4 NBI
TBR = 0.97
Approx. DTBR per port:
TBM: -0.25%
MTM: -2.0%
NBI: -0.75%

## Slide 68: R0 = 1m ST-FNSF achieves TBR = 0.88
TBM
NBI
Distribution of T production
MTM
1m device cannot achieve TBR > 1 even with design changes
Solution: purchase ~0.4-0.55kg of T/FPY from outside sources at $30-100k/g of T, costing $12-55M/FPY

## Slide 69: Backup
HTS-ST Pilot Plant Study

## Slide 70: Qeng = Pelectric / Pconsumed is maximized between A = 1.8-2.5 for tokamak using HTS magnets
Assumes fixed major radius R0
Elongation k and bN increase with increasing e=A-1
Assumes no inboard tritium breeding (WC shield only)
Chart: Avg Neutron Fluence [ MWy/m2 ]
| 0.29999999999999993 | 0.39999999999999997 | 0.5 | 0.59999999999999987 | 0.70000000000000007
scan | 0.14131 | 0.6242 | 2.7573 | 12.1799 | 53.8027
Assumes damage fluence limit of 1023 n / m2
0.3m
0.4m
0.5m
0.6m
0.7m
Shield
thickness:
R0 = 2.5m
Result: Want Dshield / R0 < ~20% for Qeng > 1

## Slide 71: HTS-ST Plasma constraints
Fix plasma major radius at R0 = 2.5-3m
  Chosen to be large enough to allow space for HTS neutron shield and access Qeng > 1
Inboard plasma/FW gap = 4cm
Use e dependent k(e), bN (e) (see next slide)
Greenwald fraction = 0.8
q* not constrained
  q* is better e-invariant than q95 for current limit
  Want to operate with q* > 3 to reduce disruptivity
0.5MeV NNBI for heating/CD – fixed PNBI = 50MW
H98y2 adjusted to achieve full non-inductive CD

## Slide 72: Aspect ratio dependence of limits: k(e), bN(e)
NSTX data at low-A (+ NSTX-U and ST-FNSF modelling)
DIII-D and EAST for higher-A
k  1.4 for A  
e = A-1
Profile-optimized no-wall stability limit at fBS ≈ 50%
  Menard PoP 2004
bN  3.1 for A  

## Slide 73: HTS-ST engineering constraints
Magnet constraints (T. Brown ST-HTS Pilot, K-DEMO)
  Maximum stress at TF magnet = 0.67-0.9GPa
  Maximum effective TF current density = 65MA/m2
  OH at small R  higher OH solenoid flux swing for higher A
Shielding / blankets
  Assume HTS fluence limit of 3x1022 - 1023 n/m2
  No/thin inboard blanket, ~1+ m thick outboard blanket
    10x n-shielding factor per 15-16cm WC for HTS TF
    Also 8cm inboard thermal shield + other standard radial builds
Electrical system efficiency assumptions:
  30% wall plug efficiency for H&CD - typical of NNBI
  45% thermal conversion efficiency - typical of DCLL
    Also include pumping, controls, other sub-systems
    See Pilot Plant NF 2011 paper for more details

## Slide 74: Selection of HTS-ST device performance goals
Decided w/ CCFE + UW for HTS-ST to have goals of:
  6MWy/m2 neutron wall loading (peak) at outboard midplane AND Qeng ~ 1 – similar to previous PPPL Pilot Plant Study
  Assume n-radiation damage limit of 3-4 × 1022/m2
    HTS already tested to this damage fluence range (see next slide)
   WC shield thickness ~ 60cm, D/R = 0.2  R0 = 3m
With only outboard breeding, optimal A ~ 2.1-2.4
But, for TBR ~ 1 probably need A ≤ 2  chose A=2
Chosen design point (so far):
  R=3m, BT = 4T, A=2, k=2.5, bN = 4.2 (~no-wall limit)
  H98y2 ~ 1.7, HPetty ~ 1.2-1.3, HST ~ 0.7, Pfusion ~ 500-600MW
  80% Greenwald fraction, 50MW of 0.5-0.7 MeV NNBI
  IP = 12MA, double-swing of small OH provides ~ 2-3MA

## Slide 76: Long-leg divertor aids heat flux reduction in HTS-ST
lq ~ 1mm, assume S ≈ lq (closed divertor)
(T. Eich NF 2013)
(Partial) detachment likely reduces peak q by further factor of 2-4

## Slide 77: Can also exhaust onto back of OB blanket (like vertical target in conventional divertor)
lq ~ 1mm, assume S ≈ lq (closed divertor)
(T. Eich NF 2013)
(Partial) detachment likely reduces peak q by further factor of 2-4

## Slide 78
OH located inside of TF bore: 854 Mpa Tresca stress with 4.0 B0 and 176.5 TF Bmax
For AR 2 device:
OH flux: 2 Vs with 70 Jc solenoid and 19.8 T
Added space between OH and TF
60 cm WC uses VV shield and shield in front of it.
T. Brown radial build (includes small OH)

## Slide 79
TF and OH magnet parameters vs. aspect ratio
using models from Brown and Zhai

## Slide 80
Latest HTS-ST: R=3m, A=2, Pfusion~ 500MW, Qeng~1-1.5

## Slide 81
OB blanket module with divertor + extended blanket at top/bottom fits through vertical ports
Potential advantages of this low-A configuration:
  Reduced part count + no inboard breeding  simplified maintenance (?)
But, very likely need to breed at top + bottom (included)
  UW will assess TBR for DCLL
  Analysis similar to Cu ST-FNSF
Breeding
regions
Initiating study of LM/Li wall and divertor compatibility with this HTS configuration