## Slide 1
Introduction to the:
National Spherical Torus eXperiment - Upgrade
(NSTX-U)
Jon Menard, PPPL
NSTX-U Program Director
March 27, 2015
NSTX-U
Supported by

## Slide 2: Aspect ratio is important geometric parameter for toroidal fusion devices
Spherical torus/tokamak (ST) has A = 1.1 - 2
Conventional tokamak typically A = 3 - 4
Aspect ratio A = R / a
a
R
R = major radius a = minor radius

## Slide 3: STs have higher natural “elongation”
Higher elongation improves stability & confinement
Elongation k = b / a
b = vertical ½ height a = minor radius
a
b

## Slide 4
A ~ 3
k = 1.5-2
bT = 3-10%
A ~ 1.5
k = 2-3
bT = 10-40%
Tokamak
ST
Magnetic field structure of ST increases
normalized pressure by factor of 3-4×
Normalized pressure: b = p / (B2/2m0) Pfusion  b2 B4
Plasma spends less time in unstable “bad” curvature region
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 5
  High b, shaping, rotation extend stability, transport knowledge
  NBI fast-ions in present STs mimic ITER DT fusion products  study burning plasma science
  STs can more easily study electron-scale turbulence at high temperature  important for all toroidal configurations
Low aspect ratio / ST extends predictive capability for ITER and toroidal science
Burning Plasma Physics - ITER

## Slide 6
Design studies show ST potentially attractive
as “Fusion Nuclear Science Facility” (FNSF)
FNSF: Qualify fusion reactor components in device much smaller than reactor
High neutron wall loading
Modular, maintainable
Can be tritium self-sufficient
  Requires sufficiently large size
PPPL ST-FNSF concept

## Slide 7
NSTX Upgrade: Two major new components
Will be most capable ST in world program
New 2nd NBI
Present NBI
~5-10× increase in nTt
NSTX-U average plasma pressure ~ tokamaks
New center-stack:
  2×toroidal field (0.51T)
  2×plasma current (12MA)
  5×pulse-length (15s)
2nd more tangential neutral beam injector (NBI):
  2×current drive efficiency
  2×heating power (510MW)
TF OD = 40cm
Previous
center-stack
TF OD = 20cm
New
center-stack

## Slide 8: Steady-state tokamak / ST must drive plasma current without transformer
External: wave and beam current drive
Self-generated: high pressure plasmas make “bootstrap” current
Efficient tokamak power plant will need 70-90% self-generated current
Question: Can NSTX-U operate without using transformer?
NSTX: 70% transformer-less current drive NSTX-U: project 100%

## Slide 9: STs observe confinement increases at higher Te (!) Will confinement trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Question: Which instabilities cause electron energy transport?
Normalized energy confinement
BtE [T-s]

## Slide 10: NSTX-U wall heat fluxes ~4× higher than NSTX Near/above ITER values (40MW/m2 unmitigated – 4× engineering limits)
Expand / lengthen exhaust channel
Spread heat using radiative “cushion”
Liquid metal walls
Combinations?
Snowflake/X Divertor
Standard Divertor
Question: What are viable ways to protect reactor walls?

## Slide 11: New Center-Stack installed in NSTX-U (!) Vacuum pump-down achieved in January, 2015

## Slide 12
Relocated 2nd NBI beam line box from TFTR
Beam Box being
lifted over NSTX-U
Beam Box placed in its final location & aligned
Beam Box being populated with components

## Slide 13
New 2nd NBI
1st NBI
NSTX Upgrade Project nearly complete
Test plasmas expected in April, research plasmas in June

## Slide 14: There are many great research opportunities on NSTX-U!
Thank you!
Any questions?