## Slide 1: Motivations for Spherical Torus research and initial results from NSTX Upgrade
Jonathan Menard (PPPL)
Thanks to many contributions from
ST community and NSTX-U Researchers
PPPL – MBG Auditorium
January 11, 2017

## Slide 2: Outline
Introduction
Why spherical tori / tokamaks (STs)
NSTX-U initial results, long-term directions
Summary

## Slide 3: Why fusion?
D: deuterium
T: tritium
n: neutron
a: helium
E = mc2
“D-T” fusion reaction:
High energy gain ≈ 1000 ×
No runaway reactions
Abundant fuel supply
Waste short-lived, low-level
No CO2 production

## Slide 4: Fusion requires very high temperatures
Fusion is easiest here at 200 million ᵒC (!!) (350 million ᵒF)
  Requires lowest pressure nT and energy confinement time tE
  Minimum fusion “triple-product” value: 8 atmosphere-seconds
Fusion difficulty
(pressure × confinement)

## Slide 5: Magnetic fusion has already achieved the necessary very high temperatures!
~250 million C
TFTR at PPPL (1990’s)
core
boundary

## Slide 6: Magnetic fusion is arguably closest to ultimate goal of electricity generation
Ryan Hamerly (Stanford)
Gravitational confinement fusion requires large device
  Need 7-8% of mass of our sun
  Approximately 10× diameter of Earth
Laser fusion ala NIF at best has Efusion / Eelectrical ~ 5%
  So far, 0.006% efficient
Magnetic fusion in ITER:
  Goal: 500MW fusion power for
  ≤ 600MW electrical input for 400s
  Industrial levels of fusion power
~25kJ fusion yield achieved

## Slide 7: Tokamaks and stellarators are the leading configurations in magnetic fusion
Stellarator advantages:
  No plasma current drive necessary
  More stable, steady-state
Disadvantages:
  More complex coils and exhaust
  Confinement < tokamaks (so far…)
Superconducting tokamak
Superconducting stellarator
Tokamak advantages:
  Best confinement, closest to “breakeven”
  Simpler planar coils and power/particle exhaust
Disadvantages:
  Must drive multi-mega-ampere plasma current
  More prone to rapid loss of plasma = “disruption”
    Potential show-stopper for tokamak power-plant
KSTAR (South Korea)
W7-X (Germany) – 1st run campaign in 2016

## Slide 8
ITER will be first device to access “burning plasma”
Burning plasma: majority of plasma heating power comes from fusion alpha particles from DT reactions
  DT reaction energy split: 1/5 in alphas, 4/5 in neutrons
ITER goal Q = Pfusion / Pexternal heating = 10
Q = 10  Palpha / Pexternal = 2
Palpha / Palpha + external = 2 / 3 > 50%
A=3.1, R=6.2m, BT=5.3T, IP=15MA
ITER under construction in Cadarache, France

## Slide 9: ITER magnets will be largest ever built
18 toroidal field magnets
12 Tesla at coil
Weight: 6500 tons
80,000 km of Nb3Sn superconducting strand in total length
Toroidal field current
165 million amps
Plasma current:
15 million amps
These are large numbers

## Slide 10: Perspective
Studying burning plasmas is essential to fusion development, and ITER is presently the best approach
But as we look beyond plasma self-heating toward economical electricity production, how might we improve?

## Slide 11: Assuming cost  size  need higher fusion power / volume = high fusion power density
Fusion power density  (plasma pressure)2
b  plasma pressure / magnetic pressure = p/(B2/2m0)
Maximum b limited by MHD instabilities
B limited by magnet stress, cooling, quench
Fusion power density  b2 B4
Maximize / optimize this product

## Slide 12: Aspect ratio is important free parameter
Spherical torus/tokamak (ST) has A = 1.1-2
Conventional tokamak typically A = 2.5-4
Aspect ratio A = R / a
a
R
R = major radius a = minor radius

## Slide 13: STs have higher natural elongation
Higher elongation improves stability, confinement
Elongation k = b / a
b = vertical ½ height a = minor radius
a
b

## Slide 14
A ~ 2.5-4
k = 1.5-2
bT = 3-10%
A ~ 1.3-2
k = 2-3
bT = 10-40%
Tokamak
ST
Favorable average curvature improves stability
Toroidal beta bT = p / (BT02/2m0)
Aspect Ratio A = R /a
Elongation k = b/a
Plasma spends less time in unstable curvature region
Notes: A spherical tokamak is a low aspect ratio tokamak. Tokamak is a donut like aspect ratio of about 3 where as ST is aspect ratio of about 1.5. As the aspect ratio is reduced, the hole of the donut is reduced and it disappears entirely at A = 1. As the aspect ratio is reduced, the plasma elongate naturally takes on the spherical shape due to self fields. Another important property is the magnetic field line. The tokamak magnetic field line goes around torus at relatively constant pitch where as the ST geometry, the field line transit the outboard unstable region quickly but spend many toroidal transits in the inboard stable region. This makes ST plasma stable for high beta and also makes the edge safety factor high ~ 10 compared to ~ 3 for tokamak.
As a result, there are a number of new unique physics regimes which can be accessed at low aspect ratio, which can be utilized to enhance the understanding of toroidal confinement physics and improve predictive capabilities for ITER and future fusion facilities.

## Slide 15: STs can access very wide range of bT
120
100
80
40
20
0
bT (%)
60
10
5
0
IN = IP / aBT
15
bT for sustained, low-ℓi, high-k, LHI-driven plasmas
Pegasus ST recently accessed bt ~ 50-100%
Notes: TO SAY:
I’m showing a sample magnetic reconstruction here on the left hand side which uses these kinetic constraints, here for a plasma current of 0.1 MA and toroidal field of 25 mT.
These plasmas are highly elongated, and have an extremely low li. For this case, we obtain a toroidal beta of 95%.
On the right hand side I’m showing a Troyon plot, a scatter plot of toroidal beta versus normalized plasma current. Operating spaces of several other tokamaks are shown as shaded regions, and updated Pegasus discharges are highlight as individual points. I should mention that the filled-in symbols represent beta-values obtained directly from kinetically-constrained equilibrium reconstructions. The empty symbols are magnetics-only reconstructions that have been calibrated based on the constrained results.
We note that some of the highest beta values come directly from kinetically-constrained equilibria.
I should also point out, too, that all of these discharges used zero Ohmic drive. Every Pegasus plasma on this plot was produced using solely Local Helicity Injection.
TO DO:
- Get list / have list on hand of caveats from Ray’s IAEA talk…

## Slide 16: Why explore spherical torus/tokamak?
Potentially attractive for electricity production
  Requires accompanying magnet innovations
High neutron wall loading in small device
  Well suited for fusion nuclear component R&D
Improve toroidal physics predictive capability
  High b and high temperature at low collisionality
  Understand confinement, fast-ion physics for ITER

## Slide 17: Why explore spherical torus/tokamak?
Potentially attractive for electricity production
  Requires accompanying magnet innovations
High neutron wall loading in small device
  Well suited for fusion nuclear component R&D
Improve toroidal physics predictive capability
  High b and high temperature at low collisionality
  Understand confinement, fast-ion physics for ITER

## Slide 18: How would magnetic fusion make electricity?
Spin turbines, generate electricity
Steam or hot helium
Magnets
(-270 - 100ᵒC)
Heat
Blanket
(350 - 1000ᵒC)
helium and deuterium exhaust
Tritium bred from lithium in blanket
External heating
(10’s of MW)
Plasma
(100 million ᵒC)
a self heating
Neutrons

## Slide 19: Electricity gain Qeng determined primarily by engineering efficiencies and fusion gain
  Parameter Assumptions:
    Mn = 1.1, Ppump = 0.03×Pth
    Psub + Pcontrol = 0.04×Pth
    haux = 0.3
    hCD = ICDR0ne/PCD  0.3×1020A/W/m2
For more details see J. Menard, et al., Nucl. Fusion 51 (2011) 103014
th  thermal power conversion efficiency
aux  injected power wall plug efficiency
Q  Pfus / Paux = fusion power / auxiliary power
Qeng 
Electricity produced
Electricity consumed
=
Qeng = hth haux Q ×

## Slide 20: Gain is very strong function of confinement: QDT  H25 from low  high gain
Fix current, field, density, geometry, auxiliary power, aP = 0.7:
QDT ≤1  QDT  Q*DT  H2 QDT >>1  QDT  Q*DT2.5  H5
e  A-1

## Slide 21: Gain vs. physics & engineering constraints
Steady-state tokamaks: current-driven kink limit less relevant
Normalized b (bN) and “bootstrap” fraction (fBS) more important
Relevant variables are bN / fBS and normalized density fgw 
Use electrostatic gyro-Bohm tE scaling with no b degradation (NSTX, JET, DIII-D)
C. Petty, et al., Phys. Plasmas 15 (2008) 080501
External current drive fraction
Need to optimize this product vs. aspect ratio

## Slide 22: High temperature superconductors (HTS) could substantially expand fusion magnet performance
HTS
Applied Magnetic Field (T)
http://magnet.fsu.edu/~lee/plot/plot.htm
LTS
Current Density
ITER CS
ARC (MIT)

## Slide 23: Cables formed from HTS tapes achieving high winding pack current density at high B
10 mm
10 mm
6 mm
7 kA CORC (4.2K, 19 T) cable
Base cable: 50 tapes YBCO Tapes with 38 mm substrate (Van Der Laan, HTS4Fusion, 2015)
Higher Jcable HTS cable concepts under development:
Base Conductor
He Gas Cooled
8kA,
JWP ~ 160MA/m2
7 mm
SS conductor jacket for strength
7 mm
Copper
Conductor on Round Core Cables (CORC)
JWP ~ 70MA/m2 19T

## Slide 24: High current density HTS cable motivates consideration of lower-A tokamak pilot plants
ITER-like TF magnets:
  JWP=20MA/m2, Bmax ≤ 12T
  Pfusion ≤ 130MW, Pnet < -90MW
JWP ~ 30MA/m2, Bmax ≤ 19T
  Pfusion ~ 400MW
  Small Pnet at A=2.2-3.5
JWP ≥ 70MA/m2,Bmax ≤ 19T
  Pfusion ~500-600MW
  Pnet = 80-100MW at A=1.9-2.3
A ~ 2 attractive at high JWP
Chart: Pnet [MWe]
| 1.6 | 1.7 | 1.8 | 1.9 | 2 | 2.1 | 2.25 | 2.5 | 2.75 | 3 | 3.5 | 4
0.3 | -42.5779 | 36.6802 | 100.5919 | 110.8791 | 110.5433 | 103.3192 | 95.5508 | 81.2005 | 65.435 | 45.4267 | 5.1489 | -28.8353
0.4 | -72.7603 | -5.8829 | 57.8131 | 79.5166 | 90.225 | 92.7252 | 95.2754 | 81.181 | 65.4314 | 45.4256 | 5.1487 | -28.8353
0.5 | -125.2658 | -73.5657 | 5.2089 | 25.8632 | 37.2943 | 41.5085 | 49.304 | 57.3246 | 59.7178 | 45.4267 | 5.1489 | -28.8353
0.6 | -138.5857 | -118.0805 | -81.9554 | -56.7195 | -34.8841 | -17.8912 | 11.4901 | 26.6647 | 30.4871 | 25.6367 | 4.5439 | -28.8353
0.7 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -87.7336 | -74.4052 | -66.6135 | -63.162 | -68.8654
20 | -144.7239 | -139.4112 | -129.7223 | -122.6517 | -116.3479 | -111.3445 | -102.4945 | -91.1684 | -96.1049 | -102.0119 | -113.118 | -121.7794
JWP [MA/m2]
(12T)
Fix plasma major radius R0=3m, heating power PNNBI=50MW

## Slide 25: A = 1.8-2.3 maximizes TF magnet utilization, and TF will be significant fraction of core cost
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:
JWP = 70MA/m2
A=4 utilization ~1/3-1/2 of max at low A
Optimal range

## Slide 26: A ≥ 3 maximizes blanket volume utilization
JWP = 70MA/m2
0.3m
0.4m
0.5m
0.6m
0.7m
Eff. shield
thickness:
Which components - magnets, blankets, ... dominate cost ?
Costing of these (never-been-built) objects has large uncertainty

## Slide 27
A=2, R0 = 3m HTS-TF FNSF / Pilot Plant
BT = 4T, IP = 12.5MA
k = 2.5, d = 0.55
bN = 4.2, bT = 9%
H98 = 1.8, HPetty-08 = 1.3
fgw = 0.80, fBS = 0.76
Startup IP (OH) ~ 2MA
JWP = 70MA/m2
BT-max = 17.5T
No joints in TF
Vertical maintenance
Pfusion = 520 MW
PNBI = 50 MW, ENBI = 0.5MeV
QDT = 10.4
Qeng = 1.35
Pnet = 73 MW
Wn = 1.3 MW/m2
Peak n-flux = 2.4 MW/m2
Peak n-fluence = 7 MWy/m2
Cryostat volume ~ 1/3 of ITER

## Slide 28: Why explore spherical torus/tokamak?
Potentially attractive for electricity production
  Requires accompanying magnet innovations
High neutron wall loading in small device
  Well suited for fusion nuclear component R&D
Improve toroidal physics predictive capability
  High b and high temperature at low collisionality
  Understand confinement, fast-ion physics for ITER

## Slide 29
Fusion technology development is major challenge
Fusion Nuclear Science Facility (FNSF) could aid development
Without R&D, fusion components could fail prematurely, requiring long repair/down time.
This would cripple power plant operation
FNSF can help develop reliable fusion components
Such FNSF facilities must be: modest cost, low T, reliable
Need to develop reliable and qualified nuclear components unique to fusion:
Divertor and plasma facing components
Blanket and first wall
Vacuum vessel and shielding
Tritium fuel cycle
Remote maintenance
ST-FNSF
Y.-K.M. Peng (ORNL)

## Slide 30
Design studies show ST potentially attractive as FNSF
Projected to access high neutron wall loading at moderate R, Pfusion
  Wn ~ 1-2 MW/m2
  Pfus ~ 50-200MW
  R ~ 0.8-1.8m
Modular design, maintenance
Tritium breeding ratio (TBR) near 1
  Requires sufficiently large R
  Careful layout / design
PPPL ST-FNSF concept

## Slide 31: R ≥ 1.7m necessary for net breeding at A=1.7
R=1.7m: TBR ≥ 1
R=1.0m: TBR < 1 (≈ 0.9)
TBM
NBI
MTM
TBM
MTM
NBI
Need to purchase Tritium from outside sources:
  $12-55M / full power year (FPY)
TBM = Test Blanket Module
MTM = Materials Testing Module

## Slide 32: Why explore spherical torus/tokamak?
Potentially attractive for electricity production
  Requires accompanying magnet innovations
High neutron wall loading in small device
  Well suited for fusion nuclear component R&D
Improve toroidal physics predictive capability
  High b and high temperature at low collisionality
  Understand confinement, fast-ion physics for ITER

## Slide 33
NSTX Upgrade Device and Test Cell – Aerial View

## Slide 34: NSTX Upgrade will access new physics with 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 35: NSTX / MAST confinement increased at higher Te (!) Will confinement trend continue, or look like conventional A?
Normalized electron collisionality ne*  ne / Te2
ITER-like scaling
ST-FNSF
?
constant q, b, r*
NSTX Upgrade
NSTX
Favorable confinement results could lead to more compact ST reactors
Low n*  need higher plasma current, toroidal field, heating power, density control

## Slide 36: NSTX achieved 70% “transformer-less” current drive Will NSTX-U achieve 100% as predicted by simulations?
Steady-state operation required for ST, tokamak, or stellarator FNSF
TRANSP Contours of Non-Inductive Fraction
IP=1 MA, BT=1.0 T, PNBI=12.6 MW
H98y2
ITER H-mode confinement scaling multiplier

## Slide 37: NBI-heated STs excellent testbed for -particle physics
NSTX-U: large fast-ion dynamic range spanning ST and conventional A
  Toroidal field 2× NSTX  Vfast < VA  stabilize modes
  Tangential 2nd NBI  very flexible fast-ion distribution
    Vary pitch angle, pressure profile
Can we find TAE-quiescent, high-performance regimes in NSTX-U?
And predict fast-ion confinement for ITER scenarios?

## Slide 38: All modern tokamaks / STs use a “divertor” to control where power and particles are exhausted
Power / particles contact target plates here
Power exhaust width outside main plasma can be very narrow (few mm)

## Slide 39
Tokamak + ST data: power exhaust width varies as 1 / Bpoloidal
Will previous ST trend continue at 2× IP , BP , BT, power?
ST data breaks aspect ratio degeneracy of data set
Wider heat-flux width may offset smaller R  maybe better than tokamak
Issue: If peak heat flux in divertor region exceeds ~10 MW/m2  material damage

## Slide 40: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet
Performance goals:

## Slide 41: Outline
Introduction
Why spherical tori / tokamaks (STs)
NSTX-U initial results, long-term directions
Summary

## Slide 42: NSTX-U had scientifically productive 1st year
Achieved H-mode on 8th day of 10 weeks of operation
Surpassed magnetic field and pulse-duration of NSTX
Matched best NSTX H-mode performance at ~1MA
Identified and corrected dominant error fields
Commissioned all magnetic and kinetic profile diagnostics
Injected up to 12MW NBI power into armor by end of run
Discovered new 2nd NBI modifies several fast-ion modes
Implemented techniques for controlled plasma shut down, disruption detection, commissioned new tools for mitigation
2016 run ended prematurely due to fault in divertor PF coil
  Coil forensics, Extent of Condition  new coil fab, other repairs
  Aim to resume plasma operation during 2018 – but timing still TBD

## Slide 43: NSTX-U has surpassed maximum pulse duration and magnetic field of NSTX
Compare similar NSTX / NSTX-U Boronized L-modes, PNBI=1MW
NSTX-U L-mode duration
exceeds longest NSTX H-mode
4x longer
NSTX-U BT > highest NSTX BT

## Slide 44: Accessed high elongation k using progressively earlier H-mode and heating + optimized EFC
L-mode flattop
H-mode flattop
NSTX-U (5 run weeks)
NSTX (10 years)
Future goal
Goal: Internal inductance li = 0.5-0.7  k = 2.4-2.7

## Slide 45: Recovered ~1MA H-modes with performance comparable to best NSTX plasmas at similar current
H98 ≥ 1, βN ~ 3.5-4 ≥ n=1 no-wall limit
202946 – no EFC 204112 – EFC v2
203679 – EFC v1 204118 – EFC v2

## Slide 46: H-mode confinement > ITER scaling, consistent with ST scaling (so far) – need higher IP, BT to test

## Slide 47: Fast-ion confinement measured to be at / near predicted values at low total NBI power ~1-2MW
Good agreement between neutron measurement and TRANSP prediction
Need small anomalous fast ion diffusivity (Daf=0.3m2/s) for agreement
Neutron rate
ENBI = 85keV
ENBI = 65keV

## Slide 48: New: Most tangential NBI generates counter-propagating Toroidal Alfvén Eigenmodes (TAEs)
Counter-propagating TAE predicted for hollow fast-ion profiles
H.V. Wong, H. Berk, Phys. Lett. A 251 (1999) 126.
TRANSP: As current builds up beam fast-ion beta profile predicted to become hollow
1st evidence of off-axis NBI in NSTX-U

## Slide 49: New: Tangential 2nd neutral beam suppresses Global Alfven Eigenmode (GAE) – consistent with simulation
t ci
HYM code simulation of #204707, n=10
|dBn |2
t=0.44s
t=0.47s
New 2nd NBI already powerful tool for fast-ion mode physics
HYM code: growth of n=10 counter-GAE from 1st NBI
HYM: suppression of n=10 counter-GAE by 2nd NBI
Most unstable n-number, mode w consistent with HYM

## Slide 50: Goals for future NSTX-U operation
Increase field to 0.8-1T, current to 1.6-2MA, extend flat-top duration (H-mode) to 2-5s
Assess global stability, energy confinement, pedestal height/structure, edge heat-flux width
Characterize 2nd beam: heating, current drive, torque / rotation profiles, fast-ion instabilities
Push toward full non-inductive current drive
Test advanced divertor heat flux mitigation

## Slide 51: STs leading advanced divertor development NSTX-U / MAST-U will collaborate on 1st plasma, scenarios, divertors
MAST-U will test range of divertors:
  Conventional, snowflake (not shown)
  Long-leg “Super-X” with variable flaring
E. Havlickova, et al., Plasma Phys. Control. Fusion 56 (2014) 075008
NSTX-U: Flared divertor using “snowflake/X” + radiation
New PF coils in NSTX-U central magnet

## Slide 52: STs investigating lithium (solid and liquid) walls to significantly increase energy confinement
NSTX (wider  higher pedestals)
D.P. Boyle, et al., J. Nucl. Mater. 438 (2013) S979
H98~1
H = 2-4 × ITER98P(y,2)
J.C. Schmitt, et al., Phys. Plasmas 22 (2015) 056112
LTX (flatter  higher T profiles)
H = 0.8  1.4 × ITER98P(y,2)

## Slide 53: NSTX-U long-term goals
5 year: Integrate high confinement + T + full non-inductive
10 year: Assess compatibility with high-Z & liquid Li PFCs
B+C BN
Li High-Z
High-Z tile row
Flowing LM module? + heatable (?) high-Z walls
Possible progression of in-vessel / plasma-facing components:
C walls + Li coatings on bottom ½ of wall
Add divertor cryo-pump
+ full-wall Li coatings
Heatable C high-Z
for liquid Li divertor
or
LTX-like
Lower n*
Near-term

## Slide 54: Summary
STs broaden our understanding of toroidal physics and enhance predictive capability for ITER & beyond
ST potentially attractive as FNSF and Pilot Plant
NSTX-U designed to be highest performance ST in world program - this is why the project is challenging
Team is working very hard to ensure NSTX-U can run reliably at high performance & get back into operation!

## Slide 55: Thank you!
Any questions?