## Slide 1: CAE-KAW coupling potentially important channel for energy transport from plasma core but coupling not yet experimentally observed – perform expt on DIII-D to identify and quantify
CAE-KAW coupling (mode conversion) predicted by HYM simulations: (not including bulk kinetic effects)
  CAEs destabilized by beams => radiate energy to edge => mode convert to KAW & dissipate energy
  Energy channel not in TRANSP: beam energy diverted from core heating to edge heating
DIII-D represents experimental opportunity to detect coupling
  validate HYM simulation
CAEs documented in DIII-D in low and high field plasmas
Multiple diagnostics sensitive to KAW (, including bulk kinetic effects, at 1T):
  Doppler Backscattering: f < 10 MHz
  Phase contrast imaging: , f < 10 MHz
Ingredients for identification of CAE-KAW coupling:
  Distinguish detection of scattering from interferometer effect
  Detection of scattering should be radially localized where => establish via profile modification or steering of diagnostic (DBS)