| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: HHFW Heating of Low Te(0), Ip Plasmas |
| OP-XP-920 | Revision: 0 | Effective Date: (Approval date unless otherwise stipulated) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Responsible Author: G. Taylor | Date |
| ATI – ET Group Leader: G.Taylor/D. Mueller | Date |
| RLM - Run Coordinator: R. Raman | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

| TITLE: HHFW Heating of Low Te(0), Ip Plasmas | No. OP-XP-920 |
| --- | --- |
| AUTHORS: G. Taylor, J.C. Hosea, C. Kessel, B.P. LeBlanc, D. Mueller, C.K. Phillips, R. Raman, P.M. Ryan | DATE: May 12, 2009 |

# 1.	Overview of planned experiment

This experiment tests HHFW heating of low Ip plasmas as a precursor to studying HHFW-assisted Ip ramp-up in the Solenoid-Free Start-up Topical Science Group. The experiment will use the new HHFW double-feed antenna and the increased lithium conditioning coverage available in 2009 to improve on previous HHFW electron heating results obtained with low Ip and Te(0) plasmas. The goal of the experiment is to couple  ~ 3 MW of kf = -8 m-1 and -14 m-1 HHFW power into a deuterium plasma with Ip ≤ 200 kA.

# 2.	Theoretical/ empirical justification

A major goal of the 30 MHz HHFW program on the NSTX is to generate bootstrap current overdrive during non-inductive Ip ramp-up. TSC Ip ramp-up simulations predict that coupling 6 MW of HHFW power into the Ip ramp-up can result in bootstrap current overdrive. 85% bootstrap current fraction was achieved in XP-521 by coupling 2.5 MW of -14 m-1 HHFW power into an Ip = 250 kA deuterium plasma. The goal of this experiment is to couple HHFW power into plasmas with Ip ≤ 200 kA. HHFW-assisted Ip ramp-up experiments have recently benefited from lithium wall conditioning, which reduces the edge density, improving HHFW heating efficiency. Last year XP-817 successfully coupled HHFW power, with kf = - 8 m-1 current drive phasing, into lithium-conditioned deuterium plasmas. 550 kW of RF power coupled after the initiation of a CHI start-up plasma increased Te(0) from 3 to 15 eV when 
ne(0) ~ 4 x 1018m-3 and Ip ~ 100 kA. Also, 1.1 MW coupled into the early phase of the Ohmically-heated Ip ramp-up, when Ip was ramping from 100 kA to 300 kA, increased Te(0) from 140 to 700 eV, when ne(0) ~ 6-9 x1018m-3. HHFW low Ip experiments in 2009 will benefit from the recent HHFW antenna upgrade from single-end fed straps to double-end fed straps, which should provide higher power than was previously achieved, as well as allowing coupling of HHFW power during a wider range of plasma edge conditions.

# 3.	Experimental run plan

This experiment should take one run day to complete, although considerable effort may be needed to develop a plasma with Ip < 200 kA.

Before starting the experiment the rtEFIT control should be setup to operate at low Ip, with Ipmin set to 
150 kA (D. Gates)

1. Setup 600 ms Ip flattop plasma, similar to 123712 (BT = 5.5 kG, deuterium), but with Ip = 200 kA, instead of 300 kA. Adjust outer gap to be 5-10 cm and introduce lithium at 20 mg/min and adjust evaporation rate as necessary later. (5 shots)

2. If the Ip = 200 kA plasma is stable add kf = -8 m-1 HHFW power, coupled from 100 – 600 ms. Increase RF power to ~ 3 MW. Adjust lithium evaporation rate, gas injection rate and outer gap to optimize HHFW heating efficiency. (5 shots)

3. Repeat (2) with kf = -14 m-1 HHFW heating. (5 shots)

4. If the 200 kA HHFW experiments are successful reduce Ip < 200 kA, and as close to Ip = 150 kA as possible while still maintaining plasma position control so that the outer gap is 5-10 cm. (5-10 shots)

5. Add kf = -8 m HHFW power, coupled from 100 – 600 ms. Increase power to ~ 3 MW. (5 shots)

6. Repeat (4) with kf =  -14 m-1 HHFW heating. (5 shots)

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

This experiment should follow HHFW conditioning and higher power HHFW experiments XP-944 and XP-946. This experiment needs rtEFIT isoflux control for the outer gap. An NBI blip from source A @ 90 keV should be added for CHERS data acquisition from 580 to 600 ms.

This experiment requires stable and reproducible plasmas at very low flattop plasma currents (Ip ~ 150-250 kA) with rtEFIT control. Reliable HHFW operation up to 3 MW at 14 m-1 and 8 m-1 is also required. Thomson scattering data are required for core and edge electron heating data. For analysis of edge power loss and coupling efficiency the experiment requires SOL reflectometry and edge ion heating data from edge rotation diagnostic, and Thomson scattering edge Te and ne data.

# 5.	Planned analysis

Planned analysis includes analysis of heating efficiency at kf = -8 m-1  and -14 m-1, TRANSP and GENRAY/CQL3D modeling.

# 6.	Planned publication of results

The results will be submitted for publication.

PHYSICS OPERATIONS REQUEST

| TITLE: HHFW Heating of Low Te(0), Ip Plasmas | No. OP-XP-920 |
| --- | --- |
| AUTHORS: G. Taylor, J.C. Hosea, C. Kessel, B.P. LeBlanc, D. Mueller, C.K. Phillips, R. Raman, P.M. Ryan | DATE: May 12, 2009 |

(use additional sheets and attach waveform diagrams if necessary)

Describe briefly the most important plasma conditions required for the experiment: Ip as low as possible, preferable Ip < 200 kA. Stable, reproducible plasma with outer gap = 0.05 – 0.1 m. Request D. Mueller and/or Dave Gates as operator for low Ip operation.

Previous shot(s) which can be repeated: Previous shot(s) which can be modified: 123712

Machine conditions (specify ranges as appropriate, strike out inapplicable cases) ITF (kA): 66 Flattop start/stop (s): 0/0.7 IP (MA): 0.15-0.3 Flattop start/stop (s): 0/0.6 Configuration: LSN Equilibrium Control: Outer gap / Isoflux (rtEFIT) Outer gap (m): 0.05-0.1 Inner gap (m): Z position (m): 0.0 Elongation : Upper/lower triangularity : Gas Species: D Injector(s): Gas programming should be similar to shot 123712 NBI Species: D Voltage (kV) A: 90 B: C: Duration (s): 20 ms ICRF Power (MW): ≤ 3.0 Phase between straps (°): -90, 180 Duration (s): 0.075-0.6 CHI: Off Bank capacitance (mF): LITERs: On Total deposition rate (mg/min): 20 mg/min to start, adjust as needed EFC coils: Off Configuration: Odd / Even / Other (attach detailed sheet)

DIAGNOSTIC CHECKLIST

| TITLE: HHFW Heating of Low Te(0), Ip Plasmas | No. OP-XP-920 |
| --- | --- |
| AUTHORS: G. Taylor, J.C. Hosea, C. Kessel, B.P. LeBlanc, D. Mueller, C.K. Phillips, R. Raman, P.M. Ryan | DATE: May 12, 2009 |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| Bolometer – tangential array | √ |  |
| Bolometer – divertor | √ |  |
| CHERS – toroidal | √ |  |
| CHERS – poloidal | √ |  |
| Divertor fast camera | √ |  |
| Dust detector |  |  |
| EBW radiometers |  |  |
| Edge deposition monitors |  |  |
| Edge neutral density diag. |  | √ |
| Edge pressure gauges |  | √ |
| Edge rotation diagnostic | √ |  |
| Fast ion D_alpha - FIDA |  |  |
| Fast lost ion probes - IFLIP |  |  |
| Fast lost ion probes - SFLIP |  |  |
| Filterscopes | √ |  |
| FIReTIP |  | √ |
| Gas puff imaging |  |  |
| H camera - 1D |  | √ |
| High-k scattering |  |  |
| Infrared cameras | √ |  |
| Interferometer - 1 mm |  | √ |
| Langmuir probes – divertor |  | √ |
| Langmuir probes – BEaP |  |  |
| Langmuir probes – RF ant. |  | √ |
| Magnetics – Diamagnetism | √ |  |
| Magnetics – Flux loops | √ |  |
| Magnetics – Locked modes | √ |  |
| Magnetics – Pickup coils | √ |  |
| Magnetics – Rogowski coils | √ |  |
| Magnetics – Halo currents | √ |  |
| Magnetics – RWM sensors | √ |  |
| Mirnov coils – high f. | √ |  |
| Mirnov coils – poloidal array | √ |  |
| Mirnov coils – toroidal array | √ |  |
| Mirnov coils – 3-axis proto. |  |  |

Note special diagnostic requirements in Sec. 4

| Diagnostic | Need | Want |
| --- | --- | --- |
| MSE |  |  |
| NPA – E¦¦B scanning |  |  |
| NPA – solid state |  |  |
| Neutron measurements |  | √ |
| Plasma TV | √ |  |
| Reciprocating probe |  |  |
| Reflectometer – 65GHz | √ |  |
| Reflectometer – correlation | √ |  |
| Reflectometer – FM/CW | √ |  |
| Reflectometer – fixed f | √ |  |
| Reflectometer – SOL | √ |  |
| RF edge probes | √ |  |
| Spectrometer – SPRED | √ |  |
| Spectrometer – VIPS | √ |  |
| SWIFT – 2D flow |  |  |
| Thomson scattering | √ |  |
| Ultrasoft X-ray arrays | √ |  |
| Ultrasoft X-rays – bicolor | √ |  |
| Ultrasoft X-rays – TG spectr. |  | √ |
| Visible bremsstrahlung det. | √ |  |
| X-ray crystal spectrom. - H |  | √ |
| X-ray crystal spectrom. - V |  |  |
| X-ray fast pinhole camera |  | √ |
| X-ray spectrometer - XEUS |  | √ |