## Slide 1: 1. EF scalings in H mode 2. 2/1 NTM stability and EF sensitivity vs q profile
Proposals for Tearing Stability Studies on NSTX in 2010
by Richard Buttery1
with Stefan Gerhardt2, Rob La Haye1, Jong-Kyu Park2, Steve Sabbagh3 and possible Holger Reimerdes!
Presented to the Macroscopic Stability meeting, Jan 2010
1General Atomics, USA
2Princeton Plasma Physics Laboratory, NJ.
3Columbia University, NY.
Work funded by the US DOE.

## Slide 2: ITER’s Error Field Scalings Deduced for *Ohmic* Plasmas – regime of concern at the time (low ne before H mode)
Scale using power law form:
Bpen / BT  nan RaR BaB qaq
  deduce aR = 2an+ 1.25aB from dimensional considerations,
    in line with approach for confinement scaling (Connor and Taylor NF 17 1047)
  But COMPASS-D behaves differently from other devices
    Rotation behavior was different!
Bpen/BT

## Slide 3: COMPASS-D had much stronger rotation scaling with BT than other devices – likely due to rotation behavior
Boron III rotation change prior to locking:
w ~ B0.9
Constant q95
Error field threshold when EF overcomes plasma rotation
  EF scaling implicitly folds in rotation variation with Bt, ne
Will plasma rotation in NBI heated H mode scale same as self generated rotation in Ohmic plasmas?
  No! (unless you’re lucky)
Need new experiment to determine how EF thresholds scale in H-modes!
COMPASS-D

## Slide 4: NSTX Readily Accesses Tearing Modes Ahead of Natural b Limit When Error Fields Applied in H modes
But can get two types of mode
  Locked or rotating
  What is practical limit given these apparently different processes?
Chart: 
| 0.467162 | 0.353236 | 0.465652 | 0.324246 | 0.157693 | 0.448206 | 0.476112 | 0.28989 | 0.388271 | 0.302922 | 0.260923 | 0.267457 | 0.342103 | 0.238313
ElectronNTMDriveq21Onset | 0.16993 | 0.15987 | 0.18201 | 0.1373 | 0.122 | 0.16793 | 0.24031 | 0.21842 | 0.22733 | 0.16138 | 0.1388 | 0.18105 | 0.19267 | 0.17104
m0LqdjBS,Sauter/Bq
-2p(dΩφ/dr) tALS
Rotating mode accessed at lower bootstrap drive with less rotation shear 

## Slide 5: In H modes, error fields can also destabilizing rotating modes – but does this matter?
Error field brakes plasma:
  If close to 2/1 NTM beta limit, the 2/1 NTM can is destabilised by the reduction in rotation shear
  Further from NTM limit rotation braking reaches bifurcation point for ‘penetration’ – bifurcation to large locked mode
Chart: 2.26In=1+2.52In=3
| 360.9179683565856 | 2451.09112295632 | 1932.281603730175 | 2439.380558236532 | 938.7086948845014 | 1079.010165417988 | 178.9100905467545 | 3184.176405405379 | 1851.576457227432 | 1998.217749606013 | 2617.456939479503 | 2485.343061852198 | 3215.444226186854 | 3061.412080864772
FM21Onset | 6578.34 | 4996.03 | 5819.05 | 4904.49 | 7555 | 6431.22 | 6488.16 | 3455.93 | 6041.42 | 5990.44 | 5552.45 | 4920.45 | 3920.11 | 4338.01
Locked modes
half the original rotation rate
Rotating modes
Ωf2/1 Hz
Key point is mode forms at lower beta/bootstrap when substantial rotation braking happens
  Criteria is about overcoming plasma rotation to reach high braking regime
  A lot like Ohmic criterion

## Slide 6: Governing Physics – á la old Ohmic theory… Penetration is about overcoming the plasma rotation
Modes form when resonant surface is braked by resonant response to EF to half it’s natural frequency
  Tiny static island induced by EF
  Viscous forces try to keep bulk plasma rotating slipping past the island - this opposes island growth
  Torque exerted through island and viscosity to brakes plasma
    N=3 NTV effects assist this process?
  If rotation slows enough, island can grow, increasing torque and bifurcating to a locked mode state
  Threshold scales as Bpen ~BT w0 tA (trec / tv)1/2
    w0 often taken to be electron diamagnetic rotation
Criteria could also be regarded/generalised as condition for when we approach rapid rotation change
Critical elements are: what determines w0; whether plasma response changes; and how readily plasma rotation is overcome

## Slide 7: DIII-D just identified likely strong scalings with ne and BT Need to confirm & want extrapolations for ST
But toroidal field scaling much worse
  And absolute levels of field required are modest (~1-2G)
  Raises concern & needs investigation elsewhere
H mode density scaling steeper than Ohmic - favorable
New Results in H Mode

## Slide 8: Experiments Are Needed to Extrapolate EF Threhsolds to Next Step Devices – like ST-CTF or ITER
Ramp up error field to measure mode thresholds
Scan in ne and Bt
  Infer machine size scaling from Connor-Taylor constraint
Hard part:
  Maintain constant shape, betan, li and q profile at time of mode onset – can we do this?
  Also what to do with rotation? (Natural beam drive, or n=3 braking to control to given MA)
These experiments are essential if you want to understand how the torque balance based error field threshold extrapolates to future devices.

## Slide 9: Proposed approach
Build on successful shot developed in 2009
  Scan in Bt(~Ip) and density
  Li to control ELMs & conditions
  Adjust NBI start time if qmin (MHD) trajectory varies
  Ramp EF to mode… but:
  bN is time varying: Adjust EF ramp to get mode strike at similar bN
Uncertainties are rotation variations (strip out from other scans) and more profound profile changes
NSTX #134071
1
4
0
3
0
20
-600
0
0
0
CHERS rotation kHz
0
800
400
Time (ms)
Error Field Current Amps
bN
Neutral Beam power MW
Plasma Current MA
core
Chord near q=2
Da a.u.
Dynamic correction
Ramp
Magnetics spectrogram color=mode
2/1 NTM
Rotation shear falls
No ELMs before NTM

## Slide 10: Shot Plan – counting good shots
Establish reference and tune if needed – 3 shots
Change density (ideally: puff gas after 300ms to avoid big profile effect) – 3 shots
  If needed tune heat switch on time
  Tune EF ramp rate/time to get mode at same betan
Repeats at different densities, anticipating adjustments based on item 2 observations: 3 more points - 6 shots
Change to lower toroidal (Ip in proportion) – 3 shots
  Repeating above – reoptimisation as in step 2.
Change to higher toroidal field – 2 shots

## Slide 11: Questions
Is profile compensation approach good enough (adjust NBI on time to get similar qmin)?
Best way to handle rotation for scaling?
  Live with whatever rotation we get from co beams (presumes a correction would be needed for future device – but leaves scope of this to an other study – JKP?)
    This is reasonable – like Ohmic we just regard rotation as a hidden variable, implicit in process but determined by other parameters
  Fix NB levels for fixed torque
  Fix rotation with n=3 fields (too difficult I think for this 1st cut & raises issues of validity, as n=3 fields help access mode!)
Impact of 2010 plasma conditions/machine changes?
Intershot MSE qmin possible?

## Slide 12: 2nd proposal
Role of q profile in 2/1 NTM stability

## Slide 13: JET Hybrid Plasma Sit Above b Limit of Other Devices: Other parameters coming into play – q profile?
JET sits above DIII-D and JT-60U trends
  JT-60U lower rotation lower bN
  But DIII-D high rotation
Possible collisionality role? No:
  JET unstable at low n*
  But stable at +high and ° low n*
Collisionality provides ‘access condition’ for NTM
  Enables q profile modification
  Can change D'
  q profile is the parameter to test…
DIII-D
JET
JT-60U
ni/ewe*
0
1
0
0.16
rif*

## Slide 14: Heating timing scan shows ‘just right’ degree of relaxation needed
Mode if profiles too ‘advanced’:
Fully relaxed plasma also less stable
  Mode at lower bN or occurs later
-IP/MA
bN
PNBI/MW
n=1 MHD a.u.
H98pby2
Da a.u.
JET: 77626,77629,77636,77633
Relaxed late mode
early mode
early modes
No mode
Power drop + late on
0
-1
0
20
0
3
1
0
2
10
Time (s)
0
Time (s)
2
4
Early heating, 77633 modes at high qmin
q at various radii
Best case, 77629, qmin stays ~1
Time (s)
8
4
q at various radii

## Slide 15: NSTX an ideal place to explore q profile role in detail
Plasma naturally relaxes vs time
Can ramp beta to excite mode
  Scan NBI timing & power to vary qmin vs bN trajectory
Repeats with EF applied
  to see if plasma response stronger as tearing mode b limit applied
NSTX #134071
1
4
0
3
0
20
-600
0
0
0
CHERS rotation kHz
0
800
400
Time (ms)
Error Field Current Amps
bN
Neutral Beam power MW
Plasma Current MA
core
Chord near q=2
Da a.u.
Dynamic correction
Ramp
Magnetics spectrogram color=mode
2/1 NTM
Rotation shear falls
No ELMs before NTM
DIII-D: Plasma response to error field increases with bN:
  How does response change with D’?

## Slide 16: Detailed Considerations
Similar approach to last experiment, but here try to vary timing of NBI start to change q profile
  Most interested in qmin value – does approach to 1 have special role?
    A fine scan of this would be very insightful
  Trajectory approach is powerful – always get mode – just change what beta and qmin we get it at
    by varying time and power to change beta ramp up rate
EF response is a novel element
  Looking for change with deltaprime (influenced by qmin) would be a first
    Can we probe EF response readily – how best done on NSTX?

## Slide 17: Shot Plan
  More straightforward than EF study as profiles and beta onset of mode are allowed to vary
Repeats of reference shot at different power levels and timings – 10-12 good shots desirable
Repeats of favorite cases with EF response probed vs time as beta rises to limit – 5-6 shots
  Possible extension to look at error field threshold with ramp applied some pre-determined interval before natural mode
    What interval?