## Slide 1
Progress and Plans for Macroscopic Stability
Jack Berkery
(Columbia University)
and the NSTX Research Team
NSTX PAC-35 Meeting
PPPL – B318
June 11-13, 2014
NSTX-U
Supported by
Culham Sci Ctr
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Inst for Nucl Res, Kiev
Ioffe Inst
TRINITI
Chonbuk Natl U
NFRI
KAIST
POSTECH
Seoul Natl U
ASIPP
CIEMAT
FOM Inst DIFFER
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
Coll of Wm & Mary
Columbia U
CompX
General Atomics
FIU
INL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Lehigh U
Nova Photonics
Old Dominion
ORNL
PPPL
Princeton U
Purdue U
SNL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Illinois
U Maryland
U Rochester
U Tennessee
U Tulsa
U Washington
U Wisconsin
X Science LLC

## Slide 2
10-13 content slides and a 20min presentation time
Here is rough suggested format:
  Title page from NSTX-U template
  Outline (1)
  Intro slide - motivation for your TSG's research - for NSTX-U, ITER, FNSF (2)
  0.5-1 slide on NSTX-U research milestones and JRTs your TSG contributes to (3)
Then:
  3-4 slides on progress during last ~1 year - both for NSTX-U and collaborations (6)
  NCC (7)
  2-3 slides on your TSG's research goals and plans for FY15 (10)
  1-2 slides on your TSG's research goals plans for FY16 (13)
  1-2 slide summary of key new physics/operational results you expect to have achieved after FY15 and FY16 runs. (14)

## Slide 3: Outline
Introduction
  MS research in stability, 3D fields, and disruptions is key for NSTX-U and future devices
  MS research is prominent in NSTX-U milestones as well as JRTs
Progress in the last year
  X
  X
  Non-axisymmetric control coil (NCC) design
MS research goals and plans for FY15
MS research goals and plans for FY16
Key new results expected by the end of the FY16 run

## Slide 4: Macroscopic stability research is crucial for the successful sustainment of high performance in future devices
Macroscopic stability research is in three key areas:
  Thrust 1, Stability:
  Understand and advance passive and active feedback control to sustain macroscopic stability at low collisionality
  Thrust 2, 3D Fields:
  Understand 3D field effects and provide physics basis for optimizing stability through equilibrium profile control by 3D fields
  Thrust 3, Disruptions:
  Understand disruption dynamics and develop techniques for disruption prediction, avoidance, and mitigation in high-performance ST plasmas

## Slide 5: Macroscopic stability research and capabilities play an instrumental role in the success of NSTX-U
MS group’s crucial role is reflected in milestones and JRTs in:
  Preparation for high performance in NSTX-U
  Development of NSTX-U capabilities
  U.S. program-wide high priority research

## Slide 6: 3-4 slides on progress during last ~1 year - both for NSTX-U and collaborations

## Slide 7: 3-4 slides on progress during last ~1 year - both for NSTX-U and collaborations

## Slide 8: 3-4 slides on progress during last ~1 year - both for NSTX-U and collaborations

## Slide 9: NCC

## Slide 10
Stability research plans, FY15:
  Establish Br + Bp active control capability in new operational regime, use with snowflake divertor, compare to theory
  Examine RWMSC with:
    independent actuation of six control coils
    multi-mode control with n up to 3
  Use new neutral beam and qmin control to determine increment of qmin above rational values to avoid internal modes
Active control techniques (Br + Bp, RWM state-space (RWMSC), and qmin) will enable long pulse, high β operation

## Slide 11: Correction of intrinsic error fields (EFs) is critical for NSTX-U performance
3D fields research plans, FY15:
  Assess intrinsic EFs in new machine
  Optimize dynamic EF correction, including n>1 and using 6 SPAs and RWMSC
  Investigate resonant EF effects on tearing mode onset

## Slide 12: NSTX-U will have new disruption research capabilities which will provide projections for ITER and FNSF
Disruption research plans, FY15:
  Investigate halo current toroidal asymmetry and loading on the center column, using newly installed center column shunt tiles
  Upgrade shunt tile diagnostics for complete coverage of divertor??????????
  Commission MGI system

## Slide 13: Practical implications of kinetic stability theory and the RWMSC model will be tested in lower ν regime
Stability research plans, FY16:
  Examine RWMSC with:
    rotational stabilization in the controller model
  Investigate the dependence of stability on reduced ν through MHD spectroscopy; compare to kinetic stabilization theory
  Measure internal modes non-magnetically with RWMSC and ME-SXR

## Slide 14: NSTX-U will investigate neoclassical toroidal viscosity (NTV) at reduced n, which is important for rotation control and ITER
3D fields research plans, FY16:
  Assess NTV profile and strength at reduced collisionality, and examine the NTV offset rotation at long pulse
  Prepare an initial real-time model of NTV profile for use in initial tests of the plasma rotation control system

## Slide 15: Disruption prediction by multiple means will enable avoidance via profile or mode control or mitigation by MGI
Disruption research plans, FY16:
  Study spatial extent and timing of the heat deposition during VDEs
  Measure plasma stability using MHD spectroscopy vs. key variables and compare to theory
  Compare the mismatch between the RWMSC observer model and sensor measurements, and disruption occurrence
  Characterize density assimilation vs. poloidal location of MGI system

## Slide 16: 1-2 slide summary of key new physics/operational results you expect to have achieved after FY15 and FY16 runs.