## Slide 1: Kickoff meeting for NSTX-U Milestone R(18-3)
T&T TSG group meeting
November 6, 2017

## Slide 2: R18-3: “Validate and further develop reduced transport models for electron thermal transport in ST plasmas”
http://nstx-u.pppl.gov/program/milestones/fy2018-research
The design of next generation spherical tori (STs) will be influenced by the scaling of energy confinement. While ion thermal transport is often near neoclassical levels in H-modes in ST plasmas, gyro-kinetic simulations have indicated a number of potential drift wave turbulence mechanisms that can influence electron thermal transport. Reduced transport models that capture the key physics and scaling of the computationally expensive first-principles gyro-kinetic simulations are required to more thoroughly validate the modeling against experimental data, which can then be used to infer the key physics that determines the overall energy confinement. A variety of reduced transport models based on drift wave turbulence have been developed and tested extensively for conventional tokamaks. These models encompass much of the physics expected to be important in STs, although they have been tested much less rigorously for ST parameters (low aspect ratio, high beta, strong flow). In order to improve the fidelity of reduced transport models (like TGLF, RLW and MMM), experimental NSTX, MAST and NSTX-U data will be used to examine predictions based on these models to assess their suitability for ST plasma. The physics accuracy of these fluid-based models will be also be qualified by comparing directly to first-principles gyro-kinetic simulations over a range of conditions. The dependence of electrostatic ITG and TEM instabilities on aspect ratio will be evaluated by comparing L-mode cases to established conventional aspect ratio conditions. Validation with high beta H-mode data will push the limits of the available reduced models to recover electromagnetic instabilities like MTM and KBM. A key outcome of this milestone will be to determine the ST physics regimes in which further model development is required. The first-principles gyro-kinetic simulations based on ST parameters will form the basis for enhancements of the TGLF reduced model.

## Slide 3: Highest T&T priority for NSTX-U: Measure & understand H-mode confinement scaling at higher BT
~WcitE
NSTX H-modes
In NSTX and MAST H-modes, dimensionless confinement time scales inversely with collisionality, WcitE~n*-0.8
If this holds at higher BT & PNBI (higher Te, lower n*)  very favorable for future STs
What determines H-mode transport & confinement scaling?
Kaye, NF (2013)
We often consider three regions:
Pedestal, r>0.9
Core, 0.4<r<0.9 (focus of R18-3)
Near-axis, r<0.4, where Te flattens (*AE effects?)
See Ren, NF (2017) for recent review

## Slide 4: At high b, microtearing modes (MTM) and kinetic ballooning modes (KBM) are predicted unstable
Predicted dominant core-gradient instability correlated with local b and n
Multiple instabilities usually predicted for a given experimental discharge
Local gyrokinetic analyses at r/a~2/3
Guttenfelder, NF (2013)
MTM
KBM
ITG, TEM, ETG
H-mode
L-mode
Notes: Looking at 2/3 radius; confinement strongly correlated with transport coefficients at 2/3 radius
Local electron beta values

## Slide 5: Milestone goals: (1) Identify ST conditions for which current core transport models work & fail, (2) Try to improve models
Focus on: Core transport in L-mode and H-mode (excluding pedestal), specifically:
  Electron thermal transport (+ ion thermal transport in L-modes)
  Drift wave (DW) based transport, i.e. not energetic particle mechanisms like GAE/CAE-KAW electron orbit stochastization/energy channeling
    But need to consider this when judging whether DW models work or fail
Two complementary components of the milestone work:
Model validation  comparing profile predictions to experimental data
Model “qualification”  comparing reduced models to gyrokinetic simulations of linear stability, thresholds and nonlinear transport
A significant amount of transport modeling and gyrokinetic analysis has been done for MAST, NSTX, NSTX-U (see 4 reference slides)

## Slide 6: General comments & concerns
Numerous theoretical drift wave mechanisms have been predicted in various NSTX discharges (ITG, TEM, DTEM, PVG, KBM, MTM, ETG, …)
In my opinion, easiest to start in regions where few (hopefully one) mechanism expected dominant, then move in parameter space from there
  One obvious distinguishing factor is b – focus on high-b H-mode & low-b L-mode
Can any one model, or kluged combination of models, reproduce the n* scaling of ST H-mode confinement?
  Neoclassical Ti + broadening Te (regardless of core flat-ness); will need pedestal BC scaling
How do we distinguish “failure” of DW models vs. other unaccounted mechanisms (e.g. GAE/CAE-KAW)?

## Slide 7: Some physics comments (MTM)
Local NL GYRO scaling of MTM with n* reproduces NSTX H-mode scaling
  But sensitive to suppression by experimental EB shear
RLW works amazingly well for high collisionality, high beta
  Need to clarify physics scaling of RLW model
Model validation questions:
  Do Rafiq-MTM model & TGLF predict Te profiles as well as RLW?
  What criteria determines when each model fails to predict Te?
    Is it just collisionality? In what normalized form? What about beta? Etc…
Model qualification questions:
  Do Rafiq-MTM & TGLF recover GK linear threshold and NL transport scalings?
  Is there a resolution to EB suppression of NSTX 120968 r/a=0.6 MTM case?
    I started working with CGYRO, suppression remains at r/a=0.6
    I tried moving out (r/a=0.65, 0.7) where glin,MTM > gE, but numerical saturation is elusive!
    Initiate benchmark with GENE or GKW? (Probably outside scope of Milestone)
  Will it be numerically feasible to simulate MTM globally due to excessive resolution requirements, Dx<Drat(r)=1/nq?

## Slide 8: Some physics comments (KBM)
Numerous H-mode cases locally sit around or above acrit
Nonlinear GYRO simulation of KBM appears physically saturated
Modes linearly transition from ITG/TEM to KBM (“hybrid modes”)
Analysis & modeling questions:
  Do profiles really sit above acrit? What is the sensitivity of aexp>acrit to experimental uncertainties?
    How does using equilibrium reconstruction with consistent Pfast influence this result? We’ve never done this routinely as far as I’m aware.
    Revisit linear stability with updated TRANSP-kEFIT workflow (e.g. via OMFIT)
    How sensitive is GK result to inclusion of kinetic fast ions?
  Does TGLF recover KBM threshold compared to gyrokinetics?
  If KBM is actually active, how do we reconcile ce,anom vs. cici,NC?
    Is it possible to have Ti=Ti,NC, and Te self-organizes until a~acrit?
  Can we make a model prediction of Te using the above recipe? (e.g. fixed ne , Pfast, u + neoclassical Ti  predict Te at marginal a=acrit)
    How do we do this using local KBM if regions are 2nd stable? Can we evolve kEFIT iteratively as part of the prediction?
  How does KBM model profile prediction vary with nu? (e.g. KBM linearly stabilized by collisions)

## Slide 9: Some physics comments (ETG)
Numerous attempts to validate ETG transport with experiment
Hundreds of nonlinear ETG simulations (NSTX, NSTX-U, MAST)
Many experimental trends (with R/LTe, R/Ln, s, gE) consistent with ETG
But, predicted ETG transport often too small
Model validation questions:
  How well do MMM-ETG and TGLF predict Te for regions of expected ETG dominance?
  What fraction of Qe comes from model ETG contributions in various discharges?
Model qualification questions :
  Does TGLF or Horton ETG model recover scalings predicted by nonlinear gyrokinetics?
  When might multi-scale issues be important?
    Tabulate (g/kq)high-k / (g/kq)low-k (incorporating gE) to identify potential importance

## Slide 10: Some physics comments (ITG/TEM/PVG)
Traditional ES DW (ITG, TEM) not often linearly unstable in high b H-mode
  Due mostly to equilibrium configuration, not EB shear
Hoping that electrostatic ITG/TEM should be easiest to recover with models  pursue in low-b L-modes
But non-local effects shown to be important
GTS simulations of DTEM show favorable n* scaling
Model validation questions:
  How well does TGLF and MMM predict L-mode Te and Ti?
Model qualification questions:
  Do MMM and TGLF recover NL GK predictions of ITG/TEM?
  Can we include non-local effects in local QL models (e.g. Waltz PoP 2004)
  Do fluid models recover DTEM? Can we benchmark DTEM in other GK codes?
  How robust is DTEM in ST H-mode plasmas?

## Slide 11: Comments on deep-core (r<0.5) transport
Te is very flat in the inner half radius of high power H-modes
We often assume thermal gradient are too weak to drive drift wave instability
Theory and observation suggest stochastic electron orbits from GAE/CAE modes and/or energy-channeling from GAE/CAE to KAW can influence Te
BUT, we should revisit DW stability thresholds including kinetic fast ions + parallel flow shear (with self-consistent kEFIT)

## Slide 12: Initial thoughts on milestone tasks
Analysis
  Revisit self-consistent kEFIT + TRANSP/NUBEAM for some high-b H-mode cases
Model validation (how well do profile predictions recover exp.)
  H-mode profile predictions using TGLF & Rafiq-MTM for same discharges used by Kaye with RLW model
  Develop and implement algorithm for locally constrained KBM profiles (e.g. fixed ne, NC Ti, fixed Pfast, fixed u, predict Te using a=acrit)
  L-mode profile predictions using TGLF, MMM
  Identify model cases where ETG provides non-negligible Qe (L & H mode)
Model qualification (how well do models recover linear & nonlinear GK)
  MTM: Document TGLF and Rafiq-MTM linear and nonlinear comparison with gyrokinetics
  KBM: Document TGLF acrit with linear GK
  ITG/TEM: Document linear stability, nonlinear saturation dependencies with aspect ratio
  ETG: Do TGLF and MMM recover GK NL ETG dependencies? Tabulate (g/kq)high-k / (g/kq)low-k (incorporating gE) as proxy for possible multi-scale effects
  ITG/TEM: Document non-local deviations from local GK, use to inform local models
  DTEM: Benchmark local GK codes with global GK for DTEM conditions; Is there a transport model available for profile predictions?
Notes: Looking at 2/3 radius; confinement strongly correlated with transport coefficients at 2/3 radius
Local electron beta values

## Slide 13: Immediate action items for November
Identify and tabulate targeted shots and TRANSP IDs (H & L mode) to focus model-experiment validation
Identify targeted shots/parameter sets (H & L mode) to focus model-GK comparisons
Begin documenting initial profile predictions using TGLF & Rafiq-MTM
…
Plan to have ~monthly meetings for group updates
  Will meet more frequently as needed for task-specific actions

## Slide 14: A number of transport solvers, transport models & gyrokinetic codes are available
Transport solvers
  TRANSP
  PT-SOLVER
  XPTOR
  TGYRO
Drift wave microturbulence transport models
  TGLF
  MMM (Weiland ITG/TEM + Horton ETG + Rafiq DRIBM)
  Rafiq-MTM
  RLW
GK codes
  GYRO
  CGYRO
  GS2/GKS
  GTS
  XGC1
  GENE, GKW, GEM, GTC, ...
Modeling frameworks
  OMFIT

## Slide 15: References

## Slide 16: Previous ST transport modeling using reduced models (not gyrokinetic predictions)
Kaye NF (2007), Horton ETG transport model comparison
Wong PRL (2008), PoP (2008) MTM R-R transport modeling
Staebler IAEA-FEC (2008), MAST TGLF profile prediction
Akers IAEA-FEC (2008), MAST ETG ce model; GLF23 profile predictions
Guttenfelder, Staebler (2011), TGLF-GYRO tests of MTM (NSTX H-mode)
Guttenfelder, Staebler (2013), TGLF-GYRO tests of ITG/TEM, linear and nonlinear (NSTX L-mode)
Kaye, PoP (2014) NSTX RLW MTM profile predictions
Rafiq, PoP (2015), MTM model development
Rafiq, APS (2016), NSTX MTM model comparison to GYRO
Guttenfelder, Staebler (2017), TGLF-GYRO linear aspect ratio scan
Rafiq, Pankin (?), MMM ETG-Horton model presentations for NSTX

## Slide 17: ST gyrokinetic simulations
Early scoping
Rewoldt, PoP (1996), linear FULL
Kotschenreuther, Dorland, NF (2000), linear GS2
H. Wilson (2004), linear GS2
Early experimental analysis
M. Redi, EPS (early 2000’s), linear GS2 (NSTX)
D. Mikkelsen, TTF (2004), linear, nonlinear GYRO (NSTX)
Applegate, PPCF (2004), linear GS2 (MAST)
Roach, PPCF (2005), linear GS2 (MAST)

## Slide 18: ST gyrokinetic simulation work - ETG
Joiner, PoP (2007), GS2 NL ETG (MAST H-mode)
Kaye, NF (2007), GYRO NL ETG prediction
Roach, PPCF (2009), GS2 NL ETG (MAST H-mode)
Mazzucato (), GS2 linear ETG thresholds
Smith, PRL (), thresholds, ExB shear
Poli, PoP (2010), Ethier (APS?), GTS NL ETG
Yuh, PRL (2011), GS2 linear ETG thresholds (reverse shear ITBs)
Guttenfelder, PoP (2011) GYRO NL ETG
Ren, PoP (2012) GYRO NL ETG
Peterson, PoP (2012) GYRO NL ETG, reverse shear
Guttenfelder, NF (2013) GYRO NL ETG
Ruiz-Ruiz, PoP (2015) GS2 linear, GYRO NL
Colyer, (2016) GS2 NL ETG, collisionality dependence
J. Chowdhury, APS (2017), ETG benchmark with XGC-1, GYRO, GENE

## Slide 19: ST gyrokinetic simulation work – ion scale
MTM
Applegate, PPCF (2006), linear GS2 (MAST H-mode)
Applegate, Thesis (2007) NL GS2 (MAST H-mode)
Wong, PRL (2008), PoP (2008) linear GS2
Smith, PPCF (2011) linear GS2, high-k MTM
Guttenfelder, PoP (2012), linear GYRO
Guttenfelder, PRL (2011), PoP (2012), NF (2013), NL GYRO
Smith, APS (2017), linear GENE (Pegasus H-mode)
ITG/TEM/PVG
Sareelma, PPCF (2012), nonlinear ORB5 (MAST L-mode)
A. Field, NF (2014), nonlinear ORB5 (MAST L-mode)
Diallo, NF (2013), linear XGC-1, GENE comparison at rho=0.7 (NSTX H-mode)
Ren, NF (2013), linear GS2, nonlinear GYRO (NSTX L-mode)
Ren, PoP (2015), nonlinear GTS (NSTX RF L-mode)
Wang, NF (2015), PoP (2015), nonlinear GTS (NSTX L & H modes)
Guttenfelder, NF (2017), linear & nonlinear GYRO (NSTX-U L-mode)
KBM
Guttenfelder NF (2013), linear & nonlinear GYRO (NSTX H-mode)
J. Liang, APS (2015), linear KBM comparison XGC1, GYRO (NSTX H-mode, Diallo case)

## Slide 20: Extra slides

## Slide 21: Action items (living document)
Q1 (Oct-Dec) | Identify target shots for profile predictions (Kaye … Identify target shots for detailed GYRO-TGLF comparisons (Guttenfelder, Staebler, …) Compare Rafiq-MTM transport to previous GYRO NL (Rafiq …) Initial linear TGLF-GYRO comparisons Document initial TGLF profile predictions Document initial Rafiq-MTM profile predictions
Q2 (Jan-Mar) | 
Q3 (Apr-June) | 
Q4 (July-Sept) |