## Slide 1: Low-density Start-up
D. Mueller, M. Bell, S. Gerhardt, J. Menard, R. Raman, S. Sabbagh
NSTX FY12 low density discussion: May 12, 2011

## Slide 2: Historically, fueling and heating help avoid MHD during start-up
Long experience with goal of achieving long, stable, high-performance discharges has led to the present prescription
  both low-field and high-field side gas puffing
  Rapid Ip ramp-rate
  Low li used
    High dIp/dt
    large aperture start-up
    early heating
Most of these also increase the plasma density

## Slide 3: New approach is needed for low density
  Simply turning off gas and/or heating does not work to produce stable plasmas
  Partial existence proof: CHI initiated discharges had low density, low li , larger R, OH(0)=0 and were stable (but no flattop and L-Mode)
  Error fields are more likely to cause locked modes (or other MHD?) at low density (does low li help?)
  Use zero OH precharge to minimize error fields
  Use high Vloop like CHI did
  Try low voltage start-up and low dIp/dt
  Use RWM coils early to correct for error fields
  (In H-Mode, nel increases about 1X1015/cm2 per 0.1s)

## Slide 4: Strategy
  Use zero OH precharge to investigate if OHXTF is source of error fields
    This at least starts with only eddy currents contributing to error (ramping coils, ramping errors?)
    If this is successful, investigate error –field reduction with RWM coils next (if not try this later)
  Try high initial Vloop, with larger R and kappa with low gas fueling, like the low li, low ne CHI shots
  Try low voltage start-up with slow dIp/dt with low gas fueling and low NBI
  Attack early error field correction
  In all cases, compare ne evolution to a 2 NB source, 700 kA fiducial plasma to evaluate success

## Slide 5: Zero OH pre-charge
Starting up is straight-forward, plasma shape like fiducial
Goal 600 or 700 kA (to have a bit of flattop)
Use only prefill, early NBI timing like 2-source fiducial
Introduce flat spot in Ip ramp to get H-Mode
Add some LFS gas if needed to get H-Mode
If LFS gas does not work add some HFS gas
Compare to same Ip, shape and gas programming, but with full OH precharge

## Slide 6: High loop Voltage (low early li )
Try about 4V/turn, about double standard
Use lower PF5 to get larger R
Reduce PF3/PF5 ratio like CHI case (taller plasma)
Will require tweaking of PF1AU&L to avoid hitting top
Make R 10cm bigger in first 70 ms
Flattop at 600-700 kA
Use only prefill, early NBI timing like 2 source fiducial
Introduce flat spot in Ip ramp to get H-Mode
Add some LFS gas if needed to get H-Mode
Add blip of 3rd NB source
If that does not work add some HFS

## Slide 7: Low loop voltage
During the slow ramp-up (~5 – 7 MA/s), we normally use ~2V/turn for L-Mode or ~ 1.5 V/turn in H-Mode.
Try to use <1.5 V for breakdown (will require lower prefill and PF5). Ramp to 700 kA at ~ 0.6s
Larger plasma size at start-up generally leads to lower li ; May need this to offset the faster current penetration due to lower Te from lower input power. Start with the usual PF3/PF5 ratio and lower it as needed to get lower li
Use only prefill, use plasma shape similar to fiducial, but taller early on
Inject beams early similar to 2 source fiducial
Use usual tricks of flat-spot in Ip ramp, LFS gas, 3rd NB source, or some HFS gas to get H-Mode

## Slide 8: No LFS gas - early Ha spikes and higher li, then shorter duration