## Slide 1
XP1111: RWM PID control optimization based on theory and experiment
S.A. Sabbagh, J.W. Berkery, J.M. Bialek, S.P. Gerhardt, Y.S. Park, B. LeBlanc, et al.
Department of Applied Physics, Columbia University, NY, NY
Plasma Physics Laboratory, Princeton University, Princeton, NJ
Advanced Scenarios & Control TSG Meeting
Friday June 3rd, 2011
PPPL
College W&M
Colorado Sch Mines
Columbia U
Comp-X
General Atomics
INEL
Johns Hopkins U
LANL
LLNL
Lodestar
MIT
Nova Photonics
New York U
Old Dominion U
ORNL
PPPL
PSI
Princeton U
Purdue U
Sandia NL
Think Tank, Inc.
UC Davis
UC Irvine
UCLA
UCSD
U Colorado
U Maryland
U Rochester
U Washington
U Wisconsin
Culham Sci Ctr
U St. Andrews
York U
Chubu U
Fukui U
Hiroshima U
Hyogo U
Kyoto U
Kyushu U
Kyushu Tokai U
NIFS
Niigata U
U Tokyo
JAEA
Hebrew U
Ioffe Inst
RRC Kurchatov Inst
TRINITI
KBSI
KAIST
POSTECH
ASIPP
ENEA, Frascati
CEA, Cadarache
IPP, Jülich
IPP, Garching
ASCR, Czech Rep
U Quebec
NSTX
Supported by
V1.0

## Slide 2: XP1111: Aims to optimize n = 1 RWM PID control for general NSTX experimental use, and comparison to theory
Motivation
  Experiments using n = 1 RWM control in 2010, and subsequent analysis using the VALEN code show that some settings for control using BR and Bp sensors are optimal, while others can be improved
  Support NSTX experiments in general by optimizing RWM PID control
Goals / Approach
  Optimize n = 1 RWM PID control focusing on scans of key parameters not presently optimized in theory
    Vary Bp feedback phase, BR feedback gain presently differ in the most in the analysis from the experimental settings. Bp sensor gain will also be examined in this experiment (never scanned with r/t/ AC compensation).
    Use two different high performance target plasmas (fiducial; low li targets)
Addresses
  General support for NSTX high beta experiments
  ITPA joint experiment MDC-17, MHD Working Group 7

## Slide 3: RWM feedback using upper/lower Bp and BR sensors shows good agreement with BR feedback phase; gain not optimized
Both Br, Bp feedback contribute to active control
  Br mode structure and optimal feedback phase agrees with parameters used in experiment
  Br feedback alone provides stabilization for growth times down to ~ 10 ms with optimal gain
  Physics of best feedback phase for Bp sensors in low li plasmas under investigation
Toroidal angle (deg)
Modeled Br field at sensors and midplane
Radial field (G)
Br feedback phase (deg)
Growth rate (1/s)
top sensors
bottom sensors
gain 2e5
250 degrees
midplane
Passive growth
Br sensors alone
Br and Bp
sensors
DCON, VALEN
codes
Br gain (arb)
Growth rate (1/s)
VALEN eqv. gain 2e5
optimal gain

## Slide 4: RWM Br sensor n = 1 feedback phase variation shows superior settings when combined w/Bp sensors; good agreement w/theory so far
VALEN calculation of Br+Bp feedback follows XP
  stable plasma (negative “s”)
  Now examining plasma response model variation
    impact of “s”, and diff. rotation (“a”) on results
Dt (s)
Radial field n = 1 (G)
Favorable (experimental) Bp feedback settings, varied BR settings
  Positive/negative feedback produced at theoretically expected phase values
180 deg FB phase
90 deg FB phase
0 deg FB phase
Vacuum error field
Vacuum EF + RFA
VALEN calculation of NSTX Br + Bp control
n = 1 BR + Bp feedback
(Bp gain = 1, BR gain = 1.5)
NSTX Experiments: Bp + BR feedback
Feedback on

## Slide 5: Tweaking Bp sensor feedback phase around 180 degrees led to long-pulse, low li, high bN/li
139347
139515
139516
139517
Steady, high bN/li
  Between 12 – 12.5
Not in agreement with theory
  VALEN indicates a value near 270 deg is optimal
  Analysis ongoing
180 deg
202.5 deg
157.5 deg
Bpn = 1 (G)
Ip (MA)
bN
li
bN/li

## Slide 6: XP1111: RWM PID control optimization based on theory and experiment – shot plan
Task Number of Shots
0) Control shots
A) Generate Fidicial target (long pulse ~ 1s, Ip ~ 0.9 MA) 1
B) Generate low li target (long pulse ~ 1s, Ip ~ 0.9 MA) - NOTE: run this AFTER fiducial scans done 1
C) Generate RWM using n > 1 magnetic braking if RWM is not generated 2
1) RWM n = 1 PID feedback control variable scans (at optimal BR feedback phase)
A) Vary RWM Bp sensor feedback phase for first target plasma 6
B) Vary RWM BR sensor feedback gain for first target plasma 3
C) Repeat scans (A) for second target plasma 6
D) Vary RWM Bp sensor feedback gain for one of the two plasma targets 3
_____________________________________________________________________________________________
Total: 22
V1.0
½ run day originally slated for RWM state space controller XMP would be used for this XP
(RWM state space controller work can be run in transparent piggyback)

## Slide 7: XP1111: RWM PID control optimization based on theory and experiment – Diagnostics, etc.
Required diagnostics / capabilities
  n = 1 RWM PID feedback control using Bp and Br sensors
  CHERS toroidal rotation measurement
  Thomson scattering
  MSE
  Toroidal Mirnov array / between-shots spectrogram with toroidal mode number analysis
  Diamagnetic loop
Desired diagnostics
  USXR, ME-SXR, BES
  FIDA variants
  FIReTip
  Fast camera