## Slide 1: Why Magnetically Confined Plasmas Rotate, and Why it is Important
Stanley M. Kaye
Princeton Plasma Physics Laboratory
Princeton University, Princeton NJ 08543
American Physical Society Meeting
Atlanta, GA
31 March-2 April 2012

## Slide 2: I would like to acknowledge the direct and indirect contributions of:
C. Angioni1, P. Diamond2, S.-H. Ku3, R. McDermott1, J.-K. Park3, J. Rice4, F. Ryter1 W. Solomon3, T. Tala5, W. Wang3, M. Yoshida6
1 Max-Planck Institut fur Plasmaphsik, Garching, Germany
2 UCSD, San Diego CA, USA
3 PPPL, Princeton University, Princeton NJ, USA
4 PSFC, MIT, Cambridge MA, USA
5 Association Euratom-Tekes, VTT, Finland
6 JAEA, Japan
This work was supported in part by U.S. DOE Contract # DE-AC02-09CH11466

## Slide 3: In this talk, I will explore aspects of rotation and momentum confinement in magnetically-confined plasmas
Background
  Magnetically confined plasmas in tokamaks/spherical tokamaks
  Rotation observed in other configurations (stellarator, RFP, linear devices), but will focus on tokamak/ST
Why is rotation important
  Stabilization of micro-, macro-turbulence leads to higher performance
How do rotation profiles develop and evolve – how can we understand rotation?
  Rotation generation (driven, self-generated)
  Transport of momentum
    Find tokamak/ST results similar gives glimpse into underlying common physics
  Predictions for fusion power devices (ITER)
Future work and summary
  What else do we need to understand
Rotation/momentum transport strongly coupled primarily to ion-gyroradius scale turbulence

## Slide 4: Fusion-grade plasmas are magnetically confined in toroidal devices
R/a~4, k=2, qa=4
R/a~1.3, k=2, qa=12
a~ 0.65 m, R~1.7 m
Ip ~ 1 MA, BT~ few T
a~ 0.65 m, R~0.85 m
Ip ~ 1 MA, BT~ 0.5 T
Most of tokamak research historically and presently conducted at conventional aspect ratio
Only a decade of research on Spherical Tokamaks (STs)
Strong toroidicity at low aspect ratio benefits
both stability and confinement
(poloidal)
(toroidal)
(radial)
Vf(center) up to 300 km/s
Rotation profiles measured by Doppler shift of spectroscopic lines

## Slide 5: Results from tokamaks/STs from around the world contribute to this talk
NSTX (US, ST)
Alcator C-Mod (US)
ASDEX-Upgrade (EU)
DIII-D (US)
JET (UK/EU)
JT-60U (Japan)
MAST (UK, ST)

## Slide 6: Evolution of key parameters during a plasma discharge
NSTX
Plasma undergoes abrupt
transition from a lower to a
higher energy state at ~ 0.2 s
Low (L-)  High (H-) confinement
mode (observed on all devices)
L -> H
Ms~0.75

## Slide 7: In this talk, I will explore aspects of rotation and momentum confinement in magnetically-confined plasmas
Background
  Magnetically confined plasmas in tokamaks/spherical tokamaks
  Rotation observed in other configurations (stellarator, RFP, linear devices), but will focus on tokamak/ST
Why is rotation important
  Stabilization of micro-, macro-turbulence leads to higher performance
How do rotation profiles develop and evolve – how can we understand rotation?
  Rotation generation (driven, self-generated)
  Transport of momentum
    Find tokamak/ST results similar gives glimpse into underlying common physics
  Predictions for fusion power devices (ITER)
Future work and summary
  What else do we need to understand
7

## Slide 8: There are two main sources of radial transport in tokamaks/STs
Most of the transport in tokamaks/STs is anomalous
Rotation plays an important role in the suppression of microturbulence
Eradial determined by p,v
Usually dominant
  Neoclassical – collisional processes in toroidal systems
             sets minimum transport level
  Anomalous– turbulent microinstabilities: scale lengths from the ion to the electron gyroradius
ErxB shear can stretch and break up turbulent eddies
Rule of thumb: turbulence suppression when wExB>gmode
ExB Shear
Turbulent
Eddies
Radial Direction
t1
t2
t3

## Slide 9: Larger ExB shear is correlated with reduced turbulence and reduced transport
Ion thermal diffusivity (a measure of
radial transport of heat) is lower when
turbulence is lower
Mazzucato et al., PRL (1996)
Reduced ion-scale
turbulence when wExB > g
Reduced turbulence
(wExB > g)
Enhanced turbulence
(wExB ≤ g)
TFTR
wExB
g

## Slide 10: Rotation important for the suppression of macro-scale MHD modes that can lead to sudden plasma termination
MHD mode growth follows damping
of rotation – disruption follows
Sabbagh et al, Nuc. Fusion (2010)
also on DIII-D: Garafalo et al, Nuc. Fusion (2001)
NSTX
Higher rate of disruptivity with lower rotation
S. Gerhardt (2012)
Disruption

## Slide 11: In this talk, I will explore aspects of rotation and momentum confinement in magnetically-confined plasmas
Background
  Magnetically confined plasmas in tokamaks/spherical tokamaks
  Rotation observed in other configurations (stellarator, RFP, linear devices), but will focus on tokamak/ST
Why is rotation important
  Stabilization of micro-, macro-turbulence leads to higher performance
How do rotation profiles develop and evolve – how can we understand rotation?
  Rotation generation (driven, self-generated)
  Transport of momentum
    Find tokamak/ST results similar gives glimpse into underlying common physics
  Predictions for fusion power devices (ITER)
Future work and summary
  What else do we need to understand

## Slide 12: Momentum balance is the basis for addressing the sources and transport of rotation and momentum
Time rate of change
of angular momentum
Input torques
Momentum
transport
Viscous torque
(c-x, i-i, etc)
Neutral beam injection provides torque
through classical collisions to drive rotation
DIII-D Neutral
Beam Injectors

## Slide 13: Magnetic field asymmetries are a source of viscous torque
3D toroidal magnetic field asymmetries can result from
  Magnetic field ripple (finite # TF coils) – studied in JET
  Intrinsic error fields (coil misalignments or motion during discharge due to JxB forces)
  Applied non-axisymmetric B-field perturbations at edge
B.
C.
NSTX
DIII-D
Magnetic field (ctr) torque increases at low rotation; consistent with theory:
Park et al. PRL (2009), Cole et al. PRL (2011)
NSTX
Sabbagh et al. (2010)
2-4 mm deflection
TNBI~ TDB
~5 m

## Slide 14: There is evidence that some “intrinsic drive” exists in tokamak/ST plasmas
Momentum evolution given by
Co-, ctr-NBI on DIII-D allows for flexibility to produce non-rotating plasmas across profile
For steady-state, can produce non-rotating plasmas when:
TNBI = -Tintrinsic
Can also measure intrinsic torque via evolution of angular momentum
Solve for two unknowns from time evolution of angular momentum, L
Solomon et al. PoP (2010)

## Slide 15: Edge intrinsic torques lead to edge intrinsic rotation
Typically use L-H transitions in OH or RF-heated (torque-free) plasmas to study change in intrinsic rotation
Self-generated flow is seen in a
number of physical systems
H-mode
Intrinsic drive
NSTX
Park (2011)

## Slide 16: Intrinsic drive and rotation appears to be controlled strongly by respectively
Intrinsic rotation scales with T
Rice et al. PRL (2011)
C-Mod
Dependences consistent with ion-scale turbulence theory:
Gurcan et al. PoP (2007), Wang et al. PoP (2010),
Kosuga et al. PoP (2010), Gurcan et al. PoP (2010)
Δ
DIII-D
Solomon et al. NF (2011)
Intrinsic torque scales with p
Δ

## Slide 17: In this talk, I will explore aspects of rotation and momentum confinement in magnetically-confined plasmas
Background
  Magnetically confined plasmas in tokamaks/spherical tokamaks
  Rotation observed in other configurations (stellarator, RFP, linear devices), but will focus on tokamak/ST
Why is rotation important
  Stabilization of micro-, macro-turbulence leads to higher performance
How do rotation profiles develop and evolve – how can we understand rotation?
  Rotation generation (driven, self-generated)
  Transport of momentum
    Find tokamak/ST results similar gives glimpse into underlying common physics
  Predictions for fusion power devices (ITER)
Future work and summary
  What else do we need to understand

## Slide 18: Now that sources of rotation are established, need to understand what controls momentum transport & development of rotation profile
Momentum
transport
A theorist’s approach
Reynold’s stress
Particle flux
Langmuir probes can measure Reynold’s stress and particle flux near the edge in lower
temperature devices (Prager, PPCF 1999); these measurements are challenging on
high temperature tokamaks/STs

## Slide 19: Momentum transport characteristics can be inferred from experimental data
Steady-state momentum balance with known torques (diffusion paradigm)
Momentum
transport
Perturbation analysis allows separation of diffusive and pinch terms
Conduction
Convection

## Slide 20: Steady-state analysis shows that momentum transport is always anomalous
Ion-scale turbulence theory predicts cf~ci
cf~ 0.1-0.4 ci from experiment
cf neoclassical ≈ 0
cf >> cf,neo(turbulence impt!)
NSTX
Kaye et al. Nuc. Fusion (2009)
Tala et al. PPCF (2009)
JET
Pr = cf/ci <1

## Slide 21: Perturbation techniques used to isolate cf , vpinch
Use forward modeling to determine cf, Vpinch by matching phase, amplitude of response
Tala et al. PRL (2009)
ΔB pulse modifies rotation near edge
Center
Edge
Separation of vf,
vf essential to
determining cf,
vpinch
Δ
NB modulation
NSTX
JET
NB pulse preferentially modifies
rotation near core

## Slide 22: Perturbative momentum transport analysis reveals significant inward pinch in outer region of plasma
NB modulation
Tala et al. PRL (2009)
NSTX
JET
ΔB pulse
Fit with vpinch=0
Fit with finite vpinch
cf/ci
cf (finite vpinch)~ 2cfeff (vpinch=0)
Including vpinch brings Pr closer to ion-scale turbulence theory prediction (~1)

## Slide 23: Developing a comprehensive theoretical model of momentum transport is challenging
Need to know
  Realistic boundary conditions
  Importance of off-diagonal terms in turbulence generation
  Nature of turbulence (strongly turbulent or near marginality)
Fluid treatment of plasma can capture much physics, but almost always need to include kinetic effects
Validation of theoretical model through comparisons with experimental data
Are there any dominant parametric dependence (or lack thereof)
predicted by theory that can be tested?
Some insight, but questions remain

## Slide 24: Ion-scale turbulence theory predicts virtually NO dependence of pinch number (Rvpinch/cf) on collisionality (n)
Peeters et al. PoP (2009)
Tala et al. Nucl. Fusion (2011)
JET
Theory
Experiment
Solomon et al. PoP (2011)
Rvpinch/cf vs n
Rvpinch/cf
n
vpinch
cf

## Slide 25: Ion-scale turbulence theory predicts dependence of pinch number (Rvpinch/cf) on density gradient (R/Ln)
vs R/Ln
Peeters et al. Nucl. Fusion (2011)
Reduced fluid models also indicate
linear dependence on R/Ln
Peeters et al. PoP (2009)
Yoon and Hahm (2011)
Gyrokinetics
Tala et al. Nucl. Fusion (2011)
Theory
Experiment
JET
Also, ASDEX-Upgrade, DIII-D, JT-60U, NSTX
Pinch Number (Rvpinch/cf)
Representative discharge

## Slide 26: ITG theory predicts dependence of pinch number (Rvpinch/cf) on density gradient (R/Ln)
vs R/Ln
Peeters et al. Nucl. Fusion (2011)
Reduced fluid models also indicate
linear dependence on R/Ln
Peeters et al. PoP (2009)
Yoon and Hahm (2011)
Gyrokinetics
Tala et al. Nucl. Fusion (2011)
Theory
Experiment
JET
Theory calculations predicts weaker
dependence than is observed in experiment
Pinch Number (Rvpinch/cf)
Representative discharge

## Slide 27
A fusion power production device is presently under construction (ITER)
Operating Parameters
a = 2.0 m
R = 6.2 m (R/a= 3.1)
Ip = 15 MA
BT = 5.3 T
Performance Parameters
Fusion Power ~ 0.5 GW
Power Amplification ~ 10
Burn Flattop > 400 s
27
24 m

## Slide 28: Do we know enough to extrapolate to ITER?
Making progress in developing a theory-based predictive capability, but not there yet
Predictive simulations based
JET values of Pr, Rvpinch/cf
Tala et al. Nucl. Fusion (2011)
Rotation boundary condition, inward pinch
most critical in determining core rotation
TNBI=35 N-m
wbound=7 krad/s
Fixed NB torque simulations indicate
importance of boundary conditions
Little change of vf profile with
different torque profiles with
fixed boundary condition

## Slide 29: Many open questions for “comprehensive” understanding
A strong coupling between turbulence/transport and ExB shear exists
  Can we establish causality (is it possible)?
Boundary conditions: typically no slip has been assumed by theory (BC critical)
  Edge flows observed, however
Effect of core MHD, energetic particle modes on rotation
Understand and quantify RF “torques”
Influence of high-k (electron mode) turbulence on rotation generation/momentum transport
LaBombard et al. Nucl. Fusion (2004)
C-Mod

## Slide 30: Summary
Rotation in tokamaks and STs can be large and can have a profound effect on discharge performance (transport and stability)
Intrinsic rotation generation and momentum transport strongly coupled to ion-scale microturbulence
A comprehensive theoretical understanding is at its early stages
  Boundary conditions critical – theory must apply across full plasma
  Requires detailed validation with existing data

## Slide 31: Backup

## Slide 32: Fusion-grade plasmas are magnetically confined in toroidal devices
Tokamak
Helical magnetic field line topology described by safety factor
Describes magnetic field “pitch”
R
b
a
Present day tokamaks have elongated cross-sections
(also, stellarators, RFPs)
Elongation
Aspect Ratio
(Helicity critical for confining plasmas)

## Slide 33: Poloidal rotation << toroidal rotation in tokamak/STs
Discrepancy between STs and higher aspect ratio tokamaks seen
DIII-D (from Solomon et al., PoP 2005)
NSTX (from Bell et al., PoP 2010)
Vq in STs consistent with predictions
from neoclassical theory*
Difference of Vq with neoclassical
predictions can be large in tokamaks
* Neoclassical transport ~ Enhanced collisional transport due to connection length,
            particle trapping effects in toroidal geometries
Theory
Data
Data
Theory

## Slide 34: ExB shear facilitates transitions to enhanced confinement regimes
~ Zero torque
Large >0 torque
DIII-D
Large Er shear leads to lower power needed for L- to H-mode transition
McKee et al, Nuc. Fusion (2009)
Strong ExB shear leads to “Internal Transport Barriers”
ITB
non-ITB
ITB
Bell et al, PPCF (1999)
Synakowski et al, Nuc. Fusion (1999)
TFTR

## Slide 35: Large Er shear leads to lower power needed for L- to H-mode transition
DIII-D
McKee et al, Nuc. Fusion (2009)

## Slide 36
Electrode biasing in TEXTOR drives ExB shear and associated reduction in turbulence levels
Boedo et al, PPCF(2002)

## Slide 37
Higher Er shear facilitates the
transition from L- to H-mode
Xu et al, Phys. Rev. Lett. (2000)
HT-6M
L->H

## Slide 38: Radio-frequency heating of plasma also provides torque - Ubiquitous, but not well understood -
High Harmonic Fast Waves
McDermott et al, PPCF (2011)
ASDEX-U
Taylor et al, PoP (2010)
C-Mod
C-Mod
Lin et al, Nuc. Fusion (2011)
(Fast wave ICW)
Ince-Cushman et al, PRL (2011)
RF can reduce
co-rotation
and/or lead to
counter-rotation

## Slide 39: Magnetic field asymmetries are a source of viscous torque
3D toroidal magnetic field asymmetries can result from
  Magnetic field ripple (finite # TF coils)
  Intrinsic error fields (coil misalignments or motion during discharge due to JxB forces)
  Applied non-axisymmetric B-field perturbations at edge
B.
C.
NSTX
DIII-D
Non-resonant magnetic field (ctr) torque increases at low rotation; consistent with theory:
Cole et al. PRL (2011)
Park et al. PRL (2009)
NSTX
Solomon et al. PoP (2010)

## Slide 40: There is evidence that some “intrinsic drive” exists in tokamak/ST plasmas (Tself-driven)
Can also measure intrinsic torque via evolution of angular momentum
Solve for two unknowns from time evolution of angular momentum, L
DIII-D
Solomon et al. PoP (2010)
Co-, ctr-NBI on DIII-D allows for flexibility to produce non-rotating plasmas across profile
- Counter torque required to offset intrinsic drive

## Slide 41: Edge intrinsic torques lead to edge intrinsic rotation
Typically use L-H transitions in OH or RF-heated plasmas to study change in intrinsic rotation
H-mode
Intrinsic drive
NSTX OH L-H-mode
Rice et al. Nucl. Fusion (2007)
Rice scaling not universal
J.-K. Park, 2011

## Slide 42: Intrinsic drive and rotation appears to be controlled strongly by respectively
Correlation found between intrinsic rotation and Ti in C-Mod and NSTX (also JT-60U)
Rice et al. PRL (2011)
NSTX
J.K. Park (PPPL)
C-Mod
Wang et al. PoP (2010)
Kosuga et al. PoP (2010)
Gurcan et al. PoP (2010)
theory ---
Δ
Intrinsic torque scales strongly with
p, consistent with low-k turbulence
theory, Gurcan et al. PoP (2007)
DIII-D
NSTX
Solomon et al. NF (2011)
J.K. Park (PPPL)
Δ

## Slide 43: Perturbation techniques used to isolate cf , vpinch
Can solve for cf, Vpinch in source-free region from amplitude & phase of response
Usually find source region broad – technique not valid
Use forward modeling to determine cf, Vpinch
Tala et al. PRL (2009)
NB step
Applied ΔB step
Center
Center
Edge
Edge
Separation of vf,
vf essential to
determining cf,
vpinch
Δ
NB modulation
NSTX
JET

## Slide 44: Perturbative momentum transport analysis reveals significant inward pinch in outer region of plasma
Including vpinch brings Pr closer to 1 (0.5 – 0.8)
cf ~ 2cfeff
MP step
NB modulation
Tala et al. PRL (2009)
Yoshida et al. Nucl. Fusion (2007)
NSTX
JET
JT-60U

## Slide 45: Not all theory predictions are seen in the data
Theory
vs q
Gyrokinetics
Experiment
Peeters et al. Nucl. Fusion (2011)
Not definitive
Theory indicates inward pinch should increase with increasing inverse aspect ratio (e)
Peeters et al, PoP (2009)
Experiments do not show this from device-to-device

## Slide 46: Drift wave turbulence is basis for understanding dependences of intrinsic rotation/torque (stress)
Conversion of turbulent energy to directed flow (leading theory)
Driven by gradients in T, p, n; requires “symmetry breaking” (rotation imbalance in F)
Symmetry breaking
accomplished in
several ways
ExB shear
Fluctuation intensity gradient
ExB shearing can come from generation of
Zonal Flows/GAMS (Geodesic Acoustic Modes)
Flow in poloidal direction with m=0/n=0
Associated with radial zones of varying Er
w~0 (ZFs) or few kHz (GAMs)
Gurcan et al. PoP (2007)
Ku et al. submitted to PoP (2011)

## Slide 47: Turbulence/flow energy coupled strongly through energy conservation (and predator-prey paradigm)
ZF is like predator (eats turbulence)
Turbulence is like prey (eats gradients)
Transport and turbulence reduced by ZFs
Gurcan et al. PoP (2007)
Predator-Prey relation observed in toroidal devices
Estrada et al. PRL (2011)
TJ-II stellarator
ASDEX-U
Conway et al. PRL (2011)

## Slide 48: Intrinsic rotation reversals may give insight into which specific drift wave modes are dominant
Alcator C-Mod finds confinement regimes/rotation directions depend strongly on density
Turbulence measurements indicate likely transition from TEM (low ne, Te>Ti) to ITG (high ne, Te~Ti) –dominated regime
Low ne
High ne
Rice et al. PRL (2011)
Rice et al. to appear in Phys. Plasmas (2012)

## Slide 49: High-k scattering shows drop in turbulence across k-spectrum with increasing ExB shear