## Slide 1: Snowflake Divertor Studies in DIII-D and NSTX Aimed at the Power Exhaust Solution for the Tokamak
V. A. Soukhanovskii
Lawrence Livermore National Laboratory, Livermore, California, USA
for the NSTX-U and DIII-D Research Teams
Oral O2.101

## Slide 2: Co-authors and Acknowledgements
S. L. Allen1, E. Kolemen2, T. H. Osborne3, J. A. Boedo4,
M. E. Fenstermacher1, R.J. Groebner3, D.N. Hill1, A.W. Hyatt3,
C. J. Lasnier1, A. W. Leonard3, M. A. Makowski1, W.H. Meyer1,
A.G. McLean1, T.W. Petrie3, D. D. Ryutov1, J.G. Watkins5,
R.E. Bell2, A. Diallo2, S. Gerhardt2, R. Kaita2, S. Kaye2, B.P. LeBlanc2,
R. Maingi2, E. T. Meier1, J.E. Menard2, M. Podesta2, R. Raman6,
A.L. Roquemore2, and F. Scotti2
    1Lawrence Livermore National Laboratory, Livermore, CA 94550, USA
    2Princeton Plasma Physics Laboratory, Princeton, NJ 08543-0451, USA
    3General Atomics, San Diego, CA 92186-5608, USA
    4University of California San Diego, La Jolla, CA 92093-0417, USA
    5Sandia National Laboratories, Livermore, CA 94550, USA
    6University of Washington, Seattle, WA 98105, USA
Work supported in part by the US DoE under DE-AC52-07NA27344, DE-AC52-07ER27344, DE-FC02-04ER54698, DE-AC02-09CH11466, and DE-FG02-07ER54917.

## Slide 3: Significant heat flux reduction between and during ELMs observed in NSTX and DIII-D snowflake divertors
Outline of talk
Snowflake divertor configuration
Snowflake divertor in NSTX
  Facilitated access to detachment
  Heat flux reduction compatible with H-mode
Snowflake divertor in DIII-D
  Heat flux reduction compatible with H-mode
  Cryopump density control within
  ne/nG = 0.4-0.75
  Detachment and ELM heat flux
Projections for NSTX-Upgrade
Conclusions
*

## Slide 4: Snowflake divertor geometry takes advantage of Bp structure in second-order null region
Snowflake-minus
Snowflake-plus
Exact
snowflake
*
+
+
+
+
D. D. Ryutov, PoP 14, 064502 2007;
EPS 2012 Invited, PPCF 54, 124050 (2012)
Predicted properties
  Increased edge shear: ped. stability
  Add’l null: H-mode power threshold, ion loss
  Larger plasma wetted-area Awet : reduce qdiv
  Four strike points : share qII
  Larger X-point connection length Lx : reduce qII
  Larger effective divertor volume Vdiv : incr. Prad
  High bp convective zone D* ≤ a (a bpm / R)1/4
Snowflake divertor configuration
  Second-order null
      Bp ~ 0 and grad Bp ~ 0 (Cf. first-order null: Bp ~ 0)
  Exact snowflake topologically unstable
  Deviation from exact snowflake
    d ≤ a (lq / a)1/3 where d – distance between nulls, a – plasma minor radius, lq – SOL width

## Slide 5: Snowflake configurations sustained in NSTX and DIII-D for many tE’s with divertor coil currents within safety margins
Divertor coil currents 0.5-4 kA within safety margins
Steady-state snowflake configurations
  NSTX: 0.5 s
  DIII-D: 3 s
Standard divertor Snowflake-minus Exact snowflake
Standard divertor Snowflake-minus

## Slide 6: Snowflake divertor in NSTX compatible with H-mode confinement, facilitated access to partial detachment
  Graphite PFCs with lithium coatings
Ip = 0.9 MA, PNBI = 4 MW, PSOL ~ 3 MW
qpeak ≤ 8 MW/m2, q|| ≤ 100 MW/m2
With snowflake divertor
H-mode confinement unchanged
  WMHD~250 kJ, H98(y,2)~ 1, bN~5
Core impurity reduced by up to 50 %
Suppressed ELMs re-appeared
Divertor heat flux significantly reduced
  Between ELMs
  During Type-I ELMs (DW/W ~ 5-15 %)

## Slide 7: In DIII-D, peak divertor heat flux reduction by 50-60 % between ELMs due to geometry
  Graphite PFCs
Ip = 1.2 MA, PNBI = 5 MW, PSOL ~ 3 MW
qpeak ≤ 2 MW/m2, q|| ≤ 100 MW/m2
Obtained snowflake-minus for up to 3 s duration over ne/nG = 0.4 – 0.75 using cryo-pump for density control
In lower-density snowflake H-mode
  Confinement unaffected
  Divertor attached
    Divertor Prad similar to standard div.
  Divertor heat flux reduced
    Plasma-wetted area increased up to 80 %
    Connection length increased up to 75 %
Standard, Snowflake

## Slide 8: Heat flux in snowflake divertor is further reduced during partial detachment in DIII-D
In higher-density snowflake H-mode
  Density ne/nG = 0.55-0.75
  Partial detachment onset (ne) similar in standard and snowflake (preliminary)
  Peak heat flux is up to 50 % lower in partially detached snowflake vs partially detached standard divertor
  Lower divertor rad. power broadly distributed in partially detached snowflake
  No MARFEs
Standard, Snowflake
Standard Snowflake

## Slide 9: In DIII-D, Type-I ELM heat loads reduced in D2-seeded (partially detached) snowflake divertor
At lower density, heat flux channels close to primary and second separatrices during ELMs
  Additional strike points
At high density (partial detachment), ELM heat flux significantly reduced
  50-75 % lower than in standard partially detached
Snowflake
Standard Snowflake
Standard Snowflake
ne/nG = 0.45
ne/nG = 0.60

## Slide 10
Snowflake divertor is a leading heat flux mitigation candidate for NSTX-Upgrade
Predictions for 12 MW NBI
  2D multifluid code UEDGE
  PSOL=9 MW, 4 % carbon
  D, c to match lq
  Outer divertor attached
    Te, Ti ≤ 80 eV
New center-stack
2nd neutral beam
BT
Ip
PNBI
pulse
1 T
2 MA
12 MW
5 s
NSTX-U Mission elements:
  Advance ST as candidate for Fusion Nuclear Science Facility
  Develop solutions for the plasma-material interface challenge
  Explore unique ST parameter regimes to advance predictive capability for ITER
  Develop ST as fusion energy system

## Slide 11: Developing the Power Exhaust Solution for the Tokamak with the Snowflake Divertor in NSTX and DIII-D
  Large zone of low poloidal field in divertor resulting in significant geometry benefits for heat exhaust
  Steady-state configurations with existing divertor coils
  Significant peak divertor heat flux reduction between and during Type I ELMs compatible with high H-mode confinement
Initial confirmation of compatibility with cryo-pump density control
  Potential to combine with radiative divertor solution
Favorable projections for NSTX-Upgrade with 12 MW NBI power

## Slide 12: Backup slides

## Slide 13: Bibliography
Theory
D. D. Ryutov, PoP 14 (2007), 064502
D. D. Ryutov et al., Plasma Phys. Control. Fusion 52 (2010) 105001.
D. D. Ryutov, Contrib. Plasma Phys. 52 (2012) 539.
D. D. Ryutov et al., Plasma Phys. Control. Fusion 54 (2012) 124050
D. D. Ryutov et al., Paper TH/P4-18, IAEA FEC 2012
DIII-D
S. L. Allen et al., Paper PD/1-2, IAEA FEC 2012.
NSTX
V. A. Soukhanovskii et al., Nucl. Fusion 51 (2011) 012001.
V. A. Soukhanovskii et al., Phys. Plasmas 19 (2012) 082504.
V. A. Soukhanovskii et al., Paper EX/P5-21, IAEA FEC 2012.

## Slide 14: Various techniques developed for reduction of heat fluxes q|| (divertor SOL) and qpeak (divertor target)
Recent ideas to improve standard divertor geometry
  Snowflake divertor (D. D. Ryutov, PoP 14, 064502 2007)
  X-divertor (M. Kotschenreuther et. al, IC/P6-43, IAEA FEC 2004)
  Super-X divertor (M. Kotschenreuther et. al, IC/P4-7, IAEA FEC 2008)

## Slide 15: Heat flux mitigation is more challenging in compact divertor of spherical torus
NSTX
  Ip = 0.7-1.4 MA, tpulse < 1.5 s, Pin ≤ 7.4 MW (NBI)
  ATJ and CFC graphite PFCs
  P / R ~ 10
  qpk ≤ 15 MW/m2
  q|| ≤ 200 MW/m2
Quantity | NSTX | DIII-D
Aspect ratio | 1.4-1.5 | 2.7
In-out plasma boundary area ratio | 1:3 | 2:3
X-point to target parallel length Lx (m) | 5-10 | 10-20
Poloidal magnetic flux expansion fexp at outer SP | 5-30 | 3-15
Magnetic field angle at outer SP (deg.) | 1-10 | 1-2

## Slide 16: Snowflake divertor configurations obtained with existing divertor coils in NSTX

## Slide 17: Snowflake divertor configurations obtained with existing divertor coils, maintained for up to 10 tE

## Slide 18: NSTX: Plasma-wetted area and connection length are increased by 50-90 % in snowflake divertor
These properties observed in first 30-50 % of SOL width (lq~6 mm)
Btot angles in the strike point region: 1-2o, sometimes < 1o
  Concern for hot-spot formation and sputtering from divertor tile edges
  Can be alleviated by q|| reduction due to radiative detachment and power partitioning between strike points

## Slide 19: Snowflake divertor configurations obtained with existing divertor coils in DIII-D

## Slide 20: Snowflake configurations obtained from the standard divertor using an algorithm developed at NSTX
Grad-Shafranov equilibria modeling of possible configurations
Inner and outer strike point positions controlled by PCS using F4B and F8B coils
Secondary null-point formed and pushed in using F5B
+
+
+

## Slide 21: Impulsive heat loads due to Type I ELMs are mitigated in snowflake divertor
H-mode discharge, WMHD ~ 220-250 kJ
  Type I ELM (W/DW ~ 5-8 %)
Steady-state At ELM peak

## Slide 22: Good H-mode confinement properties and core impurity reduction obtained with snowflake divertor
0.9 MA, 4 MW H-mode
k=2.1, d=0.8
Core Te ~ 0.8-1 keV, Ti ~ 1 keV
bN ~ 4-5
Plasma stored energy ~ 250 kJ
H98(y,2) ~ 1 (from TRANSP)
ELMs
  Suppressed in standard divertor H-mode via lithium conditioning
  Re-appeared in snowflake H-mode
Core carbon reduction due to
  Type I ELMs
  Edge source reduction
    Divertor sputtering rates reduced due to partial detachment

## Slide 23: Core carbon density significantly reduced with snowflake divertor
Standard divertor Snowflake

## Slide 24: Good H-mode confinement properties retained or slightly reduced with CD4-seeded snowflake divertor
Standard
Snowflake
Radiative divertor w/ CD4
Snowflake+CD4

## Slide 25: Divertor profiles show enhanced radiation and recombination zone in snowflake divertor w/ and w/o CD4
Standard
Snowflake
Radiative divertor w/ CD4
Snowflake+CD4

## Slide 26: NSTX: Access to radiative detachment with intrinsic carbon in snowflake divertor facilitated
Snowflake divertor (*): PSOL~3-4 MW, fexp~40-60, qpeak~0.5-1.5 MW/m2
  Low detachment threshold
  Detachment characteristics comparable to PDD with D2 or CD4 puffing

## Slide 27: Pedestal profiles very similar with and without SF(-)
Slightly steeper and higher ne, lower and flatter Te with SF-
Electron Density ne
Electron Temperature Te
S. L. Allen et al., Paper PD/1-2, IAEA FEC 2012.

## Slide 28: Detailed ELM Analysis: DW(ELM) decreased, W pedestal constant in SF
Detailed ELM analysis before/during SF shows:
Pedestal Energy (WPEDESTAL) Constant
Confinement Constant
Change in stored energy lost per ELM (ΔWELM) is reduced
Consistent with Loarte connection length scaling
S. L. Allen et al., Paper PD/1-2, IAEA FEC 2012.