## Slide 1
Studies of ST-FNSF mission and performance dependence on device size
J. Menard1, T. Brown1,
J. Canik2, L. El Guebaly3, S. Gerhardt1, S. Kaye1,
M. Ono1, R. Raman4, S. Sabbagh5, V. Soukhanovskii6,
P. Titus1, G. Voss7, A. Zolfaghari1
1st IAEA DEMO Programme Workshop
UCLA - Faculty Center, California Room
Los Angeles, CA U.S.A.
15-18 October 2012
This work supported by the US DOE Contract No. DE-AC02-09CH11466
1Princeton Plasma Physics Laboratory, Princeton, NJ 08543
2Oak Ridge National Laboratory, Oak Ridge, TN, USA
3University of Wisconsin, Madison, WI, USA
4University of Washington, Seattle, WA, USA
5Columbia University, New York, NY, USA
6Lawrence Livermore National Laboratory, Livermore, CA, USA
7Culham Centre for Fusion Energy, Abingdon, Oxfordshire, UK

## Slide 2: There are many possible pathways from ITER to commercial fusion power plant
FNSF = Fusion Nuclear Science Facility
CTF = Component Test Facility
ITER
First of a kind
Power Plant
Supporting Physics and Technology
Core Physics
Materials R&D
Plasma Material Interface
Pilot Plant
FNSF/CTF with power-plant like maintenance, Qeng ≥ 1
Qeng = 3-5
e.g. EU Demo
FNSF/CTF
Blanket R&D, T self-sufficiency

## Slide 3: This talk focuses on possible spherical tokamak (ST) contributions ranging from FNSF to Pilot Plant
FNSF = Fusion Nuclear Science Facility
CTF = Component Test Facility
ITER
First of a kind
Power Plant
Supporting Physics and Technology
Core Physics
Materials R&D
Plasma Material Interface
Pilot Plant
FNSF/CTF with power-plant like maintenance, Qeng ≥ 1
Qeng = 3-5
e.g. EU Demo
FNSF/CTF
Blanket R&D, T self-sufficiency

## Slide 4: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 5: Successful operation of upgraded STs (NSTX-U/MAST-U) could provide basis for design, operation of ST-based FNSF
Fusion Nuclear Science Facility (FNSF) mission:
  Provide continuous fusion neutron source to develop knowledge-base for materials and components, tritium fuel cycle, power extraction
FNSF  CTF would complement ITER path to DEMO
Studying wide range of ST-FNSF configurations to identify advantageous features, incorporate into improved ST design
M. Peng et al., IEEE/NPSS Paper S04A-2 - 24th SOFE Conf. (2011)
M. Abdou et al. Fus. Technol. 29 (1996) 1
Investigating performance vs. device size
  Require: Wneutron ≥ 1 MW/m2, test area ≥ 10 m2, volume ≥ 5 m3

## Slide 6: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 7: NSTX-U will access next factor of 2 increase in performance to reduce extrapolation to ST-based FNSF/CTF/Pilot
Achievable confinement
Non-inductive ramp-up and sustainment
Divertor solutions for mitigating high heat flux
Radiation-tolerant magnets
* Includes 4MW of high-harmonic fast-wave (HHFW) heating power
Key issues to
resolve for FNSF
Parameter | NSTX | NSTX Upgrade | Fusion Nuclear Science Facility | Pilot Plant
Major Radius R0 [m] | 0.86 | 0.94 | 1.3 | 1.6 – 2.2
Aspect Ratio R0 / a |  1.3 |  1.5 |  1.5 |  1.7
Plasma Current [MA] | 1 | 2 | 4 – 10 | 11 – 18
Toroidal Field [T] | 0.5 | 1 | 2 – 3 | 2.4 – 3
Auxiliary Power [MW] | ≤ 8 | ≤ 19* | 22 – 45 | 50 – 85
P/R [MW/m] | 10 | 20 | 30 – 60 | 70 – 90
P/S [MW/m2] | 0.2 | 0.4 | 0.6 – 1.2 | 0.7 – 0.9
Fusion Gain Q |  |  | 1 – 2 | 2 – 10

## Slide 8: ST-FNSF operating point of A=1.7, li = 0.5, and k=3 chosen to be at/near values anticipated for NSTX-U
Most probable NSTX thermal pressure peaking factor ~1.8
  If similar in NSTX-U/FNSF  full non-inductive li ~ 0.5 (BS + NBI)
NSTX A=1.7, li = 0.5 plasmas can operate stably at k ~ 2.8
  Expect to improve n=0 control in NSTX-U  anticipate k~3 possible in NSTX-U/FNSF

## Slide 9: ST-FNSF operating point of fGreenwald = 0.8, H98y,2=1.2 chosen to be at/near values anticipated for NSTX-U
H98y,2 ~ 1.2 has been accessed for a range of Greenwald fractions
  However, much more research needs to be carried out in NSTX-U to determine if HH=1.2 can be achieved reliably
Also need to assess feasibility of routine access to H98y,2 ~ 1.2 at k~3 in NSTX-U
Note: there is sufficient shaping margin to reduce k to 2.7-2.9 for FNS mission, but H98y,2 ~ 1 would require much higher Paux (~1.8×)

## Slide 10: NSTX disruptivity data informs FNSF operating point with respect to global stability
Increased disruptivity for q* < 2.7
  Significantly increased for q* < 2.5
Lower disruptivity for bN = 4-6 compared to lower bN
  Higher bN increases fBS, broadens J profile, elevates qmin
  Operation above no-wall limit aided by:
    NBI co-rotation
    Close-fitting conducting wall
    Active error-field and RWM control
Strong shaping also important
  S  q95 IP/aBT
  S > 30 provides strongest stabilization
  S > 22-25 good stability
  S < 22 unfavorable
Gerhardt
IAEA FEC EX/9-3

## Slide 11: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 12: Increased device size provides modest increase in stability, but significantly increases tritium consumption
Scan R = 1m  2.2m (smallest FNSF  pilot plant with Qeng ~ 1)
Fixed average neutron wall loading = 1MW/m2
BT = 3T, A=1.7, k=3, H98 = 1.2, fGreenwald = 0.8
100% non-inductive: fBS = 75-85% + NNBI-CD (ENBI=0.5MeV JT60-SA design)
Larger R lowers bT & bN, increases q*
Comparable/higher bT and bN values already sustained in NSTX
Q = 1  3, Pfusion = 60MW  300MW  5× increase in T consumption

## Slide 13: In addition to neutron wall loading and tritium breeding, FNSF study also tracking overall electrical efficiency: Qeng
th = thermal conversion efficiency
aux = injected power wall plug efficiency
Q = fusion power / auxiliary power
Mn = neutron energy multiplier
Pn = neutron power from fusion
P = alpha power from fusion
Paux = injected power (heat + CD + control)
Ppump = coolant pumping power
Psub = subsystems power
Pcoils = power lost in coils (Cu)
Pcontrol = power used in plasma or plant control that is not included in Pinj
Pextra = Ppump + Psub + Pcoils + Pcontrol
Note: blanket and auxiliary heating and current-drive efficiency + fusion gain largely determine Qeng
Electricity produced
Electricity consumed
    FNSF assumptions (from Pilot study):
    Mn = 1.1
    Ppump = 0.03×Pth
    Psub + Pcontrol = 0.04×Pth
    haux = 0.4 (presently unrealistically high)
    hCD = ICDR0ne/PCD = 0.3 × 1020A/Wm2
For more details see J. Menard, et al., Nucl. Fusion 51 (2011) 103014

## Slide 14: High performance scenarios can access increased neutron wall loading and engineering gain > 1 for sufficiently large R
Decrease BT = 3T  2.6T, increase H98 = 1.2  1.5
Fix bN = 6, bT = 35%, q* = 2.5, fGreenwald varies: 0.66 to 0.47
Size scan: Q increases from 3 (R=1m) to 14 (R=2.2m)
Average neutron wall loading increases from 1.8 to 3 MW/m2 (not shown)
Smallest ST for Qeng ~ 1 is R=1.6m  requires very efficient blankets
Note: Outboard PF coils are superconducting
Qeng 
Pelectric produced
Pelectric consumed

## Slide 15: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 16: Cost of tritium and need to demonstrate T self-sufficiency motivate analysis of tritium breeding ratio (TBR)
Example costs of T w/o breeding at $0.1B/kg for R=1  1.6m
  FNS mission: 1MWy/m2 $0.33B  $0.9B
  Component testing: 6MWy/m2 $2B  $5.4B
Implications:
  TBR << 1 likely affordable for FNS mission with R ~ 1m
  Component testing arguably requires TBR approaching 1 for all R
Performing initial analysis of R=1.6m FNSF using conformal and straight blankets, ARIES-ST neutron source profiles:
Neutron Source
63%
32%
5%

## Slide 17: R=1.6m TBR calculations highlight importance of shells, penetrations, and top/bottom blankets
Extended
conformal blanket
TBR = 1.1
Conformal blanket
TBR = 1.046
TBR = 1.02
10 NBI penetrations
NBI penetration at midplane
TBR = 1.07
Stabilizing
shell
+ 3cm thick stabilizing shell
Straight blanket
TBR = 0.8
Extended
straight blanket
TBR = 1.0
TBR = 1.047
Straight blanket
with flat top
Extended conformal + 3cm shell + NBI

## Slide 18: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 19: FNSF center-stack can build upon NSTX-U design and is incorporating NSTX stability results
Like NSTX-U, use TF wedge segments (but brazed/pressed-fit together)
  Coolant paths: gun-drilled holes or NSTX-U-like grooves in wedge + welded tube
Bitter-plate divertor PF magnets in ends of TF enable high triangularity
  NSTX data: High d > 0.55 and shaping S  q95IP/aBT > 25 minimizes disruptivity
  Neutronics: MgO insulation can withstand lifetime (6 FPY) radiation dose

## Slide 20
Glidcop plates
Insulator
Bitter coil insert for divertor coils in ends of TF

## Slide 21: Neutronics analysis indicates organic insulator for divertor PF coils unacceptable

## Slide 22: MgO insulation appears to have good radiation resistance for divertor PF coils
UW analysis of divertor PFs
  1.8x1012 rad = 1.8x1010 Gy at 6FPY for Pfus = 160MW
Pilot mission for R=1.6m:
  Pfus = 420MW vs. 160MW  2.6x higher  4.7x1010 Gy
  Even for Pilot mission, dose is < limit of 1011 Gy
Limiting factor may be Cu
Need to analyze CS lifetime
Revisit option for multi-turn TF and small OH solenoid

## Slide 23: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 24: Divertor PF coil configurations identified to achieve high d while maintaining peak divertor heat flux < 10MW/m2
Flux expansion = 15-25, dx ~ 0.55
1/sin(qplate) = 2-3
Detachment, pumping questionable
  Future: assess long-leg, V-shape divertor (JA)
Flux expansion = 40-60, dx ~ 0.62
1/sin(qplate) = 1-1.5
Good detachment (NSTX data) and cryo-pumping (NSTX-U modeling)
Snowflake
Field-line angle
of incidence at
strike-point = 1˚
Jaworski - IAEA FEC EX/P5-31
Will also test liquid metal PFCs in NSTX-U for power-handling, surface replenishment
Conventional

## Slide 25: Parameters and profiles for conventional divertor (using simple exponential heat-flux profile in R=1.6m ST-FNSF)
Pheat = 115MW, frad=0.8, fobd=0.8, sin(qpol) = 0.39
Rstrike = 1.16m, fexp = 22, lq-mid =2.7mm, Ndiv = 2
Pheat (1-frad) fobd sin(qpol)
2pRstrike fexp lq-mid Ndiv
Peak q-div 
NSTX-U simulations find q at pump entrance should be ≥ 1-2MW/m2 for efficient pumping  guesstimate Rentrance ~ 1.3m for R=1.6m ST-FNSF
Strike point radius

## Slide 26: Parameters and profiles for snowflake divertor (using simple exponential heat-flux profile in R=1.6m ST-FNSF)
Pheat = 115MW, frad=0.8, fobd=0.8, sin(qpol) = 0.87
Rstrike = 1.05m, fexp = 50, lq-mid =2.7mm, Ndiv = 2
Pheat (1-frad) fobd sin(qpol)
2pRstrike fexp lq-mid Ndiv
Peak q-div 
Strike point radius
Snowflake would also want divertor cryo-plenum entrance radius Rentrance ~ 1.3m for R=1.6m ST-FNSF

## Slide 27: Outline
Motivation for study
Physics basis for operating points
Performance vs. device size
Tritium breeding ratio calculations
Divertor poloidal field coil layout and design
Power exhaust calculations
Maintenance strategies
Summary

## Slide 28: Flexible and efficient in-vessel access important for testing, replacing, improving components, maximizing availability
Vertically remove entire blanket and/or center-stack
  Better for full blanket replacement?
Translate blanket segments radially then vertically
  Better for more frequent blanket module replacement and/or repair?
May be possible to combine features of both approaches
Several maintenance approaches under consideration:
Radial ports
for divertor
maintenance
or pumping

## Slide 29: Assembly and maintenance schemes with snowflake divertor and vertical ports
Full Blanket Assembly Removed
Centerstack Assembly Removed

## Slide 30: Possible divertor module maintenance scheme using radial installation and vertical translation through vertical ports

## Slide 31
Large cylindrical vessel of R=1.6m FNSF could be used for PMI R&D (hot walls, Super-X?), other blanket configurations
Straight blanket
TBR = 0.8
TBR = 1.047
Straight blanket
with flat top
NOTE: TBR values do not include stabilizing shells or penetrations

## Slide 32: Summary
Present STs (NSTX/MAST) providing preliminary physics basis for ST-FNSF performance studies
  Upgraded devices will provide more extensive and definitive basis
Neutron wall loading of 1MW/m2 feasible for range of major radii for b and H98 values at/near values already achieved
  High wall loading and/or pilot-level performance require bN ~ 6 and H98 ~ 1.5 which are at/near maximum values attained in present STs
TBR ~ 1 possible if top/bottom neutron losses are minimized
Divertor PF coils in ends of TF bundle enable high d, shaping
Conventional and snowflake divertors investigated, PF coils incorporated to reduce peak heat flux < 10MW/m2
Vertical maintenance strategies for either full and/or toroidally segmented blankets being investigated

## Slide 33: Future work (a highly incomplete list!)
Physics basis for operating points
  Perform sensitivity study of achievable performance vs. baseline configuration assumptions: A, k, H98y,2, ST vs. tokamak tE scaling
  TRANSP calculations of NBI heating, current drive, neutron production
Performance vs. device size
  Could/should overall machine configuration change at smaller R?
  Example questions: could/should vessel take more load?, is there sufficient shielding for divertor PF coils at smaller R?
Tritium breeding ratio calculations
  Extend calculations to smaller R, include 3D effects and final machine layout
Divertor poloidal field coil layout and design
  Assess radiation induced conductivity (RIC) in ceramic insulators
Power exhaust calculations
  Perform pumping and detachment calculations, include Super-X divertor
Maintenance strategies
  Assess space/lifting requirements above machine for vertical maintenance

## Slide 34: Backup

## Slide 35
R=1.6 m ST FNSF with JT-60SA NNBI system