## Slide 1: Overview of First Results from NSTX-U and Analysis Highlights from NSTX
Jonathan Menard (PPPL)
On behalf of the NSTX-U Research Team
26th IAEA Fusion Energy Conference
Kyoto, Japan
17–22 October 2016

## Slide 2: NSTX-U Program is Highly Collaborative
Domestic (33)
International (22)
350+ data users
55 institutions
22 US Universities

## Slide 3: Outline
NSTX-U mission
Research highlights
Progress on next-step ST concepts
Summary

## Slide 4: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Li
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 5: NSTX-U will access new physics with 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 6: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet
Performance goals:

## Slide 7: NSTX-U had scientifically productive 1st year
Achieved H-mode on 8th day of 10 weeks of operation
Surpassed magnetic field and pulse-duration of NSTX
Matched best NSTX H-mode performance at ~1MA
Identified and corrected dominant error fields
Commissioned all magnetic and kinetic profile diagnostics
New 2nd NBI suppresses Global Alfven Eigenmodes (GAE)
Implemented techniques for controlled plasma shut down, disruption detection, commissioned new tools for mitigation
2016 run ended prematurely due to fault in divertor PF coil
  Coil forensics, design (re)-reviews, preparing for new coil fabrication
  Aim to resume plasma operation end of 2017 / early 2018

## Slide 8: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 9: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 10: NSTX-U has surpassed maximum pulse duration and magnetic field of NSTX
Compare similar NSTX / NSTX-U Boronized L-modes, PNBI=1MW
NSTX-U L-mode duration
exceeds longest NSTX H-mode
4x longer
NSTX-U BT > highest NSTX BT

## Slide 11: n=1 error field correction (EFC) optimized to maximize pulse length, discharge performance
L-modes used to identify optimal correction amplitude, phase
Multiple compass scans confirm optimal L-mode EFC in flattop
EFC current [kA]
EFC current [kA]
ne = 2.9 ×1013 (solid)
ne = 1.4 ×1013 (dashed)

## Slide 12: Recovered ~1MA H-modes with weak/no core MHD (comparable to best NSTX plasmas at similar plasma current)
H98 ≥ 1, βN ~ 3.5-4 ≥ n=1 no-wall limit
202946 – no EFC 204112 – EFC v2
203679 – EFC v1 204118 – EFC v2

## Slide 13: Accessed low li and high k using progressively earlier H-mode and heating + optimized EFC
L-mode flattop
H-mode flattop
NSTX-U (5 run weeks)
NSTX (10 years)
Future goal
NSTX-U: Additional sensors improve estimation of Z, dZ/dt
Goals for next run:
  Access li = 0.5-0.7, k=2.4-2.7, BT = 0.75-1T, IP = 1.5-2MA

## Slide 14: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 15: Disruption characterization and forecasting capability initiated for NSTX-U as part of disruption avoidance plan
  New DECAF (Disruption Event Characterization And Forecasting) code written
    Identify disruption event chains and elements
      ex: vertical displacement, pressure peaking, tearing modes…
    Predict events in disruption chains
    Cues disruption avoidance system
Initial tests on NSTX RWM database
  86% of RWM shots are predicted unstable
Possible to predict growth rate in real time
gtw contours vs. ν and wf
Increasing time
ideal
Ideal + kinetic
unstable
stable
Normalized growth rate vs. time
gtw
139514
disruption
predicted instability
  Example: Reduced kinetic resistive wall mode (RWM) model developed for calculating growth rate vs. time
J.W. Berkery et al., Poster EX/P4-34, Wednesday afternoon

## Slide 16: Implemented automated ramp-down for NSTX-U
Plasma control system detects loss of control
  Central solenoid coil near maximum allowed current
  Vertical oscillations exceed threshold
  ABS(Ip–Ip request ) above threshold
“State-machine” based:
  Feedback control switches to new “states” that attempt to stably ramp-down the plasma
IP
IP Request
(including asynchronous transition to rampdown)
  ZP(dZP/dt)
  ZP(dZP/dt) threshold
Normal
Fast IP Rampdown
Insufficient IP
  ZP from EFIT
“State”
Typical ZP w/o fast ramp-down

## Slide 17: Leading studies of rotating halo currents through ITPA multi-machine analysis and M3D-C1 simulations
M3D-C1 simulations:
NSTX(-U) geometry
Simulate in 2D while q >2
Switch to 3D to resolve halo rotation (in progress)
D. Pfefferlé et al. (PPPL)
C.E. Myers et al., Poster EX/P6-46, Thursday afternoon
ITPA multi-machine analysis (MDC WG-6):
Halo current data from C-Mod, DIII-D, AUG, NSTX
All measurements in lower divertor (> 400 shots)
Halo current rotation predominantly counter-Ip (not shown)
Consistent rotation velocity, vh ~ 5 km/sec

## Slide 18: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 19: NSTX: Using global non-linear GTS gyrokinetic code to study low-k ion and electron transport
Low-k turbulence for r/a~0.7-0.85
  Turbulence later suppressed by ExB shear
Total ion energy flux Qe from GTS generally agrees with experiment
Electron energy flux Qe from GTS only significant for r/a~0.7-0.85
But GTS Qe << experimental Qe
  Electron Temperature Gradient (ETG) or electromagnetic (EM) effects important?
NSTX NBI H-mode 141767, t=332ms, BT =5.5 kG
GTS global capability important for treating larger ρ*~0.01 of NSTX
Y. Ren et al., Poster P4-35, Wednesday afternoon

## Slide 20: GYRO simulations of high-k Electron Temperature Gradient (ETG) turbulence find ne stabilizing
NSTX: Decrease in ETG turbulence amplitude w/ increasing ne
Te ~ constant
Scattering
region
ETG
NSTX 141767
Experiment ~(ne/ne)2
Low ne
High ne
Non-linear
GYRO Qe
Low ne
High ne
Simulated electron heat flux Qe [MW]
(Juan Ruiz Ruiz)
GYRO Qe << experimental Qe  Need EM, Alfvénic, low-k + high-k effects?
High-k
m-wave
scattering

## Slide 21: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 22: NSTX-U: Most tangential NBI generates counter-propagating Toroidal Alfvén Eigenmodes (TAEs)
Counter-propagating TAE predicted for hollow fast-ion profiles
TRANSP: As current builds up beam fast-ion beta profile predicted to become hollow
1st evidence of off-axis NBI deposition

## Slide 23: NSTX-U tangential 2nd neutral beam suppresses Global Alfven Eigenmode (GAE) – consistent with simulation
t ci
HYM code simulation of #204707, n=10
|dBn |2
t=0.44s
t=0.47s
New 2nd NBI already powerful tool for fast ion, AE physics
HYM code: growth of n=10 counter-GAE from 1st NBI
HYM: suppression of n=10 counter-GAE by 2nd NBI
Most unstable n-number, mode w consistent with HYM

## Slide 24: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
ST-FNSF /
Pilot-Plant
ITER
Liquid metals / Li
Snowflake/X

## Slide 25: Improving understanding of SOL heat flux width trends in NSTX using XGC1 simulations
Experiment shows contraction of SOL heat flux width at midplane with Ip as well as influence of Li conditioning
XGC-1:
Full-f, global PIC, kinetic ions and electrons
NSTX data and XGC-1: q ~ 1 / IP1.5
How will NSTX-U q scale?
Will SOL turbulence become important?
5
10
15
20
0
0.4 0.6 0.8 1 1.2 1.4
IP (MA)
Heat flux width determined primarily by neoclassical processes
Li dose 0 mg
150 mg
300 mg
BP scan
XGC1
NSTX
Experiment
Using 139047 at 665ms, 50 mg Li
q (mm)
C.S. Chang et al., Talk TH/2-1, Wednesday morning
XGC1 w/ collisions  similar trends

## Slide 26: NSTX-U: First systematic simulations of advanced divertors combined with 3D fields with EMC3-EIRENE
Divertor heat-flux trends:
  Peaked heat loads in Near Exact Snowflake
  Lowest heat loads found for X-divertor-like configurations
  RMP fields do not significantly impact toroidal average heat-flux
Standard Divertor
Near-Exact Snowflake
Snowflake Minus / X-divertor
Related snowflake results from DIII-D and NSTX:
Poster EX/P3-30 - V. Soukhanovskii, Wednesday

## Slide 27: Material Analysis & Particle Probe (MAPP) providing new measurements of surface evolution in NSTX-U
Tracked C/B/O evolution, correlated with plasma performance
Implemented remote-control + between-shot analysis
Future: Use to understand complex Li chemistry and evolution

## Slide 28: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Lithium
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 29: Recent design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) and Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7, BT=3T
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5, BT = 4T
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D (+ T self-sufficiency?)
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 (+ FNSF mission?)
Designs integrate ST higher k, bN + advanced divertors + HTS TF for Pilot Plant
FIP/P7-1 - T. Brown, Friday morning
J.E. Menard, et al., Nucl. Fusion 56 (2016) 106023

## Slide 30: NSTX-U strongly supporting advanced predictive capability, ITER, PMI solutions, and next-step STs
Productive first year of operations on NSTX-U
  Rapid H-mode access, scenario development, error field correction
  Surpassed NSTX maximum magnetic field and pulse-duration
  New fast-ion physics with 2nd NBI – GAE stabilization, counter TAE
  Commissioned new advanced PMI diagnostics – MAPP
Advancing predictive capability for core, edge, PMI
  Developing reduced models for RWM, understanding of halo rotation
  Global ion-scale turbulence (GTS), n ETG stabilization
  GAE stabilization from 2nd NBI consistent with simulation (HYM)
  Exploring SOL widths, advanced divertor interactions with 3D fields
Developed attractive ST-FNSF / Pilot Plant concepts
Aim to resume NSTX-U physics operation in ~1+ years

## Slide 31: IAEA-FEC presentations from NSTX-U
Tuesday, October 18
  OV/5-2 - J. Menard, “Overview of First Results from NSTX-U and Analysis Highlights from NSTX”
  TH/P1-2 - F. Ebrahimi, “Physics of Flux Closure during Plasmoid-Mediated Reconnection in Coaxial Helicity Injection”
  TH/P1-6 - J.-K. Park, “Self-Consistent Optimization of Neoclassical Toroidal Torque with Anisotropic Perturbed Equilibrium in Tokamaks”
  TH/P1-7 - S. C. Jardin, “Nonlinear 3D M3D-C1 Simulations of Tokamak Plasmas Crossing a MHD Linear Stability Boundary”
  TH/P1-10 - A. Fil, “Modelling and Simulation of Pedestal Control Techniques for NSTX-U”
  TH/P1-21 - Z. R.Wang, “Nyquist Analysis of Kinetic Effects on the Plasma Response in NSTX and DIII-D Experiments”
Wednesday, October 19
  FIP/2-5 - M. Ono. “Liquid Lithium Loop System to Solve Challenging Technology Issues for Fusion Power Plant”
  EX/P3-30 - V. Soukhanovskii, “Snowflake Divertor Configuration Effects on Pedestal Stability and Edge Localized Modes in NSTX and DIII-D”
  TH/P3-14 - W. Guttenfelder, “Analysis and Prediction of Momentum Transport in Spherical Tokamaks”
  EX/P4-30- J.-W. Ahn “Shielding and Amplification of Nonaxisymmetric Divertor Heat Flux by Plasma Response to Applied 3D Fields in NSTX and KSTAR”
  EX/P4-33 - S. A. Sabbagh, “Isolation of Neoclassical Toroidal Viscosity Profile under Varied Plasma and 3D Field Conditions in Low and Medium Aspect Ratio Tokamaks”
  EX/P4-34 - J.W. Berkery, “Characterization and Forecasting of Unstable Resistive Wall Modes in NSTX and NSTX-U”
  EX/P4-35 - Y. Ren, “Exploring the Regime of Validity of Global Gyrokinetic Simulations with Spherical Tokamak Plasmas”
  EX/P4-36 - F. Scotti, “Kinetic Profiles and Impurity Transport Response to 3D-Field Triggered ELMs in NSTX”
  EX/P4-38 - R. Maingi. “Comparison of Helium Glow and Lithium Evaporation Wall Conditioning Techniques in Achieving High Performance H-Mode Discharges in NSTX”
  EX/P4-40 - D. Smith, “Identification of Characteristic ELM Evolution Patterns with Alfvén-Scale Measurements and Unsupervised Machine Learning Analysis”
  EX/P4-41 - E. Fredrickson, “Parametric Dependence of EPMs in NSTX”
  EX/P4-42 - R. Perkins, “….A Proposed Mechanism for the Anomalous Loss of RF Power to the SOL of NSTX”
  EX/P4-43 - M. D. Boyer, “Feedback Control Design for Noninductively Sustained Scenarios in NSTX-U Using TRANSP”
  TH/P4-16 - G. Fu, “Hybrid Simulations of Beam-Driven Fishbone and TAEs in NSTX”
  TH/P4-17 - E. Belova, “Coupling of Neutral-Beam-Driven Compressional Alfvén Eigenmodes to Kinetic Alfvén Waves in NSTX and Energy Channelling”
Thursday, October 20
  EX/5-3 - A. Diallo, “Energy Exchange Dynamics across L-H Transitions in NSTX”
  MPT/P5-30 - M. A. Jaworski, “High-Temperature, Liquid Metal Plasma-Facing Component Research and Development for the NSTX-U”
  EX/P6-46 - C. Myers, “A Multimachine Analysis of Non-axisymmetric and Rotating Halo Currents”
  TH/P6-12 - J. Lore, “Pedestal-to-Wall 3D Fluid Transport Simulations on DIII-D and NSTX”
Friday, October 21
  FIP/P7-1 - T. Brown, “Development of a 3 m HTS FNSF Device and the Qualifying Design and Engineering R&D Needed to Meet the Low AR Design Point”
  FIP/P7-36 - R. Lunsford, “ELM Pacing with High Frequency Multispecies Impurity Granule Injection in NSTX-U H-Mode Discharges”
  FIP/P7-42 - R. Raman, “NSTX-U Contributions to Disruption Mitigation Studies in Support of ITER”

## Slide 32: Backup

## Slide 33: PF1AU coil developed turn-to-turn short(s)
PF3U
PF2U
TF
OH
PF1AU
PF1BU
PF1CU

## Slide 34: Evolution of induced current in PF1AU
Coil carries current when open circuited (open circuited every shot before plasma is produced)
 turn-to-turn short
PF1AU first starts to conduct current at the end of the March / April run period
Very fast degradation on the final run day in June
May
June
PF1AL shows no anomalies, but will pre-emptively be replaced

## Slide 35: NSTX-U plans for initiating conversion to high-Z PFCs and studying flowing liquid metal PFCs
Base high-Z tiles without Li reservoir will be tested first
  Full toroidal row on OB divertor
  Utilizes wire-EDM fabrication to obtain complex geometry
2. Later test pre-filled Li tiles:
  Similar to capillary porous system (CPS) but applicable as divertor PFC
  Passive surface replenishment
  Bakeout  erodible high-Z layer/film
  Test when technically ready