## Slide 1: Non-inductive plasma start-up experiments on the TST-2 spherical tokamak
R0
a
R0 = 0.36 m
a = 0.23 m
A = R0/a > 1.5
Bt = 0.3 T
Ip = 0.1 MA
Y. Takase for the TST-2 Group
Graduate School of Frontier Sciences
The University of Tokyo
18th International Spherical Torus Workshop (ISTW 2015)
and 2015 US-Japan Workshop on ST Plasmas
Princeton University, Princeton, NJ, USA
3-6 November 2015

## Slide 2: Outline
Motivation / Objective
4-WG array (grill) antenna experiments
  n|| dependence, polarization / wavenumber measurements
Capacitively-coupled combline (CCC) antenna experiments
  improved n|| spectrum
  comparison of current drive with other antennas
  characterization of LH driven plasma
    HX, SX, TS, ion Doppler, impurity
    equilibrium
    density limit
Planned improvements
  top-launch CCC antenna
  TF power supply upgrade
Diagnostic developments
  Multi-pass TS, local j, microwave scattering

## Slide 3: Outline
Motivation / Objective
4-WG array (grill) antenna experiments
  n|| dependence, polarization / wavenumber measurements
Capacitively-coupled combline (CCC) antenna experiments
  improved n|| spectrum
  comparison of current drive with other antennas
  characterization of LH driven plasma
    HX, SX, TS, ion Doppler, impurity
    equilibrium
    density limit
Planned improvements
  top-launch CCC antenna
  TF power supply upgrade
Diagnostic developments
  Multi-pass TS, local j, microwave scattering

## Slide 4: Motivation and Goal of Research
Economically competitive tokamak reactor may be realized at low aspect ratio (A = R0/a) by eliminating the central solenoid (CS)
S. Nishio, et al., in Proc. 20th IAEA Fusion Energy Conf., FT/P7-35 (Vilamoura , 2004).
higher Bt
lower A  higher bt
no CS
CS

## Slide 5
2002.06.21
Start-up and initial ramp-up
Noninductive
ramp-up (LH)
Transition to
self-driven phase
advanced tokamak
S. Shiraiwa, et al., Phys. Rev. Lett. 92 (2004) 035001.
Formation of Advanced Tokamak Plasma without CS was Achieved on JT-60U
Is plasma current (Ip) ramp-up by LHW possible in ST?
 Demonstrate on TST-2
Y. Takase, IAEA FEC 2002

## Slide 6
Three Antennas used on TST-2
Inductively-Coupled Combline (ICC) Antenna
excites traveling FW
Ip driven by SW (LHW)
requires mode conversion
from FW to SW
traveling wave
traveling
wave
traveling wave
excites traveling SW
sharper n|| spectrum
& higher directivity
Grill Antenna
(CCC) Antenna
excites traveling SW
n|| = ck||/w can be varied
Developed in collaboration with
C. P. Moeller (General Atomics, US)
Capacitively-Coupled Combline

## Slide 7: Outline
Motivation / Objective
4-WG array (grill) antenna experiments
  n|| dependence, polarization / wavenumber measurements
Capacitively-coupled combline (CCC) antenna experiments
  improved n|| spectrum
  comparison of current drive with other antennas
  characterization of LH driven plasma
    HX, SX, TS, ion Doppler, impurity
    equilibrium
    density limit
Planned improvements
  top-launch CCC antenna
  TF power supply upgrade
Diagnostic developments
  Multi-pass TS, local j, microwave scattering

## Slide 8: Grill Antenna
A Ni-plated Alumina block was used as a dielectric-loaded waveguide
LHW is excited directly by RF electric field in the toroidal direction
n|| = ck||/w of the excited LHW can be varied by adjusting the phase difference between adjacent waveguides
Bt
Movable private limiter
Grill Antenna
Alumina
340 mm
220 mm
T. Wakatsuki
Notes: グリルアンテナは私が設計したアンテナで、200MHzの導波管サイズを小さくするために、誘電体を用いた導波管を用いました。1mを超える巨大なアルミナのブロックに隙間なく金属板をろう付けすることは難しく、アルミナの表面にNiメッキを施したものを導波管として運用することでこの問題を克服しました。
このアンテナでは4本の導波管に入射するRFの位相差を独立に変更可能なので、励起するnparaを変化させることができます
また、このアンテナではコムラインアンテナと違い、トロイダル方向の電場によって、LHWを直接励起可能であるという利点があります。

## Slide 9: n|| Dependence of Ip and HX Spectrum (Grill Antenna)
Highest plasma current was obtained for
1.5 < n|| < 4.5
Count rate of high energy photons was lower when
n|| > 7.5
Chart: Ip
| 1.4691226482391251 | 2.9382452964782604 | 4.4073681831359908 | 5.8764905929565403 | 7.4925254821777294 | 9.5492973327636701
 | 9.3991 | 9.7292 | 9.615 | 8.7592 | 7.1993 | 6.467
[kA]
n||
T. Wakatsuki
n||
fixed PRF

## Slide 10
HX spectra were compared with Ip held constant （but with different RF powers）.
HX flux decreased for n|| > 6 even with constant Ip.
→ 1.5 ≦ n|| ≦ 6 are suitable for generating energetic electrons
HX flux is larger in the co-direction at any n||
→ asymmetric velocity distribution is formed
n¦¦ |  | 3.3 | 5.9 | 7.7
Teff_co [keV] |  | 58±3 | 56±3 | 40±7
T. Wakatsuki
n|| Dependence of Ip and HX Spectrum (Grill Antenna)
fixed Ip
Notes: そこで今度はIpを同じレベルにして、ただしその代わりにnparaが大きいときにはより多いパワーを入射することで、おなじIpでのHXスペクトルを比較した。
すると、やはりこの時でもnparaが６より大きいときにHX放射が減少することから、1.5から6が高速電子の駆動に適していることが分かりました。
この時のHXの放射温度は3.3,5.9のとき、コムラインアンテナの結果と同程度になります。
また、この場合にもやはりCo方向の温度がCtr方向に比べて高くなり、非対称な速度分布が形成されていることが分かりました。

## Slide 11: RF Magnetic Probe Array for k Measurement (Grill Antenna, ~ 1kA)
Array can be rotated about its axis
  to distinguish RF polarization
  to measure wavevector components
Dominant k components excited by the antenna are kt  50 m-1, kp  10 m-1.
  Measured kt ≲ 10 m-1 is much smaller (higher kt absorbed?)
( = 0°)
( = 90°)
radial
translation
a
b
c
d
e
rotation
30 mm
 | (SW) | (FW)
¦kt¦  ¦k¦¦¦ | < 10 m-1 | ~ 10 m-1
¦kp¦ | < 10 m-1 | < 5 m-1
¦kR¦ | ~ 35 m-1 | ~ 10 m-1
¦k¦ | ~ 35 m-1 | ~ 10 m-1
¦kt¦  ¦k¦¦¦ | < 10 m-1 | ~ 10 m-1
¦kp¦ | < 10 m-1 | < 5 m-1
¦kR¦ | ~ 35 m-1 | ~ 10 m-1
¦k¦ | ~ 35 m-1 | ~ 10 m-1
k|| = 10 m-1 corresponds to n|| = 2.4
T. Shinya

## Slide 12: Outline
Motivation / Objective
4-WG array (grill) antenna experiments
  n|| dependence, polarization / wavenumber measurements
Capacitively-coupled combline (CCC) antenna experiments
  improved n|| spectrum
  comparison of current drive with other antennas
  characterization of LH driven plasma
    HX, SX, TS, ion Doppler, impurity
    equilibrium
    density limit
Planned improvements
  top-launch CCC antenna
  TF power supply upgrade
Diagnostic developments
  Multi-pass TS, local j, microwave scattering

## Slide 13
Power and phase are monitored at 7 out of 13 elements
coil diameter: 8 mm
monitored elements:
1, 2, 4, 6, 9, 11, 13
T. Shinya
traveling wave
sharper k spectrum
higher wave directivity
Capacitively-Coupled Combline
(CCC) Antenna
LH Traveling Wave Antenna Based on a New Concept

## Slide 14
Radiating element
  house shaped cross section
  chosen to reduce the stationary spatial harmonic field
Inductive rods + rod supports
  covered by shields to reduce inductive coupling and excitation of the fast wave
Antenna consists of 13 elements
Exhibits a band-pass filter characteristic
feeder at 50W input impedance
L1U
L1L
C1
Input feeder
LL
L2U
L2L
C2
C1,2
・
・・
L13U
L13L
C13
C12,13
Output feeder
LＲ
#1
#2
#13
280 mm
CCC Antenna Element
C. Moeller

## Slide 15
Without Plasma
transmission
reflection
transmission
reflection
measured
calculated
{
{
reflection
transmission
200 MHz
Measured and Calculated Pass-Band Characteristics
C. Moeller / T. Inada
(COMSOL)

## Slide 16
k [m-1]
|Ek|2
・ Wavenumber spectrum deteriorates in the presence of plasma (depends on antenna-plasma distance)
z
x
Ez (red: positive, blue: negative)
vacuum
vacuum
plasma
plasma
vacuum
Antenna midplane cross section
Wavenumber spectra
Fourier transform of Ez(z) 5mm in front of antenna
Numerical Simulation of LHW by COMSOL
(CCC Antenna)
T. Inada
Vacuum
Plasma
Plasma (with 20mm vacuum gap)
16
Notes: 次に、真空及びプラズマ中への入射のシミュレーションを行いました。
プラズマについては一様の磁場、密度を仮定し冷たいプラズマの比誘電率テンソルを適用しました。
左上段は真空入射時のトロイダル方向の電場Ezの分布を示しています。
エレメントあたりの位相差も約60度と実際のアンテナと一致しています。
左中段は冷たいプラズマ中への入射、左下段は中段の状態からさらにプラズマをアンテナから20mm離してシミュレーションを行いました。
プラズマ境界をアンテナから離したほうがよりプラズマ中にLHWが伝播していることがわかります。
右図はそれぞれの場合でアンテナ前面から5.5mmの位置でのEzをフーリエ変換した波数スペクトルです。
赤、青、緑はそれぞれ真空、プラズマ、プラズマを20mm離した時のスペクトルです。
プラズマの存在下で波数スペクトルが劣化し、その劣化の度合はアンテナとプラズマとの距離に依存していることがわかりました。
(次スライドへ)%%%%%%%%%%%%%%%%%%%%%%%%%%%%%

## Slide 17
Typical Ip Ramp-up with LHW+ECH
(CCC Antenna)
T. Shinya

## Slide 18: Improvement of Excited N|| Spectrum (CCC Antenna)
Excited N|| spectrum was calculated from RF powers and phases measured by magnetic probes installed on the antenna.*
Excited N|| spectrum was sharpened while maintaining 100% radiation efficiency by adjusting the limiter position.
improved N|| spectrum
improvement
measured data (R585, -)
*T. Shinya et al., Nucl. Fusion 55, 073003(2015).
antenna
limiter,
antenna
at R = 621mm
main
limiter

## Slide 19: Improved N|| Spectrum is Excited by the CCC Antenna
The CCC antenna excites a sharp, highly uni-directional N|| spectrum compared to the 4-waveguide grill antenna.

## Slide 20
R = 585 mm
R = 550 mm
R = 550 mm
(limiter moved in z
direction by 75 mm)
(present limiter position)
Further Improvement Expected
by Avoiding Reflection from the Limiter
LHW
reflected LHW
75 mm
20
T. Inada
Notes: 次に、励起されるLHWについてトロイダル方向の電場Ezの分布を比較します。
上段は現在のリミター端の位置R-585mmであり、中段が今回最適化されたリミター位置であるR-550mmの場合です。
現在のリミター位置ではパワーが減衰しきって数エレメント程度からしか波を励起できておらずさらにリミターでの反射も発生しているのに対し、R=550mmでは最後のエレメントまで波を励起できている様子がわかります。
また、波数スペクトルをみるかぎりR-550mmのとき反射波は1/10以下で無視できる程度ですが仮にこの微小な反射波も抑えたいならばリミターをz方向に7.5cm程度移動させればよいことがわかりました。

## Slide 21: Scaling of Ip with Bv and Bt
Ip increases with Bv (equilibrium).
Upper bound of Ip increases with Bt (wave accessibility).
T. Shinya
Chart: Bt [T]
Grilll | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675 | 6.039 | 6.2314 | 5.8925 | 4.0927 | 5.8284 | 6.5616 | 7.7673 | 5.8093 | 5.4289 | 7.7091 | 7.3723 | 7.4418 | 5.9016 | 8.0659 | 10.0928 | 10.012 | 8.8372 | 8.5802 | 8.8795 | 4.5828 | 3.4313 | 2.7774 | 2.2411 | 4.0252 | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675
Chart: Bt [T]
Grilll | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675 | 6.039 | 6.2314 | 5.8925 | 4.0927 | 5.8284 | 6.5616 | 7.7673 | 5.8093 | 5.4289 | 7.7091 | 7.3723 | 7.4418 | 5.9016 | 8.0659 | 10.0928 | 10.012 | 8.8372 | 8.5802 | 8.8795 | 4.5828 | 3.4313 | 2.7774 | 2.2411 | 4.0252 | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675
Chart: Bv [mT]
Grill | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675 | 6.039 | 6.2314 | 5.8925 | 4.0927 | 5.8284 | 6.5616 | 7.7673 | 5.8093 | 5.4289 | 7.7091 | 7.3723 | 7.4418 | 5.9016 | 8.0659 | 10.0928 | 10.012 | 8.8372 | 8.5802 | 8.8795 | 4.5828 | 3.4313 | 2.7774 | 2.2411 | 4.0252 | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675
Chart: Bv [mT]
Grill | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675 | 6.039 | 6.2314 | 5.8925 | 4.0927 | 5.8284 | 6.5616 | 7.7673 | 5.8093 | 5.4289 | 7.7091 | 7.3723 | 7.4418 | 5.9016 | 8.0659 | 10.0928 | 10.012 | 8.8372 | 8.5802 | 8.8795 | 4.5828 | 3.4313 | 2.7774 | 2.2411 | 4.0252 | 5.639 | 5.6049 | 5.4537 | 5.7196 | 6.092 | 5.9985 | 4.731 | 4.8335 | 4.3066 | 4.5053 | 4.1346 | 4.7471 | 5.1435 | 4.7675
co-drive
counter-drive
CCC
ICC
Grill
CCC
ICC
Grill

## Slide 22
Comparison with Grill and ICC antennas
_
Highest hCD is obtained with the CCC antenna.
An order of magnitude improvement in hCD may be possible by suppression of edge wave power loss and fast electron loss
 operation at higher Bt, ne, Ip , PRF, Te
T. Shinya

## Slide 23
Grill Antenna
CCC Antenna
Plasma current
Line integrated electron density
LH power
■: Co
■: Ctr
■: Co
■: Ctr
Co/Ctr X-ray Spectra for Grill/CCC Antenna
vacuum vessel
NaI + collimator
K. Imamura
Co/Ctr asymmetry is more pronounced for the CCC antenna.
Notes: まずグリルアンテナとCCCアンテナでの電流駆動、反電流駆動の測定を行いました。
左上の図は測定の概念図で、2方向同時測定型硬X線測定装置で、プラズマ中心を測定しています。
右上が測定した際の典型的な放電波形です。
上からプラズマ電流、線積分電子密度、LHWパワーを表します。
下の図はそれぞれグリルアンテナとCCCアンテナの放射のエネルギースペクトルです。
黒色が電流駆動方向、赤色が反電流駆動方向を表しています。
グリルアンテナでは、Co方向とCtr方向で、2倍程度の差で、CCCアンテナでは10倍以上の放射量の差があります。
これはグリルアンテナではアンテナの特性上反電流駆動方向に進む波が存在するため、反電流駆動方向にも高速電子が存在することを示しており、
CCCアンテナでは反電流駆動方向の高速電子はほぼ存在せずに、相対論的効果によって放射される電流駆動方向に動いている電子が出す硬X線を測定していると考えられます。
よって、CCCアンテナの方が電流駆動効率は良いと考えられます。

## Slide 24
Higher energy
X-ray profile is
peaked on the
outboard side.
Yueng-Kay Martin PENG, et al., Plasma and Fusion Research 9 3403146 (2014)
◇:20～30 ms
◇:30～40 ms
◇:40～50 ms
◇:50～60 ms
◇:60～70 ms
◇:70～80 ms
Spatial X-ray Profiles (CCC Antenna)
Example of
two-fluid equilibrium
K. Imamura
Notes: 25点の硬X線の分布計測のアーベル変換後の結果を左側に示します。
右側に示したTST-2プラズマの平衡計算の電流密度と電子とイオンの流速と熱速度の比の結果を示します。
まずエネルギー範囲を変えて測定を行っていますが、時間発展によって放射量は増加しますが、放射の分布に変化はありません。
そして50～100keVの結果で、520 mm付近に放射が多くそこからプラズマの内側に行くに従って、滑らかに低下しています。
次に50～200keVで解析した結果を見ると径方向外側の放射が更に大きくなっています。
前スライドで話した分解能の悪化による放射量の増加も多少あるかもしれませんが、一番外側や内側の部分の放射が少ないことから
この520mm付近の上昇に対する寄与は大きくないと考えられます。
ここで右側に示したTST-2プラズマの平衡計算の結果と比較してみると、
平衡計算では電流密度のピークは450 mm付近にあり、電子の流速と熱速度の比は550mm付近にあります。
この結果は電流駆動を担う電子の中でも高速な成分は径方向の外側に存在するということを示します。
ここで実際の測定結果と比較をしてみると、高いエネルギー範囲での測定結果は径方向外側の放射が顕著に大きい
というのはつまり電流駆動を担う電子の中でも高いエネルギーを持つものは外側に多く存在することを示唆していると考えられ、
平衡計算の結果と一致します。
よってこの硬X線の計測によって電流を担っている高速電子の計測が出来たと考えられます。

## Slide 25
Energy Flux []
R [mm]
◇:0.0838 T
◇:0.0747 T
◇:0.0667 T
◇:0.0547T
Fast electron population and Ip increase at high Bt.
Radial profile shows stronger radiation from the plasma core at higher Bt.
LHW propagates to the core and accelerate electrons.
magnetic axis
Toroidal Field Dependence of X-ray Profile (CCC Antenna)
Wave propagation improves at high Bt.
Bt [T]
Bt [T]
Bt [T]
Bt [T]
(a) X-ray flux
(40-50 ms)
(b) Ip (40-50 ms)
(c) max Ip
(d) X-ray flux
at max Ip
K. Imamura
Notes: 次にトロイダル磁場を変化させた時の測定結果を示します。
左下がトロイダル磁場を変化させた時の25点径方向分布です。
右上に40～50 msの硬X線放射量、プラズマ電流、
最大プラズマ電流、その時の硬X線の放射量のグラフを示します。
この測定結果から次の２点が分かります。
トロイダル磁場が大きいほど硬X線の放射量は増加する。
最大プラズマ電流もトロイダル磁場が大きいほど大きくなる。
よってトロイダル磁場の増加により波の伝搬が良くなり高速電子が増加し、その高速電子によって最大のプラズマ電流も増加すると考えられます。
更に特にプラズマ中心で顕著に放射量が増加しているのは、中心までLHWが伝播しプラズマ中心付近で高速電子を生成するというLHWの
近接性の向上が観測されたと考えられます。

## Slide 26
Modulation Experiment Shows
Evolution of Absorption Profile
no modulation
modulation
@ R = 0.39 m (l = 0.6 m)
2. t = 58-67ms
1. t = 49-58ms
3. t = 67-76ms
4. t = 76-86ms
t [ms]
1
2
3
4
S. Yajima
core absorption
edge absorption
modulation amplitude profile of visible to SX emission

## Slide 27
Measurement result (near the plasma center)
Measurement of Te Anisotropy in LH Start-up Plasma
H. Togashi
Te in the direction of Δk (= ks - ki) is measured by TS.
Δk for forward and backward paths are nearly perpendicular and parallel to the magnetic field B, respectively
B
forward
path
backward
path
ki
ki
Δk
Δk
ks
Collection
optics
TST-2 TS system
Maxwellian fits
Significant anisotropy was not found
Te
Te||
ne = 3 x 1017 m-3
PRF = 70 kW
Bt = 0.1 T
Ip = 15 kA
_

## Slide 28
H. Togashi
Te and ne Profiles Measured by TS
Profiles measured by Thomson scattering (TS) in TST-2 discharges with Ip = 5 kA maintained by LHW alone.
Bulk Te in the plasma core is low (hollow Te profile). Bulk electron heating by the LHW is limited.
pe(TS) << pMHD  pressure dominated by energetic electrons.
limiter
LCFS
measurement limit
limiter
LCFS
Ip = 5 kA

## Slide 29
Measurements of Ti and Flow in RF Driven Plasmas in TST-2 and LATE
S. Tsuda, et al., Plasma Fusion Res. 10, 1202064 (2015).
Typical errors of Ti and flow are DTi ~2 eV and DV <1 km/s.
Collimator lens and fiber bundle
Rotatable fiber holder with multiple holes
Impurity (C2+) Ti and flow velocity were measured in TST-2 and LATE plasmas with similar plasma currents (~ 9 kA), but sustained by different waves (LHW, ECW).
Lines of sight in TST-2 (a) and LATE (b)
Wavelength spectra for two symmetric sightlines at Rtan = 310 mm in LATE

## Slide 30
PLHW ~ 20 kW
ne ~ 1 x 1017 m−3, Ti ~ 3–5 eV
Vf ~ 1 ± 0.5 km/s (Co Ip), Vq ~ ±0.5 km/s
PECW ~ 50 kW
ne ~ 1 .4 x 1017 m−3, Ti ~ 10 eV.
Vf ~ 4 ± 0.5 km/s (Co Ip), Vq ~ 5±1 km/s (Diam.)
Er ~ +290 ± 60 V/m
TST-2
LATE

## Slide 31: Spectroscopic Identification of Cu Impurity Source
CuI emission is stronger on the side viewing in front of the CCC antenna.
 Antenna is the source of Cu impurity
Profile of CuI emission
CuI emission intensity increases as the plasma approaches the antenna, and increases with RF power.
consistent with Cu impurity generation by RF sheath sputtering
The observed amount of Cu does not affect the current drive efficiency.

## Slide 32
LH Start-up Discharge
EFIT reconstruction

## Slide 33
3-Fluid Axisymmetric Equilibrium Model Applied to TST-2 LHW Sustained Plasma
A. Ishida, et al., Plasma Fusion Res. 10 (2015) (in press).
A three fluid (i, high energy e, low energy e) equilibrium reconstruction method was developed, and applied to a TST-2 LHW sustained plasma
(Ip ~ 9 kA, Te0 ~ 10 eV, Ti ~ 5 eV, ne0 ~ 4x1017m-3,
Vf ~ 0.5 km/s).
Flux function and
Flux + toroidal flow effect
for high energy electron fluid
Chart: 
Chart: 
Chart: 
0.1
0.2
0.3
0.4
0.5
0.6
0.7
R [m]
Force [Nm-3]
Force [Nm-3]
Force [Nm-3]
4
0
-4
20
0
-20
100
0
-100
Radial force balance
ions
high energy electrons
low energy electrons
ions:
high energy electrons:
low energy electrons:
ni
nel
neh
Ti [eV]
Tel [eV]
Teh[keV]
f [V]
[1018m-3]
[eV], [keV], [V]

## Slide 34
GENRAY/CQL3D Calculation
Bt = 0.1 T; Ip = 12 kA; fRF = 200 MHz; PRF = 25 kW; Te0 = 0.1 keV
ne0 = 0.3  1018 m-3
ne0 = 1  1018 m-3
ne0 = 2  1018 m-3
PCQL = 22 kW
ICD = 67 kA
PCQL = 24 kW
ICD = 98 kA
PCQL = 0.5 kW
ICD = 0.5 kA
Y. Takase / J. Wright
f (v||, v)
j (r)

## Slide 35: Is Density Limit Due to Accessibility?
Chart: Ave. ne [1018 m-3]
| 6.7041745E-2 | 0.13408349 | 0.20112524000000001 | 0.26816698 | 0.43577131000000002 | 0.53633396 | 0.67041742000000004 | 0.83802178999999999
Midplane | 42 | 87.8 | 184.9 | 200.5 | 187.9 | 150 | 96.7 | 53
GENRAY + CQL3D
Chart: Ave. ne [1018 m-3]
Experiment
Ave. ne = nel (R = 390 mm) / 0.5
2
4
5
7
Na=6
8
Ray-tracing (GENRAY)
Density scan:
Na = 2, 4, 5, 6, 7, 8
Ave. ne = 0.034, 0.24, 0.38, 0.56, 0.77, 1.0
x 1018 m-3
Abrupt limit
Gradual degradation
  ,
  ,
Fixed: Bt = 0.08 [T], N|| = 5.5, shot=111821
Accessibility: N|| > Na
T. Shinya

## Slide 36
Pump (199.9-200.1 MHz)
LFS (180-199.9 MHz)
UFS (200.1-220 MHz)
112299
LH resonance frequency
for TST-2 RF plasma
toroidal
poloidal
2-channel RF mag. probe
(R, z) = (580 mm, 250 mm)
Is Density Limit Due to Parametric Decay?
density limit
T. Shinya

## Slide 37: Outline
Motivation / Objective
4-WG array (grill) antenna experiments
  n|| dependence, polarization / wavenumber measurements
Capacitively-coupled combline (CCC) antenna experiments
  improved n|| spectrum
  comparison of current drive with other antennas
  characterization of LH driven plasma
    HX, SX, TS, ion Doppler, impurity
    equilibrium
    density limit
Planned improvements
  top-launch CCC antenna
  TF power supply upgrade
Diagnostic developments
  Multi-pass TS, local j, microwave scattering

## Slide 38: Calculated Wave Field and Driven Current Profiles
Bt must be higher to ensure LHW accessibility to the plasma core.
n|| = ck||/w must be lower to avoid edge absorption of LHW.
n|| = 8.9
n|| = 5.9
ne =1018 m-3
Bt =0.3 T
Te = 200 eV
PRF = 100 kW
-300 kA total
Edge current
center
edge
-300 kA total
Core current
center
edge
full wave code
Fokker-Planck code
iteration
collaboration with
Bonoli, Wright (MIT, US)
T. Wakatsuki

## Slide 39: Orbit Loss is Important at Low Ip
CQL3D Fokker-Planck code calculation shows that the orbit loss is the dominant loss for ρ  0.2 at Ip = 10kA.
Orbit loss from the core is greatly reduced at Ip = 50kA.
This will require TF power supply upgrade (maintain Bt = 0.3T for
> 100ms) and density control (keep density low during Ip ramp-up).
T. Wakatsuki
Notes: SXモジュレーションの位相から推定される速いロスは、本当に軌道損失であるかどうかを考察します。
Fokker-Planckコードで軌道損失の大きさを計算すると、10kAのプラズマ電流では、規格化した小半径で0.2以上という広い範囲で軌道損失が支配的になっていることが分かり、速いロスは軌道損失であることを強く示唆しています。
このロスはプラズマ電流が50kAまで増えればかなり小さくできることもわかります。

## Slide 40: TF Power Supply Upgrade
In order to demonstrate ramp-up to higher Ip, power supply upgrade is needed to sustain higher Bt (~ 0.3 T) for longer duration (> 0.1 s).
Ip
Bt
?

## Slide 41
Top-launch CCC antenna is being developed jointly with GA
Accessible to the plasma core even at high density
1
Reduction of losses in the SOL (outside LCFS)
3
Absorption (Landau damping) in the plasma core
2
3 advantages of top-launch based on GENRAY analyses
top-launch
midplane-launch
good
LCFS
low density
high density
bad
top-launch CCC antenna
Top-launch CCC Antenna
good
bad

## Slide 42: Outline
Motivation / Objective
4-WG array (grill) antenna experiments
  n|| dependence, polarization / wavenumber measurements
Capacitively-coupled combline (CCC) antenna experiments
  improved n|| spectrum
  comparison of current drive with other antennas
  characterization of LH driven plasma
    HX, SX, TS, ion Doppler, impurity
    equilibrium
    density limit
Planned improvements
  top-launch CCC antenna
  TF power supply upgrade
Diagnostic developments
  multi-pass TS, local j, microwave scattering

## Slide 43
A laser pulse is confined between two mirrors and passes through the plasma many times
・・・
ON
OFF
OFF
1st pass
2nd pass
3rd pass
4th pass
#1
#2
#1
Laser
Polarization
beam splitter
Pockels cell
Mirror #2
Mirror #1
ON OFF
Plasma
OFF
PBS
PC
Accumulate these TS signals
Multi-Pass TS is Being Developed
Plasma
H. Togashi

## Slide 44
Ip
Bt
Bp
Br
Langmuir probes
Rogowski probe consists of two multi-layer Rogowski coils, five pick-up coils and two Langumuir probes.
Local current was measured successfully.
open hole
closed hole
H. Furui, et al., Rev. Sci. Instrum. 85, (2014) 11D813
Local Current Measurement by Rogowski Probe

## Slide 45
Ip spike due to IRE (internal reconnection event)
plasma current
1. Fluctuations of j, Iis, dB/dt start at -0.2 ms.
2. j and Iis at the plasma edge start to increase at -0.2 ms
3. After 2, high frequency components of j and Iis can be seen.
4. Ip shows a positive spike with the decrease of j and Iis.
Measurement of Current Filament at IRE
power spectra of
@ v.v. wall
local current
ion saturation current

## Slide 46
12-40 GHz covered with Ku, K and Ka band
N. Tsujii
Microwave Scattering Diagnostic is
Being Prepared to Measure LH Waves

## Slide 47
Density fluctuation increases as the wave propagates inwards
Typical density fluctuation 2x1016 m-3 at 20 kW
Scattered amplitude ~3%
  Detectable with proper focusing
Electron density fluctuation simulated by AORSA (Maxwellian at 500 eV, 1W)
N. Tsujii
Scattered Amplitude is Appreciable
at Typical RF Power on TST-2

## Slide 48: Conclusions
ST plasma initiation and Ip ramp-up by waves in the LH frequency range were demonstrated on TST-2.
  Inductively-coupled combline antenna (FW launch), dielectric-loaded waveguide array (“grill”) antenna (LHW launch), and capacitively-coupled combline antenna (LHW launch) were used.
    Similar Ip was obtained with different antennas for similar Bv and PRF, but hCD is higher with the CCC antenna (improved n|| spectrum).
  Grill antenna (variable n||)
    Current drive maximizes for n|| = 2~4
    Wavenumber/polarization measured by a magnetic probe array
  CCC antenna (fixed n||)
    Ip initiated and ramped up to 25 kA
    HX/SX indicate deterioration of accessibility at low Bt and high ne
  Characteristics of LH driven plasmas
    pe dominated by energetic electrons
    ion flow is in the co- Ip direction
    3-fluid equilibrium model was developed
    density limit (a little lower than accessibility limit?)
    orbit loss of high energy electrons is important at low Ip

## Slide 49: Near-Future Plans
Coil Power Supply Upgrade
  Sustained high field (Bt = 0.3 T for > 0.1 s) for further Ip ramp-up.
Antenna Upgrade
  Top-launch CCC antenna.
Wave/Turbulence Diagnostics
  Electrostatic probe array
  Microwave scatteriing
Plasma diagnostics
  Multi-pass Thomson scattering
  Current profile measurement by Rogowski probe / magnetic probe
  Ion flow measurement
  EBW emission