## Slide 1: Overview of NSTX Upgrade Initial Results and Modelling Highlights
J.E. Menard (PPPL)
for the NSTX-U Research Team
International Spherical Torus Workshop - 2017
Seoul National University, Seoul, South Korea
September 19-22, 2017

## Slide 2: Outline
NSTX-U mission
Research highlights
Progress on next-step ST concepts
Summary

## Slide 3: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Li
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 4: NSTX-U will access new physics with 2 major new tools:
Higher T, low n* from low to high 
 Unique regime, study new transport and stability physics
Full non-inductive current drive
 Not demonstrated in ST at high-T
Essential for any future steady-state ST
2. Tangential 2nd Neutral Beam
1. New Central Magnet

## Slide 5: NSTX-U will have major boost in performance
2× toroidal field (0.5  1T)
2× plasma current (1  2MA)
5× longer pulse (1  5s)
2× heating power (5  10MW)
Tangential NBI  2× current drive efficiency
4× divertor heat flux ( ITER levels)
Up to 10× higher nTE (~MJ plasmas)
2. Tangential 2nd Neutral Beam
1. New Central Magnet
Performance goals:

## Slide 6: NSTX-U had scientifically productive 1st year
Achieved H-mode on 8th day of 10 weeks of operation
Surpassed magnetic field and pulse-duration of NSTX
Matched best NSTX H-mode performance at ~1MA
Identified and corrected dominant error fields
Commissioned all magnetic and kinetic profile diagnostics
New 2nd NBI suppresses Global Alfven Eigenmodes (GAE)
Implemented techniques for controlled plasma shut down, disruption detection, commissioned new tools for mitigation
2016 run ended prematurely due to fault in divertor PF coil
  Coil + other issues  major reviews of design, fab, procedures

## Slide 7: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 8: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 9: NSTX-U has surpassed maximum pulse duration and magnetic field of NSTX
Compare similar NSTX / NSTX-U Boronized L-modes, PNBI=1MW
NSTX-U L-mode duration
exceeds longest NSTX H-mode
4x longer
NSTX-U BT > highest NSTX BT

## Slide 10: Examples of highest-performance L and H-modes achieved thus far in NSTX-U
(motivates future cryo-pump)

## Slide 11: Shutdown handler used for well-controlled disruption-free L-mode ramp-down
Three morning fiducials
One operator waveform used to start ramp-down at t=1.5s
Ramp-down is inner-wall limited, power and current slowly ramped off
204179
204163
204155
I [MA]
P
Pinj [MW]
WMHD [kJ]
ne [1013 cm-3]

L-mode Rampdowns Triggered By a Single Switch
Beam power ramped down
See D. Mueller presentation for more details

## Slide 12: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 13: n=1 error field correction (EFC) optimized to maximize pulse length, discharge performance
L-modes used to identify optimal correction amplitude, phase
Multiple compass scans confirm optimal L-mode EFC in flattop
EFC current [kA]
EFC current [kA]
ne = 2.9 ×1013 (solid)
ne = 1.4 ×1013 (dashed)

## Slide 14: Coil metrology conducted on TF rod, center-stack casing (CSC), and PF5 coil
Combine metrology techniques: ruler, ROMER arm, laser tracker
PF5 n = 1 amplitude and phase:
  δR ~ 6 mm at ϕ = 16°
TF rod shift and tilt:
  Shift = 4.9 mm at ϕ = 246°
  Tilt = 1.2 mrad at ϕ = 206° (6 mm)

## Slide 15: Modeling results  need to impose 2 mm tolerance for TF alignment to mitigate TF error field effects
Metrology  coil shape models
  Feed to IPEC & M3D-C1
Resonant fields and currents:
  TF error field is dominant
  TF EF phase not constant
  Difficult to correct
Neoclassical toroidal viscosity:
– RWM coils are poorly matched to TF NTV spectrum
Tolerance of 2 mm:
  Resonant fields below locking threshold without EFC
  Reduces TF NTV by 10×
Model H-mode
142301
See J.-K. Park presentation for more details

## Slide 16: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 17: H-mode confinement so far consistent with “ST” scaling

## Slide 18: Reduction in ce Going From L- to H-; RLW model consistent with Te
Caveat: Linear GYRO indicates
microtearing is NOT dominant
μ-instability

## Slide 19: NSTX-U: Bimodal turbulence seen in some L-modes using upgraded 48 channel Beam Emission Spectroscopy (BES) system
Modes propagate in opposite directions
  Similar spectra seen with DIII-D and TFTR BES
  Potential link to grad B direction?
  Gyro-kinetic modelling underway
13 km/s in electron
diamagnetic direction
11 km/s in ion
diamagnetic direction
ΔZ = 3 cm
R = 142 cm
Δt = 24 ms

## Slide 20: At ion scales (kqrs<1), linear GYRO* simulations predict unstable spectra of ITG and microtearing modes (MTM)
ITG unstable R>135 cm, propagates in ion direction
  Propagation direction consistent with BES ion mode (need to consider Doppler shift, although also in ion direction)
MTM also unstable R>127 cm, propagates in electron direction
  Surprised to find MTM unstable  sufficient beta (4.1%) and large collisionality enhances MTM
*GYRO (Candy, Waltz, 2003)
e-direction
i-direction
ITG
MTM

## Slide 21: Same NSTX-U L-modes: Nonlinear ETG simulations give significant transport (R=129-140 cm, r/a=0.47-0.67)
r  0.45 0.55 0.65 0.75
Qe,etg large enough to account for Qe,exp if Zeff=Zeff,c1.2
  Larger Zeff (VB Zeff2)  lower Qe,etg
New high-k microwave scattering diagnostic (for 20** run) will be ideal for probing region of ETG turbulence
May require multiscale simulations for validation
See W. Guttenfelder presentation for more details
Notes: Future new high-k scattering diagnostic will probe this
SOMETHING ABOUT MULTISCALE, HOWARD NF 2016, HOLLAND IAEA TH/6-1

## Slide 22: NSTX-U Mission Elements:
Topical science areas:
  Scenario Development
  Macroscopic Stability
  Transport and Turbulence
  Energetic Particles
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
ITER

## Slide 23: Explored fast-ion behavior with original and new NBI via beam blips with different NBI energies
Good agreement between neutron measurement and TRANSP prediction
~20% discrepancy between data and TRANSP predictions
Neutron rate
Exploring possible causes, including NBI source energy split
ENBI = 85keV
ENBI = 65keV

## Slide 24: Agreement improved for Einj = 65keV using small anomalous fast-ion diffusion
TRANSP decay time gets reasonable agreement with data when a small anomalous fast ion diffusivity (Daf=0.3m2/s) is used
 Beam ion behavior is still close to classical theory

## Slide 25: NSTX-U: Tangential 2nd neutral beam suppresses Global Alfven Eigenmode (GAE) – consistent with simulation
t ci
HYM code simulation of #204707, n=10
|dBn |2
No outboard NBI (t=0.44s)
With outboard NBI (t=0.47s)
Published in PRL in June 2017 - E. Fredrickson et al.
HYM code: growth of n=10 counter-GAE from 1st NBI
HYM: suppression of n=10 counter-GAE by 2nd NBI
Most unstable n-number, mode w consistent with HYM
See E. Belova presentation for more details

## Slide 26: Analytic theory providing insight into HYM simulations of GAE stability
Fast ions can be stabilizing/ destabilizing depending:
Stable : Unstable:
Resonant outboard beam ions with pitch > 0.9 have small , are stabilizing by this theory.
Estimates based on dispersion relation and resonant condition suggest that 65keV outboard beam ions might be just marginal to reach resonant condition.
NSTX (low field) parameter regime might be very different.
b) 0.47s
Energy (keV)
NSTX-U 204707A02
1.0
50
100
a) 0.44s
Resonant
Resonant
k⊥ρ>1.9
⊥
k ρ<1.9
k⊥ρ>1.9
⊥
k ρ<1.9
2
5
10
20
2
5
10
20
0
0.0 0.5 1.0 0.0 0.5
Pitch (V||/V)
(Gorelenkov, NF 2003)
0  k  1.9
1.9  k  4

## Slide 27: NSTX-U: Off-axis co-NBI destabilizes counter-propagating Toroidal Alfvén Eigenmodes (TAEs)
Hollow fast ion profile reduces stabilization of counter-propagating TAEs
H.V. Wong, H. Berk, Phys. Lett. A 251 (1999) 126.
Preliminary analysis reveals important role of large orbit width, FLR effects
TRANSP: as current builds up, fast-ion beta profile predicted to become hollow
  1st evidence of off-axis NBI in NSTX-U
Co-TAEs are stabilized, but cntr-TAEs become unstable with only 1MW NBI

## Slide 28: Linear TAE stability vs time from TRANSP + kick model is consistent with NSTX-U experiments
Compute power from fast ions to mode
  Infer growth rate
  Using damping rate from NOVA-K
Timing of most unstable |n|=1 TAE modes compares well with experiments
Stability related to gradients in both radius & energy
  Not the usual “universal drive”
[Podestà, PPCF 2017]
M. Podesta
Flexibility of TRANSP + kick model approach enables scenario development for realistic geometry
  Example: ~0.5MW “blips” with 1st NBI predicted to stabilize cntr-TAEs

## Slide 29: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
ST-FNSF /
Pilot-Plant
ITER
Liquid metals / Li
Snowflake/X

## Slide 30: Material Analysis & Particle Probe (MAPP) providing new measurements of surface evolution in NSTX-U
Tracked C/B/O evolution, correlated with plasma performance
Implemented remote-control + between-shot MAPP analysis
Future: Use with Li, understand complex Li chemistry/evolution

## Slide 31: Designed controlled experiment for NSTX-U to assess heat flux and detachment vs. flaring (UT Austin)
Can hold core fixed while varying divertor (CORSICA+SOLPS)
  IP = 1.1MA, BT = 0.74T, A~1.73, q95~6, k=2, dL = 0.47, PSOL = 2.9MW
X-divertor (2nd x-point under target plate) promotes detachment
  Gas-puff scan: 4, 6, 8, 10 ×1021 particles / second
Standard divertor
X-divertor

## Slide 32
XGC1 predicts SOL heat-flux width significantly larger than Eich-Goldston scaling for 2MA NSTX-U
An up-scaled NSTX-U plasma equilibrium from NSTX #139047 is used.
  Similar magnetic equilibrium shape, Bp=0.58 T, heat input = 7.8MW
  XGC1 finds that λqEich for lower divertor in NSTX-U is ≈ 3 mm  ~1.5-2x larger than the Eich-Goldston scaling prediction.
  Electron contribution (turbulence) becomes significantly higher than the ion contribution (neoclassical), potentially indicating enhanced role of turbulence
Physics bifurcation
2MA NSTX-U
See S. Ku presentation for more details

## Slide 33: NSTX-U Mission Elements:
Explore unique ST parameter regimes to advance predictive capability - for ITER and beyond
Develop solutions for plasma- material interface (PMI)
Advance ST as Fusion Nuclear Science Facility and Pilot Plant
Liquid metals / Lithium
Snowflake/X
ST-FNSF /
Pilot-Plant
ITER

## Slide 34: Recent design studies show ST potentially attractive as Fusion Nuclear Science Facility (FNSF) and Pilot Plant
FNSF with copper TF coils
A=1.7, R0 = 1.7m, x = 2.7, BT=3T
Fluence = 6MWy/m2, TBR ~ 1
FNSF / Pilot Plant with HTS TF coils
A=2, R0 = 3m, x = 2.5, BT = 4T
6MWy/m2, TBR ~ 1, Qeng ~ 1
FNSF: Provide neutron fluence for material/component R&D (+ T self-sufficiency?)
Pilot Plant: Electrical self-sufficiency: Qeng = Pelec / Pconsumed ≥ 1 (+ FNSF mission?)
Designs integrate ST higher k , bN and advanced divertors (+ HTS TF for Pilot Plant)
J.E. Menard, et al., Nucl. Fusion 56 (2016) 106023
See Menard presentation for more details

## Slide 35: Summary
Productive first (partial) year of NSTX-U operations
  Rapid H-mode access, control development, EF correction
  Surpassed NSTX maximum magnetic field and pulse-duration
  First glimmer of new data for H-mode confinement scaling
  New fast-ion physics: 2nd NBI – GAE stabilization, counter TAE
Run halted due to failed divertor PF coil + other issues
2017: Major reviews to identify issues, corrective actions
  12 Design Validation and Verification reviews of entire machine
  2 Extent of Condition reviews
  Conceptual Design Review (CDR) + cost and schedule review
Aim to resume plasma ops in late 2019 / early 2020
See M. Ono presentation for more details
See M. Reinke presentation for PFC details

## Slide 36: Thank you!
Any questions?

## Slide 37: Backup

## Slide 38: Enhanced collaborations during NSTX-U outage Targets NSTX-U research goals
DIII-D, HL-2A (China): Dedicated campaigns – several run weeks
MAST-U: Break-down/scenario modeling supporting first plasma
  D. Battaglia (on-site for several months this summer), D. Boyer
QUEST: Coaxial Helicity Injection (CHI) + ECH/EBW heating
  R. Raman (UW), M. Ono, G. Taylor, N. Bertelli
EAST: edge physics, plasma materials interactions (high-Z, Li)
  R. Maingi + collaborators leading expts
JET: EP studies, plasma ramp-down scenarios and modeling
  M. Podesta, F. Poli
KSTAR: Core MHD, rotation physics, plasma control
  Columbia Univ (Sabbagh, Berkery, Park et al.), J-K Park, J-W Ahn (ORNL)
W7-X: wall conditioning using boron powder dropper
  R. Lunsford
WEST: RF physics, high-Z PMI, real-time wall protection
  RF physicists, M. Reinke (ORNL)
LAPD: RF coupling and heating physics, cavity modes
  R. Perkins

## Slide 39: Region where problems have occurred
PF1A
PF1B
PF1C
Horizontal Inboard Divertor
Copper Tubes
OH Grounding

## Slide 40: Boroscopy and sectioning of failed PF1AU
Shorted Turns
Region of Shorted Turns
Large Void on This Turn
Section A-B, Layer 3, Row 9 Void Anomaly

## Slide 41: PF1AU insulation damaged between layers

## Slide 42: NSTX-U “Recovery” Project includes significant rebuild of components in ends of center-stack
PF1 coil improvements (6 new coils):
  No mandrels to improve turn-to-turn testing
  No joints, pure spiral windings for no joggles
  PF1B thermally isolated (attached at cold end)
Vacuum improvements
  All coils air-side (PF1C was in vacuum can)
  Single  pumped double O-rings
  Improved divertor cooling / heating tubes
  Lower ceramic break removed to reduce # of O-rings, reduce risk of fracture, lithium contact  NO Coaxial Helicity Injection
  Future: consider bias-plate and/or plasma guns
New divertor PFCs for higher heat flux handling
New castellated design to increase stress margins

## Slide 43: Investigating newly observed Ion Cyclotron Emission (ICE) from NSTX-U discharges
Spatially coherent  argues for mode
Bursty rather than CW  unstable mode - what defines mode f ?
Doesn’t follow Alfvénic scaling - not Alfvén eigenmode?
Like conventional ICE, higher harmonics largest amplitudes
Strongest ICE correlated with source 1C – the most perpendicular source
Amplitude decreases with increasing density
TRANSP runs started to study fast dependence
Can ICE be correlated with confined fast-ion distribution parameters?
Needs theory support
0.15
0.20
0.30
0.35
5.0
4.0
3.0
2.0
1.0
0.25
Time (s)
Frequency (MHz)
NSTX-U 204645
0.0
6
4
2
0
1
2
6
5
3
4
7

## Slide 44: Strong variation in turbulence, stability and EB shear over  30 rs  motivates the need for global simulations
Strong local EB shearing rates (gE > gITG, gMTM at R=135 cm)
  BES amplitudes increasing where gITG > gE
Significant variation over ~30 rs (r* = rs/a ~ 1/120, rs / LT ~ 1/35)
Motivates the need for global simulations
BES dI/I
(50-200 kHZ)
~30 rs

## Slide 45: Granule Injector Commissioned on NSTX-U
Granule sizes :
900mm, 700mm, 500mm, 300mm
Injection Species : Li, B4C, C
Injection Velocity : 50 – 150 m/sec
Granule to Granule Injection Frequency : 50 – 500 Hz
Particle drop rates are controlled by a piezoelectric disk.
Granules driven into the plasma by a pneumatic rotary impeller
NSTX-U Granule Injector

## Slide 46: Materials Analysis Particle Probe fully commissioned
Full remote operation (EPICS and LabView® Interface) now possible for in between plasma discharges measurements
XPS, ISS, DRS
measurements
Flush with LD tiles at bay J
(boronization, lithiumization, D+ plasma exposures)
Sequence of operation

## Slide 47: MAPP used to track effect of boronization on PFCs Supported PhD Thesis, will be vital to understanding Li surface chemistry
Boron oxidation due to plasma exposure measured with MAPP via X-ray Photoelectron Spectroscopy (XPS)
1. ATJ graphite
2. ATJ post boronization
3. ATJ post boronization post plasma exposure
Days after boronization
D+ fluence increasing
Low oxygen % High % of B in metallic state
High oxygen % Low % of B in metallic state
XPS data obtained at the end of each plasmas operations day

## Slide 48: Static EFC scan early in time  different EFC phase
Static EFC scan early in the discharge shows different optimum correction phase
Flattop phase of 15° is counter-productive early on
Phase asymmetry visible in density, neutrons, and core rotation
Search for the time-evolving error field source is ongoing
  Tilted TF, vessel currents?

## Slide 49: Extended-MHD Modeling Is Being Used to Understand Tearing Modes in NSTX(-U)
Modeling tearing modes in NSTX-U is challenging
  Strong coupling among rational surfaces
  Strong rotation and rotation shear
Extended-MHD codes are being developed and used to address this challenge
  Resistive DCON, M3D-C1, MARS
M3D-C1 calculations find unstable TM in NSTX discharge with 2/1 TM
M3D-C1
M3D-C1
δBnorm
N. Ferraro

## Slide 50
The concern for ITER:
  Concern is for asymmetric halo currents during unmitigated disruptions
  Forces are dynamically amplified if Nrot > 2-3
  Critical mechanical resonances in the 3-8 Hz range [Schioler FED 2011]
  Overall response is broader (10-20 Hz) [Bachmann FED 2011 & Lehnen]
Could halo current forces be dynamically amplified in ITER?
  Could the halo currents rotate at frequencies below 20 Hz?
  Could the rotation last long enough to complete 2-3 rotations?
Substantial halo current rotation observed in a number of devices:
  JET Noll 1996, Riccardo 2004 & 2009, Gerasimov 2014 & 2015
  C-Mod Granetz et al. Nucl. Fusion 36, 545 (1996)
  DIII-D Evans et al. J. Nucl. Mater. 241-243, 606 (1997)
  AUG Pautasso et al. Nucl. Fusion 51, 043010 (2011)
  NSTX Gerhardt Nucl. Fusion 53, 023005 (2013)
Leading halo current propagation studies
C. Myers (PPPL)

## Slide 51: Leading studies of rotating halo currents through ITPA multi-machine analysis and M3D-C1 numerical simulations
ITPA multi-machine analysis (MDC WG-6):
Halo current data from C-Mod, DIII-D, AUG, and NSTX
All measurements in lower divertor (> 400 shots)
Halo current rotation is predominantly counter-Ip
Consistent rotation velocity, vh ~ 5 km/sec
C. E. Myers et al. (EX/P6-46)
M3D-C1 simulations:
NSTX(-U) geometry
Simulate in 2D while q >2
Switch to 3D to resolve halo rotation (in progress)
D. Pfefferlé et al. (PPPL)

## Slide 52: Simple rotation frequency scaling: fh ~ 1/R Cannot rule out dynamic force amplification in ITER
Key quantities:
  Nrot = number of rotations
  trot = rotation duration
  fh = Nrot / trot = rotation frequency
Carry out regression using two parameters  R, trot
Additional parameters do not improve regression (e.g., Ip, BT)
  fh ~ 1/R ~ constant vh
ITER projection:
  Rotation at fh < 20 Hz probable
  Rotation duration analysis  Cannot rule out dynamic force amplification in ITER
C. E. Myers, et al. (Manuscript submitted to Nuclear Fusion)

## Slide 53: Resistive DCON Solves Reliable Outer Region Δ′ and Indicates Δ′ is Destabilized by Plasma Pressure
Resistive DCON reproduces Δ’ behavior in Furth, Rutherford and Selberg, Phys. Fluids 16, 1054(1973).
First resistive DCON paper has been published.
Glasser, Wang and Park, Phys. Plasmas 23, 112506 (2016)
n=1 m=2
n=1 m=3
Higher Increase Δ’ at q=2,3
More unstable tearing mode
Resistive DCON solves Δ’ in full toroidal geometry.
Δ’ at q=2
Z. Wang

## Slide 54: RDCON: Optimization of NSTX-U L-Mode discharge to stabilize n=1 tearing mode ( and )
For this scenario, reducing + increasing Decrease in at q=2,3
Resistive DCON is applied to optimize NSTX-U equilibrium to avoid tearing instability (varying equilibrium parameters to minimize ).
A sequence of equilibria are generated by scanning current and pressure profiles with CHEASE code, where plasma boundary of discharge 204718 is used.
(q=2)
(q=3)
Z. Wang