## Slide 1: Recent activities on TST-2
19th International Spherical Torus Workshop (ISTW 2017)
Seoul National University, 18-22 September 2017
Ejiri1, Y. Takase1, N. Tsujii1, S. Yajima1, H. Yamazaki1, Y. Takei1, Y. Tajiri1, B. Roidl1, Y. Yoshida1, A. Kitayama1, A. Sato1,
N. Matsumoto1 Y. Iida1, K. Iwasaki1, Y. Kawamata1, S. Sakamoto1, C.P. Moeller2, K. Saito3, T. Seki3, H. Kasahara3, S. Kamio3
and O. Mitarai4
1The University of Tokyo, Kashiwa 277-8561, Japan
2General Atomics, San Diego, CA 92186, U.S.A.
3National Institute for Fusion Science, Toki 509-5292, Japan
4Kyushu Tokai University, Kumamoto 862-8652, Japan

## Slide 2
Outline
TST-2 device
Lower hybrid wave (LHW) start-up experiment
AC-Ohmic coil operation experiment
Summary and future plan
Background and objectives
Two capacitively-coupled combline (CCC) antennas are used in TST-2 to study the start-up by LHW [1, 2]. Bt and ne dependences are investigated. The performances of the two antennas are compared.
AC Ohmic coil operation is a pre-ionization method and has a potential ability of DC current drive with a quite small flux swing capability [3]. Features of the pre-ionization [4] and applications are presented.
[1] T. Shinya, et al., Nucl. Fusion 57 (2016) 073003.
[2] N. Tsujii, et al., Nucl. Fusion 58 (2017) in press.
[3] A. Ejiri, et al., Plasma Fusion Res. 11 (2016) 1202004.
[4] A. Ejiri, et al., submitted to Nucl. Fusion.

## Slide 3
TST-2 device and the heating systems
X/O-mode horn for ECH
2.45 GHz, Up to 5 kW
Major radius R ～ 0.36 m
Minor radius a ～ 0.23 m
Aspect ratio A = R/a > 1.5
Toroidal field Bt < 0.3 T
For OH/RF(LHW) operation
Plasma current
Ip < 120 kA/26 kA
Discharge duration
Δt < 25 ms/120 ms
CCC antenna
for LHW (200 MHz)
AC Ohmic coil operation

## Slide 4: Outboard-launch and Top-launch capacitively coupled combline (CCC) antennas for LHW current drive
Developed in collaboration with C.P. Moeller (GA, US)
Traveling SW is excited directly
Sharp n|| spectrum & high directivity

## Slide 5: Bt and ne dependences (for the outboard antenna)
Fig. 10 from [2]
Ip increases with ne, and higher Bt is necessary to sustain higher ne

## Slide 6
Explanation of the ne dependence using the GENRAY/CQL3D chord (I)
Lower density
(& weak n|| up-shift)
Better accessibility for low n|| waves

## Slide 7
Explanation of the ne dependence using the chord GENRAY/CQL3D (II)
For detail,
visit Poster-19 by
N. Tsujii (Y. Takase).

## Slide 8: Comparison of the performances (I)
Bt : CW
Bt : CCW
High Bt/ Low Bt
Top (solid)/Outboard (dotted)
Bt:CW(left)/CCW(right)
Outboard is better at the initial phase (to increase Ip).
To achieve higher Ip higher Bt (and higher ne) is better, and Top is better.
Ip [kA]
Bt [T]
PLHW [kW]
PLHW [kW]
Top
Outboard
SX [a.u.]
nel [1018m-2]
8 discharges:

## Slide 9: Comparison of the performances (II)
Low bulk Te, hollow Te profile, peaked ne profile.
Slightly higher edge Te for Outboard.
Outboard
Top
Measurements by
Thomson scattering

## Slide 10
Poloidal flow
Comparison of the performances (III)
Line of sight: Rtan=300 mm
Near magnetic axis
Top/Outboard
Toroidal flow
Ip
Bt
Vp
Er=
Top: ~ +2 (outward)
Outboard: ~+300 V/m
Ion temperature and flow of CIII (C2+)
Ip [kA]
PLHW [kW]
nel [1017m-2]
Intensity of CIII
Intensity of CIII

## Slide 11: Comparison of the performances (IV)
Hard X-ray spectra measured by an NaI(TI) scintillator
Top/Outboard
Line of sight:Rtan=260 mm
Rtan=360 mm
Rtan=560 mm
Inboard side
Near magnetic axis
Outboard edge
Teff ~ 51 keV
Teff ~ 41 keV
Teff ~ 34 keV
Teff ~ 30 keV
Teff ~ 33 keV
Teff ~ 27 keV
A larger energy flux and a higher Teff for Top.
High at the inboard side Top.

## Slide 12: Comparison of the GENRAY results
Bt : CW
Bt : CCW
Outboard
Top
In the case of Outboard, both CW and CCW Bt should show similar rays as long as the plasmas have up-down symmetry.
In the case of Top, CW Bt should be better because of the core accessibility and the upshift in n||.
The experimental high Ip for Top+CCW Bt, requires further understanding.

## Slide 13: Spectrum obtained by an RF pickup coil
Bt, Ip
High Bt
Low Bt
Asymmetric spectrum broadening (parametric decay instability?) of the injected wave
RF pickup coil:1-turn loop

## Slide 14
AC Ohmic coil operation for pre-ionization, current ramp-up and heating
IGBT
H-bridge
DC
Capacitance
PS
Resistive V.V. INCONEL625
(t=1.57mm)
1/e Frequency: 133 kHz
t
VL
t
Y
Square AC VL with frequencies < 10 kHz
Small flux swing capability
Ip ?
t
Cumulative effect to increase ne (i.e., pre-ionization)?
Heating power: <IpVL> → DC current drive?
Targets:
a reliable pre-ionization method for reactors
a new current start-up tool

## Slide 15
Discharges without vertical field ramp-up
to study pre-ionization
20
22
24
26
0
1
-1
Time [ms]
28
30
0
0.4
-0.4
100
10-2
10-4
10-6
VL [V]
Ip [kA]
Radiation & Visible [a.u.]
#137292
Vis. PMT
Vis PD
Rad
After a certain time, Ip, ne, light emissions grows exponentially and saturate at a level. A thin plasma attached to the inboard wall is formed
R [mm]
Z [mm]
~800 mm
~130 mm
130 mm
Visible emissions, radiation ne are nearly proportional.
Growth rate, appearance time and saturation level of visible emissions characterize the pre-ionization.

## Slide 16
Growth rate [1/ms]
Saturation level of radiation [a.u.]
|VL| [V]
0.4
0.6
0.8
1.0
3.0
1018
1012
0.0
(a)
(b)
BZext=
-0.52 mT
0 mT
+0.08 mT
(fAC=2 kHz/pG=3.9x10-5 Torr/Bt=0.41 T/BZext=-0.52, 0, +0.08 mT)
0.2
0.01
0.1
1
Saturation level of Ip [kA]
(c)
Growth rate [1/ms]
Saturation level of
Ip [kA]
3.0
0.0
(a)
(b)
H2
(|VL|=0.94 V/fAC=2 kHz/Bt=0.41 T/BZext=0)
0.0
0.4
D2
1
10
pG [10-5 Torr]
Saturation level of radiation [a.u.]
(c)
Loop voltage VL dependence
Filling pressure (D2, H2) dependence
Minimum |VL|~0.4 V = 0.5 V/m

## Slide 17
BZext [mT]
-1.0
+1.0
0
-0.5
+0.5
-1.0
+1.0
0
-0.5
+0.5
BZext [mT]
2
1
0
50
10
1
5
1
0.1
0.001
0.01
(a)
(b)
(c)
(d)
(e)
(f)
Saturation level of radiation [a.u.]
Growth rate [1/ms]
Appearance time [ms]
-BZTF-0.12 [mT]
-BZTF-0.12 [mT]
(|VL|=0.67, 0.72 V/fAC=2 kHz/pG=3.9x10-5 Torr/Bt=+0.41, -0.41T)
External BZ dependence

## Slide 18
0-dimensional model
Equation of motion
Evolution of density

## Slide 19
R
Z
2RWidth=0.13 m
2Zlimit =0.8 m
Rin=0.13 m
Ohmic coil
Vt
Bt
BZ, BR
Lc
0
(a)
(b)
(c)
(d)
Ip
(e)
Plasma region
Error field by TF coil
Self field by Ip
Leak field by Ohmic coil
Field line
BZOH
BZTF
BZP
Z [mm]
0
R [mm]
0.2
0.4
0.6
0
R [mm]
0.2
0.4
0.6
0
R [mm]
0.2
0.4
0.6
0
-0.5
0.5
(c)
(d)
(VF)
Magnetic configuration in the AC Ohmic coil operation
Ohmic coil
Thin INCONEL wall
Thick SUS wall
Reconstructed flux surfaces

## Slide 20: Time evolution calculated by the 0-dimensional model
1
-1.5
1.5
1017
1014
VL [V]
Vt
[106 m/s]
Time [ms]
0
0.2
0.4
0.6
0.8
1
0.4
10
-0.1
0.3
-1
1
BZ [mT]
-0.4
0
0
0
0
Birth & loss rate
[1/ms]
ne
[m-3]
Ip [kA]
(a)
(b)
(c)
(d)
(e)
(f)
Birth rate
loss rate
(|VL|=0.8 V/fAC=4 kHz/pG=3x10-5 Torr/Bt=0.34T/Te=10 eV)
Linear growth, saturation of Ip and various dependences can be reproduced by the model.
Quantitative agreements between the model and experiments are typically within a factor of 10.
However, D2/H2 and Bz dependence of the appearance time can not be reproduced.
In addition, 0-dimensional model is not appropriate theoretically due to the diffusive loss and the impossibility in ambipolar diffusion state. -> development of 1-dimensional model

## Slide 21
10
20
30
40
0
0.8
1
2
0
0
1
2
0.4
Time [ms]
ne [1018m-3]
Bz [mT]
-10
0
+10
Ip [kA]
(a)
(c)
(d)
(e)
-10
0
+10
VL [V]
Ip [kA]
(<1.2 kHz)
(b)
(f)
(g)
0.26 m
0.26 m
Application of external BZ induces a DC component in Ip
Enlarged
BZ ramp up
Time averaged camera image
Thin cylindrical plasma
ST-like shape
Gas puff

## Slide 22: Pre-ionization by ECH and AC Ohmic coil operation for LHW start-up
PECH~2.5 kW
|VL|=0.7 V, fAC=2 kHz
Successful pre-ionization by AC Ohmic coil operation for LHW plasma
PECH & VL [V]
Ip [kA]
Radiation [a.u.]
PLHW [a.u.]
20
40
60
80
Time [ms]
0

## Slide 23
Summary
LHW current drive
Two capacitively coupled combline (CCC) antennas at the outboard side and the top of the plasma were used.
Ip increases with Bt and ne. The top launch antenna seems to be slightly better in achieving higher Ip.
AC Ohmic coil operation
AC Ohmic operation experiments has been performed and it was shown that it can be used as a reliable pre-ionization tool.
A 0-dimensional model was developed, and it can reproduce various experimental dependences, but 1-dimensional model is preferable for better understanding of the physics of the AC Ohmic coil operation.
External BZ induces a DC component in Ip
This work is supported by JSPS Grant-in-Aid for Scientific Research 21226021 and 23360409, NIFS Collaboration Research Program NIFS14KOCR001 and NIFS12KUTR078, JSPS A3 Foresight Program.

## Slide 24
Future plan and targets
According to experimental and numerical studies, improvements in the current drive efficiency and in Ip is expected by the following methods.
Optimization of antenna position and n|| spectrum.
3-D control of wavevector
Combination of 200 MHz and 450 MHz (core heating)
Ip Reduction of SOL losses
Higher Bt
Z [mm]
0
R [mm]
0.2
0.4
0.6
0
-0.5
0.5
In order to understand boundary effects (e.g. secondary electron emission) in AC Ohmic operation
A new short coil at the center would be useful

## Slide 25: Backup

## Slide 26: Comparison between experiment and 0-dimensional model
Growth rate [1/ms]
Saturation level of radiation [a.u.]
|VL| [V]
0.4
0.6
0.8
1.0
3.0
1018
1012
0.0
(a)
(b)
BZext=
-0.52 mT
0 mT
+0.08 mT
(fAC=2 kHz/pG=3.9x10-5 Torr/Bt=0.41 T/BZext=-0.52, 0, +0.08 mT)
0.2
0.01
0.1
1
Saturation level of Ip [kA]
(c)
Growth rate [1/ms]
Saturation level of ne [1016 m-3]
10
5
0
BZext=
-0.52 mT
0 mT
+0.08 mT
(fAC=2 kHz/pG=3.9x10-5 Torr/Bt=0.41 T/Te=10 eV)
(a)
(b)
|VL| [V]
0.4
0.6
0.8
1.0
0.2
0
0
0.2
0.4
(c)
Saturation level of
Ip [kA]
Ip0/8
ne0/4
|VL| [V]
0.4
0.6
0.8
1.0
0.2
(d)
(e)
(f)

## Slide 27: Comparison between experiment and 0-dimensional model
Growth rate [1/ms]
Saturation level of
Ip [kA]
3.0
0.0
(a)
(b)
H2
(|VL|=0.94 V/fAC=2 kHz/Bt=0.41 T/BZext=0)
0.0
0.4
D2
1
10
pG [10-5 Torr]
Saturation level of radiation [a.u.]
(c)
Growth rate [1/ms]
Saturation level of
Ip [kA]
Saturation level of ne [1017 m-3]
0.0
0.5
1
10
pG [10-5 Torr]
0.0
2.0
10
0
(|VL|=0.94 V/fAC=2 kHz/Bt=0.41 T
/Bzext=0 /Te=10 eV)
(a)
(b)
C0=1
C0=1/2
C0=1
(c)
Ip0/8
ne0/4
C0=1/2
C0=1/2
C0=1

## Slide 28: Comparison between experiment and 0-dimensional model
Frequency [kHz]
0.1
10
1
Growth rate [1/ms]
& VLrms [V]
0.2
0.6
1.0
1.4
0.2
0.4
0.0
Saturation level of Ip [kA]
and radiation [a.u.]
(a)
(b)
VLrms
(VLrms=0.62-0.72 V/pG=5.2x10-5 Torr/Bt=0.42 T/BZext=0)
Ip
radiation
(pG=5.2x10-5 Torr/Bt=0.42 T
/Bzext=0 /Te=10 eV)
C0=1/2
|VL|=0.72 V
|VL|=0.6 V
(d)
(f)
(e)
fAC [kHz]
0.1
10
1
Growth rate [1/ms]
Saturation level of
Ip [kA]
Saturation level of ne [1017 m-3]

## Slide 29: Comparison between experiment and 0-dimensional model
BZext [mT]
-1.0
+1.0
0
-0.5
+0.5
10
0
1.0
0.1
(a)
(b)
(c)
Growth rate [1/ms]
(|VL|=0.68 V/fAC=2 kHz/pG=3.9x10-5 Torr/Te=10 eV)
-2
Saturation level of ne [m-3]
1017
1016
1015
Inverse growth rate [ms]
Bt=+0.41 T
Bt=-0.41 T
3.0
ne0/4
C0=1
C0=1/2
BZTF
BZext [mT]
-1.0
+1.0
0
-0.5
+0.5
-1.0
+1.0
0
-0.5
+0.5
BZext [mT]
2
1
0
50
10
1
5
1
0.1
0.001
0.01
(a)
(b)
(c)
(d)
(e)
(f)
Saturation level of radiation [a.u.]
Growth rate [1/ms]
Appearance time [ms]
-BZTF-0.12 [mT]
-BZTF-0.12 [mT]
(|VL|=0.67, 0.72 V/fAC=2 kHz/pG=3.9x10-5 Torr/Bt=+0.41, -0.41T)

## Slide 30: 1-dimensional model
+
+
+
+
Limiter
Limiter
Limiter
Limiter
R
Z
0
(a)
Plasma region
(b)
Field line
0
2p
Toroidal angle
Z
x
2RWidth
2Zlimit
+
+
0000
ri
Wall
(Eext=-1 V/m / xl=200 m /pG=1x10-4 Torr /
kTe=kTi=5 eV / gs=1)
0
200
x [m]
100
0
200
-10
0
ne & ni [107 m-3]
0
1
2
(a)
(b)
(c)
E [V/m]
f [V]
500 ms
40 ms
500 ms
40 ms
500 ms
40 ms
ne
ni
500 ms
0 ms
0 ms
40 ms
Reproduction of ambipolar diffusion state.
Secondary electron emission by ion impact at the walls are candidate mechanism to mitigate or destroy the ambipoloar state.