## Slide 1: Status of the Lower Hybrid Fast Wave Research on VEST 2017 ISTW Workshop @ SNU
20th. Sep. 2017
S. H. Kima, B. K. Junga, S. H. Jeonga, H. W. Leeb, B. J. Leeb, J. G. Joc, J. I. Wangc, H. Y. Leec,
and Y. S. Hwangc
aKorea Atomic Energy Research Institute
bKwangwoon University
cSeoul National University
Notes: I will present the status of LHFW research at KAERI.

## Slide 2: Contents
Introduction to LHFW (Lower Hybrid Fast Wave)
- LHFW on CMA / Dispersion relation / Propagation boundary
- Advantages & Disadvantages
Simulation of LHFW on VEST
- Ray tracing simulation (Genray)
- Coupling efficiency simulation (1D full wave)
RF System development & Installation & Coupling experiment
- Klystron / Antenna & Integration Test
- Installation & Antenna S-parameter measurement
- Coupling experiment at low power
Summary & Future Plans
Notes: Then, let’s move on LHFW.

## Slide 3: Introduction to LHFW(0)
The continuous current drive is one of the key issues toward steady-state operation of tokamak fusion reactors.
Though the current drive by using bootstrap is the main strategy in tokamak, the external current drive is still required to control pressure profile and fill the gap between the bootstrap and target current.
Most efficient current drive ever is the LHCD which is a scheme by using slow wave in lower hybrid resonance frequency range.
However, LHCD has density limit and it is hard to propagate into the central region in high temperature due to highly damping.
Therefore, new ways to improve LHCD or alternatives to LHCD are required.
LHFW could be an alternative.
Notes: Then, let’s move on LHFW.

## Slide 4: Introduction to LHFW(1) Lower Hybrid Fast Wave(LHFW) on CMA diagram
<H plasmas>
LHFW is a fast wave between lower hybrid resonance frequency and electron cyclotron resonance frequency.
Notes: Then, let’s move on LHFW.

## Slide 5
Dispersion Relation
Introduction to LHFW(2)
Dispersion & Propagation Boundary
Propagation Boundary
The perpendicular wave number of LHFW is less than that of slow wave in this frequency range(LHSW).
The imaginary wave number of LHFW becomes higher as the density increases.
Notes: Then, let’s move on LHFW.

## Slide 6
Advantages of LHFW(1)
Parallel electric field Ez to B
<Polarization of FW and SW on CMA>
It has favorable polarization for current drive compared to FWs in other frequency range.
Notes: The dispersion relation in lower hybrid resonance frequency range can be expressed like this. The left is the real perpendicular refractive index which represent the propagation. And the right is the imaginary part which represent damping or absorption. There are two wave branches, Slow and fast waves. And the slow wave has large wave number as wave approaches the resonance S=0. On the contrary, fast wave has small wave number compared to slow wave. For the damping, once the Landau damping condition is satisfied, the slow wave can be efficiently absorbed. In contrast, fast wave depends on the plasma density.
If the plasma density is low, as in the edge region of plasmas, the denominator becomes very large so that the damping becomes very low. But, if the density is as high as it becomes order of one, fast wave can efficiently absorbed as well as slow wave.
Unfortunately, the LHFW has two limiting conditions, launching and accessibility condition. The launching density of LHFW is proportional to the driving frequency. It is several to several tens times of that of HHFW or ICRF, so the launching density is actually very large compared to that of the fast waves in ICRF or HHFW. It makes the LHFW to start to propagate into plasmas compared to fasts waves in other frequency range. The confluence density, It is more generalized accessibility condition of Stix-Golant. The LHWs should avoid the density as they propagates into the plasmas. Otherwise, the fast and slow wave mode converted each other at the confluence density. The two limiting conditions make a density window interior of plasmas in 1D configuration.

## Slide 7
It has deep penetration property in high density.
<Angle of Group Velocity Vg to magnetic field of LHFW and LHSW>
Advantages of LHFW(2)
More perpendicular Vg to B
B
Vg
Notes: The dispersion relation in lower hybrid resonance frequency range can be expressed like this. The left is the real perpendicular refractive index which represent the propagation. And the right is the imaginary part which represent damping or absorption. There are two wave branches, Slow and fast waves. And the slow wave has large wave number as wave approaches the resonance S=0. On the contrary, fast wave has small wave number compared to slow wave. For the damping, once the Landau damping condition is satisfied, the slow wave can be efficiently absorbed. In contrast, fast wave depends on the plasma density.
If the plasma density is low, as in the edge region of plasmas, the denominator becomes very large so that the damping becomes very low. But, if the density is as high as it becomes order of one, fast wave can efficiently absorbed as well as slow wave.
Unfortunately, the LHFW has two limiting conditions, launching and accessibility condition. The launching density of LHFW is proportional to the driving frequency. It is several to several tens times of that of HHFW or ICRF, so the launching density is actually very large compared to that of the fast waves in ICRF or HHFW. It makes the LHFW to start to propagate into plasmas compared to fasts waves in other frequency range. The confluence density, It is more generalized accessibility condition of Stix-Golant. The LHWs should avoid the density as they propagates into the plasmas. Otherwise, the fast and slow wave mode converted each other at the confluence density. The two limiting conditions make a density window interior of plasmas in 1D configuration.

## Slide 8
Launching density condition
Accessibility condition.
Disadvantages of LHFW
Coupling Issue
< Propagation Boundary >
* High density is required to launch LHFW compared to LHSW.
☞ Coupling Problem
* The same accessibility condition as LHSW should satisfy. (Stix-Golant)
* The confluence density condition is a generalized accessibility condition.
Notes: Then, let’s move on LHFW.

## Slide 9
Propagation and Absorption of LHFW (VEST)
Real and Imaginary perpendicular wave number (0.2T/ 500 MHz /3x1018#/m3/ N||=4)
Notes: Then, let’s move on LHFW.

## Slide 10: RAY tracing simulation on VEST (GENRAY)
LHFW launching
LHSW launching
10
Comparison between LHFW and LHSW launching
(0.2T/ 500 MHz / 3x1018 #/m3/ 3 keV/ N||=4)
LHFW
launching
LHSW
launching
100 kA / 10kW
125 kA / 10kW
Normalized radius
Notes: Then let’s compare the LHFW launching with LHSW launching cases. As shown in this figure, LHFW can propagated into more central region. In addition, the current drive is comparable to LHSW.

## Slide 11: Coupling efficiency (1) 1D full wave code
11
Edge density profile model
A system of ordinary differential equation
Boundary condition
LHS : Ey (poloidal) = 1,
Ez(toroidal) = 0
RHS : No reflection from bulk
plasmas (WKB boundary)
Governing Equation
a
(d)
Pedestal
: Pedestal width
: Pedestal top-density
Notes: As I explained before, the launching density of LHFW is very large compared to that of fast waves in other frequency range and even larger than that of LHSW. It means that it could be very difficult to couple the input power to LHFW. So, we need to estimate the coupling efficiency of LHFW. In lower density than about 3x1017#/m3 which is close to FW launching density, the coupling of LHSW is superior to LHFW. And even for Ey exciaton, all power is coupled to LHSW. However, the density is greater than the launching density, it is reversed. The coupling efficiency of LHFW is almost 10 times greater than that of LHSW. Interesting thing is that in both cases, a part of the input power is coupled to other branches. And the density gradient increases, the ratio increases. It is because that it is impossible to separate two wave branch in high density gradient region. The most power coupling theory is based on WKB approximation, but the approximation breaks in high density gradient region.

## Slide 12: Coupling efficiency (2) Density effect
12
for LHFW launching
for LHSW launching
Parameters | Values
B0 | 0.2 T
Frequency | 500 MHz
N∥ | 4.0
n0 | 6x1015 ~ 5x1017 #/m3
nb | 4x1015 #/m3
d(X2-X1) | 3 cm
X1 | 2 cm
Pedestal
: Pedestal width
: Pedestal top-density
Notes: As I explained before, the launching density of LHFW is very large compared to that of fast waves in other frequency range and even larger than that of LHSW. It means that it could be very difficult to couple the input power to LHFW. So, we need to estimate the coupling efficiency of LHFW. In lower density than about 3x1017#/m3 which is close to FW launching density, the coupling of LHSW is superior to LHFW. And even for Ey exciaton, all power is coupled to LHSW. However, the density is greater than the launching density, it is reversed. The coupling efficiency of LHFW is almost 10 times greater than that of LHSW. Interesting thing is that in both cases, a part of the input power is coupled to other branches. And the density gradient increases, the ratio increases. It is because that it is impossible to separate two wave branch in high density gradient region. The most power coupling theory is based on WKB approximation, but the approximation breaks in high density gradient region.

## Slide 13: RF System for LHFW experiment on VEST
Schematic of LHFW RF System
- Frequency : UHF
- Power : 10 kW(Klystron)
- Antenna : Comb-line type

## Slide 14: Klystron (1)
Klystron
- Old klystron system for UHF broadcasting has been refurbished.
 | Varian
Frequency | 470~700 MHz
Output | 37.5 kW
Drive Power | 600 mW
Gain | 48 dB
Beam voltage | 19.5 kV
Beam current | 5.4 A
Electrode voltage | 19.5 kV
Heater voltage | 7 V
Heater current | 17 A
Body current | 50 mA
Magnet Voltage | 145 V
Magnet Current | 32 A
Magnet Cooling | Water 2.0 gal/min
Cooling(Collector) | Water 1.5 gal/min
Cooling(Body) | Water 2.0 gal/min
Cooling(Gun/Heater) | Forced Air 50 ft3/min
Harris transmitter frame(SNU)
Varian Tube (SNU/KAPRA)
NEC Beam P/S(KAPRA)
Harris UHF transmitter Specification

## Slide 15
Integration of Klystron System
15
Klystron (2)
DC P/S
15kV-6A
Dummy Load
(10kW CW)
Magnet
H/V, Filament
Connector
Collector
T/L
3-1/8 EIA
Cooling
Water
Inlet

## Slide 16
Beam perveance & RF power Test
16
Klystron (3)
Klystron Output Power (@ ~500 MHz)
Beam Perveance

## Slide 17
LHFW Antenna (1)
Research Objective |  | Consideration Points | 
Frequency | UHF | Antenna Length | ~ 418 mm
Bandwidth | < 50 MHz | Antenna width | < 200 mm
VSWR | < 3 | E-field ratio(Ey/Ez) | 4~6
Peak n∥ | 3 ~ 5 | Peak E-field | < 30 kV/cm
<VEST>
<Combline type Antenna>
designed by KWU

## Slide 18
LHFW Antenna (2)
Antenna Structure
Simulation Domain for Design(HFSS / COMSOL)
Antenna in Vacuum
Plasmas or Vacuum
Perfect Matched Layer
Periodic B.C.
Periodic B.C.
Exciting strap
Field isolator
Radiating strap
Faraday shield
Port 1 : Feeding
Port 2 : dummy
(back side)

## Slide 19
Field distribution & S-parameters (Vacuum load- HFSS)
LHFW Antenna (3)
Condition
S-parameters
- Vacuum load
- Frequency : 500 MHz
S11 = -19.65 dB
S21 = -0.06 dB

## Slide 20
Field distribution & S parameters (Plasma load - COMSOL)
LHFW Antenna (4)
Condition / S-parameters
Density Profile
- Plasma load(gap : 0.5cm)
- Frequency : 500 MHz
- B0 : 0.2 T
S11 = -14.9 dB
S21 = -15.0 dB

## Slide 21
Antenna Parallel wave number N|| (Plasma load)
475~510 MHz
N|| : 3.5 ~ 5
LHFW Antenna (5)

## Slide 22
22
Antenna Fabrication & Test
Comb-line Antenna Inside
Comb-line Antenna with FS + Internal TR
Current
Straps
Port 2
Dummy
Port 1
Feeder
Faraday
Shield(FS)
Internal Transformer
Comparison between S-parameters measured and simulated(HFSS)

## Slide 23
23
RF System Integration & Test
Klystron
Circulator
Antenna
Comb-line Antenna
Antenna with RF shield
Output Power (10 kW@496.5MHz)
DC
Beam P/S
Remote
Control & Monitor
SSA
Transmission Line
Dummy
Integrated RF system

## Slide 24
Reflection coefficient (S11)
Transmission coefficient (S21)
24
Installation on VEST
RF System installed on VEST site
Klystron
Circulator
DC
P/S
Dummy
Load
Antenna installed in VEST chamber
Chamber
inside
Chamber
outside
* Feeding power lines for DC P/S, Cooling system, and Transmission lines are under construction.

## Slide 25: Plasma Coupling Experiment @ Low Power (Signal Generator)
~5 kA
~18 kA
~38 kA
LHFW launching density range
20
#15355
Notes: Then, let’s move on LHFW.

## Slide 26: Summary
The steady-state operation is one of the key issues of tokamak fusion reactors.
A current drive by using a fast wave in lower hybrid frequency range(LHFW) was suggested and the proof of principle experiment was planned on VEST.
Because it has favorable parallel electric field for current drive and good penetration property in high density, though it has coupling issue due to its high launching density.
==========================================================================
RF power have been prepared by refurbishing an old broadcasting klystron system through collaboration with SNU and KAPRA. It is successfully integrated and proved to generate RF power up to10 kW stably.
As a LHFW launcher, a compact comb-line antenna has been designed with COMSOL /HFSS codes by KWU. It is turned out that the design and fabrication is successful through the S-parameter measurement & 10 kW power test.
All the RF system are finally installed on VEST except transmission lines and utilities for the system.
Summary
Notes: Then, let’s move on LHFW.

## Slide 27: Summary & Future Plan
A series of coupling experiments are progressing at low power with a signal generator.
The first experiment result shows that the comb-line antenna works normally in plasma environment at low power.
It seems that the RF power is coupled to Lower Hybrid Fast Wave(LHFW) because the power coupling increases dramatically in relation to LHFW launching density.
==========================================================================
Coupling characterization experiment.
High power LHFW H&CD experiment based on coupling characterization.
(after completion of utilities and transmission lines)
TF upgrade to 0.2 T to increase upper density boundary limit by confluence and make current drive possible in higher density.
Future Plan
Summary
Notes: Then, let’s move on LHFW.