## Slide 1: Merging Formation of High-b STs in UTST
M. Inomoto, T. Ushiki, X. Guo, T. Sugawara,
K. Kondo, T. Mihara, Y. Minami, Y. Inai,
H. Tanabe and Y, Ono
Graduate School of Frontier Sciences, The University of Tokyo
This work is supported by A3 Foresight Program, JSPS KAKENHI 16K14525, 15H05750, 15K14279, 26287143 and NIFS collaboration program NIFS15KBAR012, NIFS15KNTR001, NIFS16KOAP030, NIFS17KNWP006.
19th International Spherical Torus Workshop (ISTW 2017)

## Slide 2: Goal of UTST Research
To demonstrate ST start-up without use of center-solenoid (CS) coil.
1) Formation of two STs by using outer (ex-vessel) poloidal field (PF) coils
2) Axial merging of two STs providing reconnection heating to form high-b plasma
3) NBI H&CD
Dynamic formation within ~1 ms
Merging start-up
demonstrated in
TS-3/TS-4/START/MAST
TS-U/ST40

## Slide 3: Required performance for UTST start-up scheme
ST plasma with high-Ip, high-ne and high-Te should be formed to apply NBI H&CD.
Since outer PF coil start-up cannot sustain the plasma current for a long period, Ohmic heating is not expected in this start-up scheme.
Utilization of MW-order reconnection heating is essential to form high-b equilibrium
Initial density + compression
+fueling
Reconnection heating
Outer PF coil start-up

## Slide 4: Present status of UTST
Four pairs of outer PF coils are energized by total 1 MJ capacitor banks.
Typical parameters (merging start-up)
R ~ 0.35 [m] / a ~ 0.2 [m]
Ip < 120 [kA]
Bt ~ 0.2 [T]
ne < 5 x 1019 [m-3] ~ 0.5 x nG
Te, Ti ~ 10 [eV] (initial plasma)
Te < 30 [eV], Ti < 50 [eV] (after merging)
These parameters are not sufficient as a target plasma for 500 kW/25 keV NBI.

## Slide 5: UTST-NBI initial experiment in 2016-17
NBI was applied on the ST plasma produced by recently-developed longer-pulse discharge without CS current drive.
T. Sugawara

## Slide 6: Density increase is required for effective NBI
Ip and SXR waveforms showed no significant change by NBI.
Expected shine-through loss was as high as 40 % for peak density of 5x1019 [m-3].
Gas puffing is helpful to reduce the shine-though loss.
T. Sugawara
Improvement of plasma performance is needed.
SXR signal (Filter : Mylar 1mm (>200eV))

## Slide 7: Necessary improvement for effective NBI heating
Three plasma parameters, Ip, Te and ne should be improved. Particularly the plasma current is essential because it determines the reconnection heating power, density limit, and fast ion orbit loss.
H. Tanabe, et al., Nucl. Fusion 2017.
Ion heating by merging
~Bp

## Slide 8: Electron heating in merging start-up period
Electron heating mechanism in merging process is still unclear. Localized electron heating was observed in MAST experiment.
T. Yamada, et al., Nucl. Fusion 2016.
X-point?
Peak Te depends strongly on Bt, while Bt does not reconnects.

## Slide 9: UTST current tasks
Increase initial plasma current driven by outer PF coils.
  Optimization of pre-ionization and coil waveform
Improve reconnection heating effect in merging period.
  Well balanced merging
  Efficient electron heating
  Compression
Density increase.
  Gas puffing or compact torus injection
Increase initial plasma current driven by outer PF coils.
  Optimization of pre-ionization and coil waveform
Improve reconnection heating effect in merging period.
  Well-balanced merging
  Efficient electron heating
  Compression
Density increase.
  Gas puffing or compact torus injection

## Slide 10
For well-balanced merging…

## Slide 11: Well-balanced merging
Generate two “identical” initial ST plasmas and control their motion precisely to merge on the center of the device.
Reconstruction of shape and current of each initial STs is required.
Since large eddy current flows on the vessel wall in the start-up period, development of fine reconstruction scheme with eddy current estimation is needed.

## Slide 12: Modified-Cauchy Condition Surface (M-CCS) method applied to merging STs
Magnetic flux at sensors
Magnetic field at sensors
Magnetic flux on CCS
Three boundary integral functions are solved by truncated singular value decomposition (TSVD) technique.
Contributions from plasma current (CCS)
Contributions from eddy current
Advantage of M-CCS method is that it can estimate the plasma and eddy current in a single manner.
CCS : K. Kurihara, Fusion Eng. Des. 51-52, 1049 (2000).
M-CCS : M. Itagaki, et al., Plasma and Fusion Res. 9, 1402046 (2014).

## Slide 13: Modified-Cauchy Condition Surface (M-CCS) method applied to merging STs
T. Ushiki, et al., submitted to Fusion Eng. Des.
Reference data
Reconstructed profile
Flux surfaces with two magnetic axes are accurately reconstructed by M-CCS method.
Magnetic sensors : 43
Flux loops : 47
Nodes on CCS : 18 (unknowns : 36)
Nodes (unknowns) on the wall : 51

## Slide 14: Eddy current profile is well estimated by M-CCS method
The M-CCS method well reconstructs the eddy current profile as well as the plasma current and LCFS.
T. Ushiki, et al., submitted to Fusion Eng. Des.

## Slide 15: Limiters and flux loops installed
Based on the analytic results of reconstruction, limiters and flux loops were installed on the UTST vessel wall.
Other upgrades for start-up improvement, such as pre-ionization and fueling, are ongoing.

## Slide 16
Electron heating by reconnection

## Slide 17: Electron heating by reconnection
Magnetic reconnection converts magnetic energy to plasma kinetic/thermal energy within a short period, resulting in >MW order (30J/20ms) heating power.
It is believed that the released magnetic energy largely energizes ions at the downstream region in MHD regime due to ion’s heavy mass.
Inomoto+, NF 2015

## Slide 18: Ion heating in UTST merging
Ti measurement (CIII 464.74nm, 46 chords and z-scan) showed that ion heating up to 50 eV localized at the downstream region in UTST merging start-up.
H. Tanabe
Reconstructed temperature

## Slide 19: Reconnection heating in UTST
Small heating effect was achieved in UTST because the initial two STs with low Ip contain small poloidal magnetic energy that is partially converted to the plasma thermal energy.
Inomoto+, NF 2015

## Slide 20: Reconnection heating on ions and electrons
In MHD picture of anti-parallel reconnection, ions and electrons flow with same velocity out from the X-point by ExB drift. Thus, ions are dominantly energized by reconnection.
On the other hand, the localized electron heating observed in MAST, could be provided by another mechanism of direct electron energization.

## Slide 21: Soft X-ray burst found in reconnection period
SXR signal indicates that energetic electrons were generated during reconnection event.
Non-thermal energetic component could be generated by parallel electron acceleration.

## Slide 22: Ring-shaped SXR emission formed in early reconnection phase
T. Ushiki
9.516msec
9.520msec
9.525msec
Center stack
Measurement system looking up at the reconnection region.
SXR image (Filter : Mylar 1mm (>100eV))

## Slide 23: Non-thermal electrons rotate toroidally at the X-point?
Slim ring-shape emission from the X-point seen by SXR and visible line spectra.
Te^ and ne slightly increase near the X-point but do not peak so sharply (UTST Thomson scattering).
Electrons with high toroidal velocity are likely to rotate near the X-point where Bp is negligible.
CIII (464nm)
Center stack

## Slide 24: Electron acceleration in high guide field reconnection
In non-relativistic regime, the peak electron velocity v// is given by
and the accelerated electrons flow out from the reconnection region and accumulate in the downstream region.
In UTST experiments with high guide field (Bt/Bp>10), accelerated electrons stays longer at the reconnection point to form a ring-shaped emission region.
Drake+ PRL 2005.
Lapenta+ POP 2010.
Bguide / Breco ~ 1
Lc : cavity length along Breco

## Slide 25: Why fast electrons stay near the X-point?
Since strong toroidal field exists at the X-point, electrons are well confined when the poloidal closed surface is formed.
Even though the number of the fast electrons is smaller than the bulk electrons, they might carry significant current and modify the magnetic structure.
Double- or Triple-ring emission is sometimes observed. Multiple closed flux surfaces may be formed.

## Slide 26: The SXR burst and magnetic fluctuations were observed in the early phase
merging
Fluctuation signals consist of two components, (1) ~fci, (2) ~10fci.
SXR emission and fluctuation occur only in the early phase of merging.
Fluctuation Spectra

## Slide 27: ~ fci fluctuation modifies the magnetic field structure in current layer
Shot:140430010
Once a single-peaked current layer is formed, then locally-enhanced current modifies the magnetic structure to confine fast electrons.

## Slide 28: Closed flux surface inside the current layer
Closed flux surface inside the reconnection current layer helps to confine electrons to reach high energy range by parallel electric field.
Long-lived closed flux surfaces will enhance the conversion ratio to electron energy although they are radially unstable.
VIS/SXR emission, ~10 fci fluctuation

## Slide 29: Summary
For effective NBI heating, improvements of ST formation scheme are in preparation (reconstruction, pre-ionization, waveform optimization, fueling, etc.).
To achieve high electron temperature, reconnection heating mechanism has been investigated.
Assumed mechanism
  Magnetic reconnection with strong guide field involves significant electron acceleration by parallel reconnection electric field.
  The accelerated electrons rotate toroidally near the X-point, forming current channel.
  The enhanced current modifies magnetic field profile inside the current layer to confine fast electrons.
Need further investigation on thermalization/transport process.

## Slide 30
Thanks for listening

## Slide 31: Reconnection electric field largely fluctuates
Global magnetic structure changes within 60 ms,
The reconnection electric field revealed large fluctuation in the early phase of merging.

## Slide 32: Extreme high-b plasma (so-called “FRC”) was sustained only by NBI
The FRC is a torus plasma confined only by poloidal magnetic field, Recent experiments show that the FRC is sustained quasi-steadily only by 10 MW-NBI.
H. Gota, et al., 26th IAEA-FEC EX/P3-41

## Slide 33: UTST Thomson scattering
Since laser is injected along axial direction and radially-directed scattered light is collected, poloidal electron temperature is measured.
T. Sugawara