## Slide 1
Configuration Studies for an ST-Based Fusion Nuclear Science Facility (FNSF)
Dr. Jonathan Menard
on behalf of:
M. Boyer1, T. Brown1, J. Canik2, B. Covele3, C. D’Angelo4, A. Davis4, L. El-Guebaly4,
S. Gerhardt1, S. Kaye1, C. Kessel1, M. Kotschenreuther3, S. Mahajan3, R. Maingi1, E. Marriott4,
L. Mynsberge4, C. Neumeyer1, M. Ono1, R. Raman5, S. Sabbagh6, V. Soukhanovskii7, P. Valanju3,
R. Woolley1, A. Zolfaghari1
American Nuclear Society
21st Topical Meeting on the Technology of Fusion Energy (TOFE)
9-13 November 2014, Anaheim, CA
This work supported by the US DOE Contract No. DE-AC02-09CH11466
1Princeton Plasma Physics Laboratory, Princeton, NJ 08543
2Oak Ridge National Laboratory, Oak Ridge, TN, USA
3University of Texas, Austin, TX, USA
4University of Wisconsin, Madison, WI, USA
5University of Washington, Seattle, WA, USA
6Columbia University, New York, NY, USA
7Lawrence Livermore National Laboratory, Livermore, CA, USA

## Slide 2: There are several possible pathways from ITER to a commercial fusion power plant
FNSF = Fusion Nuclear Science Facility
CTF = Component Test Facility
ITER
First of a kind
Power Plant
Supporting Physics and Technology
Core Physics
Materials R&D
Plasma Material Interface
Pilot Plant
FNSF/CTF with power-plant like maintenance, Qeng ≥ 1
Qeng = 3-5
e.g. EU DEMO
FNSF/CTF
Blanket R&D, T self-sufficiency
DEMO

## Slide 3: This talk considers possible spherical tokamak (ST) Fusion Nuclear Science Facility (FNSF) options
FNSF = Fusion Nuclear Science Facility
CTF = Component Test Facility
ITER
First of a kind
Power Plant
Supporting Physics and Technology
Core Physics
Materials R&D
Plasma Material Interface
Pilot Plant
FNSF/CTF with power-plant like maintenance, Qeng ≥ 1
FNSF/CTF
Blanket R&D, T self-sufficiency
Qeng = 3-5
e.g. EU DEMO
DEMO

## Slide 4: Overview
Recent U.S. studies for ST-FNSF have focused on assessing achievable missions versus device size
Possible missions:
  Electricity break-even
    Motivated 2010-12 analysis of R=2.2m ST Pilot Plant
  Tritium self-sufficiency (tritium breeding ratio TBR ≥ 1)
    Motivates present (2013-14) analysis of R=1m, 1.7m ST FNSF devices to address key questions:
      How large must ST device be to achieve TBR ≥ 1?
      How much externally supplied T would be needed for smaller ST?
      What are device and component lifetimes?
  Fusion-relevant neutron wall loading and fluence
    STs studied here access 1MW/m2, 6MW-yr/m2 (surface-avg. values)

## Slide 5: Outline
Physics design
Configuration, shielding, tritium breeding
Conclusions

## Slide 6: PF coil set identified that supports combined Super-X + snowflake divertor for range of equilibria
2nd X-point/snowflake increases SOL line-length
Breeding in CS ends important for maximizing TBR
PF coil set supports wide range of li: 0.4 – 0.8
  Elongation and squareness change with li variation
  Fixed strike-point R, controllable B-field angle of incidence (0.5-5˚)
Divertor coils in TF coil ends for equilibrium, high d
Increased strike-point radius reduces B, q||
Strike-point PFCs also shielded by blankets
TF coil
All equilibrium PF coils outside vacuum vessel
PF coil
Blanket
Vessel
Components:

## Slide 7: Up/down-symmetric Super-X/snowflake projected to maintain peak divertor heat flux below material limits
lq = 0.8mm, assume S ≈ lq (closed divertor)
(T. Eich NF 2013)
(Partial) detachment projected
to reduce peak q to < 2MW/m2
Upstream
Te
[eV]
Max.
q
[MW/m2]
Divertor
Target
Conducted
Radiation
lq ≈ 1.2mm (J. Canik IEEE 2013)
Peak q < 10MW/m2

## Slide 8: 0.5 MeV NNBI favorable for heating and current drive (CD) for R=1.7m ST-FNSF
NBCD increases for Einj ≤ 0.5 MeV but saturates for Einj = 0.75 – 1MeV
Fixed target parameters in DD:
  IP = 7.5MA, bN = 4.5, li = 0.5
  ne / nGreenwald = 0.75, H98y,2 = 1.5
  A=1.75, R=1.7m, BT = 3T, k = 2.8
  Te=5.8keV, Ti=7.4keV
Optimal tangency radii:
1.7m ≤ Rtan ≤ 2.4m
Control q(0), qmin
Shine-thru limit
Maximum efficiency: Rtan=2.3-2.4m
0.50

## Slide 9: Free-boundary TRANSP/NUBEAM used to compute profiles for 100% non-inductive plasmas with QDT ~2
Neoclassical cion
ne / nGreenwald = 0.7
H98,y2 = 1.4
IP = 8.9MA, BT = 2.9T
fNICD = 100%, fBS = 65%
PNNBI = 80MW (0.5MeV)
Pfus = 200MW (50-50 DT)
  2.6% alpha bad orbit loss
QDT = 2.5
bN = 5.5, Wtot = 58MJ
  Wfast / Wtot = 14%
Maintain qmin > 2
q(0) / qmin controllable via Rtan and density

## Slide 10: Outline
Physics design
Configuration, shielding, tritium breeding
Conclusions

## Slide 11
R=1.7m configuration with Super-X divertor
Cu/SC PF coils housed in VV lower shell structure
SC PF coils pairs located in common cryostat
TF leads
Vertical maintenance
Design features
Cu/SC PF coils housed in VV upper lid
VV outer shell w/ shield material
Angled DCLL concentric lines to external header
Ports for TBM, MTM, NBI
Blankets
TF coils

## Slide 12: ST-FNSF shielding and TBR analyzed with sophisticated 3-D neutronics codes
CAD coupled with MCNP using UW DAGMC code
Fully accurate representation of entire torus
No approximation/simplification involved at any step:
  Internals of two OB DCLL blanket segments modeled in great detail, including:
    FW, side, top/bottom, and back walls, cooling channels, SiC FCI
  2 cm wide assembly gaps between toroidal sectors
  2 cm thick W vertical stabilizing shell between OB blanket segments
  Ports and FS walls for test blanket / materials test modules (TBM/MTM) and NNBI
TBM
LiPb,
cooling channel,
FCI
Heterogeneous OB Blanket Model,
including FW, side/back/top/bottom walls, cooling channels, and SiC FCI
NBI

## Slide 13: Two sizes (R=1.7m, 1m) assessed for shielding, TBR
Parameter:
Major Radius 1.68m 1.0m
Minor Radius 0.95m 0.6m
Fusion Power 162MW 62MW
Wall loading (avg) 1MW/m2 1MW/m2
TF coils 12 10
TBM ports 4 4
MTM ports 1 1
NBI ports 4 3
Plant Lifetime ~20 years
Availability 10-50%
30% avg
6 Full Power Years
(FPY)
Neutron source distribution

## Slide 14: Peak Damage at OB FW and Insulator of Cu Magnets
Peak dpa at OB midplane = 15.5 dpa / FPY
3-D Neutronics Model of Entire Torus
Dose to MgO insulator = 6x109 Gy @ 6 FPY < 1011 Gy limit
Dose to MgO insulator = 2x108 Gy @ 6 FPY < 1011 Gy limit
Peak He production at OB midplane = 174 appm/FPY
He/dpa ratio = 11.2
Center Stack
OB Blanket
R=1.7m configuration

## Slide 15: Mapping of dpa and FW/blanket lifetime (R=1.7 m Device)
dpa / FPY
Peak =
15.5 dpa / FPY
FW/blanket could operate for 6 FPY
if allowable damage limit is 95 dpa
R=1.7m configuration
 Peak EOL Fluence = 11 MWy/m2

## Slide 16: TBR contributions by blanket region
Inner Blanket Segment = 0.81
Outer Blanket Segment = 0.15
Total TBR ~ 1.03 with no penetrations or ports
(heterogenous outboard blanket)
0.0004
0.0004
0.034
0.034
Breeding at CS ends important:
DTBR = +0.07
R=1.7m configuration

## Slide 17: Impact of TBM, MTM, NBI ports on TBR
No ports or penetrations,
homogeneous breeding zones:
TBR = 1.03
Add 4 Test Blanket
Modules (TBMs)
TBR = 1.02 (DTBR = -0.01)
TBM
LiPb,
cooling channel,
FCI
1 Materials Test Module (MTM)
TBR = 1.01 (DTBR = -0.02)
Ferritic Steel
MTM
4 TBM + 1 MTM + 4 NBI
TBR = 0.97
Approx. DTBR per port:
TBM: -0.25%
MTM: -2.0%
NBI: -0.75%

## Slide 18: Options to increase TBR > 1
Add to PF coil shield a thin breeding blanket (DTBR ~ +3%)
Smaller opening to divertor to reduce neutron leakage
Uniform OB blanket (1m thick everywhere; no thinning)
Reduce cooling channels and FCIs within blanket (need thermal analysis to confirm)
Thicker IB VV with breeding
Potential for TBR > 1 at R=1.7m
PF Coils

## Slide 19: R0 = 1m ST-FNSF achieves TBR = 0.88
TBM
NBI
Distribution of T production
MTM
1m device cannot achieve TBR > 1 even with design changes
Solution: purchase ~0.4-0.55kg of T/FPY from outside sources at $30-100k/g of T, costing $12-55M/FPY

## Slide 20: Summary: R = 1m and 1.7m STs with Γn = 1MW/m2 and QDT = 1-2 assessed for FNS mission
Ex-vessel PF coil set identified to support range of equilibria and Super-X/snowflake divertor to mitigate high heat flux
0.5MeV NNBI optimal for heating & current drive for R=1.7m
Vertical maintenance approach, NBI & test-cell layouts identified
Shielding adequate for MgO insulated inboard Cu PF coils
  Outboard PF coils (behind outboard blankets) can be superconducting
Calculated full 3D TBR; TBR reduction from TBM, MTM, NBI
Threshold major radius for TBR ~ 1 is R0 ≥ 1.7m
R=1m TBR = 0.88  0.4-0.55kg of T/FPY  $12-55M/FPY
R=1m device will have lower electricity and capital cost  future work could assess size/cost trade-offs in more detail

## Slide 21
Backup slides

## Slide 22: FNSF center-stack can build upon NSTX-U design and incorporate NSTX stability results
Like NSTX-U, use TF wedge segments (but brazed/pressed-fit together)
  Coolant paths: gun-drilled holes or grooves in side of wedges + welded tube
Bitter-plate divertor PF magnets in ends of TF achieve high triangularity
  NSTX data: High d > 0.55 and shaping S  q95IP/aBT > 25 minimizes disruptivity
  Neutronics: MgO insulation can withstand lifetime (6 FPY) radiation dose

## Slide 23
Glidcop plates
Insulator
Bitter coil insert for divertor coils in ends of TF

## Slide 24: PF coil currents and current densities
1
2
3
4
5
6
7
8
bN = 5
li = 0.58

## Slide 25
VV lid / PF cryostat enclosure
Full blanket assembly
TF center-stack
Upper TF horizontal legs
Upper dome structure located on test cell shield plug
TF power supplies
JT-60SA NNBI
R=1.7m ST-FNS facility layout
using an extended ITER building

## Slide 26: Summary of ST-FNSF TBR vs. device size
R=1.7m: TBR ≥ 1
R=1.0m: TBR < 1 (≈ 0.9)
TBM
NBI
MTM
TBM
MTM
NBI
1m device cannot achieve TBR > 1 even with design changes
Solution: purchase ~0.4-0.55kg of T/FPY from outside sources at $30-100k/g of T, costing $12-55M/FPY

## Slide 27: MgO insulation appears to have good radiation resistance for divertor PF coils

## Slide 28: Up/down-symmetric Super-X/snowflake  q-divertor < 10MW/m2 even under attached conditions (if integral heat-flux width lq-int > 2mm)
Pheat = 115MW, frad=0.8, fobd=0.8, qpol = 2.1ᵒ
Rstrike = 2.6m, fexp = 1.4, lq-int =2.05mm, Ndiv = 2
Pheat (1-frad) fobd sin(qpol)
2pRstrike fexp lq-int Ndiv
q-strike 
Peak q|| = 0.45GW/m2
1ᵒ angle of incidence
Peak q < 10MW/m2
Eich NF 2013: lq-int = lq + 1.64 × S, lq = 0.78mm, S ≈ lq (closed divertor)
Partial detachment expected to further reduce peak q factor of 2-5×