Shutdown of the EPICPC01 Computer for NSTX Vacuum System

# ==============================================================

# Rev. 0	22JUN00	P. Sichta

# Rev. 1	29JUN00	PS

==============================================================

# 1.0 Introduction

This procedure provides a description of how to shutdown the Personal Computer named EPICPC01.  This computer is located in the NSTX Control Room and is used for remote control of the NSTX Vacuum System.  The control program is RSView32 running on the Windows98 operating system.  Reference (a) describes system startup.

# 2.0 References

- Startup of the EPICPC01 Computer

# 3.0 Procedure

- Select the window called RSView32 Runtime 1500.

- Close the program using the X in the upper-right corner of the title bar.  The program will take about 30 seconds to close.

- Shutdown the computer by poking the mouse on the Start icon on the taskbar, then selecting Shut Down, then poking the Shut down radio button.

- The computer will automatically power down.

- Make a notation in the Vacuum Operations Logbook,  located near the computer.