Shutdown of the NSTXPC05 Computer for NSTX RGA System

# ==============================================================

# Rev. 0	22JUN00	P. Sichta

Rev. 1	29JUN00	PS

Rev. 2    25APR01   JD

==============================================================

# 1.0 Introduction

This procedure provides a description of how to shutdown the Personal Computer named NSTXPC05.  This computer is located in the NSTX Control Room and is used for remote control of the NSTX RGA System.  The control program is Dycor2000 running on the Windows98 operating system.  Reference (a) describes system startup.

# 2.0 References

- Startup of the NSTXPC05 Computer, NSTX-WBS6-OP-011

# 3.0 Procedure

- Select the main Dycor2000 window by poking on the top Title Bar.

The icon looks similar to this:

- Close the program using the X in the upper-right corner of the Title Bar.

- Shutdown the computer by poking the mouse on the Start icon on the taskbar, then selecting Shut Down, then poking the Shut down radio button.

- The computer will automatically power down.

- Make a notation in the Vacuum Operations Logbook, located near the computer.