Startup of the NSTXPC06 Computer for NSTX Vacuum System

# ==============================================================

Rev. 0    25APR01   JD

==============================================================

# 1.0 Introduction

This procedure provides a description of how to startup the Personal Computer named NSTXPC06.  This computer is located in the NSTX Control Room and is used for remote control of the NSTX Shot Mode RGA System.  The control program is Dycor2000, by Ameritek, running on the Windows 2000 operating system.  Reference (a) describes system shutdown.

# 2.0 References

- Shutdown of the NSTXPC06 Computer, NSTX-WBS6-OP-017

# 3.0 Procedure

- The following must be operating normally:

- CI&C RS-232 Communications to NSTX Test Cell

- NSTX Engineering Network

- NSTX Physics Network

- NSTX Engineering Network Firewall

- Turn the NSTXPC05 computer on using its front-panel power switch. Do not use the Ctrl-Alt-Del method.

- During the boot sequence a dialog box will appear entitled Network Password Prompt.  Enter a carriage return at this prompt, no networking password is required.

- Note that the NetBackup program may automatically start.

- Start the Dycor2000 program by double-poking the Ameritek desktop icon entitled shot mode.

The icon looks similar to this :

- Start the Shot Mode RGA program by double-poking the desktop icon entitled shotrga.