# CI&C Operator's Console

# Rev  0  30AUG99  P. Sichta

# Rev  1  29JUN00  P. Sichta

# Rev  2  11APR01  P. Sichta

# 1.0 Introduction

This document will describe how to use a console or x-terminal to support CI&C operations.  Normally the epicsrv console is used, but any x-terminal will do.

# 2.0 References

1)  NSTX-WBS6-OP-008, Engineering Computers Startup Procedure.

# 3.0 Overview

Some EPICS application programs are required to be (continuously) running as an x-windows application in order to properly support NSTX operations.  An example of this is the save_set archiver. This program is used to restore the most-recent operator commands upon an IOC reboot.

Solaris CDE (common desktop environment) offers a 'screen lock' capability.  When the lock icon is depressed or the terminal is not used for 15 minutes, the display will darken and lock.  The password for the current account (or root account) is needed to unlock the screen.  Therefore,  a lockable CDE session will be used by the CI&C operator to run critical applications, those which must be left 'running'.

This procedure is used to establish a CDE-based operator environment for starting and running the software for NSTX Engineering computing.  Reference 1 is a procedure describing how to start and check the necessary programs needed to support NSTX.

# 4.0 Procedure

- Logon to the epicsrv computer using the CI&C Operator account.

- Logon to the epicsrv console using the CI&C Operator's account.  Four CDE desktops will be present:

- Primary

- Archivers

- Logger

- General Purpose

From the Primary session, launch medm (e.g. using the EPICS icon) and navigate to display CH01.

- From the Archivers session, launch medm (e.g. using the EPICS icon) and navigate to display CH01.

- From the Logger session, launch a Terminal application, if one is already not present.

- Follow the epicsrv startup procedures described in Reference 1.

- Lock the display before leaving the control room.