Procedure to Shutdown an EPICS IOC

# Created  09AUG99  P. Sichta

Rev 01  29JUN00  PS

## Table of Contents

### 1.0  Introduction

### 2.0  References

3.0  Procedure

# 1.0 Introduction

This procedure provides a detailed description of how to shutdown an EPICS Input-Output Controller (IOC). Note that all control functions, display pages,  and trending will not work when the IOC is down.

At NSTX, there are presently four IOC.  IOC1 through IOC3 are for NSTX Operations and IOC9 is for development and test.

# 2.0 References

- VxWorks/Tornado Manuals (Wind River Systems).

- Procedure o Reboot an IOC

# 3.0 Procedure

- Local shutdown :

- Depress the RESET button on the front panel of the MVME-177 computer (IOC leftmost slot).

- Remote shutdown :

- Telnet or rlogin to the IOC :

epicsrv1: rlogin epicioc2

(then enter username and password at prompt )

- IOC#2 >   prompt will appear if the IOC#2 is running.

- From the IOC's  '>' prompt type,

IOC2> <st.shutdown_ioc2    (for IOC#2)

(space)

(no space)

It is very important to type the '<' less than sign and not the '>' sign.  The '<' is a "load and execute" instruction. The '>' is a 'redirect/overwrite file' instruction, which will cause the st.shutdown file to be corrupted.

- On some occasions, the current direcory may have been changed and the shutdown file cannot be found by the IOC.  Type pwd to check the current directory, and ls to show the files in that directory.  If the files are not there, change to the correct directory and run the shutdown program again.  The syntax is shown below :

IOC2> cd "/export/home/epics/nstx/epicapps/iocBoot/iocce"