Configuring a Solaris Workstation for running EPICS CA Gateway

Rev 00  21FEB02  P. Sichta

This procedure briefly describes how to configure a new Sun Workstation to run the EPICS Channel Access Gateway Server. This procedure was written for a Sun Workstation running Solaris 8 and EPICS Base R3.13.2 and CA Gateway Server 1.3.2  .

- Partition External Hard disk. For example:

# df -k

Filesystem            kbytes    used   avail capacity  Mounted on

/dev/dsk/c0t1d0s0     242633  124957   93413    58%    /

/dev/dsk/c0t1d0s6    4035072 1386925 2607797    35%    /usr

/proc                      0       0       0     0%    /proc

fd                         0       0       0     0%    /dev/fd

mnttab                     0       0       0     0%    /etc/mnttab

/dev/dsk/c0t1d0s3     963343   78214  827329     9%    /var

swap                  539816       8  539808     1%    /var/run

swap                  717216  177408  539808    25%    /tmp

/dev/dsk/c0t1d0s4    5043072       9 4992633     1%    /data

/dev/dsk/c0t1d0s5    1491121  591199  840278    42%    /opt

/dev/dsk/c0t1d0s7    4884792  105543 4730402     3%    /export/home

- Install Solaris OS (5.8) and patches as req’d.

- Install Solaris SDK

- Install the following (unless stated, more recent versions OK) :

- GNU make-3.79.1

- perl 5.005_01

- gcc-2.95.2

- GNU regex library (version 0.12).

- patchdiag-1.0.4

- ssh-1.2.30

- netbackup client 3.2

- netscape_6.2.1

- acroread-4.05

- tcp_wrappers-7.6

- java JDK